| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Text for M2M Application Addressing |
| Source:* | NEC |
| Contact: | JaeSeung Song, JaeSeung.Song@neclab.eu |
| Date:* | 2013-10-06 |
| Abstract:* | This contribution proposes text for M2M Application Addressing |
| Agenda Item:* | TBD |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this text into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

This contribution proposes text for clause 7.3 M2M Application Addressing.

- Proposal

#### 7.3 	M2M Application Addressing

#### 7.3.1 	M2M Application Addressing

In M2M communication, the goal of M2M addressing is to reach the M2M CSE with which the target M2M application is registered and ultimately the correct application on the M2M Device/Gateway on which the target application is resident. This principle applies to all applications: AE on Application Service Node and Middle Node.

Reachability and routing from/to AE on Application Service Node, Application Dedicated Node and Middle Node M2M applications is always associated with the CSE, with which these applications are registered, and which is resident on M2M Device/Gateway connected to the underlying network. Reaching an application shall be performed through reaching the CSE the application registered to. An M2M-PoA (M2M Point of Access) shall provide the set of information needed to reach an CSE from a network perspective. Typically an M2M-PoA contains information that is e.g. is resolved into a network address.

#### M2M Application Reachability

#### 7.3.2.1		M2M Communication Point of Access (M2M-PoA)

The M2M-PoA shall be used by the M2M system to communicate with a CSE on Application Service Node or Middle Node. Once communication with a CSE is achieved, any application registered in the CSE can be reached as long as this application can be uniquely identified.

The M2M-PoA for a CSE shall be provided to the M2M system at registration of a CSE. For Application Dedicated Nodes, the M2MPoA shall be provided at registration of the CSE on Middle Node. For Application Service Nodes, the M2M-PoA shall be provided at the registration of the M2M device.

The information included in the M2M-PoA, as well as the refresh of the M2M-PoA, depends on the underlying network and the M2M transport device capabilities.

#### 7.3.2.2		Principles guiding Locating Applications

Locating a D/GA/D'A M2M application is a two-step process as follows:

Step 1: There is a need to locate the M2M CSE (for Application Service Node and Middle Node) where the M2M Application Entity is registered. Locating the M2M CSE shall be accomplished as follows:

For AEs associated with Application Service Nodes the M2M-PoA of the CSE (for Application Service Node) registered object shall be used for that purpose.

For AEs associated with Application Dedicated Nodes and Middle Nodes, the M2M-PoA of the CSE (for Middle Node) registered object shall be used for that purpose.

Step 2:  the CSE on Middle Node and CSE on Application Service Node shall locate the appropriate AE using the registered application identifier (i.e., APP-Inst-ID) for that purpose.

#### 7.3.2.3		Usage of M2M-PoA by the M2M System

The M2M-PoA holds the information used by the M2M system to locate routing information for a CSE. This information shall be provided by the registered CSE at registration time. However, locating routing information related to a CSE (and ultimately to the desired application) in an M2M system depends on the characteristic of the underlying access network. This impacts the criteria for updating the M2M-PoA by the registered CSE (in addition to the regular CSE registration refresh) and the information to be conveyed in there as well to support the access network specifics.

In general the easiest routing information related to a CSE is achieved when a static public IP address is assigned to M2M Device/Gateway, as it is possible to rely on direct DNS address translation or dynamic DNS address translation.

In those circumstances, the M2M-PoA for an M2M registered CSE shall have a URI conforming to RFC 3986 [xx] as follows:

URI = scheme:/fullyqualifieddomainname/path/; or

URI = scheme://ip-address/path/

The following clauses further specify the information to be conveyed in the M2M-PoA by a registered CSE for the various access networks, as well as criteria for updating the M2M-PoA for the registered M2M CSE, in addition to the normal M2M CSE registration refresh.

7.3.2.3.1	M2M-PoA related to M2M CSEs associated with a Fixed Network

In this case the M2M-PoA for an M2M registered CSE shall have a URI as described above. If the IP address is private, then the address is usually built based on the address of the related PPP protocol which is a public IP address. This in turn is mapped to the corresponding private address.

7.3.2.3.2	M2M-PoA related to M2M CSEs associated with Mobile Networks

If the IP address for the registered CSE cannot be reliably used, and as such cannot be included in the M2M-PoA, then in this case the M2M-PoA for the registered CSE shall include appropriate information as defined by various access networks.

Each access network shall specify the means for allowing an M2M SP to fetch the IP address associated with a CSE attaching to that access network and consequently the information to be included in the M2M-PoA for the registered CSE.

In the event that the M2M SP has connections to multiple access networks, there is a need to establish a binding between the registered CSE and the access network. That binding may be established through CSEs explicitly listing the access network at registration/update time, otherwise the M2M SP may derive it (using the link over which the registration arrived), store it and bind it to the registration information.

7.3.2.3.3	M2M-PoA to M2M CSEs associated with multiple access networks

When the M2M transport device attaches to a fixed network, the M2M-PoA for a registered M2M CSE shall conform to the procedures associated with a fixed network.

When the M2M transport device attaches to a mobile network, the M2M-PoA for a registered M2M CSE shall conform to the procedures associated with mobile networks.

If an M2M transport device already attached to an access network attaches to a new access network, the M2M CSE shall update its reachability data.