| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Introduce a new section for Z Reference point |
| Source:* | NEC Corporation |
| Contact: | JaeSeung Song, NEC Lab Europe, (JaeSeung.Song@neclab.eu) Joerg Swetina, NEC Lab Europe, (Joerg.Swetina@neclab.eu) Ataru Kobayashi, NEC, (a-kobayashi@df.jp.nec.com) Takanori Iwai, NEC, (t-iwai@hx.jp.nec.com) Tetsuo Inoue (t-inoue@fp.jp.nec.com) Masaharu Hattori (m-hattori@kddilabs.jp) |
| Date:* | 2013-10-14 |
| Abstract:* | This contribution proposes a new section for Z reference point. |
| Agenda Item:* | Tbd |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and adaption to add the skeleton of a new chapter for Z reference point. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

This contribution proposes the skeleton of a new Section for Z reference point and to add normative references to 3GPP.

-------------------------------The first change start -----------------------------------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	 ETSI TR 102 473: "<Title>".

[i]	 3GPP TS 23.682: "<Architecture enhancements to facilitate communications with packet data networks and applications>".

[i+1]           3GPP TS 29.368: “<Tsp interface protocol between MTC-IWF and SCS>”.

------------------------------ End of the first change ----------------------------------------

------------------------------- A new chapter start -----------------------------------------

# x.			Z Reference Point

Z reference point is for communication between CSE and Underlying Networks, accessing network service functions provided by Underlying Netwokrs, and optimizing network service processing for Underlying Networks. Such services do not include the general transport services.

Z reference point shall be taken into account the type of CSE, type of Underlying Network, and provided network functions, how control the connection link and the procedure of requests.

This chapter includes following sub-clauses.

- General communication flow scheme (mainly link management)

- Network Service Exposure functions for different type of CSE

- Type of Underlying networks, NSE, and Protocol characteristics

- Protocol specific message flow

## x.1		General Communication Flow Scheme

### x.1.1  Description

As Z reference point, following common flows mainly as link managements are described on this sub-clause.

- Link Connection

- Link Disconnection

- Link Monitoering

These procedures are applied for connection oriented.

Editor’s Note; another opinion says that link management depends on selected protocol. So oneM2M does not necessary to standardize the link management. Just mentioning to adapt some protocols is enough. This is FFS.

- Request

- Successful Response

- Unsuccessful Response

- Asyncronous response toward previous request

- Procedure for accessing resources in CSE

Editor’s Note; How to ensure the request to be confirmed for connection-less is FFS.

### x.1.2 	Link connection

Editor’s Note; Description is FFS.

### x.1.3 	Link disconnection

Editor’s Note; Description is FFS.

### x.1.4 	Link monitoring

Editor’s Note; Description is FFS.

### x.1.5 	Request

Editor’s Note; Description is FFS.

### x.1.6 	Successful response

Editor’s Note; Description is FFS.

### x.1.7 	Unsuccessful response

Editor’s Note; Description is FFS.

### x.1.8 	Asyncronous response toward previous request

Editor’s Note; Description is FFS.

### x.1.9 	Procedure for accessing resources in CSE

CSE can have possibility to help M2M application developers.

One of them is a protocol conversion.

In oneM2M, RESTful in X reference point converted into another protocol in Z reference point for example Tsp Diameter protocol.

And for X reference point, something resources are necessary.

So end-to-end communication between X and Z reference points are following principles.

- Communication from AE to NSE via CSE;

Step-1. AE requests to update the resource (attributes or contents) in CSE

Step-2. CSE updates the resource

Step-3. CSE triggers communication to NSE by the updating of the resource

- Communication from NSE to AE via CSE;

Step-1. NSE requests to communicate with CSE

Step-2. CSE updates some resources by the receiving from NSE

Step-3. CSE informs the updating of the resources to AE if it has been subscribed in advance

Case-1) Originator is AE

Editor’s Note; Description is FFS.

Case-2) Originator is NSE

Editor’s Note; Description is FFS.

## x.2	Network Service Exporsure Functions for different type of CSE

Editor’s note; Description is FFS.

### x.2.1 	NSE for Application Service Node(ASN)

Editor’s note; Description is FFS.

### x.2.2 	NSE for Mddle Node(MN)

Editor’s note; Description is FFS.

### x.2.2 	NSE for Infrastructure Node(IN)

Editor’s note; Description is FFS. Requirement OSR-006 mentionded following.

The M2M System shall be able to reuse the services offered by underlying networks to M2M Applications and/or M2M Service Layer, by means of open access models (e.g. OMA, GSMA OneAPI framework). An example of available services is:

- IP Multimedia communications

- Messaging

- Location

- Charging and billing services

- Device information and profiles

- Configuration and management of devices

- Triggering, monitoring of devices

- Small data transmission

- Group management

The set of features or APIs to be supported depends on the M2M Service Capabilities and access to available APIs.

## x.3	Type of Underlying networks, NSE, and protocol characteristics

Editor’s note; Description is FFS.

### x.3.1 	3GPP Tsp Reference Point

This sub-clause summarizes 3GPP MTC architecture and its protocol characteristic based on 3GPP specifications (ref.[i], ref.[i+1]).

Editor’s note; Description is FFS.

#### x.3.1.1	 MTC Architecture

Editor’s note; Description is FFS.

Figure x.3.1-1  3GPP Architecture for Machine-Type Communication

#### x.3.1.2	 Tsp reference point requirements

Editor’s note; Description is FFS.

#### x.3.1.3	 A 3GPP Network Element (MTC-IWF) related to oneM2M

Editor’s note; Description is FFS.

#### x.3.1.4	 Device Triggering Function

Editor’s note; Description is FFS.

#### x.3.1.5	 External Identifier

Editor’s note; Description is FFS.

#### x.3.1.6	 Security Requirements on Tsp Reference Point

Editor’s note; Description is FFS.

#### x.3.1.7	 Device triggering procedure over Tsp

Editor’s note; Description is FFS.

Figure x.3.1-2 Device triggering procedure over Tsp

#### x.3.1.8	 Procedures over Tsp reference point

Tsp reference point provides following procedures. Detail procedures are given by 3GPP Tsp interface protocol specification (ref.[i+1]).

- Request and confirmation of a device trigger

- Notification of Device trigger

- Reference number handling

- MTC-IWF selection

- MTC-IWF load control

#### x.3.1.9  Tsp protocol characteristics

Tsp protocol has following characteristics. Detail features are given by 3GPP Tsp interface protocol specification(ref[i+1]).

- Use of Diameter base protocol

- Transport protocol

- Advertising Application Support

- Initialization and maintenance of connection and session

- Mutual authentication

- Security profiles

- Tsp Messages

- Table x.3.1-1: Command-Code values for Tsp

| Command-Name | Abbreviation | Code | Section |
| --- | --- | --- | --- |
| Device-Action-Request | DAR | 8388639 | 6. 6.2 |
| Device-Action-Answer | DAA | 8388639 | 6. 6.3 |
| Device-Notification-Request | DNR | 8388640 | 6. 6.4 |
| Device-Notification-Answer | DNA | 8388640 | 6. 6.5 |

- Tsp specific AVPs

- Table x.3.1-2: Tsp specific Diameter AVPs

|  |  |  |  | AVP Flag rules (note 1) |
| --- | --- | --- | --- | --- |
| Attribute Name | AVP Code | Clause defined | Value Type | Must | May | Should not | Must not |
| Device-Action | 3001 | 6. 4.2 | Grouped | M,V | P |  |  |
| Device-Notification | 3002 | 6.4.3 | Grouped | M,V | P |  |  |
| Trigger-Data | 3003 | 6.4.4 | Grouped | M,V | P |  |  |
| Payload | 3004 | 6.4.5 | OctetString | M,V | P |  |  |
| Action-Type | 3005 | 6.4.6 | Enumerated | M,V | P |  |  |
| Priority-Indication | 3006 | 6.4.7 | Enumerated | M,V | P |  |  |
| Reference-Number | 3007 | 6.4.8 | Unsigned32 | M,V | P |  |  |
| Request-Status | 3008 | 6.4.9 | Enumerated | M,V | P |  |  |
| Delivery-Outcome | 3009 | 6.4.10 | Enumerated | M,V | P |  |  |
| Application-Port-Identifier | 3010 | 6.4.11 | Unsigned16 | M,V | P |  |  |

## x.4	Protocol specific message flow

Editor’s note; Description is FFS.

This sub-clause provides message flow for each protocol with relation of oneM2M part (i.e. X and/or Y reference points).

### x.4.1 	3GPP Tsp protocol

Editor’s note; Description is FFS.

------------------------------ End of second change -----------------------

--------------------------- End of contribution ---------------------------------

# Text boxes

Originator

Receiver

- Connect link request

- Connect link accept

- Create link credential

- Create link credential

Originator

Receiver

- Disconnect link request

- Disconnect link accept

- Remove link credential

- Remove link credential

Originator

Receiver

- Watch dog request

- Watch dog response

- Decide link status

- Trigger to request

Originator

Receiver

- Request

- Action

Originator

Receiver

- Response (success)

2. Action incl. check whether subsequent response may come

Originator

Receiver

- Response (failure or error)

2. Action incl. check whether recommended next action exists or not

Originator

Receiver

- Request

2. Response (Acknologed)

- Request (for result)

4. Response (Acknologed)

AE

CSE

NSE

- Trigger to request to NSE

- Request (Update resources)

- Response (success)

- Request

- Action

NSE

CSE

AE

3. Update resources and then trigger to request to AE

- Request

- Response (success)

- Request

- Action