| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | CR against TS0001v0.1.2 including change marks |
| Date:* | 2013-10-05 |
| Contact:* | Josef Blanz (jblanz@qti.qualcomm.com) |
| Reason for Change/s:* | This CR is proposing changes to clarify how synchronous procedures to access resources could be specified such that synchronous and asynchronous processing could be accomplished without enforcing potentially long blocking times |
| Clause/Sub Clause Affected* | 8.2 |
| Agenda Item:* |  |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | Architecture TS 0001v0.1.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed changes into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Rationale

We cannot expect that an Originator will always be able to wait for a ‘synchronous’ response when accessing a resource, i.e. a response that is in synch with the completion of the requested operation. So far in Clause 8.2 it is assumed that such “Blocking” requests are used. In practice this may lead to  possibly long blocking times for pending request, especially when they target remotely hosted resources or the access to resources is very slow.

In case this blocking or requests takes a (very) long time, we need a way to respond to the originator before the operation has completed and allowing the originator to get the result of the requested operation later on.

For instance power-constraint devices acting as an Application Dedicated Node may not be able to wait for a response, not even a short time. They may want to express a request as quickly as possible and find out if the Local CSE got the request and then go sleep ASAP. If needed at all, they may poll the result of the requested operation when they wake up next time.

Even for devices that are not power constraint, long blocking periods for pending requests may require to program AE with multiple threads, which is not always feasible.

More capable Originators may actually want the local CSE to send back the result of an operation to a specific reference (URI) as an asynchronous notification that the Originator can handle.

Therefore, we need a way to respond to the Originator before the operation has completed and allowing the originator to get the result of the requested operation later on

This is partially anticipated by some of the parameters in clause 8.1.2 (response type)… but the concept is not consistently defined in the specs so far.

The attached CR is aiming at fixing this.

### ==================== Start Text Proposal ===================

## 8.2	Procedures for Accessing Resources

This clause describes the procedures for accessing the resources. The procedures include:

- Generating Responses to the Requests for accessing resources,

- Accessing the resources that may be located in different CSEs.

Editor’s Note: Other procedures related to accessing the resources are FFS.

### 8.2.1	Generating Responses

The following types of Responses are supported for accessing the resources over the X and Y reference points:

- Success: indicates to the Originator that the Request has been executed successfully by the Hosting CSE.

- Failure: indicates to the Originator that the Request has not been executed successfully by the Hosting CSE.

Both, the Success and the Failure Response types may convey other information – e.g. the result of the requested operation –to the Originator of the Request. More specific details on what other information shall be conveyed with the responses may be defined by using the ‘rc’ information as part of the original request, see clause 8.1.2.

Detailed Success and Failure codes are provided in the Protocol specifications.

Editor’s Note: References to Protocol specifications will be provided when available.

- In addition to the above mentioned Success and Failure Response types, there is another Response type that indicates an Acknowledgement of the Request. This indicates to the entity that issued the Request that the Request has been received and accepted by the attached CSE,  i.e. by the CSE that received the request from the issuing entity directly , but it has not executed the Request yet. The Success or the Failure of the execution of the Request is to be conveyed later.

Editor's Note: Details of Acknowledgement Response type is FFS.

### 8.2.2	Accessing Resources in CSEs – Blocking Requests

For the procedures described herein, the addressed resource can be stored in different CSEs. Table 8.2.2-1 describes the possible scenarios, where the addressed resource may be on the local-CSE or on a CSE located elsewhere in the oneM2M System.

In this sub-clause – for simplicity – it is assumed that the Originator of a request can always wait long enough to get a response to the request after the requested operation has finished. This implies potentially long or unknown blocking times (time for which a pending request has not been responded to) for the Originator of a request.

For scenarios that avoid such possibly long blocking times, sub-clause 8.2.3 specifies mechanisms to handle synchronous and asynchronous resource access procedures via returning appropriate references.

Editor’s Note: How the target of a Request (i.e, an Application or local/hosting CSE) is identified and addressed, is FFS.

Editor’s Note: A message (Request, Response) can be forwarded immediately or forwarded at a later time (e.g in the case of congestion).The procedures related to the forwarding of the Request at a later time are FFS.

Table 8.2.2-1 Accessing Resources in different CSEs

| Traversals across X/Y Reference Points | Description | Reference |
| --- | --- | --- |
| No Hops | The Originator of the Request accesses a resource. The Originator of the Request can be an Application or a CSE. Local CSE and Hosting CSE are the same entity. The CSE shall check the Access Rights for accessing the resource. Depending on the expected result content, the CSE shall respond to the Originator of the Request, either with a Success or Failure Response or not at all. | Figure 8.2.2-1 |
| 1 Hop | The Originator of the Request accesses a resource. The Originator of the Request may only be an Application. Local CSE and Hosting CSEs different entities. Local CSE shall forward the Request to the Hosting CSE, after an optional checking of the Access Rights for accessing the resource and the syntax of the Request message.. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response or not at all. | Figure 8.2.2-2 (Editor's Note-1) |
| Multi Hops | The Originator of the Request accesses a resource. The Originator of the Request may be an Application or a CSE. Local CSE, Intermediate CSE(s) and the Hosting CSE are different entities. Local CSE shall forward the Request to an Intermediate CSE (e.g. MN-CSE) that the Local CSE is registered with, if it cannot communicate with the Hosting CSE directly. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message may be performed prior to forwarding the Request. Intermediate CSE may forward the Request to another Intermediate CSE (e.g. another MN-CSE) that the Intermediate CSE is registered with, if it cannot communicate with the Hosting CSE directly. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message can be performed prior to forwarding the Request.. The Intermediate CSE shall forward the request to the Hosting CSE. An optional checking of the Access Rights and the syntax of the Request message can be performed prior to forwarding the Request.. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response or not at all. | Figure 8.2.2-3 (Editor's Note-2) |
| Editor's Note-1: One-Hop case could potentially include the CSE-to-CSE communication also. The need for such procedures is FFS. Editor's Note-2: The multi-hop procedures addresses the scenario when the target is on a specific remote CSE. How a flow will works when the target is distributed on multiple remote CSEs is FFS. |

Figure 8.2.2-1: Originator accesses a resource on the Local CSE (No Hops)

Figure 8.2.2-2: Application accesses a resource at the Hosting CSE (One Hop)

### Figure 8.2.2-3: Originator accesses a resource at the Hosting CSE (Multi Hops)

### 8.2.3	Accessing Resources in CSEs – Non-Blocking Requests

8.2.3.1	Response with Reference to Result of Requested Operation

In case the Originator of a request has asked for only responding with an Acknowledgement of the request and a reference to the result of the requested operation – see ‘rt’ information in clause 8.1.2 – it is necessary to provide a prompt response to the Originator with a reference to an internal resource on the Local CSE or another specified reference, so that the Originator can retrieve the outcome of the requested operation at a later time. The details of such an internal resource are defined in clause 9.6.X. The reference is provided in the response to the request. The abbreviation Req-Ref is used for simplicity in the figures of the following clauses.

Two different cases are defined in the following two clauses for allowing the Originator of a request to retrieve the result of a requested operation.

8.2.3.2	Synchronous Case

In the synchronous case, it is assumed that the Originator of a request is not able to receive asynchronous messages, i.e. all exchange of information between Originator and Local CSE need to be initiated by the Originator.

In that case the information flow depicted in Figure 8.2.3.2-1 is applicable. For the flow depicted in Figure 8.2.3.2-1 it is assumed that completion of the requested operation happens before the Originator is trying to retrieve the result of the requested operation with a second request referring to the Req-Ref provided in the response to the original request.

Another variation of the information flow for the synchronous case is depicted in Figure 8.2.3.2-2. In this variation it is assumed that the requested operation completes after the second request but before the third request sent by the Originator.

Equivalent information flows are valid also for cases where the target resource of the requested operation is not hosted on the Local CSE. From an Originator’s perspective there is no difference as the later retrieval of the result of a requested operation would always be an exchange of request/response messages between the Originator and the Local CSE using the reference to the original request.

### Figure 8.2.3.2-1 Non-blocking access to resource in synchronous mode (Hosting CSE = Local CSE), requested operation completed before second request.

Figure 8.2.3.2-2 Non-blocking access to resource in synchronous mode (Hosting CSE = Local CSE), requested operation completed after the second but before the third request.

### 8.2.3.3	Asynchronous Case

In the asynchronous case, it is assumed that the Originator of a request is actually able to receive notification messages, i.e. the Local CSE could send an unsolicited message to the Originator at an arbitrary time to send the result to a notification target. The possible mechanisms how the notification then reaches the Originator are the same as in the case of a notification after a subscription.

In that case the information flow depicted in Figure 8.2.3.3-1 is applicable. In this caseit is assumed that the Originator of the request provided a reference – notificationReference – for notification when the result of the requested operation is available.

### Equivalent information flows are valid also for cases where the target resource of the requested operation is hosted on the Local CSE. From an Originator’s perspective there is no difference as the later notification of the result of a requested operation would always be an exchange of request/response messages between the Originator and the Local CSE using reference to the original request.

### Figure 8.2.3.3-2 Non-blocking access to resource in notification mode (Hosting CSE not equal to Local CSE), Originator provided reference for notification.