| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP7 |
| Title:* | Functional architecture in oneM2M-TS-0001 oneM2M Functional Architecture-V-0.1.2 |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2013-10-04 |
| Abstract:* | Proposal to include the following definitions in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes modification to the current definition of M2M-Request-ID to remove some of the editor notes

# 7.	M2M Identification and addressing

### 7.1.8 CSE Request Identifier (M2M-Request-ID)

This is an identifier that tracks a request initiated by a CSE, over the Y-interface and Z interface, if applicable, end to end. It is also included in the response to the request. The M2M-Request-ID is allocated by the CSE initiating the request. The request initiated by the CSE could be the result of an application request, or a request initiated autonomously by the CSE to fulfil a service.

To enable applications initiating multiple instances simultaneously to track requests and corresponding responses over the X-interface, these applications shall include a distinct request identifier per request over the X-interface to the CSE for an initiated request. The CSE shall maintain a binding between the application request identifier and the M2M-Request-ID it initiates towards other peer CSEs until a response is returned to the application.  The CSE shall include the application request identifier in its response to the application where applicable.

A CSE receiving a request from a peer CSE shall include the received M2M-Request-ID in all additional requests it has to generate (including propagation of the incoming request) and that are associated with the incoming request, where applicable.

The CSE shall include the same M2M-Request-ID in its interactions with the underlying network, over the Z-interface where applicable

An M2M-Request-ID allocated to a request by a CSE shall be globally unique.

Editor’s Note: Bring in a contribution to indicate where this information will carried