| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | M2M Identifiers lifecycle and characteristics |
| Source:* | LG Electronics |
| Contact: | SeungMyeong Jeong (seungmyeong.jeong@lge.com) |
| Date:* | 2013-10-07 |
| Abstract:* | Summary of oneM2M Identifiers |
| Agenda Item:* | TBD |
| Work item(s): | WI-0002 oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate this into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

Though there are descriptions for oneM2M identifiers in clause 7.1, it cannot be assured that we have the same understanding on each ID. During the process of this summary work, we’d have better common understanding.

Some descriptions do not contain necessary information, so this contribution points out them as FFS.

A few ID may need to be reconsidered whether we really need that, for example M2M-App-ID has many out-of-scope characteristics.

*********************** Beginning of Text1 ***********************

## 7.2	M2M Identifiers lifecycle and characteristics

| Name | Assigned by | Assigned to | Assigned during | Lifetime | Scope | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M-SP-ID | (out-of-scope) | AE, CSE | (out-of-scope) | (out-of-scope) | global | FFS |  |
| M2M-App-Inst-ID | FFS | AE | registration unless pre-provisioned | Lifetime of AE (from registration to de-registration of application) | global | information flows (clause 10) | Editor’s Note: Discussion on App-Inst vs. AE needed |
| M2M-App-ID | (out-of-scope) | (out-of-scope) | (out-of-scope) | (out-of-scope) | global | Assigning M2M-App-Inst-ID |  |
| M2M-CSE-ID | M2M-SP | CSE | registration unless pre-provisioned | equal to CSE lifetime | global | information flows (clause 10) | CSE-ID and Node-ID can be the same |
| M2M-Node-ID | M2M-SP | M2M Node | pre-provisioned | equal to M2M Node | global | FFS | CSE-ID and Node-ID can be the same |
| M2M-Sub-ID | M2M-SP | CSE | pre-provisioned | (out-of-scope) | M2M-SP | charging and accounting | Editor’s Note: M2M Service needs to be clarified |
| M2M-Request-ID | AE, CSE | A request message initiated by an AE or a CSE | When a CSE sends a request to a peer CSE. | from the ID assignment at CSE to retrieval of the response | CSE | information flows (clause 10) |  |
| M2M-Ext-ID | FFS | CSE | FFS | Lifetime of CSE | FFS | Call flows on Z reference point | M2M-Ext-ID shall be mapped with M2M-CSE-ID |

*********************** End of Text1 ***********************