| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#7 - ARC WG |
| Title:* | M2M Service Session Usage Scenario Call Flow Examples |
| Source:* | InterDigital |
| Contact: | Guang Lu (guang.lu@interdigital.com) Paul Russell (Paul.Russell@InterDigital.com) |
| Date:* | <2013-10-06> |
| Abstract:* | Provides usage scenario call flows that use M2M service sessions and Session Management CSF functionality |
| Agenda Item:* | Session Management CSF |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussions of session management functionality |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Rationale

Present some usage scenario call flows for M2M service session management.

2	M2M Session Management Call Flows

# Summary of M2M Service Session Use Case Scenario Call Flows:

- Call Flow #1 – M2M service session establishment between AE1 and AE2 using SMG CSF resources and functionality hosted on CSE1 and CSE2

- Call Flow #2 – M2M service session usage – AE1 performs a session-based update of AE2 container resource hosted on CSF2 using SMG CSF resources and functionality hosted on CSE1 and CSE2

- Call Flow #3 – M2M service session termination -  AE1 terminates session using SMG CSF  functionality hosted on CSE1 and CSE2 to tear down session resources

Step 1: 	CSE1 and CSE2 register to one another and exchange M2M Service Session Management capabilities with one another

Step 2: 	AE1 and AE2 register to CSE1 and CSE2 and advertise they support M2M session based communication using a CREATE request

Step 3:	AE2 subscribes to the sessions collection resource hosted on CSE2.  Included in the subscription request is a callback URI which notifications can be sent to.  This is done to receive notifications if/when a M2M service session establishment request is received by CSE2.  This is done via a CREATE request

Step 4:	CSE2 creates a subscriptions to the sessions resource for AE2, respectively.

Step 5:	CSE2 return a positive response to the subscription CREATE request

Step 6:	AE1 discovers AE2 and its capability to support M2M session-based communication.  This is done via a resource discovery request that is serviced CSE1 and CSE2.  Discovery results include information such as the M2M identifiers (e.g. application ID, node ID, etc) for AE2 which AE1 can use to establish a M2M session with AE2.

Step 7: 	AE1 requests to establish M2M service session with AE2 by sending a <session> resource CREATE request to CSE1 that includes AE2 identifier information as well as AE1 information.

Step 8: 	CSE1 allocates a unique end-to-end session identifier and session credentials

Step 9:	CSE1 forwards the session establishment request to the next hop (which is CSE2 in this example).

Step 10:	Session Management CSF on CSE2 receives and processes M2M service session establishment request targeting AE2.

Step 11:	Session Management CSF on CSE2 sends notification of the M2M service session establishment request to AE2.  CSE2 includes the session identifier and credentials as well as AE1 session information in the notification such as AE1’s M2M identifier(s), etc.  This information is used by AE2 to form messages to send to AE1 via the M2M service session.

Step 13: 	AE2 returns a positive response to the notification request indicating that it is interested and willing to enter into a M2M service session with AE1.  Included in the response is session establishment information specified by AE2.

Step 14:	Session Management CSF on CSE2 creates a M2M service <session> resource and <sessionEndpoint> resources for both AE1 and AE2 in which it stores session information (e.g. sessionID, endpoint identifiers, etc).  In addition a <nextHop> resource is also created for CSE1.

Step 15:  	Session Management CSF on CSE2 returns a positive response to the M2M service session establishment CREATE request to the Session Management CSF on CSE1

Step 16: 	Session Management CSF on CSE1 creates M2M <session> resource and <sessionEndpoint> resources for both AE1 and AE2 in which it stores session information (e.g. sessionID, endpoint identifiers, etc).  In addition a <nextHop> resource is also created for CSE2.

Step 17: 	Session Management CSF on CSE1 returns positive response to M2M service session establishment CREATE request to AE1.  Response includes session ID and other information.

Step 18:	AE1 sends a request to CSE1 to create a session policy to support a desired level of QoS that it requires for the session (e.g. message should not be store-and-forwarded).

Step 19:	Session Management CSF on CSE1 forwards request to next hop Session Management CSF on CSE2.

Step 20:	Session Management CSF on CSE2 creates <sessionPolicy> resource.

Step 21:	Session Management CSF on CSE2 returns a positive response to Session Management CSF on CSE1

Step 22:	Session Management CSF on CSE1 creates <sessionPolicy> resource

Step 23:	Session Management CSF on CSE2 returns a positive response to AE1

Step 1:	AE1 sends a session-based request to CSE1 to update an AE2 container resource hosted on CSE2 (Note, example assumes AE2 has already created container resource on CSE2 and AE1 is aware of container resource)

Step 2:	CSE1 detects request is session based and passes it to SMG CSF to process

Step 3:	Based on sessionID, SMG CSF on CSE1 verifies URI targets a valid session endpoint (AE2’s container1 resource)

Step 4:	Based on targeted session endpoint, SMG CSF on CSE1 determines next hop is CSE2

Step 5:	Based on sessionID and targeted session endpoint,  SMG CSF on CSE1 finds session policy defining store-and-forward scheduling policy

Step 6:	Based on policy, CSE1 stores request until off-peak hours and then forwards it to CSE2 during off-peak hours

Step 7:	CSE1 forwards request to CSE2

Step 8:	CSE2 detects request is session based and passes it to SMG CSF to process

Step 9:	Based on sessionID, SMG CSF on CSE2 verifies URI targets a valid session endpoint (AE2’s container1 resource)

Step 10:	Based on targeted session endpoint, SMG CSF on CSE2 determines request targets local AE2 container resource

Step 11:	Based on sessionID and targeted session endpoint, SMG CSF on CSE2  finds session policy that requires immediate response

Step 12:	Based on policies, CSE2 services request and returns immediate response

Step 13:	SMG CSF on CSE2 creates session context to keep track of session request/response history

Step 14:	CSE2 sends response to CSE1

Step 15:	SMG CSF on CSE1 creates session context to keep track of session request/response history

Step 16:	SMG CSF on CSE1 sends response to AE1

Step 17:	SMG CSF on CSE2 notifies session endpoint that container was updated

Step 18:	Session Management CSF on CSE2 sends notification to AE2 that container1 resource was updated as part of the session.

Step 19:	AE2 responds with a positive response that it received the notification

Step 20:	AE2 sends session-based RETRIEVE request to CSE2 to retrieve updated container resource

Step 21:	CSE2 detects request is session based and passes it to SMG CSF to process

Step 22:	Based on sessionID, SMG CSF on CSE2 verifies URI targets a valid session endpoint (AE2’s container1 resource)

Step 23:	Based on targeted session endpoint, SMG CSF on CSE2 determines request targets local AE2 container1 resource

Step 24:	Based on sessionID and targeted session endpoint, SMG CSF on CSE2 finds session policy that requires immediate response

Step 25:	Based on policies, CSE services request and returns immediate response

Step 26:	SMG CSF on CSE 2 creates session context to keep track of session request/response history

Step 27:	CSE2 returns response to AE2

# Step 1: 	AE1 sends a M2M session termination request to CSE1 using a DELETE

Step 2: 	Session Management CSF on CSE1 processes request and determines which next hop Session Management CSFs on other CSEs it needs to forward session termination request to such that session state on these CSEs can be torn-down.   In this example, Session Management CSF on CSE2 is the next hop detected.

Step 3:	Session Management CSF on CSE1 forwards session termination request to Session Management CSF on CSE2

Step 4:	Session Management CSF on CSE2 notifies session endpoint (AE2) that session is being terminated

Step 5:	AE2 processes notification and deletes locally stored M2M session state

Step 6:	AE2 returns a positive response to the notification request indicating it has removed its local M2M session state

Step 7: 	Session Management CSF on CSE2 deletes its locally hosted <session> resource and all child resources.  Session Management CSF also deletes any local session state such as security credentials and identifiers allocated to the session

Step 8: 	Session Management CSF on CSE2 returns a positive response to the session termination DELETE request to the Session Management CSF on CSE1

Step 9:	Session Management CSF on CSE1 deletes its locally hosted <session> resource and all child resources.  Session Management CSF also deletes any local session state such as security credentials and identifiers allocated to the session

Step 10:	Session Management CSF on CSE1 returns a positive response to the M2M service session termination DELETE request to AE1

Step 11:	AE1 deletes locally stored M2M session state