| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Virtual Resource Description |
| Source:* | LG Electronics |
| Contact: | Heedong Choi (heedong.choi@lge.com) |
| Date:* | 2013-10-07 |
| Abstract:* | This contribution revises a description of the virtual resource in the chapter 9. |
| Agenda Item:* | Tbd |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussions and adoption in Functional Architecture Technical Specifications |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

Although the virtual resource is one of resources, the description is defined vaguely. In this contribution, we focus on distinct descriptions and differences compared to the generic resource.

- Proposal

## Beginning of Text ##

9.3		Resource Structure

9.3.4	Types of Virtual resources

A virtual resource is a resource that does not a resource representation (e.g., child resource, attributes), so it does not have any child resources and attributes, and the CRUD operations for the virtual resource are limited. However, virtual resources are still addressable; they can be accessed and manipulated by using the resource specific procedures.

One of the virtual resource examples is the discovery resource.

Editor’s Note: The list of virtual resources is FFS.

## End of Text ##