| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Containers, Content instances and Access Rights resources and flows |
| Source:* | DoCoMo, IDC, Cisco, NEC, Fujitsu, HTC , Huawei , ALU, LG Electronics Telecom Italia |
| Contact: |  |
| Date:* | 2013-17-06 |
| Abstract:* | This contribution describes the Container, containeristance and Access Rights resources,togheter with their correlated flows |
| Agenda Item:* | Tbd |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Adopt the proposed description |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# 2. Proposal

## begin of proposed text ##

### 9.5.1	Common attributes

Many of the attributes of the resources described in the present document are common. Those attributes are described here once in order to avoid duplicating the description for every resource that contains it.

Attributes that are only used in one or two resource types are described only in the section for that resource.

In all tables representing resource attributes, each attribute name is followed by its “short name” in brackets that shall be used in XML resource representations to be transferred across reference points.

Table 9.2

| Common Attributes | Description |
| --- | --- |
| resourceType (rT) | Resource type. URI of addressed resources are concatenation of resource name tokens assigned at creation time by the issuer without indication of resource type. The WO resourceType attribute stores in a two capital letters token the information usefeul for procedure processings, e.g. CO for <container>, CI for <instance>. |
| accessRightID (aRI) | URI of an access rights resource. The permissions defined in the accessRight resource that is referenced determine who is allowed to access the resource containing this attribute for a specific purpose (retrieve, update, delete etc.). If a resource type does not have an accessRightID attribute definition, then the accessRights for resources of that type are governed in a different way, for example, the accessRight associated with the parent may apply to a child resource that does not have an accessRightID attribute definition, or the permissions for access are fixed. Refer to the corresponding procedures to see how permissions are handled in these cases. If a resource type does have an accessRightID attribute definition, but the (optional) accessRightID attribute is not set, or it is set to a value that does not correspond to an valid, existing, accessRight resource, or it refers to an accessRight resource that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access permissions shall apply. The system default access permissions grant all permissions (i.e. the full set of permissionsFlags) to the following permission holders depending on the prefix of URI of the resource. |
| creationTime (cT) | Time of creation of the resource. |
| expirationTime (eT) | Absolute time after which the resource will be deleted by the hosting CSE. This attribute can be provided by the issuer, and in such a case it will be regarded as a hint to the hosting CSE on the lifetime of the resource. The hosting CSE can however decide on the real expirationTime. If the hosting CSE decides to change the expirationTime attribute value, this is communicated back to the issuer. The lifetime of the resource can be extended by providing a new value for this attribute in an UPDATE verb. Or by deleting the attribute value, e.g. by not providing the attribute when doing a full UPDATE, in which case the hosting CSE can decide on a new value. |
| filterCriteria (fC) | This are criteria that filter the results. They can either be used in a GET (as query parameters) or in a subscribe. |
| lastModifiedTime (mMT) | Last modification time of a resource. |
| link (lk) | URI of the related remote resource. In an announced resources, this is the URI of the announcing resource. In an <cse> resource, this is the URI of the <cseBase> resource of the registered CSE. |
| searchStrings (sS) | Tokens used as keys for discovering resources. |
| creator (cr) | Id of the application instance or CSE which created the resource |

Editor’s note:  Mechanisms for announcing are for FFS

Editor’s note:

The following attributes are for FFS depending on resource structure discussion

- child: resources with child relation with the considered resource

- parent: resources with paren relation with the considered resource

### 9.5.x	Resource accessRight

Access rights are defined as "white lists" or permissions, i.e. each permission defines "allowed" entities (defined in the permissionHolders) for certain access modes (permissionFlags). Sets of permissions are handled such that the resulting permissions for a group of permissions are the sum of the individual permissions. I.e., an action is permitted if it is permitted by some / any permission in the set.

By setting an accessRightID attribute on a resource, the permissions for accessing that resource are then defined by the permissions defined in the accessRight resource.)

Figure 9.5.x-.1: Structure of accessRight resource 
(only specific resource attributes are shown)

Editor’s note: Susbscription relation with this resource is for FFS

Table 9.5.y-1: Child resources of accessRight resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| subscriptions (subs) | <subscriptions> | 1 | See section 9.5.z |

The resource shall contain the attributes according to their multiplicitly in Table 9.5.x-2 (0 indicated the optionality of the attribute).

Table 9.5.x-2: Attributes of accessRight resource

| AttributeName | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section <XRef <section> where the common attribute is described.> |
| expirationTime (eT) | 1 | RW | See section <XRef <section> where the common attribute is described.> |
| searchStrings (sS) | 0..1 | RW | See section <XRef <section> where the common attribute is described.> |
| creationTime (cT) | 1 | RO | See section <XRef <section> where the common attribute is described.> |
| lastModifiedTime (lMT) | 1 | RO | See section <XRef <section> where the common attribute is described.> |
| permissions (ps) | 1 | RW | The list of permissions defined by this accessRight resource. These permissions are applied to resources referencing this accessRight resource using the accessRightID attribute. |
| selfPermissions (sP) | 1 | RW | Defines the list of permissions for the accessRight resource itself. |

Editor’s note:  Mechanisms for announcing are for FFS

The permissionFlags and the permissionHolders could then be generalised to actions (which might be granting access, but might also be more specific, like granting access to a subset, i.e. filtering part of the data). The permissionHolders could be generalised to conditions, which may include things like the identity of the requestor, everybody except specified identities, but it might also include time based conditions etc.

### 9.5.y	Resource container

This resource represents a container for data instances. It is used to share information among theother entities and potentially to track the data. A container resource has no associated content, only attributes and child resources.

Figure 9.5.y-1: Structure of container resource
(only child resources and specific resource attributes are shown)

The resource shall contain the child resources according to their multiplicitly in Table 9.5.y-1 (0 indicated the optionality of the child resource).

Editor’s note: Susbscription relation with this resource is for FFS.

Editor’s note: location resource relationwith containers is for FFS.

Table 9.5.y-1: Child resources of container resource

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <instance> | 0..n | <XRef <section> where the resource type is described.> |
| [variable] | <subscription> | 0..n | <XRef <section> where the resource type is described.> |
| [variable] | <container> | 0..n | See section 9.5.y |
| subscriptions (subs) | <subscriptions> | 1 | See section 9.5.z |

The resource shall contain the attributes according to their multiplicitly in Table 9.5.y-2 (0 indicated the optionality of the attribute).

Table 9.5.y-2: Attribute of container resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | XRef <section> where the common attribute is described. |
| expirationTime (eT) | 1 | RW | XRef <section> where the common attribute is described. If no accessRightID is given at thetime of creation, the accessRightIDof the parent resource is linked to this attribute |
| accessRightID (aRI) | 0..1 | RW | XRef <section> where the common attribute is described. If no accessRightID is given at thetime of creation, the accessRightIDof the parent resource is linked to this attribute |
| searchStrings (sS) | 0..1 | RO | XRef <section> where the common attribute is described. |
| creationTime (st) | 1 | RW | XRef <section> where the common attribute is described. |
| Creator (cr) | 1 | RW | XRef <section> where the common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | XRef <section> where the common attribute is described. |
| announceTo (aT) | 0..1 | RW | See section <XRef <section> where the common attribute is described.>. This shall be used to announce <containerAnnc> over Y’ reference point. |
| maxNrOfInstances (mi) | 0..1 | RW | Maximum number of instances of <instance> child resources |
| maxByteSize (mb) | 0..1 | RW | Maximum number of bytes that is allocated for a <container> resource for all instances of a <instance> resources within the ‘instances’ collection. |
| maxInstanceAge (ma) | 0..1 | RW | Maximum age of instances of a <instance> resources within the ‘instances’ collection , the value is expressed in seconds. |
| currentNrOfInstances (ni) | 1 | RO | Current number of instances in a <container> resource. It is limited by the maxNrOfInstances. |
| currentByteSize (nb) | 1 | RO | Current size in bytes of data stored in a <container> resource. It is limited by the maxNrOfBytes. |
| Latest (lt) | 0..1 | RO | Reference to latest instance, when present. |
| LocationID (LID ) | 0..1 | RW | URI of the resource where the attributes/policies that define how location information are obtained and managed. This attribute is defined only when the <container> resource is used for containing location information. |

Editor’s note:  Mechanisms for announcing are for FFS

Editor’s note:

The following attributes are for FFS depending on resource structure discussion

- child: resources with child relation with the considered resource

- parent: resources with paren relation with the considered resource

### 9.5.z	Resource instance

The instance resource represents a data instance in the container. The content of the instance is opaque to the M2M platform and it might even be encrypted. However, there is meta-data associated with an instance which shall be accessible.

Contrary to other resources, the <instance> resource cannot be modified once created, regardless of the accessRightID associated with the parent resource. An instance may be deleted explicitly or it may be deleted by the platform based on policies. If the platform has policies for the instance retention these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge on the <container> resource. If multiple policies are in effect, the strictest policy shall apply.

The <instance>resource inherit the same access rights of the parent <container> resource, and does not have its own <accessRights> attribute.

Figure 9.5.z-1: Structure of instance resource
(only child resources and specific resource attributes are shown)

The resource shall contain the attributes according to their multiplicitly in Table 9.5.z-2 (0 indicated the optionality of the attribute).

Table 9.5.z-2: Attribute of contentIstance resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| rT (resourceType) | 1 | RO | XRef <section> where the common attribute is described. |
| sS(searchStrings) | 0..1 | RW | XRef <section> where the common attribute is described. |
| cT(creationTime) | 1 | RO | XRef <section> where the common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | XRef <section> where the common attribute is described. |
| tOC(typeOfContent) | 1 | WO | Optional type of the content included in the content attribute. This is media-type as defined in reference to stage 3 |
| cS(contentSize) | 1 | WO | Size in bytes of the content attribute. |
| c(content) | 1 | WO | Real opaque content of an instance. This may for example be an image taken by a security camera, or a temperature measurement taken by a temperature sensor. |

## 10.2	Message flow

### 10.2.x	<container> Resource

#### 10.2.x.1	Create <container>

This flow is used for creating a <container> resource.

Originator: the originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the receiver or hosting CSE shall validate whether the originator has proper permission for creating a <container> resource.

Table 10.2.x.1.1 <container> CREATE flow

|  | Description |
| --- | --- |
| Call flow type | CREATE |
| Pre-conditions | N/A |
| Information on Request message | op: C fr: Originator App-Inst-ID or CSE-ID to: Receiver CSE-ID cn: Name of <container> resource (optional), some mandatory and/or optional attributes defined in x.y.z as it is needed. Editor’s note: x.y.z refers to the table which describes the attributes of <container> |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1.1) |
| Information on Response message | fr: Receiver CSE-ID to: Originator App-Inst-ID or CSE-ID cn: URI of the created <container> if the URI sent by the originator has been changed by the CSE or was not provided in the request |
| Post-condition | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. The CSE does not have storage capacity to create the <container> |

#### 10.2.x.2	Retrieve <container>

This flow is used for retrieving the attributes  of a <container> resource.

Originator: the originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the receiver or hosting CSE shall validate whether the originator has proper permission for retrieving a <container> resource.

Table 10.2.x.1.1 <container> RETRIEVE flow

|  | Description |
| --- | --- |
| Call flow type | RETRIEVE |
| Pre-conditions | Originator needs to retrieve a resource |
| Information on Request message | op: R fr: Originator App-Inst-ID or CSE-ID to: Receiver CSE-ID cn: void Editor’s note: x.y.z refers to the table which describes the attributes of <container> |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1.2) |
| Information on Response message | fr: Receiver CSE-ID to: Originator App-Inst-ID or CSE-ID cn: attributes of the <container> resource Editor’s note: The retrievalof subresources if for FFS |
| Post-condition | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. |

#### 10.2.x.3	Update <container>

This flow is used for updating the attributes and the actual data of a <container> resource.

Originator: the originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the receiver or hosting CSE shall validate whether the originator has proper permission for updating a <container> resource.

Table 10.2.x.1.1 <container> UPDATE flow

|  | Description |
| --- | --- |
| Call flow type | UPDATE |
| Pre-conditions | Originator needs to update a resource |
| Information on Request message | op: U fr: Originator App-Inst-ID or CSE-ID to: Receiver CSE-ID cn: the attributes which to be updated. |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1.3) |
| Information on Response message | No change from the basic procedure (clause 10.1.1.3) |
| Post-condition | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. |

#### 10.2.x.4	Delete <container>

This flow is used for deleting a <container> resource residing under a <container> or <locationContainer> resource.

Originator: the originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the receiver can be a CSE.

Table 10.2.x.1.1 <Container> DELETE flow

|  | Description |
| --- | --- |
| Call flow type | DELETE |
| Pre-conditions | Originator needs to delete a resource |
| Information on Request message | op: D fr: Originator App-Inst-ID or CSE-ID to: Receiver CSE-ID cn: void |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1.4). Shall check for child resources and delete all child resources and shall delete child references in parents resources. |
| Information on Response message | No change from the basic procedure (clause 10.1.1.4) fr: Receiver CSE-ID to: Originator App-Inst-ID or CSE-ID cn: void |
| Post-condition | None |
| Exceptions | None |

Other procedures: search container for specific instances?

### 10.2.y	<instance> Resource

The resource <instance> contains the actual data. It also contains meta-data associated with this actual data. This can be used to gauge the interest in the actual data, before getting the actual content data, since the size of the instance’s actual data can be quite large.

This clause shows how to create, retrieve, and delete the <instance> resource. Contrary to other resource, the <instance> resources cannot be modified once created, there is no update flow.

Editor’s Note: if we have any RW-attributes in the <instance> resource, we need to add update flow.

#### 10.2.y.1	Create <instance>

This flow is used for creating the attributes and the actual data of a <instance> resource residing under a <container> resource.

Originator: the originator can be an AE or a CSE.

Receiver or Hosting CSE: the receiver or hosting CSE shall validate whether the originator has proper permission for creating a <instance> resource.

Table 10.2.x.1.1 <Instance> CREATE flow

|  | Description |
| --- | --- |
| Call flow type | CREATE |
| Pre-conditions | Originator needs to create a <instance> resource. |
| Information on Request message | op: C fr: Originator App-Inst-ID or CSE-ID to: Receiver CSE-ID cn: Name of <container> resource (optional), some mandatory and/or optional attributes defined in x.y.z as it is needed. cn: <container>/<instance> resource (optional), the actual date (content), some mandatory and/or optional attributes defined in x.y.z as it is needed. Editor’s note: x.y.z refers to the table which describes the attributes of <instance> or we can clearly state some importance attributes. Editor’s Note: Detail flow of sharing-based is FFS |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1.1) |
| Information on Response message | URI of the created <instance> if the URI sent by the originator has been changed by the CSE or was not provided in the request |
| Post-condition | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or the Hosting CSE does not provide mandatory attributes. The CSE does not have storage capacity to create the <instance> |

#### 10.2.y.2	Retrieve <instance>

This flow is used for retrieving the attributes and the actual data of a <instance> resource residing under a <container> or <locationContainer> resource.

Originator: the originator can be an AE or a CSE.

Receiver or Hosting CSE: the receiver or hosting CSE shall validate whether the originator has proper permission for retrieving a <instance> resource.

Table 10.2.x.1.1 <instance> RETRIEVE flow

|  | Description |
| --- | --- |
| Call flow type | RETRIEVE |
| Pre-conditions | Originator needs to retrieve a <instance> resource |
| Information on Request message | No change from the basic procedure (clause 10.1.1.2) |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1.2) |
| Information on Response message | No change from the basic procedure (clause 10.1.1.2) |
| Post-condition | None |
| Exceptions | None |

#### 10.2.y.3	Delete <instance>

This flow is used for deleting a <instance> resource residing under a <container> or <locationContainer> resource.

Originator: the originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the receiver or hosting CSE shall validate whether the originator has proper permission for deleting a <instance> resource.

Table 10.2.x.1.1 <instance> DELETE flow

|  | Description |
| --- | --- |
| Call flow type | DELETE |
| Pre-conditions | Originator needs to delete a <instance> resource. |
| Information on Request message | No change from the basic procedure (clause 10.1.1.4) |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1.4) |
| Information on Response message | No change from the basic procedure (clause 10.1.1.4) |
| Post-condition | None |
| Exceptions | None |

Editor’s note: How a container elaborate the instances needs to included.

Editor’s note: AR information flows are not yet included

## end of proposed text ##

# Comments

It clarify if the attribute is:

- Read/Write (RW ), i.e.it can be set by an update or a create,

- Rread Only (RO), i.e. it is set by the CSE and it can only be read,

- Write Once (WO), i.e. it is set by at the creation and then it can only be read.

It clarify if the attribute is:

- Read/Write (RW ), i.e.it can be set by an update or a create,

- Rread Only (RO), i.e. it is set by the CSE and it can only be read,

- Write Once (WO), i.e. it is set by at the creation and then it can only be read.

It clarify if the attribute is:

- Read/Write (RW ), i.e.it can be set by an update or a create,

- Rread Only (RO), i.e. it is set by the CSE and it can only be read,

- Write Once (WO), i.e. it is set by at the creation and then it can only be read.

It clarify if the attribute is:

- Read/Write (RW ), i.e.it can be set by an update or a create,

- Rread Only (RO), i.e. it is set by the CSE and it can only be read,

- Write Once (WO), i.e. it is set by at the creation and then it can only be read.

# Text boxes

currentNrOfInstances

currentByteSize (nb)

Latest (lt)

Oldest (ot)

1

subscriptions

<subscription>

n

minimalTimeBetweenNotifications)

dT(delayTolerance)

fC(filterCriteria)

cU(contactURI)

tR(timeoutReason)

nR(noRepresentation)

subscriptionType

aggregateURI (aU)

subscriberId (sI)

contentSize

dT(delayTollerance)

c(content)

content

c(content)

Latest

Oldest (ot)

currentByteSize

Latest (lt)

Oldest (ot)

1

<acessRightAnnc>

n

1

1

1

selfPermissions

permissions

1

<accessRight>

n

1

1

0..n

1

<container>

0..n

maxNrOfInstances (mi)

maxByteSize (mb)

maxInstanceAge (ma)

currentNrOfInstances (ni)

currentByteSize (nb)

Latest (lt)

Oldest (ot)

<subscriptions>

<container>

maxByteSize

maxInstanceAge (ma)

currentNrOfInstances (ni)

currentByteSize (nb)

Latest (lt)

Oldest (ot)

maxInstanceAge

currentNrOfInstances (ni)

currentByteSize (nb)

Latest (lt)

Oldest (ot)

1

<instance>

1

1

1

1

1

1

LocationID

1

<instance >

0..n

typeOfContent

cS(contentSize

dT(delayTollerance)

c(content)

1

n

< containerAnnc>

1

1

1

1

1

1

1

1

0..n

1

<locationecontainer>

maxNrOfInstances (mi)

maxByteSize (mb)

maxInstanceAge (ma)

currentNrOfInstances (ni)

currentByteSize (nb)

Latest (lt)

Oldest (ot)

<subscriptions>

maxByteSize

maxInstanceAge (ma)

currentNrOfInstances (ni)

currentByteSize (nb)

Latest (lt)

Oldest (ot)

maxInstanceAge

currentNrOfInstances (ni)

currentByteSize (nb)

Latest (lt)

Oldest (ot)

currentNrOfInstances

currentByteSize (nb)

Latest (lt)

Oldest (ot)

currentByteSize

Latest (lt)

Oldest (ot)

Latest

Oldest (ot)

Oldest

0..n

locationContainerType

n

< containerAnnc>

1

Oldest

1

n

delayTolerance

fC(filterCriteria)

cU(contactURI)

tR(timeoutReason)

nR(noRepresentation)

subscriptionType

aggregateURI (aU)

subscriberId (sI)

n

filterCriteria

cU(contactURI)

tR(timeoutReason)

nR(noRepresentation)

subscriptionType

aggregateURI (aU)

subscriberId (sI)

n

contactURI

tR(timeoutReason)

nR(noRepresentation)

subscriptionType

aggregateURI (aU)

subscriberId (sI)

n

timeoutReason

nR(noRepresentation)

subscriptionType

aggregateURI (aU)

subscriberId (sI)

n

noRepresentation

subscriptionType

aggregateURI (aU)

subscriberId (sI)

n

subscriptionType

aggregateURI (aU)

subscriberId (sI)

n

aggregateURI

subscriberId (sI)

n

subscriberId