| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | “To” parameter clarifications |
| Source:* | LG Electronics, Cisco |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com Philip Jacobs, phjacobs@cisco.com |
| Date:* | 2013-10-31 |
| Abstract:* | This contribution proposes to clarify/modify the description of the “to” parameter |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Introduction

The “to” parameter of the Request message is described in several incompatible ways. This contribution proposes to correct and make consistent the descriptions.

------------------------------------------------------START OF FIRST CHANGE--------------------------------------------------

### 8.1.2	Request

Request from an Originator to a Receiver includes the following information:

op:  operation to be executed: Create (C), Retrieve (R), Update (U), Delete (D),

to:  URI of the target resource or the parent of the target resource, e.g. /m2m.provider1.com/netBase/temp1,

Editor's Note: This is made under the assumption that the CSE-ID is incorporated in the URI of the target resource or the parent of the target resource.

fr:  ID of the Originator,

NOTE:  fr is used for access control of the target resource.

mi:  meta-information about the Request,

Editor's Note: Defaults for meta-information are FFS.

cn:  resource content to be transferred.

Note: The to target resource needs to be known by the Originator. It can be known either by pre-provisioning or by discovery.

Editor’s Note: How pre-provisioning and discovery are performed is FFS.

------------------------------------------------------END OF FIRST CHANGE--------------------------------------------------

------------------------------------------------------START OF SECOND CHANGE--------------------------------------------------

# 10.	Information Flows

Editor’s Note: It is FFS about the suitable section for the proposed generic call flows and potential re-org of the sections due to the correlation of current section 8 and 10.

## 10.1	Basic Procedures

### 10.1.1		CREATE (C)

The CREATE procedure shall be used by an Originator CSE or AE to create a resource on a Receiver CSE (also called the hosting CSE).

Originator requests to create a resource by using the CREATE method. See clause 8.1.2 for the information to be included in the Request message.

Receiver, after ensuring that the Originator has been authenticated, creates the resource. The creation of a resource shall always be allowed if the Originator has been authenticated. This is due to the fact that the requested resource is not known prior to the creation by the Originator, therefore the accessRights resource in the Receiver does not contain a priori the permission for the resource that is being created.

Editor' s Note: The statement above assumes that accessRights resources has been agreed to in the resource structure. This is a presumptive statement. The statement above to be reviewed once the definition of resource structure has stabilized.

Figure 10.1.1-1: Procedure for CREATEing a Resource

Step 001: The Originator shall send the following information in the CREATE Request message:

op: 	C (Create);

to: 	URI of the parent of the target resource

fr: 	ID of the Originator

Editor's Note: AE or CSE may not have the ID upon its registration request. Alternative information for fr is FFS.

ty:	type the resource to be created

cn: 	mandatory attributes of the resource to be provided by the Originator:

Note: Who (Originator or Receiver) provides which mandatory attributes to be specified in the Protocol Technical Specification.

Editor’s Note: references to elements defined in sect 8 have been added here. They may be removed if we decide to move sect 8.1.2-4 to stage 3 doc. In this case, these references will be removed and sect 1 of this document would replace sect 8.1.2-4 in the TS-0001.

Note: The identifier of the <target resource> (i.e., the name of the resource) can be optionally provided in the cn. If cn does not contain the identifier of the <target resource>, the hosting CSE shall provide an identifier for that <target resource>.

------------------------------------------------------END OF SECOND CHANGE--------------------------------------------------

------------------------------------------------------START OF THIRD CHANGE--------------------------------------------------

### RETRIEVE (R)

The RETRIEVE operation shall be used for retrieving the information stored for any of the attributes for a resource at the Receiver CSE. The Originator CSE or AE may also request to retrieve only a specific attribute or part of an attribute by including the identity of such attribute in the Request message.

Editor's Note: The statement in the para above is not clear. Is this operation targeted for retrieving ALL attributes for a resource together (as a Group) or for specific attributes only? Depending on the answer, the text above needs to be updated. The text in the para that follows assumes that this operation is for retrieving all attributes for a resource. If the Request is for retrieving only a specific attribute, then the identity of such attribute is included in the Request message.

Originator requests to retrieve all attributes of the target resource by using RETRIEVE Request.  See clause 8.1.2 for the information to be included in the Request message. If only specific attribute(s) or part of an attribute needs to be retrieved, the address of such attribute (e.g., the URI) shall also be included in the Request message.

Receiver performs local processing to verify the existence of requested resource and checks permissions for retrieving the information related to the resource. After the successful verification, the Receiver shall return the requested information, else an error indication shall be returned.

Figure 10.1.2-1: 	Procedure for RETRIEVing a Resource

Step 001:	The Originator shall request to RETRIEVE a resource from the Receiver.

op:	R (Retrieve)

to: 	URI of the target resource

fr:	 ID of the Originator

------------------------------------------------------END OF THIRD CHANGE--------------------------------------------------

------------------------------------------------------START OF FOURTH CHANGE--------------------------------------------------

### 10.1.3	UPDATE (U)

The UPDATE operation shall be used for updating the information stored for any of the attributes at a target resource. Especially important is the "expirationTime", since a failure in refreshing this attribute may result in the deletion of the resource. Alternatively, the Originator CSE or AE can request to update only a specific attribute or part of an attribute at the target resource.

Originator requests to update any of the attributes at the target resource by using UPDATE Request message. The Originator shall send new (proposed) values for the attribute(s) that need to be updated.  See clause 8.1.2 for the information to be included in the Request message.

Receiver after verifying the existence of the addressed resource, the validity of the attributes provided and the permissions to modify them, shall update the attributes provided and shall return a Response message to the Originator with the operation results as specified in clause 8.1.3.

Figure 10.1.3-1: 	Procedure for UPDATing a Resource

Step 001:	The Originator shall send the following information in the UPDATE Request message:

op:	U (Update)

to: 	URI to the target resource

fr: 	ID of the Originator

------------------------------------------------------END OF FOURTH CHANGE--------------------------------------------------

------------------------------------------------------START OF FIFTH CHANGE--------------------------------------------------

### 10.1.4	DELETE (D)

The DELETE operation shall be used by an Originator CSE or AE to delete a resource at a Receiver CSE. The delete procedure shall consist of the deletion of all related information of the target resource.

Originator requests to delete a resource by using a DELETE Request message. See clause 8.1.2 for the information to be included in the Request message.

Receiver shall verify the existence of the requested resource, and the permissions for deleting the resource. The Receiver shall remove the target resource and shall return a Response message to the Originator with the appropriate operation results as specified in clause 8.1.3.

Figure 10.1.4-1:  Procedures for DELETING a Resource

Step 001:	The Originator shall send a DELETE Request message to the Receiver.

op:	D (Delete)

to: 	URI of the target resource

fr: 	ID of the Originator

------------------------------------------------------END OF FIFTH CHANGE--------------------------------------------------

------------------------------------------------------START OF SIXTH CHANGE--------------------------------------------------

Table 10.2.1.1-1 <container> CREATE flow

| Description |
| --- |
| Call Flow Yype | CREATE |
| Pre-Conditions | N/A |
| Information on Request message | op: C fr: Originator App-Inst-ID or CSE-ID to: URI of the parent of the <container> resource cn: Name of <container> resource (optional), Some mandatory and/or optional attributes defined in section x.y.z are needed. Editor’s Note: Section x.y.z refers to the table which describes the attributes of <container> resource. |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1) |
| Information on Response message | fr: Receiver CSE-ID to: Originator App-Inst-ID or CSE-ID cn: URI of the created <container> if the URI sent by the originator has been changed by the CSE or was not provided in the Request |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. The CSE does not have storage capacity to create the <container> |

------------------------------------------------------END OF SIXTH CHANGE--------------------------------------------------

----------------------------------------------------START OF SEVENTH CHANGE--------------------------------------------------

Table 10.2.1.2-1 <container> RETRIEVE flow

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to retrieve a resource |
| Information on Request message | op: R fr: Originator App-Inst-ID or CSE-ID to: URI of the <container> resource cn: void Editor’s Note: Section x.y.z refers to the table which describes the attributes of <container> |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.2) |
| Information on Response message | fr: Receiver CSE-ID to: Originator App-Inst-ID or CSE-ID cn: attributes of the <container> resource Editor’s Note: The procedures for the retrieval of subresources is FFS. |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. |

------------------------------------------------------END OF SEVENTH CHANGE--------------------------------------------------

----------------------------------------------------START OF EIGHTH CHANGE--------------------------------------------------

Table 10.2.1.3-1 <container> UPDATE flow

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to update a resource |
| Information on Request message | op: U fr: Originator App-Inst-ID or CSE-ID to: URI of the <container> resource cn: the attributes which to be updated. |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.3) |
| Information on Response message | No change from the basic procedure (clause 10.1.3) |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. |

----------------------------------------------------END OF EIGHTH CHANGE--------------------------------------------------

----------------------------------------------------START OF NINTH CHANGE--------------------------------------------------

Table 10.2.1.4-1 <container> DELETE flow

| Description |
| --- |
| Call Flow Yype | DELETE |
| Pre-Conditions | Originator needs to delete a resource |
| Information on Request message | op: D fr: Originator App-Inst-ID or CSE-ID to: URI of the <container> resource cn: void |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.4). Shall check for child resources and delete all child resources and shall delete child references in parent resources. |
| Information on Response message | No change from the basic procedure (clause 10.1.4) fr: Receiver CSE-ID to: Originator App-Inst-ID or CSE-ID cn: void |
| Post-Conditions | None |
| Exceptions | None |

----------------------------------------------------END OF NINTH CHANGE--------------------------------------------------