| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Subscription Call Flows |
| Source:* | LG Electronics |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com |
| Date:* | 2013-12-02 |
| Abstract:* | CRUD call flows for <subscription> resource type. |
| Agenda Item:* | TBD |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate this text into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

This contribution proposes information flows for subscription resource using <subscription> resource type.

It is assumed to utilize some attributes which are not yet agreed, but proposed in other contributions during TP#8.

In the create procedure, it is also assumed that the relationship between a subscribed-to resource and a corresponding subscription resource is represented parent-child resource structure as we have an example in <container> resource type in the TS (see clause 9.6.3 resource type <container>). <container> resource type can have subscription resource(s) as child(ren).

- Proposal

# 10.2.X 		<subscription> Resource

##### 10.2.X.1		Introduction

An Originator can create a subscription resource on a subscribed-to resource Hosting CSE to be notified when the resource is modified. After the successful subscription resource creation, the Hosting CSE shall notify the Originator of a subscribed-to resource modification that meets conditions configured in the subscription resource.

A subscription shall be represented by a <subscription> resource type (see clause 9.6.9). This allows manipulation of the subscription in a resource oriented manner, e.g. the conditions of a subscription may be modified by modifying a subscription resource, or a resource subscriber may unsubscribe by deleting the subscription resource.

Following clauses describe procedures for creation, retrieval, update and deletion of a subscription resource.

##### 10.2.X.2		Create <subscription>

This procedure shall be used to request a new subscription to be notified for modifications of a subscribable resource.

Originator: The Originator can be an AE or a CSE. The Originator shall request to create a <subscription> resource. The request shall address a subscribable resource.

The request shall include notificationURI(s).

Hosting CSE: The Hosting CSE shall validate the followings:

- if the subscribed-to resource, addressed in to parameter in the request, is a subscribable resource

- if the Originator has RETRIEVE permission to the subscribed-to resource

- if the Originator has access rights to send notifications to the entity(ies) hosting notificationURI(s) when the Originator is not a hosting notificationURI

- if it has access rights to send notifications to the entity(ies) that hosting notificationURI(s).

Editor's Note: Access right to send notification to an entity can be represented as NOTIFY permission.

Editor’s Note: The validation process described in the last two bullet points above needs to be investigated more, this is FFS.

If all those checks are successfully done, the Hosting CSE shall send positive response to the Originator.

Table 10.2.x.2.1 <subscription> CREATE flow

|  | Description |
| --- | --- |
| Call flow type | CREATE |
| Pre-conditions | The Originator configures proper permissions and access rights described above. |
| Information on Request message | cn: Mandatory and/or optional attributes defined in clause 9.6.9. |
| Local processing on Hosting CSE | Check access rights regarding creation of the subscription resource and sending notification to the notificationURI |
| Information on Response message | No change from the basic procedure (see clause 10.1.1) |
| Post-condition | None |
| Exceptions | One of validations on the Hosting CSE above fails |

##### 10.2.X.3		Retrieve <subscription>

This procedure shall be used to retrieve information of a subscription such as notificationURI, filterCriteria, expirationTime etc.

Originator: The Originator can be an AE or a CSE. The request shall address a subscription resource or one of its attributes.

Hosting CSE: If the Hosting SCE validates the Originator has RETRIEVE permission referring accessRightID , it shall return the complete representation of the subscription resource or the value of a specific attribute of the subscription.

Table 10.2.x.3.1 <subscription> RETRIEVE flow

|  | Description |
| --- | --- |
| Call flow type | RETRIEVE |
| Pre-conditions | The Originator has RETRIEVE permission to the subscription resource. |
| Information on Request message | No change from the basic procedure (see clause 10.1.2) |
| Local processing on Hosting CSE | No change from the basic procedure (see clause 10.1.2) |
| Information on Response message | No change from the basic procedure (see clause 10.1.2) |
| Post-condition | None |
| Exceptions | No change from the basic procedure (see clause 10.1.2) |

##### 10.2.X.4		Update <subscription>

This procedure shall be used to update an existing subscription, e.g. extension of its lifetime or the modification of the notificationURI.

Originator: The Originator can be an AE or a CSE. The Originator may send new value(s) for read-write attribute(s) of a subscription resource.

Hosting CSE: After the Hosting CSE verifying the existence of the addressed resource, the validity of the attributes provided and the permissions to modify them referring accessRightID, shall update the attributes provided and shall send positive response to the Originator.

Table 10.2.x.4.1 <subscription> UPDATE flow

|  | Description |
| --- | --- |
| Call flow type | UPDATE |
| Pre-conditions | The Originator has UPDATE permission to the subscription resource. |
| Information on Request message | No change from the basic procedure (see clause 10.1.3) |
| Local processing on Hosting CSE | No change from the basic procedure (see clause 10.1.3) |
| Information on Response message | No change from the basic procedure (see clause 10.1.3) |
| Post-condition | None |
| Exceptions | No change from the basic procedure (see clause 10.1.3) |

##### 10.2.X.5		Delete <subscription>

This procedure shall be used to unsubscribe an existing subscription.

Originator: The Originator can be an AE or a CSE. The request shall address a subscription resource.

Hosting CSE: If the Hosting CSE validates the Originator has the DELETE permission to delete a subscription resource, it shall delete the resource and shall send a positive response to the Originator.

Table 10.2.x.5.1 <subscription> DELETE flow

|  | Description |
| --- | --- |
| Call flow type | DELETE |
| Pre-conditions | The Originator has DELETE permission to the subscription resource. |
| Information on Request message | No change from the basic procedure (see clause 10.1.4) |
| Local processing on Hosting CSE | No change from the basic procedure (see clause 10.1.4) |
| Information on Response message | No change from the basic procedure (see clause 10.1.4) |
| Post-condition | None |
| Exceptions | No change from the basic procedure (see clause 10.1.4) |