| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#8 |
| Title:* | <nodeSpecific> Resource Type |
| Source:* | LG Electronics, Sierra Wireless, Sprint |
| Contact: | hongbeom.ahn@lge.com, ndamour@sierrawireless.com, laurent.laporte@sprint.com |
| Date:* | 2013-12-01 |
| Abstract:* | This is about <nodeSpecific> resource. |
| Agenda Item:* | Contribution – New Resource Type |
| Work item(s): | oneM2M-WI-0002 Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Functional Architecture v0.2.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG2 review this contribution and agree to input this contribution in ARC TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

Please see the contribution, oneM2M-ARC-2013-0573-Introduction_to_nodeSpecific.

2	Proposal

### 9.6.X		Resource Type node

The <node> resource represents specific information of a M2M Node that can be utilized by other oneM2M operations. For example, the CMDH CSF can determine when the CSE sends a request message to the target CSE based on the target CSE’s reachability schedule. This resource type mainly contains the properties of a M2M node such as reachability schedule, context information (e.g., memory and storage) and network topology.

This node specific information such as memory and storage can be obtained either by the existing device management techonologies (OMA DM, BBF TR-069) or any other way (e.g., through JNI(Java Native Interface)). Since <mgmtObj> resource type represents the management functions including both ways, the type of sub-resources are <mgmtObj> resource type.

The location of <node> resource can be differentiated according to the type of node.

- ASN: under <baseURI> of the local CSE

- ADN: under <AE> resource of the hosting CSE

- MN: under <baseURI> of the local CSE

Editor’s Note: more specific information regarding a node can be added.

The <node> resource type shall contain the sub resources with the indicated multiplicity in Table 9.x.1.

Table 9.x.1: Child Resource of <node>

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| memory | <mgmtObj> | 0..1 | This resource provides the memory (typically RAM) information of the node. (e.g. the amount of total volatile memory) |
| storage_<i> | <mgmtObj> | 0..n | This resource provides the storage (typically flash or disk) information of the node. (e.g. the amount of total writable persistent storage) |
| power | <mgmtObj> | 0..1 | The resource provides the power information of the node. (e.g. remaining battery charge) |
| networkTopology | <mgmtObj> | 0..1 | This resource describes the list of Nodes attached behind the MN node and its relation among the nodes. This attribute is defined in case the Node is MN. |
| schedule | <schedule> | 0..1 | This resource defines the reachability schedule information of the node. |

Editor’s Note: the naming convention of storage that the multiplicty is more than 1 is just following what WG2 discussed in the drafting session. If the convention or the rule is changed in the template section, the notation will be changed.

Editor’s Note: legacy nodes described in networkTopology attribute is FFS.

Editor’s Note: some device characteristic information (external ID, profile and device-specific ID) can be added.

The resource shall contain the attributes according to their multiplicity in Table 9.6.X-1 (0 indicates the optionality of the attribute).

Table 9.6.X-1:  Attributes of <node> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID<n> | 1..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| searchStrings | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| nodeID | 1 | RW | The ID of the Node which is specified in the resource type. |