| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP#8 (Mizazaki, Japan) |
| Title:* | Application Resource Type |
| Source:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com Yonglae Cho, KT, yonglae.cho@kt.com Michele Lupano, Telecom Italia, michele.lupano@telecomitalia.it |
| Contact: | See source |
| Date:* | <2013-12-11> |
| Abstract:* | This contribution introduces the notion of an Application resource that represents, in a Common Services Entity, an Application Entity known to the CSE. |
| Agenda Item:* | Contributions |
| Work item(s): | WI-0002 – Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To adopt the suggested modification for inclusion into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

In its current version, the Architecture Technical Specification introduces in the section 9.2 the concept of a resource type “Application”. This resource is succinctly described to store information related to an application, without being completely specified.

As a result, this present contribution proposes to specify the resource type Application, and to extend its scope to other means deemed useful.

- Proposal

# Start of proposed new text #

### 9.6.X		Resource Type Application

The <application> resource represents information about an Application Entity known to a given Common Services Entity.

The <application> resource shall contain the following attributes.

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| searchStrings (sS) | 0..1 | RO | See section 9.6.1 where this common attribute is described. |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (eg. “HeatingMonitoring”) |
| appID | 1 | RO | Application Identifier |
| appInstID | 0..1 | RO | When the application resource refers to an actual application instance in the executing environment. |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the application |

The <application> resource shall contain the following sub resources.

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9 |
| [variable] | <container> | 0..n | See section 9.6.3 |
| [variable] | <group> | 0..n | See section 9.6.5 |
| [variable] | <accessRight> | 0..n | See section 9.6.2 |
| software.<n> | <mgmtObj> | 1..n | This resource represents the software component (or components, if the multiplicity is greater than 1) that compose the application. This mgmtObj shall have at least the following <parameters> child resources of its “parameters” subresource: name (multiplicity 1) version (multiplicity 1) state (multiplicity 1) |
| [variable] | <commCapabilities> | 1..n | This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. |

# End of proposed text #