| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP8 |
| Title:* | Functional architecture in oneM2M-TS-0001 oneM2M Functional Architecture-V-0.3.2 |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2014-01-05 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes clarification of the baseURI resource type and a comprehensive cleanup of the specification to ensure consistency

Base URI is currently the main resource type that is essential for creation of all other resource types in the ROA. In that respect it is considered as a root resource type.

The usage of the term URI for the resource type is rather undesirable as that term is generally used to reference resources in general .

It is thus desirable to have a global change in the TS from base URI to CSE rootResource with <CSE-rootResource> as an instance

* * * Start of 1st Change * * *

Introduce a global change in the specification as follows:

- Replace <baseURI > with  <CSE-rootResource>

- Replace Base URI with CSE rootResource

* * * End of 1st Change * * *

* * * Start of 2nd Change * * *

## 9.3  Resource Addressing

Resources shall be uniquely addressable via URI. The following are examples of addressable resources.

/<CSE-rootResource> /Entity Instance 1

/<CSE-rootResource> /Entity Instance n

/<CSE-rootResource> /Application Instance 1

/<CSE-rootResource> /Application Instance n

/<CSE-rootResource> /Container1/Container2

Resources may be associated by using a link with reference to another resource.

The <CSE-rootResource>  shall contain all resources of the hosting node. A <CSE-rootResource>  is the root of all other resources it contains. The <CSE-rootResource>  shall represent the first element of the path representing a resource in an absolute URI, as per [i-4]. All other resources hosted in the CSE shall also be identified by an absolute URI.

The authority part of the absolute URI, as per [i.9] and [i.4] shall be either an Infrastructure Node public domain name, a Middle Node public domain name or an Application Service Node public domain name and shall conform to the naming convention described in section 6.5.1.1.

Example of a URI identifier of a container resource hosted by a CSE could be "http://IntermediatenodeCSEID.infrastructurenodeCSEID.m2m.myoperator.org/<CSE-rootResource> /container1/myExampleContainer2"

Editor's Note: With this change of /baseURI to /baseRoot:  we need to examine the whole specification for

* * * End of 2nd Change * * *