| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2014-01-08 |
| Contact:* | SeungMyeong Jeong (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* | Due to the decision on ARC-2013-514 (App-Inst vs. AE), “application instance” should be replaced with AE and some “application” depending on context will be replaced to AE too. This contribution also contains other terminology clarifications such as M2M Application Service Provider. |
| Clause/Sub Clause Affected* |  |
| Agenda Item:* | n/a |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate changes to the ARC TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

************************ START OF CHANGE 1  ************************

6.2.1.2.2.2	CSE Monitoring

CSE Monitoring provides operating characteristics of the CSE capabilities. These operating characteristics include attributes for operational status, configuration and statistics as well as management of alerts.

CSE Monitoring is provided by the following CSF’s:

- ASM Software Management Function:

- Retrieval of  log files associated with the software module

- Retrieval of the lifecycle state and associated information related to the artefacts and software modules of the Software Package

- Notifications for faults associated with software lifecycle state transitions

- Others ... TBD

A CSE’s operational characteristics information exchange shall be provided to an AEby the CSE as a result of a retrieval request, alert generation or bulk transfer operations.

************************* END OF CHANGE 1  *************************

************************ START OF CHANGE 2  ************************

6.2.3	Data Management and Repository

6.2.3.1	General Concepts

One of the goals of CSEs is to enable AEs to exchange data with each other.

Data Management and Repository (DMR) CSF is responsible for providing data storage and mediation functions. It includes the capability of collecting and aggregating large amounts of data, converting this data into a specified format, and storing it for analytics and semantic processing. The "data" can be either raw data transparently retrieved from an M2M Device, or processed data which is calculated and/or aggregated by M2M entities. This collection of large amounts of data constitutes what is known as the Big Data Repository functionality.

6.2.3.2	Detailed Descriptions

DMR CSF shall provide the capability to store data such as Application data, subscriber information, location information, device information, semantic information, communication status, access permission, etc. The "data" stored by the DMR CSF enables management of the data and provides the foundation of Big Data. Further, the DMR CSF shall be able to support the physical replacement of M2M Devices and/or Gateways in terms of the stored data.

The DMR CSF shall support transfer of data to/from the AEs, other CSFs and remote CSEs. The DMR CSF shall support transfer of data regardless of the peer entity being on-line or not. The DMR CSF shall support operations such as Create, Read, Update and Delete. The DMR CSF may associate event categorization (e.g., normal, urgent) with the data for supporting differentiated services. External entities such as AFs, other CSFs or remote CSEs shall be able to be granted access to the data in the DMR CSF based on defined policies.

Editor's Note:  Needs to clarify what is meant by "peer entity" being on-line or not. Is the reference to peer-CSE or something more than that?

The organization of the data helps describe how they relate with each other and how they are addressed. DMR CSF shall allow removal, addition, search of the data. The DMR CSF shall support structured data. Some structures may be specified by oneM2M, others may not. Elements of data stored in the DMR CSF shall be uniquely addressable.

The DMR CSF shall support aggregating the data from the same device or from different devices.

The DMR CSF shall enable the sharing of the data amongst local CSFs, remote CSEs and AFs.

Contextual information such as data types, semantic information, time stamps, location etc. shall complement the data stored by the DMR CSF. This will allow the DMR CSF to access and search the data based on a rich set of parameters. The DMR CSF shall be able to trigger data processing based on access to its data.

The DMR CSF shall provide a means to perform analytics on large amount of data, so that service providers can provide value-added services to AEs. The DMR CSF shall be responsible for enabling AEs to discover, execute and use analytics based on large amount of data from different sources.

Semantic information needs to be available on the data that are transferred within the M2M System. The DMR CSF shall provide functions annotating such semantic information to M2M data and exposing M2M resources using the semantic information so that the M2M resources can be discovered by AEs that do not have prior knowledge of them. The DMR CSF shall be responsible for enabling AEs to discover, interpret and use M2M data from different sources.

************************* END OF CHANGE 2  *************************

************************ START OF CHANGE 3  ************************

6.2.5	Discovery

6.2.5.1	General Concepts

Discovery (DIS) CSF is responsible for searching information e.g., supported attributes and resources according to a Request from an Originator within a given scope and subject to permissions, including those allowed by M2M service subscription. An Originator could be an AE or another CSE. The scope of the search could be in one CSE, or in more than one CSE. The discovery results are returned back to the Originator.

************************* END OF CHANGE 3  *************************

************************ START OF CHANGE 4  ************************

6.2.6	Group Management

6.2.6.1	General Concepts

Group Management (GMG) CSF is responsible for handling Group related requests. The request is sent for the management of a Group and its membership as well as for the bulk operations supported by the Group. When adding or removing members to/from a Group, it is necessary to validate if the member complies with the purpose of the Group. Bulk operations includes read, write, subscribe, notify, device management, etc. Whenever a request or a subscription is made via the Group, the Group is responsible for aggregating its responses and notifications. The members of a Group can have the same role with regards to access rights control towards a resource. In this case, access control is facilitated by grouping. When the Underlying Network provides broadcasting and multicasting capability, the GMG CSF is able to utilize such capability.

6.2.6.2	Detailed Descriptions

GMG CSF shall be responsible for the management of a Group and its membership. The GMG CSF shall support bulk operations to multiple resources of interest and aggregate the results. The GMG CSF shall be able to facilitate access control based on grouping. When needed and available, the GMG CSF may leverage the existing capabilities of the Underlying Network including broadcasting/multicasting.

The GMG CSF handles requests from AEs and/or from other CSEs.

Grouping enables the oneM2M System to perform bulk operations to multiple devices, applications, or resources. The GMG CSF shall manage the resources and operations associated with grouping.

The GMG CSF shall handle the requests to create, query, update, and delete a Group. An AE or a CSE may request the creation/retrieve/update/deletion of a Group as well as the addition and deletion of members of the Group. The GMG CSF shall be able to create one or more Groups in CSEs in any of the Nodes in oneM2M System for a particular purpose (i.e. facilitation of access control, device management, fan-out common operations to a group of devices, etc.). The GMG CSF shall handle the requests to retrieve the information (e.g. URI, metadata, etc.) of a Group and its associated members.

The GMG CSF shall manage Group membership. The GMG CSF shall handle requests to add or remove members to and from a Group’s member list. A member may belong to one or more Groups. A Group may be a member of another Group. When new members are added to a Group, the GMG CSF should validate if the member complies with the purpose of the Group.

In order to fulfil the functionalities of the GMG CSF, functionalities from other CSFs may be needed. Examples include Network Service Exposure CSF for leveraging broadcasting/multicasting capability from the Underlying Network, Security CSF for authentication and authorization etc.

Editor’s Note: How the Underlying Network supports broadcasting/multicasting is FFS.

When facilitating access control using a Group, only members with the same access rights towards a resource shall be included in the same Group. Also, only AEs or CSEs which have a common role with regards to access rights shall be included in the same Group. This shall be used as a representation of the "role" when facilitating role based access control.

Editor's Note:  Suggest adding description on what is meant by Group member, what entities can be members of a Group?  Can a Group consist of heterogeneous members?

The GMG CSF shall forward requests to all members in the Group. In case the Group contains another Group as a member, the forwarding process shall be done recursively, i.e. the nested Group shall forward the request to its members. After forwarding the request to all members in the Group, the GMG CSF shall generate an aggregated response by aggregating the corresponding responses from the Group members.

Editor’s Note: The structure of the resource in oneM2M System is FFS.

The GMG CSF shall support subscriptions to individual Groups. Subscriptions to a Group shall be made only if the subscriber is interested in all members of the Group. If subscription to a Group is made, the GMG CSF shall aggregate the notifications from the Group members, and it shall notify the subscriber with the aggregated notification. Responses and event notifications relevant to a subscription may be selectively filtered by filtering criteria. The filtering criteria shall be managed by the GMG CSF. In order to subscribe to or query a Group, methods for group discovery shall be provided.

************************* END OF CHANGE 4  *************************

************************ START OF CHANGE 5  ************************

6.2.7	Location

6.2.7.1	General Concepts

The Location (LOC) CSF allows M2M AEs to obtain geographical location information of M2M Nodes (e.g., ASN, MN) for location-based services. Such location information requests may be from an M2M AE residing on either a local Node or a remote Node.

NOTE: Geographical location information can be more than simply the longitude and the latitude information.

6.2.7.2	Detailed Descriptions

LOC CSF shall obtain and manage geographical location information based on the requests from M2M AEs residing on either a local Node or a remote Node. The LOC CSF shall interact with any of the following: a location server in the Underlying Network, a GPS module in the M2M Node, or, information for inferring location stored in other M2M Nodes.

In order to Update the location information, an M2M AE shall be able to configure an attribute (e.g., update period). Based on the such defined attribute, the LOC CSF shall Update the location information using one of interactions defined above.

NOTE: The location technology (e.g., Cell-ID, Assistant-GPS, and Fingerprint) used by the Underlying Network depends on the capabilities of the Underlying Network.

The LOC CSF shall be able to request M2M Nodes to share and report their own or other M2M Node's geographical location information with the requesting AEs.

The LOC CSF shall be able to provide means for protecting the confidentiality of geographical location information.

************************* END OF CHANGE 5  *************************

************************ START OF CHANGE 6  ************************

6.2.8	Network Service Exposure, Service Execution and Triggering

6.2.8.1	General Concepts

Network Service Exposure, Service Execution and Triggering (NSSE) CSF manages communications with the Underlying Networks for accessing network service functions over the Mcn reference point. The NSSE CSF uses the available/supported methods for service "requests" on behalf of AEs. The NSSE CSF shields other CSFs and AFs from the specific technologies and mechanisms supported by the Underlying Networks.

NOTE: The NSSE CSF provides adaptation for different set of network service functions supported by various Underlying Networks.

The network service functions provided by the Underlying Network include service functions such as, but not limited to, device triggering, small data transmission, location notification, policy rules setting, location queries, IMS services, device management. Such services do not include the general transport services.

6.2.8.2	Detailed Descriptions

NSSE CSF shall manage communication with the Underlying Networks for obtaining network service functions on behalf of other CSFs, remote CSEs or AEs. The NSSE CSF shall use the Mcn reference point for communicating with the Underlying Networks.

NOTE: The network services provided by the Underlying Networks include services such as, but not limited to, device triggering, small data transmission, location notification, policy rules setting, location queries, IMS services, device management. Such services do not include general transport services.

The M2M System shall allow the Underlying Networks to control network service procedures and information exchange over the Underlying Networks while providing such network services. For example, for the 3GPP networks, the Underlying Network may chose to provide the network services based on control plane signalling mechanisms.

Other CSFs in a CSE that need to use the services offered by the Underlying Network shall use the NSSE CSF.

The NSSE CSF shall shield other CSFs and AFs from the specific technology and mechanisms supported by the Underlying Networks.

NOTE: The NSSE CSF provides adaptation for different set of network service functions supported by various Underlying Networks.

The NSSE CSF shall maintain over the Mcn reference point, the necessary connections and/or sessions between the CSE and the Underlying Network when local CSFs are in need of a network service.

The NSSE CSF shall provide to the CMDH CSF information related to the Underlying Network so the CMDH CSF can include them to determine proper communication handling.

************************* END OF CHANGE 6  *************************

************************ START OF CHANGE 7  ************************

6.2.9	Registration

6.2.9.1	General Concepts

Registration (REG) CSF is responsible for handling an AE or another CSE to register with a CSE in order to allow the registered entities to use the services offered by the registered-with CSE. The REG CSF handles registration of a Device also, so as to allow registration of Device's properties/attributes with the CSE.

6.2.9.2	Detailed Descriptions

Registration is the process of delivering AE or CSE information to another CSE for being able to use the M2M Services.

The CSE on an Application Service Node or on a Middle Node shall perform registration with the CSE in the Infrastructure Node in order to be able to use M2M services offered by the CSE in the Infrastructure Node. An AE on an Application Service Node or on a Middle Node shall perform registration locally with the corresponding CSE in order to use M2M services offered by that CSE. The same holds for the registration of an AE on the Infrastructure Node. An AE on an Infrastructure Node shall perform registration locally with the associated CSE on Infrastructure Node. A registered AE shall be able to have interactions with its local CSE without the need to have the local CSE register with other CSEs. Such registrations are applicable to a single M2M Service Provider Domain.

A CSE on an Application Service Node or on a Middle Node shall perform registration with the CSE on an Infrastructure Node and vice versa. As a result of successful CSE registration, the CSEs on ASN/Middle Node and Infrastructure Node establish a peering relationship and shall be able to exchange context information.

A (physical) Device shall be able to register with its local CSE for registering its properties/attributes. Such registration enables correlation of Devices Identities such as M2M-Node-ID with the CSE-ID.

Editor’s Note: The need for Device Registration and the relationship with CSE Registration are FFS.

Editor’s Note: The use of External ID in Registration is FFS.

Registration information shall be able to include:

  - Reachability schedules, which are elements of a node’s policy, and specify when messaging may occur between nodes. Reachability schedules may be used in conjunction with other policy elements. When reachability schedules are not present in a node then that node is expected to be always reachable.

The following is included in the Registration information:

  - Identifier

  - Reachability

Editor’s note: Further Registration information is FFS.

6.2.10	Security

6.2.10.1	General Concepts

Security (SEC) CSF comprises the following functionalities:

- Sensitive Data Handling functionality;

- Security Administration functionality;

- Security Association Establishment functionality;

- Authorization and Access Control functionality;

- Identity Protection Functionality.

Sensitive Data Handling functionality in the SEC CSF protects the local credentials on which security relies during storage and manipulation. Sensitive Data Handling functionality performs other sensitive functions as well such as security algorithms. This functionality is able to support several cryptographically separated security environments.

Security Administration functionality enables services such as the following:

- Creation and administration of dedicated security environment supported by Sensitive Data Handling functionality;

- Post-provisioning of a root credential protected by the security environment;

- Provisioning and administration of subscriptions related to M2M Services and M2M Application Services.

Security Association Establishment functionality is responsible for establishing security association between corresponding M2M nodes, in order to provide services such as confidentiality, integrity, authentication, authorization, etc.

Authorization and Access Control functionality is responsible for authorizing services and data access to authenticated entities, according to provisioned security policies and assigned roles.

While unique identifier of an entity are used for authentication, the Identity Protection functionality provides pseudonyms which serve as temporary identifiers which cannot be linked to the true identity of either the associated entity or its user.

6.2.10.2	Detailed Descriptions

SEC CSF shall comprise the following functionalities:

- Sensitive Data Handling functionality;

- Security Administration functionality;

- Security Association Establishment functionality;

- Authorization and Access Control functionality;

- Identity Protection Functionality.

Sensitive Data Handling Functionality in the SEC CSF shall have the capability to protect the local credentials on which security relies during storage and manipulation. The SEC CSF shall be able to extend sensitive data handling functionality to other sensitive data used in the M2M Systems such as subscription related information, security policies and personal data pertaining to individuals. The Sensitive Data Handling functionality shall perform other sensitive functions as well, such as security algorithms. The Sensitive Data Handling functionality shall be able to support several cryptographically separated security environments.

Security Administration functionality in the SEC CSF shall enable the following services:

- Creation and administration of a dedicated security environment supported by Sensitive Data Handling functionality;

- Post-provisioning of a root credential protected by the security environment;

NOTE: The security environment can also be pre-provisioned with a root credential prior to deployment; therefore this capability is not always required. Post-provisioning is required when the security bootstrapping needs to be performed or re-initiated after deployment.

- Provisioning and administration of subscriptions related to M2M services and M2M application services. Besides the root secret, a subscription includes other information classified as sensitive data such as associated authorization and security policies.

Security Association Establishment functionality in the SEC CSF shall be able to establish security associations between corresponding M2M nodes, in order to provide specific security services (e.g. confidentiality, integrity, authentication, authorisation, or support for application level signature generation and verification) involving specified security algorithms and sensitive data. This involves key derivation based on provisioned root secrets. This functionality of the SEC CSF is mandatory when security is supported.

Editor's Node: The definition of Security Association will be provided by WG4. A definition may be: "Security associations (SAs) are logical relationships between 2 entities that may be associated with a communications link, but SAs are not communications links. Security associations may take a number of forms but in each case they identify the nature of the security service (confidentiality, integrity, authentication or authorisation), the required algorithm and key. Security associations may be established for single transactions (and thus their establishment may form part of the transaction itself) or for session based associations (in such instances the association is generally established independently of the individual transactions that are to be secured)".

The Authorization and Access Control functionality in the SEC CSF shall be able to authorize services and data access to authenticated entities, according to provisioned security policies and assigned roles. This functionality is mandatory when any services relying on authorization and access control are present. Among other usages, the services of this functionality may be applied to personal information as a means to preserve privacy.

Although a Subscriber is generally considered to be an AE or functional agent that represents a human, there are links between a device and its User that can be either directly derived or indirectly deduced. Consequently, identifiers used for communication in the M2M System shall not be directly related to the real identity of either the device or its User, except where this is a requirement for operation of a specific AE.

While the unique identifier of an entity shall be used for authentication, the identity protection functionality provides pseudonyms which serve as temporary identifiers which shall not be able to be linked to the true identity of either the associated entity or its user.

************************* END OF CHANGE 7  *************************

************************ START OF CHANGE 8  ************************

6.2.12	Service Session Management

6.2.12.1	General Concepts

An M2M service session is an end-to-end Service Layer connection managed by the Service Session Management (SSM) CSF.  The SSM CSF manages M2M service sessions between AEs, between an AE and a CSE, or between CSEs.

Editor's Note: Provide information as to when an M2M service session is needed.

The management of a M2M service session includes capabilities such as the management of session state, session authentication and establishment, management of Underlying Network connections and services related to the session, coordination of sessions spanning multiple hops of CSEs, exchange of information between session endpoints, and session termination.

The SSM CSF uses the CMDH CSF within its local CSE for sending/receiving messages to/from the next-hop CSE or to/from an AE for a given M2M service session. The SSM CSF also uses the SEC CSF for the management of session related security credentials and authentication of session participants. The SSM CSF generates session specific charging events also that it communicates to the SCA CSF within its local CSE.

6.2.12.2	Detailed Descriptions

An M2M service session is an end-to-end Service Layer connection managed by the SSM CSF. The SSM CSF shall support the management of the following M2M service session related information.

- Session Identifier: The Service Session Identifier is used by the SSM CSF and session endpoints to uniquely identify M2M service layer session.

- Session Credentials: Security credentials associated with M2M service session.  For example, E2E security certificates, public keys, etc. An M2M service session can support an independent set of credentials or it can optionally leverage security credentials from Underlying Network sessions or network connections.

- Session Descriptor: Information describing the M2M service session that can be used by the existing session endpoints or prospective session participants in order to discover an existing session.  For example, a description for each session participant (e.g. device identifiers, type of participant, services that participant supports, interface requirements of participant, type of compression used, etc.).

- Session Routing Information: Information describing how to route M2M service session messages. For example, list of CSEs in the routing path, or next-hop CSE in the routing path.

- Session Context/History: Information related to M2M service session activity such as session related events that have occurred or transactions that have been processed.  For example, keeping track of the type, number, rate, size, etc. of the resources targeted by the session endpoints. Or keeping track of different service sessions that a specific application establishes (e.g. rate, type, etc).

- Session Policies: Policies that define rules for how SSM CSF manages sessions. For example, session routing policies, session store-and-forward policies, session access control policies, session data management policies, etc.  The SSM CSF can use these policies by itself or provide such policies to other CSFs (e.g. CMDH CSF, DMR CSF, SEC CSF, etc).

Some M2M service sessions may require security. In order to secure an M2M service session, proper security credentials shall be used by session endpoints (e.g., AEs and/or CSEs).  If M2M service session credentials are not pre-provisioned, the SSM CSF shall support securely bootstrapping of the session credentials to the session endpoints. The SSM CSF shall use the SEC CSF for supporting such bootstrapping. The SSM CSF may also leverage security credentials and trust relationships from Underlying Networks.

The SSM CSF shall support requests to establish an M2M service session between AEs, between an AE and a CSE, or between CSEs.  Before a request to establish an M2M service session is granted, the SSM CSF shall first authenticate the requester using session credentials. The SSM CSF shall use the SEC CSF to support session authentication. Once authenticated, the SSM CSF shall establish the M2M service session between the requesting and targeted session endpoints. This shall involve the SSM CSF coordinating with the targeted session endpoint on an agreed upon session ID that can be used to identify the session messages. The SSM CSF shall return this session ID to the requester. The SSM CSF shall also maintain additional session information for the management of the session such as session policies, session routing information, session descriptor, etc.

The SSM CSF shall support layering of a M2M service session over the top of Underlying Network connections. The SSM CSF shall support persistency of the M2M service sessions with respect to the Underlying Network connections.  The SSM CSF shall maintain an active M2M service session independent of the state of the Underlying Network connections and shall be robust to network connections that are dynamically torn-down and re-established. The SSM CSF shall support initiating or providing input to other CSFs and/or the Underlying Network on whether the network connections should be torn-down/re-established based on M2M service session activity or state.

The SSM CSF shall support requests to terminate an M2M service session between AEs, between an AE and a CSE, or between CSEs. Before a request to terminate an M2M service session is granted, the SSM CSF shall first authenticate the requester using session credentials. The SSM CSF shall use the SEC CSF to support session authentication. Once authenticated, the SSM CSF shall terminate the M2M service session between the requesting and targeted session endpoints. This shall involve removal of session information on the session endpoints as well as the SSM CSF.

The SSM CSF shall support M2M service sessions that span multiple intermediate CSE hops. The SSM CSF shall leverage the SEC CSF on its local CSE as well the SSM CSF and the SEC CSF on intermediate CSEs to support multi-hop M2M service sessions. In doing so, SSM CSFs on different CSEs shall support coordinated M2M service session management. This includes bootstrapping of session credentials, session authentication and establishment, management of underlying network connections and services related to the session, management of session routing information, and session termination across multiple SSM CSFs.

************************* END OF CHANGE 8  *************************

************************ START OF CHANGE 9  ************************

6.4	Security Aspects

The oneM2M Security Analysis Technical Report [i.x] differentiates security domains related to the transport layer (Underlying Network), service layer (M2M common services) and Application Layer. It also considers possible trust scenarios involving these different security domains, and investigates countermeasures to threats that potentially affect the security of the M2M System.

Each of the security domains may provide their own set of security capabilities. The oneM2M security solution shall provide configurable security services through an API for upper security domains to leverage on, or enable the use of the exposed security features of other security domains when appropriate.

As a result, beyond providing security solutions that protect the integrity of the M2M Service Layer, the oneM2M architecture exposes, through its APIs, further security services that are made available to M2M Applications. This enables M2M Applications to benefit from security solutions deployed in the M2M Service Architecture, without adding redundant and/or proprietary security solutions on application nodes and devices.

NOTE: It remains the responsibility of M2M Application Service Providers to perform their own risk assessment process to identifying the specific threats affecting them and derive their actual security needs.

************************* END OF CHANGE 9  *************************

************************ START OF CHANGE 10  ************************

6.5.1.1 	Public Domain Names and CSEs

To enable the usage of public DNSs as described above, there is a need for a naming convention for public names for CSEs.  This naming convention facilitates the creation of the necessary entries of the public domain names of CSEs in the DNS by the Infrastructure Node.

CSEs public domain names shall be a sub-domain of the Infrastructure Node public domain name. This naming convention allows the Infrastructure Node to include the needed DNS entry corresponding to the CSE to whom access from other domains is allowed. This would typically occur when the CSE registers with the Infrastructure Node, subject to policies, or administratively. The Infrastructure Node shall also have a public domain name.

Accordingly, the structure of the public domain of the CSEs in Middle Node and Application Service Node shall follow the following naming convention, which relies on the CSE identifier (CSE-ID) as part of the naming convention to facilitate the entry creation:

    - Infrastructure Node public domain name: <Infrastructure Node CSE Identifier>.<M2M Service Provider domain name>

    - MN-CSE public domain name: <Middle Node CSE Identifier>.<Infrastructure Node public domain name>

    - ASN-CSE public domain name: <Application Service Node CSE Identifier>.<Infrastructure Node public domain name>

Both the MN-CSE and the ASN-CSE are sub-domains of the Infrastructure Node.

The A/AAAA records in the DNS, as per [i.5], [i.6], and [i.10] shall consist of the public domain name of the CSE and the IP address of the M2M Infrastructure Node, since the M2M Infrastructure Node is the entry point of the M2M Service Provider domain name where it belongs to.

************************* END OF CHANGE 10  *************************

************************ START OF CHANGE 11 ************************

7.1.2	Application Entity Identifier (AE-ID)

An Application Entity Identifier (AE-ID) uniquely identifies an AE resident on an M2M Node, or an AE that requests to interact with an M2M Node. An AE-ID shall identify an Application for the purpose of all interactions from/to the Application within the M2M System.

It is the responsibility of the M2M Service Provider to ensure that the AE-ID is globally unique. The AE-ID shall include the Application ID (see section 7.1.3.)

************************* END OF CHANGE 11  *************************

************************ START OF CHANGE 12  ************************

7.1.5	M2M Node Identifier (M2M-Node-ID)

An M2M Node, hosting a CSE and/or AE(s) shall be identified by a globally unique identifier, the M2M-Node-ID.

The M2M System shall allow the M2M Service Provider to set the CSE-ID and the M2M-Node-ID to the same value.

The M2M-Node-ID enables the M2M Service Provider to bind a CSE-ID to a specific M2M node.

************************* END OF CHANGE 12  *************************

************************ START OF CHANGE 13  ************************

7.1.6	M2M Service Subscription Identifier (M2M-Sub-ID)

The M2M-Sub-ID enables the M2M Service Provider to bind AE(s), M2M Nodes, CSEs and services identified by service identifiers to a particular M2M service subscription.

Editor's Note: The specification needs to include a section on services, service identifiers.

The M2M Service Subscription Identifier has the following characteristics:

•	belongs to the M2M Service Provider,

•	identifies the subscription to an M2M Service Provider,

•	enables communication with the M2M Service Provider,

•	can differ from the M2M Underlying Network Subscription Identifier,

There can be multiple M2M Service Subscription Identifiers per M2M Underlying Network subscription.

************************* END OF CHANGE 13  *************************

************************ START OF CHANGE 14  ************************

7.1.7	M2M Request Identifier (M2M-Request-ID)

This is an identifier that tracks a Request initiated by an AE over the Mca reference point, and by a CSE over the Mcc and Mcn reference points, if applicable, end to end. It is also included in the Response to the Request over all the above reference points.

To enable AE to track Requests and corresponding Responses over the Mca reference point, AEs shall include a distinct Request Identifier per request over the Mca Reference point to the CSE for any initiated request.

If the Request Identifier used by the AE over the Mca reference point is guaranteed to be globally unique, then the CSE can reuse the AE request identifier over the Mcc and Mca reference points where applicable. If the request identifier used by the AE cannot be guaranteed to be globally unique, then the CSE shall allocate a new globally unique request identifier in its interactions with peer CSEs to service the AE request. Note that the request initiated by the CSE could be the result of an AE request, or a request initiated autonomously by the CSE to fulfil a service.

Note that the Request Identifier can be made globally unique by including the CSE-ID in combination with any random number.

If the CSE creates a Request Identifier, then the CSE shall maintain a binding between the AE request identifier and the CSE request identifier it created in its interactions towards other peer CSEs. The CSE shall include the AE request identifier in its response to the AE. This binding shall be maintained by the CSE until the Request is deposed off.

A CSE receiving a Request from a peer CSE shall include the received Request Identifier in all additional requests unspanned (i.e.1:1) it has to generate (including propagation of the incoming Request) and that are associated with the incoming Request, where applicable.

The CSE shall include the same received Request Identifier in its interactions with the Underlying Network, over the Mcn reference point where applicable

************************* END OF CHANGE 14  *************************

************************ START OF CHANGE 15  ************************

7.2 M2M Identifiers lifecycle and characteristics

Table 7.2-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | FFS |  |
| AE Identifier | FFS | AE | Note that the AE identifier is created when the executing AE registers to a local CSE | AE Registration | Global | - AE Registration - Other operations FFS |  |
| CSE Identifier | M2M SP | CSE | During the first M2M Service connection unless pre-provisioned | Life of the CSE | Global | Information flows (section 10) |  |
| M2M Node Identifier | M2M SP | M2M Node hosting CSE | Pre-provisioned | Life of the M2M Node | Global | Out of scope |  |
| M2M Subscription Identifier | M2M SP | Application Entities, and one or more CSEs belonging to the same M2M Subscriber | At M2M Service signup | Life of the M2M Service Subscription with the M2M SP | Global | - Charging and Information Recorded - Other operations are FFS | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M-Request-ID | Mcc: CSE Mca: AE | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global | Requests and corresponding responses |  |
| External Identifier | Manual mode: Jointly between the Underlying Network provider and M2M SP, where applicable. Plug-And- Play: FFS | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Manual Mode: Administrative Agreement. Plug-And- Play: FFS | Life time of the CSE. | FFS | Requests initiated by a CSE over the Interface, where applicable. |  |

************************* END OF CHANGE 15  *************************

************************ START OF CHANGE 16  ************************

7.3.2		Application Entity Reachability

7.3.2.1		CSE Point of Access (CSE-PoA)

The CSE-PoA shall be used by the M2M System to communicate with a CSE on an M2M Node. Once communication with a CSE is achieved, an AE registered with  that CSE can be reached as long as the AE can be uniquely identified.

The CSE-PoA for a CSE shall be provided to the M2M System at the registration of the CSE. For ADNs, the CSE-PoA shall be provided at the registration of the CSE on the registered-to MN/IN. For an ASN/MN/IN, the CSE-PoA shall be provided at the registration of the CSE on the ASN/MN/IN respectively.

Editor's Note: It is suggested to delete the para above. It is repetitive.

The information included in the CSE-PoA, as well as the refresh of the CSE-PoA, depends on the characteristics of the Underlying Network and the M2M Node transport  capabilities.

7.3.2.2		Locating Application Entities

Locating an AE is a two-step process as follows:

- Step 1: There is a need to locate the CSE where the AE is registered. Locating the CSE shall be accomplished as follows:

- For AEs associated with ASNs/MNs/INs, the CSE-PoA of the ASN-CSE/MN-CSE/IN-CSE registered object shall be used.

- For AEs associated with ADNs, the CSE-PoA of the MN-CSE/IN-CSE registered object shall be used.

- Step 2:  the CSE shall locate the appropriate AE using its AE Identifier (AE-ID).

************************* END OF CHANGE 16 *************************

************************ START OF CHANGE 17  ************************

8.1.1	Description

Figure 8.1.1-1 shows the general flow that governs the information exchange within a procedure, which is based on the use of Request and Response scheme. The scheme applies to communications such as:

- between an AE and a CSE (Mca reference point), and

- among CSEs (Mcc reference point).

The communications can be initiated either by the AEs or by the CSEs.

Figure 8.1.1-1: Resource Manipulation by an Application within an Entity

************************* END OF CHANGE 17  *************************

************************ START OF CHANGE 18  ************************

8.2.2	Accessing Resources in CSEs – Blocking Requests

For the procedures described herein, the addressed resource can be stored in different CSEs. Table 8.2.2-1 describes the possible scenarios, where the addressed resource may be on the local-CSE or on a CSE located elsewhere in the oneM2M System.

In this sub-clause – for simplicity – it is assumed that the Originator of a Request can always wait long enough to get a Response to the Request after the requested operation has finished. This implies potentially long or unknown blocking times (time for which a pending Request has not been responded to) for the Originator of a Request.

For scenarios that avoid such possibly long blocking times, section 8.2.3 specifies mechanisms to handle synchronous and asynchronous resource access procedures via returning appropriate references.

Editor’s Note: How the target of a Request (i.e, an Application or local/hosting CSE) is identified and addressed, is FFS.

Editor’s Note: A message (Request, Response) can be forwarded immediately or forwarded at a later time (e.g in the case of congestion).The procedures related to the forwarding of the Request at a later time are FFS.

Table 8.2.2-1 Accessing Resources in different CSEs

| Traversals across X/Y Reference Points | Description | Reference |
| --- | --- | --- |
| No Hops | The Originator of the Request accesses a resource. The Originator of the Request can be an AE or a CSE. Local CSE and Hosting CSE are the same entity. The CSE shall check the Access Rights for accessing the resource. Depending on the expected result content, the CSE shall respond to the Originator of the Request, either with a Success or Failure Response, or not at all. | Figure 8.2.2-1 |
| 1 Hop | The Originator of the Request accesses a resource. The Originator of the Request may only be an AE. Local CSE and Hosting CSEs different entities. Local CSE shall forward the Request to the Hosting CSE, after an optional checking of the Access Rights for accessing the resource and the syntax of the Request message. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-2 (Editor's Note-1) |
| Multi Hops | The Originator of the Request accesses a resource. The Originator of the Request may be an AE or a CSE. Local CSE, Intermediate CSE(s) and the Hosting CSE are different entities. Local CSE shall forward the Request to an Intermediate CSE (e.g. MN-CSE) that the Local CSE is registered with, if it cannot communicate with the Hosting CSE directly. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message may be performed prior to forwarding the Request. Intermediate CSE may forward the Request to another Intermediate CSE (e.g. another MN-CSE) that the Intermediate CSE is registered with, if it cannot communicate with the Hosting CSE directly. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message can be performed prior to forwarding the Request. The Intermediate CSE shall forward the request to the Hosting CSE. An optional checking of the Access Rights and the syntax of the Request message can be performed prior to forwarding the Request. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-3 (Editor's Note-2) |
| Editor's Note-1: One-Hop case could potentially include the CSE-to-CSE communication also. The need for such procedures is FFS. Editor's Note-2: The multi-hop procedures address the scenario when the target is on a specific remote CSE. How a flow will work when the target is distributed on multiple remote CSEs is FFS. |

Figure 8.2.2-1: Originator accesses a resource on the Local CSE (No Hops)

Figure 8.2.2-2: AE accesses a resource at the Hosting CSE (One Hop)

Figure 8.2.2-3: Originator accesses a resource at the Hosting CSE (Multi Hops)

************************* END OF CHANGE 18  *************************

************************ START OF CHANGE 19  ************************

8.2.3.3	Asynchronous Case

In the asynchronous case, it is assumed that the Originator of a Request is actually able to receive notification messages, i.e. the Local CSE could send an unsolicited message to the Originator at an arbitrary time to send the result to a notification target. The possible mechanisms how the notification then reaches the Originator are the same as in the case of a notification after a subscription.

In that case the information flow depicted in Figure 8.2.3.3-1 is applicable. In this case it is assumed that the Originator of the Request provided a reference – notificationReference – for notification when the result of the requested operation is available.

Equivalent information flows are valid also for cases where the target resource of the requested operation is hosted on the Local CSE. From an Originator’s perspective there is no difference as the later notification of the result of a requested operation would always be an exchange of request/response messages between the Originator and the Local CSE using reference to the original Request.

Figure 8.2.3.3-2 Non-blocking access to resource in notification mode 
(Hosting CSE not equal to Local CSE), Originator provided reference for notification.

************************* END OF CHANGE 19  *************************

************************ START OF CHANGE 20  ************************

# 9	Resource Management

All entities in the oneM2M System, such as AEs, CSEs, "data", etc., are represented as "resources". A "resource structure" is specified as a representation of the "resources". Such "resources" are uniquely addressable. Procedures for accessing such resources are also specified.

************************* END OF CHANGE 20  *************************

************************ START OF CHANGE 21  ************************

## 9.5	Resource Specification Guidelines

The following guidelines shall be used for the specification of resources.

Resources shall be specified by a tabular notation and the associated graphical representation as follows:

- The resources shall be specified in association with a CSE. The resources are the representation in the CSE of the components and elements within the M2M System. Other CSEs, AEs, application data representing sensors, commands, etc. are known to the CSE by means of their resource representation.

Resource: is a uniquely addressable entity in the RESTful architecture. A resource shall be transferred and manipulated using the verbs, such as those specified in section 8.1.

- A resource may contain child resource(s) and attribute(s).

Child Resource: It is a resource that has a containment relationship with the addressed (parent) resource. The parent resource representation contains references to the child resources(s). The lifetime of a child resource is limited by the parent's resource lifetime.

Attributes: store information about the resource itself. The set of attributes, which are common to all resources, are not detailed in the graphical representation of a resource.

- When an instance of a resource is created, a URI is assigned. URI is used to uniquely address the resource.

- Resources and attributes are addressed in the same manner, e.g., by the use of the URI.

- Resource names and attribute names are strings in lower case. In case of a composed name, the subsequent word(s) start with a capital letter; e.g., accessRights, creationTime, expirationTime.

- A string delimited with ‘<’ and ‘>’ e.g., ‘<resourceType>’ is a placeholder for the type of a resource.

- A collection is a parent resource that contains attributes and child resources. All child resources of a collection are of the same type. A collection is represented by a collection name.

- Read/Write access modes for attributes can assume the following values:

- Read/Write (RW), it can be set by a Create or an Update operation,

- Read Only (RO), it is set by the CSE when the resource is Created and/or Updated. Such an attribute can only be read,

- Write Once (WO), it is set by the Create operation. It can then only be read.

- The graphical representation of a resource shows the multiplicity of the attributes and child resources. The following graphical representations are used for representing the attributes, child resources and collection resources:

- Square boxes are used for resources and child resources

- Square boxes with round corners are used for attributes

- Parallelograms are used for collection resources.

- If a child resource of a given resource type with a specific name or an attribute can occur more than once within the containing (parent) resource and if the child resource/attribute is created at runtime then the name of the child resource or the attribute shall consist of a fixed part and a variable part separated with ‘_’ (underscore) between the two parts. The fixed part is a character string and the variable part is indicated by [x] whereby the distinguishable value of [x] (numbers and/or strings) can be assigned by the Originator, or assigned by the CSE if not provided by the Originator. For example:

- For the child resource case, childResourceName_[x] will be instantiated as childResourceName_1, childResourceName_2 etc.

- For the attribute case, attributeName_[x] will be instantiated as attributeName_abc, attributeName_def, etc.

************************* END OF CHANGE 21  *************************

************************ START OF CHANGE 22  ************************

9.6.1	 Common Attributes

Many of the attributes of the resources described in the present document are common. Such attributes are described here once in order to avoid duplicating the description for every resource that contains it.

Attributes that are only used in one or two resource types are described only in the section for that resource type.

In all tables representing resource attributes, each attribute name is followed by its “short name” in brackets that shall be used in resource representations to be transferred across reference points.

Table 9.6.1-1: Common Attributes

| Common Attribute | Description |
| --- | --- |
| resourceType (rT) | Resource Type. This WO resourceType attribute stores <in a two capital letters token> the information useful for procedure processing, e.g. CO for <container>, CI for <instance>. |
| parentID (pID) | The flat URI used to identify the parent resource without using the full structured URI. Editor's Note: The adoption of a URI format is still to be confirmed. |
| accessRightID (aRI) | The URI of an <access rights> resource. The permissions defined in the <accessRight> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g., Retrieve, Update, Delete etc.). If a resource type does not have an accessRightID attribute definition, then the accessRights for resources of that type are governed in a different way, for example, the accessRight associated with the parent may apply to a child resource that does not have an accessRightID attribute definition, or the permissions for access are fixed. Refer to the corresponding procedures to see how permissions are handled in such cases. If a resource type does have an accessRightID attribute definition, but the (optional) accessRightID attribute is not set, or it is set to a value that does not correspond to an valid, existing <accessRight> resource, or it refers to an <accessRight> resource that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access permissions shall apply. The system default access permissions grant all permissions (i.e. the full set of permissionsFlags) to the following permission holders depending on the prefix of URI of the resource.: << Editor's Note: what is the list of permission holders>> |
| creationTime (cT) | Time/date of creation of the resource. |
| expirationTime (eT) | Time/date after which the resource will be deleted by the hosting CSE. This attribute can be provided by the issuer, and in such a case it will be regarded as a hint to the hosting CSE on the lifetime of the resource. The hosting CSE can however decide on the real expirationTime. If the hosting CSE decides to change the expirationTime attribute value, this is communicated back to the Originator. The lifetime of the resource can be extended by providing a new value for this attribute in an UPDATE verb. Or by deleting the attribute value, e.g. by not providing the attribute when doing a full UPDATE, in which case the hosting CSE can decide on a new value. |
| filterCriteria (fC) | Criteria to be used to filter the results. They can either be used in a GET (as query parameters) or in a subscription. Editor's Note: Is GET a supported operation. Editor's Note: The applicability of this attribute is FFS. |
| lastModifiedTime (lMT) | Last modification time/date of the resource. |
| labels (lBs) | Tokens used as keys for discovering resources. |
| creator (cr) | The AE-ID or CSE-ID of the entity which created the resource |
| link (ln) | This attribute shall be present only for the announced resource. This attribute shall provide the URI to the original resource. |
| announceTo (aT) | This attributes shall be present only for the announceable original resource. This attribute maintains the list of URIs to the announced resources. Updates on this attribute will trigger the new resource announcement or de-announcement. In case of new resource announcement, the exact URI to the announced resource that will be created can be provided, or the CSE-ID can be provided, which means the resource-hosting CSE will decide the exact location in the CSE identified by the CSE-ID. |
| announcedAttribute (aA) | This attributes shall be present only for the announceable original resource. This attribute maintains the list of the announced attributes in the original resource. Updates on this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |

************************* END OF CHANGE 22  *************************

************************ START OF CHANGE 23  ************************

### 9.6.8	 Resource Type request

The use of this resource type is optional depending on the configuration.

When a CSE is requested to initiate an operation for which the result should be available to the Originator by reference (‘rt’ information of the request set to ‘Acknowledgement'), the local CSE which received the Request directly from the Originator may need to provide a reference back to the Originator so that the Originator can access attributes of the Request at a later time – for instance in order to retrieve the result of an operation that was taking a longer time. The Originator (or any other authorized entity depending on access rights) can access the request status and the requested operation result through it.

The <request> resource may get deleted by the CSE that is hosting it:

- when the result of the requested operation (if any result was requested at all) has been sent back to the Originator (either by notification to the Originator or by retrieval initiated by the Originator);

- when the expiration time of the <request> resource is reached;

- at any other time -  depending on local settings in the CSE that hosts the <request> resource.

Editor’s Note: The exact way how to define that setting (e.g. via DM) is FFS.

For the purpose of providing a standardized structure for expressing and accessing the context of a previously issued Request, the resource type request is defined.

Figure 9.6.8-1: Structure of resource <request>
(only resource specific attributes are shown)

The resource <request> shall contain the attributes according to their multiplicity shown in Table 9.6.8-1.

Table 9.6.8-1: Attributes of <request> resource

| Attribute Name of <request> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime (et) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| operation | 1 | RO | The operation requested by the Originator, e.g. modifying the content of a container, registering an AE. |
| target | 1 | RO | The address or the target resource for the requested operation. |
| originator | 1 | RO | The originating entity for the request. |
| metaInfromation | 1 | RO | Meta information about the request. The content of this attribute is equivalent to the “mi” information in section 8.1. |
| content | 1 | RO | Contains the content that is supposed to be sent to the target resource. |
| requestStatus | 1 | RO | Contains information on the current status of the Request, e.g. “accepted and pending”. |
| operationResult | 1 | RO | Contains information on the result of the requested action, e.g. “Resource created with URI: XXX”. |

Creation of a <request> resource can only be done on a local CSE implicitly by an AE issuing a generic CRUD equest for any other resource type to the Local CSE. A Local CSE cannot accept requests to create a <request> resource directly.

Retrieving of <request> resources or attributes of a <request> resource is allowed for authorized entities.

Update of a <request> resource can only be done by the CSE that hosts the <request> resource or by CSEs that provide operation results pertaining to the request (for instance when the result of an operation requested for a remote CSE becomes available).

Deletion of a <request> resource is possible by authorized entities. If the execution of the request was still pending at the time of deletion, the hosting CSE is supposed to stop any further attempts to execute the request.

************************* END OF CHANGE 23  *************************

************************ START OF CHANGE 24  ************************

### 9.6.15	 Resources for Service Charging and Accounting

The <chargingPolicy> and <chargingRule> resources enable the SCA CSF to generate accounting information for particular services based on policies provided by the Service Provider. The SCA CSF and its resources residing on one CSE can be used by other CSEs and AEs that subscribed to this CSE.

************************* END OF CHANGE 24  *************************

************************ START OF CHANGE 25  ************************

#### 9.6.15.3 	Resource Type chargingRule

The resource type <chargingRule> shall be used to define different rules for charging purpose. One node may setup multiple rules. One rule may be activated or de-activated.

Figure 9.6.15.3-1: Structure of <chargingRule> resource 
(only resource specific attributes are shown)

The <chargingRule> resource shall contain the attributes described in Table 9.6.15.3-1.

Table 9.6.15.3-1: Attributes of <chargingRule> resource

| Attribute Name of <chargingRule> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1..n | RW | See section 9.6.1 where this common attribute is described |
| Creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described |
| chargingRuleID | 1 | RO | This is the unique ID of the charging rule. It is created by the CSE when the charging rule resource is first created. |
| chargingEntityID | 1 | WO | This is the unique ID of the entity that charges another entity. For example, it can be an AE ID (AE-ID) or a CSE ID (CSE-ID). |
| chargedEntityID | 1 | WO | This is the unique ID of the entity that is being charged. For example, it can be an AE ID (AE-ID) or a CSE ID (CSE-ID) or a resource ID. |
| ruleStatus | 1 | RW | This attribute indicates whether the rule is “active” or “inactive”, or “information recording only” which means no charging is performed. |
| chargingType | 1 | RW | This attribute indicates whether the charging rule applies for ONLINE or OFFLINE charging. |
| chargingModel | 1 | RW | This attribute indicates the charging model, such as “Subscriber based charging”, “event based charging”, “service based charging”, “session based charging”, etc. |
| subscriberID | 1 | WO | This attribute indicates the service subscriber (M2M-Sub-ID) being charged. |
| collectPeriod | 0..1 | RW | This attribute defines the duration for the SCA to collect service charging information. |
| sessionID | 0..1 | RW | This attribute indicates the unique service session ID, if the chargingType is “session based charging”. It is mandatory of the chargingModel is session based charging. |
| serviceID | 0..1 | RW | This attribute indicates the unique ID of the service being charged. A service provider can define its own services. It is mandatory if the charging model is service based charging. |
| chargeableEventID | 0..1 | RW | This attribute refers to the resource that defines the chargeable event that should be applied to this charging rule. It is mandatory if the charging model is event based charging. |

************************* END OF CHANGE 25  *************************

************************ START OF CHANGE 26  ************************

### 9.6.20	 Resource Type m2mServiceSubscription

This resource represents an M2M Service Subscription. It is used to represent all data pertaining to the M2M Service Subscription (the technical part of the contract between an M2M Application Service Provider and an M2M Service Provider).

Editor’s Note: The link between the M2M Service Subscription resource and RBAC will be added once RBAC is included in the specification.

Figure 9.6.20-1: Structure of <m2mServiceSubscription> resource 
(only resource specific attributes are shown)

Editor’s Note: The actual node resource shall include information such as, extID, profile, device specific ID if applicable and link to CSE and Applications running on the node.

Editor’s Note: the M2M-Sub-ID storage is FFS

The <m2mServiceSubscription> resource shall contain the attributes described in Table 9.6.20-1.

Table 9.6.20-1: Attributes of <m2mServiceSubscription> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| serviceId_[i] | 0..n | RW | This attribute indicates the unique ID of the service being subscribed to. A service provider can define its own services. |
| nodeId_[i] | 0..n | RW | Identifier of a node pertaining to the M2M Service Subscritption. The node identifier is specified in section 7.1.5. The nodeId attributes link to the actual node resource that provides information pertaining to the node such as the external identifier, etc. |
| AE-ID_<i> | 0..n | RW | Identifier of an AE identifier as defined in section 7.1.2. It shall link to an application resource. |

************************* END OF CHANGE 26  *************************

************************ START OF CHANGE 27  ************************

#### 10.2.1.1	Create <container>

This flow is used for creating a <container> resource.

Originator: the Originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the Receiver or Hosting CSE shall validate whether the Originator has proper permissions for creating a <container> resource.

Table 10.2.1.1-1 <container> CREATE flow

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | N/A |
| Information on Request message | op: C fr: Originator AE-ID or CSE-ID to: URI of the parent of the <container> resource cn: Name of <container> resource (optional), Some mandatory and/or optional attributes defined in section 9.6.3 are needed. Editor’s Note: Section x.y.z refers to the table which describes the attributes of <container> resource. |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1.1) |
| Information on Response message | fr: Receiver CSE-ID to: Originator AE-ID or CSE-ID cn: URI of the created <container> if the URI sent by the originator has been changed by the CSE or was not provided in the Request |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. The CSE does not have storage capacity to create the <container> |

Editor's Note: The type of the resource to be created (ty) needs to be specified by the contributor as part of "Information on Request message".

#### 10.2.1.2	Retrieve <container>

This flow is used for retrieving the attributes of a <container> resource.

Originator: the Originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the Receiver or Hosting CSE shall validate whether the Originator has proper permissions for retrieving a <container> resource.

Table 10.2.1.2-1 <container> RETRIEVE flow

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to retrieve a resource |
| Information on Request message | op: R fr: Originator AE-ID or CSE-ID to: URI of the <container> resoruce cn: void Editor’s Note: Section 9.6.3 refers to the table which describes the attributes of <container> |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1.2) |
| Information on Response message | fr: Receiver CSE-ID to: Originator AE-ID or CSE-ID. In case this is a Response carrying the result of an operation triggered by a non-blocking Request, rd information can be used. cn: attributes of the <container> resource Editor’s Note: The procedures for the retrieval of subresources is FFS. |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. |

### 10.2.1.3	Update <container>

This flow is used for updating the attributes and the actual data of a <container> resource.

Originator: the Originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the Receiver or Hosting CSE shall validate whether the originator has proper permissions for updating a <container> resource.

Table 10.2.1.3-1 <container> UPDATE flow

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to update a resource |
| Information on Request message | op: U fr: Originator AE-ID or CSE-ID to: URI of the <container> recource cn: the attributes which to be updated. |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1.3) |
| Information on Response message | No change from the basic procedure (section 10.1.1.3) |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The provided attributes are not acceptable to the Hosting CSE or mandatory attributes are not provided by the Hosting CSE. |

#### 10.2.1.4	Delete <container>

This flow is used for deleting a <container> resource residing under a <container> or <locationContainer> resource.

Originator: the Originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: the Receiver can be a CSE.

Table 10.2.1.4-1 <Container> DELETE flow

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Originator needs to delete a resource |
| Information on Request message | op: D fr: Originator AE-ID or CSE-ID to: URI of the <container> resource cn: void |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1.4). Shall check for child resources and delete all child resources and shall delete child references in parent resources. |
| Information on Response message | No change from the basic procedure (section 10.1.1.4) fr: Receiver CSE-ID to: Originator AE-ID or CSE-ID. In case this is a response carrying the result of an operation triggered by a non-blocking Request, rd information can be used. cn: void |
| Post-Conditions | None |
| Exceptions | None |

************************* END OF CHANGE 27  *************************

************************ START OF CHANGE 28  ************************

#### 10.3.1.3	Retrieve <delivery>

This procedure shall be used for requesting a CSE to provide information on a previously created <delivery> resource which represents delivery of data to a target CSE.

Originator: Originator can be a CSE or an AE.

Receiver: The Receiver shall provide the content of the addressed <delivery> resource or the addressed attributes thereof.

Editor’s Note: This call flow template will be evolving as we handle more examples.

Table 10.3.1.3-1 Retrieve <delivery> Information Flow

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to retrieve information about a previously issued delivery. |
| Information on Request message | cn: URI of the <deliver> resource (optional) filter to retrieve only certain attributes. All other information in the Request message are the same as in the generic procedure |
| Local processing on Hosting CSE | No change to generic procedure. |
| Information on Response message | No change to generic procedure. |
| Post-Conditions | None |
| Exceptions | The Originator CSE is not authorized to retrieve the <delivery> resource or the addressed parts of it. The addressed <delivery> resource does not exist. |

#### 10.3.1.4	Update <delivery>

This procedure shall be used for requesting a CSE to update information on a previously created <delivery> resource which represents a pending delivery of data to a target CSE. The update may have impact on further processing of the delivery.

Originator:  Originator can be a CSE or an AE. Originator needs to be authorized to modify the addressed <delivery> resource, i.e. it needs to be authorized to change the represented delivery process.

Receiver:  The Receiver shall change the content of the addressed <delivery> resource or the addressed attributes thereof and also modify the corresponding parameters of the delivery process

Editor’s Note: This call flow template will be evolving as we handle more examples.

Table 10.3.1.4-1 Update <delivery> Information Flow

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to modify information about a previously issued delivery that is still pending, i.e. it has not yet been forwarded to another CSE. |
| Information on Request message | cn: URI of the <deliver> resource Content of a <delivery> resource in line with the definition in Section 9.6.4 representing a valid request for delivery of data to a target CSE All other information in the Request message are the same as in the generic procedure. |
| Local processing on Hosting CSE | Receiver CSE checks if the requested changes to the delivery process can actually be accomplished. If possible, the Receiver CSE modifies the previously established delivery process and changes the respective content of the <delivery> resource. |
| Information on Response message | Same as in the generic procedure. Successful response messages indicate that the delivery process was modified as requested. |
| Post-Conditions | None |
| Exceptions | The Originator CSE is not authorized to modify the <delivery> resource or the addressed parts of it. The addressed <delivery> resource does not exist. The responsibility for the further processing of the delivery process represented by the addressed <delivery> process was already forwarded to another CSE. |

#### 10.3.1.5	Delete <delivery>

This procedure shall be used for requesting a CSE to cancel a pending delivery of data to a target CSE or to delete the <delivery> resource of an already executed delivery.

Originator:  Originator can be a CSE or an AE. Originator needs to be authorized to modify the addressed <delivery> resource, i.e. it needs to be authorized to change the represented delivery process.

Receiver:  The Receiver shall remove the addressed <delivery> resource and stop the corresponding delivery process if it is still pending

Editor’s Note: This call flow template will be evolving as we handle more examples.

Table 10.3.1.5-1 Delete <delivery> Information Flow

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Originator needs to cancel a previously issued delivery that is still pending, i.e. it has not yet been forwarded to another CSE or Originator needs to remove the <delivery> resource representing an already executed delivery. |
| Information on Request message | No change to generic procedure. |
| Local processing on Hosting CSE | Receiver CSE checks if the corresponding delivery process is still pending. If so, it stops that delivery process. Receiver CSE removes the addressed <delivery> resource. |
| Information on Response message | Same as in the generic procedure. Successful response messages indicate that the delivery process was stopped as requested. |
| Post-Conditions | None |
| Exceptions | The Originator CSE is not authorized to delete the <delivery>. The addressed <delivery> resource does not exist. |

************************* END OF CHANGE 28  *************************

************************ START OF CHANGE 29  ************************

#### 10.3.3.5	Delete <group>

This procedure shall be used for deleting an existing <group> resource.

Originator: The Originator shall request to delete an existing <group> type resource by using the DELETE verb. The request shall address the specific <group> resource of a Hosting CSE. The Originator may be an AE or a CSE.

Receiver: The Receiver shall check if the Originator has DELETE permission on the <group> resource. Upon successful validation, the CSE shall remove the resource from its repository and shall respond to the Originator with the appropriate responses.

Table 10.3.3.5-1 : <group> Delete

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | None |
| Information on Request message | op: D fr: Identifier of the AE or the CSE that initiates the Request to: Th eURI of the <group> resource. |
| Local processing on Hosting CSE | Same as the generic procedure. |
| Information on Response message | Same as the generic procedure. |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure. |

************************* END OF CHANGE 29  *************************

************************ START OF CHANGE 30  ************************

#### 10.3.5.2	Create <mgmtCmd>

A CREATE request is used by an Originator to create a specific <mgmtCmd> resource in a hosting CSE.

The created <mgmtCmd> resource will be mapping a RESTful method to management commands and/or procedures which may be translated from existing management protocols (e.g. BBF TR-069). At run-time the hosting CSE can expose the translated commands, over the Mcc reference point, to the remote entities (i.e. ASN/MN-CSE).

Originator: The Originator shall request to create a new <mgmtCmd > resource to be named as "mgmtCmd" by using a CREATE verb. The request shall address baseURI resource of the hosting CSE. The request may also provide the attributes of the <mgmtCmd> resource to be created as described in section 9.6.12 such as "cmdType".

The Originator may be:

- An AE registered to the IN-CSE.

- The local CSE on the managed entity: In this case, the local CSE transforms supported management command into the <mgmtCmd> resource representation, then requests the hosting CSE to create the corresponding <mgmtCmd> resource.

NOTE 1:	The hosting IN- CSE in the network domain may also create the <mgmtCmd> resource locally by itself. The details are out of scope. Then an AE can discover the created <mgmtCmd> and manipulate it.

NOTE 2:	The <mgmtCmd> resource may also be created in the hosting CSE by other offline provisioning means which are out of scope.

Receiver: The Receiver shall check if the Originator has the CREATE permission on the addressed baseURI resource (or the parent <mgmtCmd> resource in the case of child resource creation). The hosting CSE shall also check the validity of provided attributes. Upon successful validation, a new resource with name "mgmtCmd" shall be created in the hosting CSE with the provided attributes. The hosting CSE shall maintain the mapping between the created <mgmtCmd> resource and the corresponding nonRESTful commands represented by the "cmdType" attribute of <mgmtCmd> resource. The hosting CSE shall respond to the Originator with the appropriate generic response code. It shall also provide in the Response the URL of the created new resource.

The hosting CSE shall be:

- An  IN-CSEIN-CSE.

Table 10.3.5.2-1:  <mgmtCmd> Create

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | The CSE on the originating node shall first collect local management command. |
| Information on Request message | op: C fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in 9.6.12, as needed |
| Local processing on Hosting CSE | No change from the basic procedures |
| Information on Response message | fr: Receiver CSE-ID to: Originator AE-ID or CSE-ID cn: URI of created <mgmtCmd> resource. |
| Post-Conditions | No change from the basic procedures. |
| Exceptions | If the creation is not allowed, the <mgmtCmd> resource shall not be created, and a proper error code shall be returned to the originator in the Response message |

#### 10.3.5.3	Retrieve <mgmtCmd>

A RETRIEVE Request is used by an Originator to retrieve all or part information from an existing <mgmtCmd> resource on a hosting CSE. Alternatively, the Originator can request to retrieve only a specific attribute or part of an attribute.

Originator: The Originator shall request to retrieve all or part of the information from an existing <mgmtCmd> resource by using a RETRIEVE verb. The request shall address a specific "<mgmtCmd>" resource to retrieve all attributes and the references to the sub-resources of the <mgmtCmd> resource.  Alternatively, the request shall address the individual attributes of the specific "<mgmtCmd>" resource to retrieve the corresponding attribute value.

Editor's Note: We need to agree on a terminology on how to refer to a specific instance of a resource type.

The Originator may be:

- An AE.

- A CSE.

Receiver: The Receiver shall check if the Originator has the READ permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall retrieve the corresponding attributes the <mgmtCmd> resource and the references to the sub-resources from its repository and shall respond to the Originator with the appropriate generic responses.

The hosting CSE shall be:

- An  IN-CSE.

Table 10.3.5.3-1:  <mgmtCmd> Retrieve

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to create a resource. |
| Information on Request message | op: R fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in 9.6.12, as needed |
| Local processing on Hosting CSE | No change from the basic procedures, |
| Information on Response message | No change from the basic procedures. |
| Post-Conditions | No change from the basic procedures. |
| Exceptions | If the retrieval is not allowed, or the specific <mgmtCmd> resource does not exist in the IN-CSE, a proper error code shall be returned to the originator |

#### 10.3.5.4	Update <mgmtCmd>

An UPDATE request is used by an Originator to update all or part information of an existing <mgmtCmd> resource on a hosting CSE with new attributes. Alternatively, the Originator can request to update only a specific attribute or part of an attribute.

Originator: The Originator shall request to update all or part information of an existing <mgmtCmd> resource by using a UPDATE verb. The request shall address a specific "<mgmtCmd>" resource of a CSE to update all attributes of the <mgmtCmd> resource with the provided new value.  Alternatively, the request shall address the individual attribute of the specific "<mgmtCmd>" resource to update the corresponding attribute with the provided new value.

The Originator may be:

- An AE.

- A CSE.

Receiver: The Receiver shall check if the Originator has the WRITE permission on the addressed <mgmtCmd> resource. The hosting CSE shall also check the validity of provided attributes if any. Upon successful validation, the hosting CSE shall overwrite the corresponding attributes of the <mgmtCmd> resource with the provided new data. The CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An IN-CSE.

Table 10.3.5.4-1: <mgmtCmd> Update

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to retrieve a resoruce |
| Information on Request message | op: U fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID. cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in 9.6.12, as needed |
| Local processing on Hosting CSE | No change from the basic procedures, |
| Information on Response message | No change from the basic procedures, |
| Post-Conditions | No change from the basic procedures, |
| Exceptions | If the update is not allowed or the specific <mgmtCmd> resource (or its sub-resource) does not exist in the IN-CSE, a proper error code shall be returned to the Originator |

#### 10.3.5.5	Delete <mgmtCmd>

A DELETE request is used by the Originator to delete an existing <mgmtCmd> resource on a hosting CSE. An AE may also use this procedure to cancel all initiated <execInstance> of an <mgmtCmd> if applicable.

Originator: The Originator shall request to delete an existing <mgmtCmd> resource by using a DELETE verb. The request shall address the specific "<mgmtCmd>" resource on the hosting CSE.

The Originator may be:

- The CSE on the manageable entity: In this case, the local -CSE issues the request to the hosting CSE to hide the corresponding management command from being exposed by the <mgmtCmd> resource.

- An AE: In this case, the AE requests the hosting CSE to delete the <mgmtCmd> resource from the hosting CSE and cancel all initiated <execInstance> of an <mgmtCmd> if applicable.

NOTE 1:	The hosting CSE in the network domain may also delete an <mgmtCmd> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <mgmtCmd> resource may also be deleted in the hosting CSE by other offline provisioning means which are out of scope.

Receiver: The Receiver shall check if the Originator has the DELETE permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall remove the resource from its repository. If the Originator is an AE and there is any initiated <execInstance> under the <mgmtCmd> that can be cancelled by a corresponding management command. The hosting CSE shall also issue the management command to the remote entity to cancel those initiated <execInstance> based on existing management protocol (i.e. BBF TR-069). Then the CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An IN-CSE.

Table 10.3.5.5-1 : <mgmtCmd> Delete by ASN-CSE or MN-CSE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Before issuing a DELETE request to the IN-CSE, the originating CSE may perform cancelling of the corresponding management command locally. |
| Information on Request message | op: D fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in 9.6.12, as needed |
| Local processing on Hosting CSE | The <mgmtCmd> resource shall be deleted from the repository of the IN-CSE. |
| Information on Response message | No change from the basic procedures, |
| Post-Conditions | No change from the basic procedures, |
| Exceptions | If the deletion is not allowed or the specific <mgmtCmd> resource does not exist in the IN-CSE, the deletion shall be failed and a proper error code shall be returned to the Originator |

Table 10.3.5.5-2 : <mgmtCmd> Delete by an AE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Originator needs to delete the resource. |
| Information on Request message | op: D fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in 9.6.12, as needed |
| Local processing on Hosting CSE | If there is any initiated <execInstance> under <mgmtCmd> and it is cancellable, IN-CSE shall cancel those initiated <execInstance> from the remote entity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF TR-069). The <mgmtCmd> resource shall be deleted from the repository of the IN-CSE. |
| Information on Response message | No change from the basic procedures, |
| Post-Conditions | No change from the basic procedures, |
| Exceptions | If the deletion is not allowed or the specific <mgmtCmd> resource does not exist, there is no local processing in the IN-CSE and a proper error code shall be returned to AE If the corresponding initiated commands cannot be deleted from remote entity due to some reason (e.g. not found) al response with the proper indication shall be returned to AE |

#### 10.3.5.6	Execute <mgmtCmd>

The Execute procedure is used by an originator for execution of a specific management command on a remote entity, through an existing <mgmtCmd> resource on the hosting CSE.

Originator: The Originator shall request to execute a specific management command which is represented by an existing <mgmtCmd> resource by using an UPDATE verb. The UPDATE request shall address the execEnable attribute of the <mgmtCmd> resource without any payload. Alternatively, the UPDATE request shall address the URI provided as the value of the execEnable attribute of the <mgmtCmd> resource.

After issuing the execution request, the Originator may request to retrieve the execution result or status from an <execInstance> sub-resource of the <mgmtCmd>by using a RETRIEVE method as described in section 10.3.5.8.

The Originator shall be:

- An AE.

Receiver: The Receiver shall check if the Originator has the WRITE permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall perform command conversion and mapping, and send the converted management command over mId reference point to execute the corresponding management command with the provided arguments on the remote entity based on existing device management protocol (i.e. BBF TR-069). Then the hosting CSE shall create a corresponding <execInstance> resource under <mgmtCmd> for this command execution. And the hosting CSE shall respond to the originator with the appropriate generic responses. It shall also provide in the response the URL of the created <execInstance> resource.

Upon receiving from the remote entity a management notification (i.e. BBF TR-069 "Inform" message) regarding the execution result or status, the hosting CSE may update the corresponding <execInstance> sub-resource locally.

The hosting CSE shall be:

- An  IN-CSE.

Editor’s note: The definition of Execute is to be for FFS in 10.1.

Table 10.3.5.6-1: <mgmtCmd> Execute

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator Need to retrieve a retrieve a resource. |
| Information on Request message | op: U fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: <mgmtCmd> / execEnbale The UPDATE request shall address to <mgmtCmd>/execEnable without any payload. The mandatory and/or optional attributes defined in 9.6.12, as needed. |
| Local processing on Hosting CSE | (a). If the execution is allowed, Hosting CSE will do command conversion and mapping. (b) The Hosting CSE shall trigger existing device management procedures (i.e. BBF TR-069) to execute the corresponding management command on the remote entity. (c) The Hosting CSE shall perform local processing: if Step b is successful, the IN-CSE shall create an <execInstance> resource under the triggered <mgmtCmd> to maintain status and results for this execution. |
| Information on Response message | No change from the basic procedures, |
| Post-Conditions | The following processing on the Hosting CSE is dependent on the type of the command and execution status and may occur after the Response message has been sent. (a) After the command execution is finished, the remote entity sends response including execution results to the Hosting CSE, who will store the execution results in corresponding <execInstance> resource. This step may occur any time after the Response message has been sent and might occur after step b below. (b) The AE may use normal RETRIEVE procedure to retrieve the execution results or status of an <execInstance>. (c) After receiving the RETRIEVE request from the AE, the Hosting CSE can retrieve the execution status or results on the remote entity using existing management protocol. If step d. occurs before step e, step f. may not be needed. (d) A response shall be returned to the AE. |
| Exceptions | If the execution is not allowed or the specified <mgmtCmd> resource or its attribute/sub-resource does not exist in the IN-CSE, no further processing is required in the Hosting CSE and a proper error code shall be returned to AE in the Message response If the corresponding management command cannot be executed in remote entity due to some reason, step 004 <??> shall be skipped and a proper error code shall be returned to AE in step 005 <??>. |

#### 10.3.5.7	Cancel <execInstance>

The Cancel procedure is used by an originating AE to disable/stop/cancel an initiated management command execution on the remote entity, through an existing <execInstance> resource on the hosting CSE.

Originator: The Originator shall request to disable/stop/cancel an initiated management command execution which is represented by an existing <execInstance> resource, by using an UPDATE verb. The UPDATE request shall address the execDisable attribute without any payload.

The Originator shall be:

- An AE.

Receiver: The Receiver shall check if the Originator has the WRITE permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall perform command conversion and mapping, then use existing management protocol (i.e. BBF TR-069) to cancel the corresponding management command execution initiated on the remote entity, and the hosting CSE shall respond to the originator with the appropriate responses.

The hosting CSE shall be:

- An IN-CSE.

Table 10.3.5.7-1: <execInstance> Cancel

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to disable/stop/cancel an initiated management command execution on the remote entity |
| Information on Request message | op: U fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: <mgmtCmd> / execInstance. The mandatory and/or optional attributes defined in 9.6.12, as needed. |
| Local processing on Hosting CSE | If the cancellation is allowed, IN-CSE will do command conversion and mapping. The IN-CSE shall cancel the <execInstance> from the remote entity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF TR-069). The IN-CSE shall delete the corresponding <execInstance> resource. |
| Information on Response message | No change from the basic procedures, |
| Post-Conditions | No change from the basic procedures, |
| Exceptions | If the execution is not allowed or the specified <execInstance> resource does not exist in the IN-CSE or the <execInstance> is finished, the local processing on Hosting CSE shall be skipped and a proper error code shall be returned to AE in the Response message. If the corresponding management command cannot be executed in remote entity due to some reason, the IN-CSE shall still delete the corresponding <execInstance> resource and return a Response message. |

Editor’s Note: The Cancel flow shall be updated based on the definition of EXEC procedure.

#### 10.3.5.8	Retrieve <execInstance>

A RETRIEVE request is used by an Originator to retrieve an existing <execInstance> resource, including individual attributes, from a hosting CSE. Alternatively, the Originator can request to retrieve only a specific attribute or part of an attribute.

Originator: The Originator shall request to retrieve all or part of information from an existing <execInstance> resource by using a RETRIEVE verb. The Request shall address a specific "<execInstance>" resource of a hosting CSE to retrieve all attributes of the <execInstance> resource. Or the request shall address the individual attribute of the specific "<execInstance>" resource to retrieve the corresponding attribute value.

The Originator shall be:

- An AE.

Receiver: The Receiver shall check if the Originator has the READ permission on the addressed <mgmtCmd> resource. Upon successful validation, the CSE shall retrieve the corresponding attributes of the <execInstance> resource and the references to the sub-resources from its repository and shall respond to the originator with the appropriate generic responses.

The hosting CSE may be:

- An IN-CSE.

Table 10.3.5.8-1:  <execInstance> Retrieve

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to create a resource. |
| Information on Request message | op: R fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: <mgmtCmd> resoruce. The mandatory and/or optional attributes defined in 9.6.12, as needed. |
| Local processing on Hosting CSE | If the retrieval is allowed, the IN-CSE can retrieve the execution status or results on the remote entity using existing management protocol (i.e. BBF TR-069). If the retrieval is allowed, the addressed attributes of the <execInstance> resource shall be retrieved from the repository of the IN-CSE. |
| Information on Response message | No change from the basic procedures, |
| Post-Conditions | No change from the basic procedures, |
| Exceptions | If the retrieval is not allowed or the specific <execInstance> resource does not exist in the IN-CSE, there is no local processing on the hosting CSE and a proper error code shall be returned to AE in the Response Message. |

#### 10.3.5.9	Delete <execInstance>

The DELETE request is used by an originating AE  to delete an existing <execInstance> resource on a hosting CSE.

Originator: The Originator shall request to delete an existing <execInstance> resource by using a DELETE verb. The request shall address the specific "<execInstance>" resource of an <mgmtCmd> on the hosting CSE.

The originator shall be:

- An AE.

NOTE 1:	The hosting CSE in the network domain may also delete an <execInstance> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <execInstance> resource may also be deleted in the hosting CSE by other offline provisioning means which are out of scope.

Receiver: The Receiver shall check if the Originator has the DELETE permission on the addressed <execInstance> resource. Upon successful validation, the hosting CSE shall remove the resource from its repository. If the <execInstance> is not finished on the remote entity and it is cancellable, the hosting CSE shall also use existing management protocols (i.e. BBF TR-069 CancelTransfer RPC) to cancel the corresponding management currently initiated at the remote entity. Then the CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An IN-CSE.

Table 10.3.5.9-1 : <execInstance> Delete

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Originator needs to delete the resource. |
| Information on Request message | op: D fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in 9.6.12, as needed |
| Local processing on Hosting CSE | If the <execInstance> is not finished yet and it is cancellable, the IN-CSE shall cancel the <execInstance> from the remote entity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF TR-069 [xx]). The <execInstance> resource shall be deleted from the repository of the IN-CSE. If the corresponding initiated commands cannot be deleted from remote entity due to some reason (e.g. not found), the <execInstance> resource shall be still deleted be performed |
| Information on Response message | No change from the basic procedures, |
| Post-Conditions | No change from the basic procedures, |
| Exceptions | If the deletion is not allowed or the specific <execInstance> resource does not exist in the IN-CSE, there is no processing on the Hosting CSE and a proper error code shall be returned to AE in the Response message If the <execInstance> is already complete or it is not cancellable, there is no processing on the Hosting CSE |

************************* END OF CHANGE 30  *************************

************************ START OF CHANGE 31  ************************

# Annex <X> (Informative):	Mapping of Requirements with CFSs

The following table illustrates the mapping of the Requirements specified in TS-0002 with the CSFs specified in this document.

Table X-1: Mapping of Requirements to CSFs

| CSF Name | Supported Sub-Functions | Associated Requirements | Notes |
| --- | --- | --- | --- |
| Addressing and Identification (AID) | Management of identifiers | OSR-026 OSR-023 OSR-024 OSR-025 | Overlap w/: DSC for OSR-023, OSR-024, and OSR-025 |
| Communication Management / Delivery Handling (CMDH) | Providing communications with other CSE’s, AE’s, and NSE’s Communications management: best effort Communications policy management Underlying Network connectivity management Communications management: data store and forward Ability to trigger off-line device | OSR-001 OSR-002 OSR-005 OSR-006 OSR-008 OSR-009 OSR-012 OSR-013 OSR-014 OSR-015 OSR-018 OSR-019 OSR-021 OSR-027 OSR-032 OSR-035 OSR-038 OSR-039 OSR-040 OSR-048 OSR-049 OSR-050 OSR-053 OSR-062 OSR-063 OSR-064 OSR-065 OSR-066 OSR-067 OSR-068 CRPR-001 CRPR-002 CRPR-003 MGR-016 | Overlap w/: DMR for OSR-001, OSR-009, OSR-021, OSR-032 SSM for OSR-009 LOC for OSR-006 GMG for OSR-006 NSSE for OSR-006, OSR-027 SSM for OSR-009 |
| Data Management and Repository (DMR) | Data storage and management Semantic support Data aggregation Data analytics Device data backup and recovery | OSR-001 OSR-007 OSR-009 OSR-016 OSR-020 OSR-021 OSR-032 OSR-034 OSR-036 OSR-058 SMR-006 SER-015 | Overlap w/: CMDH for OSR-001, OSR-009, OSR-021, OSR-032 SUB for OSR-016 GMG for OSR-020 . |
| Device Management (DMG) | Configuration Management Diagnostics and Monitoring Firmware management Software management Device Area Network topology management | OSR-017 OSR-069 OSR-070 OSR-071 OPR-001 OPR-002 OPR-003 MGR-001 MGR-003 MGR-004 MGR-006 MGR-007 MGR-008 MGR-009 MGR-011 MGR-012 MGR-013 MGR-014 MGR-015 MGR-019 MGR-020 MGR-021 SER-013 SER-014 | Overlaps w/: GMG for OSR-017 SEC for SER-013 |
| Discovery (DIS) | Discover resource Local discovery (within CSE) Directed remote discovery | OSR-023 OSR-024 OSR-025 OSR-059 OSR-060 OSR-061 MGR-002 SMR-004 | Overlaps w/: AID for OSR-023, OSR-024, OSR-025 |
| Group Management (GMG) | Management of a group and its membership CRUD Use Underlying Network group capabilities Bulk operations Access control | OSR-006 OSR-017 OSR-020 OSR-029 OSR-030 OSR-031 OSR-037 OSR-047 MGR-005 | Overlaps w/: CMDH for OSR-006 LOC for OSR-006 GMG for OSR-006 NSSE for OSR-006, OSR-037 DMR for OSR-020 DMG for OSR-017 |
| Location (LOC) | Location management Network-provided GPS-provided Confidentiality enforcement as it relates to location | OSR-006 OSR-051 OSR-052 SER-026 |  |
| Network Service Exposure / Service execution and triggering (NSSE) | Access Underlying Network service Location Device triggering Small data Policy and charging Support multiple Underlying Network functions | OSR-006 OSR-011 OSR-027 OSR-037 OSR-054 OSR-055 OSR-056 MGR-017 MGR-018 OPR-004 OPR-005 OPR-006 | Overlaps w/: CMDH for OSR-027 GMG for OSR-006, OSR-037 LOC for OSR-006 |
| Registration (REG) | CSE registration AE registration Device registration ID correlation | MGR-010 | Overlaps w/: SEC |
| Security (SEC) | Sensitive Data Handling Secure storage Secure execution Independent environments Security administration Pre-provisioning Dynamic bootstrap Network bootstrap Security association Link level Object level Authorization and access Identity protection | SER-001 SER-002 SER-003 SER-004 SER-005 SER-006 SER-007 SER-008 SER-009 SER-010 SER-011 SER-012 SER-013 SER-016 SER-017 SER-018 SER-019 SER-020 SER-021 SER-022 SER-023 SER-024 SER-025 MGR-010 | Overlap w/: DMG for SER-013 REG for MGR-010 SSM for SER-007 |
| Service Charging and Accounting (SCA) | Charging enablers Sending charging information to charging server Subscription-based charging Event-based charging Session-based charging Service-based charging Correlation with Underlying Network Charging management Offline charging Online charging | CHG-001, CHG-002a, CHG-002b, CHG-003, CHG-004, CHG-005 |  |
| Service Session Management (SSM) | Service Session Management (CSE to CSE, AE to CSE, and AE to AE) Session persistence over link outage Session context handling Assignment of session ID Session routing Multi-hop session management Session policy management | OSR-003 OSR-004 OSR-009 OSR-045 SER-007 | Overlap w/: CMDH and DMR for OSR-009 SEC for SER-007 |
| Subscription/Notification Support (SUB) | Subscribe (CSE, AE) Local Remote Subscription to a group Notification Synchronous Asynchronous | OSR-010 OSR-016 OSR-033 | Overlaps w/: DMR for OSR-016 |

************************* END OF CHANGE 31  *************************

************************ START OF CHANGE xx  ************************

************************* END OF CHANGE xx  *************************