| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC |
| Title:* | baseRoot Resource Type |
| Source:* | LG Electronics, Telecom Italia |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com Lupano Michele, Telecom Italia, michele.lupano@telecomitalia.it |
| Date:* | 2014-01-14 |
| Abstract:* | This contribution proposes baseRoot resource type. R01: change the figure to align with attribute/child resource tables |
| Agenda Item:* | ARC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes new section for missing baseRoot resource type.

============================Start of 1st Change==============================

### 9.6.X	 Resource Type baseRoot

A <baseRoot> resource shall represent a local CSE. This <baseRoot> resource shall be the root for all the resources that are residing on local CSE.

Editor’s Note: naming of <baseRoot> is FFS.

This resource shall be instantiated at the node after M2M service bootstrap procedure.

Figure 9.6.19-1: Structure of <baseRoot> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.X-1 (0 indicates the optionality of the child resource).

Table 9.6.X-1: Child resources of <baseRoot> resource

| Child Resource Name of <baseRoot> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCse> | 0..n | See section 9.6.19. |
| [variable] | <node> | 1 | See section 9.6.17. |
| [variable] | <application> | 0..n | See section 9.6.18. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <mgmtObj> | 0..n | See section 9.6.10. This child resource shall be able to exist only at IN-CSE. |

The <baseRoot> resource shall contain the attributes described in Table 9.6.X-2.

Table 9.6.X-2: Attributes of <baseRoot> resource

| Attribute Name of <baseRoot> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessRightID_[i] | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType | 1 | RO | List of the resource types which are supported in local CSE |
| pointOfAccess_[i] | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this local CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |

============================End of 1st Change===============================