| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2(ARC)/WG4(SEC) |
| Title:* | CR regarding AR resource type |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-02-10 |
| Abstract:* | selfPermission of AR may occur inconsistency to implement access policy. This contribution proposed to remove selfPermission attribte. |
| Agenda Item:* | Access Control |
| Work item(s): | WI-0002(arc |
| Document(s) Impacted* | TS-0001 (Arch-TS) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG member should agree on proposal. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Change 1: remove description for selfPermissions and updating figure

### 9.6.2	Resource Type accessRight

Access rights are defined as "white lists" or permissions, i.e. each permission defines "allowed" entities (defined as permissionHolders) for certain access modes (defined as permissionFlags). Sets of permissions are handled such that the resulting permissions for a group of permissions are the sum of the individual permissions; i.e. an action is permitted if it is permitted by some/any permission in the set.

By setting an accessRightID attribute on a resource, the permissions for accessing that resource are then defined by the permissions defined in the <accessRight> resource.

Figure 9.6.2-1: Structure of <accessRight> resource 
(only resource specific attributes are shown)

Table 9.6.2-1: Child resources of <accessRight> resource

| Child Resource Name of <accessRight> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.9 |

This resource shall contain the attributes according to their multiplicitly in table 9.6.2-2 (0 indicates the optionality of the attribute).

Table 9.6.2-2: Attributes of <accessRight> resource

| Attribute Name of <accessRight> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| permissions (ps) | 1 | RW | The list of permissions defined by this <accessRight> resource. These permissions are applied to resources referencing this <accessRight> resource using the accessRightID attribute. |

Editor's Note:  Mechanisms for announcing are FFS.

The permissions could then be generalised to actions (which might be granting access, but might also be more specific, like granting access to a subset, i.e. filtering part of the data). The permissions could be generalised to conditions, which may include things like the identity of the requestor, everybody except specified identities, but it might also include time based conditions, etc.