| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC |
| Title:* | Access right privileges |
| Source:* | Telecom Italia |
| Contact: | Michele Lupano, Telecom Italia, michele.lupano@telecomitalia.it Enrico Scarrone, Telecom Italia, enrico.scarrone@telecomitalia.it |
| Date:* | 2014-02-19 |
| Abstract:* | This contribution proposes a description of access right privileges attribute. |
| Agenda Item:* | ARC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes a description of access right privileges.

============================Start of 1st Change==============================

### 9.6.2	Resource Type accessRight

Access rights are defined as "white lists" or privileges, i.e. each privilege defines "allowed" entities (defined  as originatorPrivilege) for certain access modes (defined as privilegeFlags). Sets of privileges are handled such that the resulting privileges for a group of privileges are the sum of the individual privileges; i.e., an action is permitted if it is permitted by some / any privilege in the set. The selfPrivileges attribute lists those that have the rights to Read/Update/Delete for the resource <accessRight>.

By setting an accessRightID attribute on a resource, the privileges for accessing that resource are then defined by the privileges defined in the <accessRight> resource.

Figure 9.6.2-1: Structure of <accessRight> resource 
(only resource specific attributes are shown)

Table 9.6.2-1: Child resources of <accessRight> resource

| Child Resource Name of <accessRight> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See section 9.6.9 |

This resource shall contain the attributes according to their multiplicitly in Table 9.6.2-2 (0 indicates the optionality of the attribute).

Table 9.6.2-2: Attributes of <accessRight> resource

| Attribute Name of <accessRight> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described. |
| labels | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| privileges | 1 | RW | The list of privileges defined by this <accessRight> resource. These privileges are applied to resources referencing this <accessRight> resource using the accessRightID attribute. |
| selfPrivileges | 1 | RW | Defines the list of privileges for the <accessRight> resource itself. |

Editor’s Note:  Mechanisms for announcing are FFS.

The privileges could then be generalised to actions (which might be granting access, but might also be more specific, like granting access to a subset, i.e. filtering part of the data). The privileges could be generalised to conditions, which may include things like the identity of the requestor, everybody except specified identities, but it might also include time based conditions etc.

The access granting mechanism based on access right operates by matching the request originator with originator privilegelist stored in an <accessRight> resource. When a positive match is found then the requested operation e.g. RETRIEVE is checked with a set of allowed operations associated to the matching privilege holder; if this check fail, then the operation becomes forbidden for the originator. These sets are called privilege flags.

Self privileges and privileges are both lists of originator privilege associated with privilege flags applied respecively to <accessRight> resource itself and to all other resource types addressing an <accessRight> resource with the accessRightID common attribute.

### 9.6.2.1	Originator privileges

The following originator privilege types shall be considered for access right check.

Table 9.6.x: Originatorprivileges types

| Name | Description |
| --- | --- |
| Domain | FQDN domain |
| p | IP address domain with port |
| url | Generic URL |
| Token | Access token usually provided as query parameter |
| All | All originators |

### 9.6.2.2	Privilege flags

The following privilege flags shall be considered for access right check in association to an originator privilege.

Table 9.6.x: Privilege flags

| Name | Description |
| --- | --- |
| RETRIEVE | Privilege to retrieve the content of an addressed resource |
| CREATE | Privilege to create a child resource |
| UPDATE | Privilege to update the content of an addressed resource |
| DELETE | Privilege to delete an addressed resource |
| DISCOVER | Privilege to discover the resource |
| NOTIFY | Privilege to receive a notification |

Editor’s note: a non-verbose stage 3 privilege flag description could be the following: <pf>RcUeDN</pf> that means: RETRIEVE allowed, CREATE not allowed, UPDATE allowed, DELETE not allowed, DISCOVER allowed, NOTIFY allowed.

============================End of 1st Change===============================