| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC 8.1 |
| Title:* | Functional architecture in oneM2M-TS-0001 oneM2M Functional Architecture-V-0.4.0 |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2014-02-07 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes some clarification to enable CSEs to handle routing in  a clear fashion

* * * Start of 1st Change * * *

Table 8.2.2-1 Accessing Resources in different CSEs

| Traversals across X/Y Reference Points | Description | Reference |
| --- | --- | --- |
| No Hops | The Originator of the Request accesses a resource. The Originator of the Request can be an Application or a CSE. Local CSE and Hosting CSE are the same entity. The CSE shall check the Access Rights for accessing the resource. Depending on the expected result content, the CSE shall respond to the Originator of the Request, either with a Success or Failure Response, or not at all. | Figure 8.2.2-1 |
| 1 Hop | The Originator of the Request accesses a resource. The Originator of the Request may only be an Application. Local CSE and Hosting CSEs different entities. Local CSE shall forward the Request to the Hosting CSE if it is registered with the Hosting CSE, after an optional checking of the Access Rights for accessing the resource and the syntax of the Request message. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-2 (Editor's Note-1) |
| Multi Hops | The Originator of the Request accesses a resource. The Originator of the Request may be an Application or a CSE. Local CSE, middle CSE(s) and the Hosting CSE are different entities. Local CSE shall forward the Request to a middle CSE (e.g. MN-CSE) that the Local CSE is registered with. The local CSE shall ensure that this middle CSE can either reach the Hosting CSE or it can forward the request to another middle CSE that can either reach the Hosting CSE, or be able to forward the request to an IN Node. How this knowledge is acquired by the local CSE is out of scope. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message may be performed prior to forwarding the Request. Middle CSE may forward the Request to another middle CSE (e.g. another MN-CSE) that the middle CSE is registered with The middle CSE shall ensure that the selected middle CSE can either reach the Hosting CSE or it can forward the request to another middle CSE that can either reach the Hosting CSE, or be able to forward the request to an IN Node. How this knowledge is acquired by the middle CSE is out of scope .Alternatively the middle CSE can send the request directly to the IN node. The middle CSE must be registered with the IN node to do that. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message can be performed prior to forwarding the Request. The middle CSE shall forward the request to the IN node.The middle CSE must be registered with the IN node to do that An optional checking of the Access Rights and the syntax of the Request message can be performed prior to forwarding the Request. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-3 (Editor's Note-2) |
| Editor's Note-1: One-Hop case could potentially include the CSE-to-CSE communication also. The need for such procedures is FFS. Editor's Note-2: The multi-hop procedures address the scenario when the target is on a specific remote CSE. How a flow will work when the target is distributed on multiple remote CSEs is FFS. |

* * * End of 1st Change * * *