| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | CR against TS0001v0.3.2 including change marks |
| Date:* | 2014-02-08 |
| Contact:* | Josef Blanz (jblanz@qti.qualcomm.com) |
| Reason for Change/s:* | Adding a new resource type to support provisioning of CMDH related policies for setting limits to buffer usage in CMDH related processing of requests on a CSE. |
| Clause/Sub Clause Affected* | 9.6 |
| Agenda Item:* |  |
| Work item(s): | WI-0002 Architecture |
| Document(s) Impacted* | Architecture TS 0001v0.3.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed changes into the TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Rationale

### Please refer to contribution ARC-2014-0098R03-CMDH_Policies.ppt for all details on the rationale.

The intention with this CR is to create the needed resource structures for being able to provision CMDH-related policies that govern the limits for usage of buffers during CMDH-related processing of requests within a CSE into entities of the oneM2M architecture via Device or Application and Service Management. These resources would only be set / modified by managing entities of the Infrastructure Domain. It is expected that these resources would appear only as sub-resources to certain management object resources.

### ==================== Start Text Proposal ===================

### 9.6	Specified Resource Types

### 9.6.X	Resource Type cmdhBuffer

The <cmdhBuffer> resource type is used to define limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE. When an incoming request is processed by a CSE, it can only use buffers for temporary storage in compliance with the rules defined by the corresponding <cmdhBuffer> resource.

If a request cannot be processed in compliance with the rules defined in the corresponding <cmdhBuffer> resource, that request shall either be rejected in case it has not already been accepted by the CSE or it has to be purged. Error reporting on failed CMDH processing depends on error reporting parameters (TBD).

Figure 9.6.X-.1: Structure of <cmdhBuffer> resource 
(only resource specific attributes are shown)

The resource <cmdhBuffer> shall contain attributes according to their multiplicity shown in Table 9.6.X-1.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.X-1: Attributes of <cmdhBuffer> resource

| Attribute Name | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| (aEC) | 1 | RW | The ‘applicableEventCategory’ attribute defines for which requests the limits contained in this <cmdhBuffer> resource shall be applied. The ‘applicableEventCategory’ attribute is a list of zero or more Event Category values (‘ec’ parameter of a request), or the string ‘default’. When an Event Category vlaue appears in the ‘applicableEventCategory’ attribute, the buffer usage limits defined inside this <cmdhBuffer> resource are applicable for requests associated with that specific Event Category (‘ec’) value. When the string ‘default’ appears in the ‘applicableEventCategory’ attribute, the buffer usage limits defined inside this <cmdhBuffer> resource are applicable for all requests whose associated Event Category value (‘ec’) is not listed in the ’applicableEventCategory’ attribute of any other provisioned <cmdhBuffer> resource on the hosting CSE. A specific Event Category value (‘ec’) shall appear at most once in any of the ‘applicableEventCategory’ attributes of any of the provisioned <cmdhBuffer> resources on the hosting CSE. The string ‘default’ shall appear exactly once in any of the ‘applicableEventCategory’ attributes of any of the provisioned <cmdhBuffer> resources on the hosting CSE. |
| maxBufferSize (mBS) | 1 | RW | Maximum amount of memory that can be used for buffering requests matching with the ‘applicableEventCategory’ attribute of this <cmdhBuffer> resource. |
| storagePriority (sP) | 1 | RW | Storage priority for data that is stored for buffering requests matching with the ‘applicableEventCategory’ attribute of this <cmdhBuffer> resource. The storage priority defines the how to handle purging of buffered data when buffer memory is exhausted and buffered requests need to be purged. Buffered requests associated with a lower storage priority shall be purged before buffered requests with a higher storage priority. The range of storage priority is from 1 … 10. |

# Comments

Inconsistent definition of this common attribute across different resource types:

Found 1, 0..n, 1..n
Should it be just 1 and contain a list of accessRight-IDs with 0 or more entries?