| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | Some Enhancements for Supporting Device Triggering Definitions for CSE-capable and non-CSE-capable Nodes |
| Source:* | Rajesh Bhalla, ZTE |
| Contact: | rabhalla@ztetx.com |
| Date:* | 2014-02-17 |
| Abstract:* | This contribution proposes some changes to definitions etc. for supporting device triggering This proposal has been split in two: - ARC#127R01: definitions for CSE-capable and non-CSE-capable Nodes - ARC#1176 : Proposal to add support for M2M-Node-ID mapping to M2M-Ext-ID |
| Agenda Item:* | Input Contributions |
| Work item(s): | WI-0002 |
| Document(s) Impacted* | TS-0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discuss and adopt. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 1.		Background

1.  The current version of TS-0001 does not provide definition for Nodes that do not contain CSE. The definition of Node in section-6 has been updated.

2.   AEs on Nodes such as ADNs should be able to support device triggering. Definition of M2M-Ext-ID has been updated to reflect that M2M-Node-ID can also be mapped to M2M-Ext-ID.

==============  Start of first change  ==========================

# 6.		Configurations supported by oneM2M Architecture

Figure 6-1 illustrates some configurations supported by oneM2M architecture, illustrating the relations amongst the functional entities in relation to the reference points identified in Figure 5.2.1-1.

Figure 6-1: Configurations supported by oneM2M Architecture

Node-less AEs: This entity indicates that IN-AEs maybe hosted by an Application Service Provider. Any relationship, binding or management of these IN-AEs to other co-located functions is out-of-scope.

Node:	A oneM2M Node is a functional entity that shall contain at least one oneM2M Common Services Entity and/or one oneM2M Application Entity. A oneM2M Node may be contained in a physical object e.g., M2M Device, Gateway or Server Infrastructure.

Nodes: Two types of oneM2M Nodes are supported:

- A CSE-Capable Node is a functional entity that contains at least one oneM2M Common Services Entity and zero or more oneM2M Application Entities. ASN and MN are examples of such type of Nodes.

- A Non-CSE-Capable Node is a functional entity that contains one or more oneM2M Application Entities and no oneM2M Common Service Entity. ADN, Nodeless-AE are examples of such type of Nodes.

NOTES:

1.	CSEs resident in different Nodes are not identical and are dependent on the services supported by the CSE in that Node.

2.	Mcc' reference point aims to be as similar as possible to the Mcc reference point. But due to the nature of inter-M2M Service Provider communications, some differences are anticipated.

Editor's Notes:

•	The illustration above does not provide an exhaustive list of possible configurations and is subject to qualifications. Other possible functions/configurations are FFS.

•	Mcc' reference point aims to be as similar as possible to the Mcc reference point. But due to the nature of inter-M2M Service Provider communications, some differences are anticipated.

Editor's Note:

- In Figure 6-1, should we explain how Application Entity (AE) and Application (A) relate?

==============  End of first change  ==========================

==============  Start of Second change  ==========================

### 7.1.8	M2M External Identifier (M2M-Ext-ID)

This is an identifier used by an M2M Service Provider (M2M SP) when services targeted to a CSE-capable Node (e.g., ASN, MN), identified by a CSE-ID; or targeted to a non-CSE capable Node (e.g., ADN), identified by M2M-Node-ID  are requested from the Underlying Network.

The M2M External Identifier allows the Underlying Network to identify the M2M Device associated with the CSE-ID or with the M2M-Node-ID, as appropriate, for the service request. To that effect, the Underlying Network maps the M2M-Ext-ID to the Underlying Network Identifier it allocated to the target M2M Device. In addition, the M2M SP shall maintain the association between the CSE-ID/M2M-Node-ID, the M2M-Ext-ID and the identity of the Underlying Network.

Both pre-provisioned and dynamic plug and play association between the CSE-ID/M2M-Node-ID with the M2M-Ext-ID should to be supported.

NOTE: There shall be 1:1:1 mapping between M2M-Ext-ID, the identity of the Underlying Network and the CSE-ID/M2M-Node-ID. Hence an M2M SP interworking with multiple Underlying Networks shall have a different M2M-Ext-IDs associated with the same CSE-ID/M2M-Node-ID, one per Underlying Network and  shall select the appropriate M2M-Ext-ID for any service request it initiates towards an Underlying Network.

NOTE: The mapping by the Underlying Network of the M2M-Ext-ID to the M2M Device is access network specific.

Editor's Note:  The method for dynamic plug-and-play association of M2M-Ext-ID and the 3GPP Underlying Network Identifier is FFS.

Editor's Note: Define "identity of the Underlying Network".

==============  End of Second change  ==========================