| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC WG |
| Title:* | Precondition for Subscription of Request-Unreachable Receiver |
| Source:* | LG Electronics |
| Contact: | Heedong Choi (heedong.choi@lge.com) |
| Date:* | 2014-02-10 |
| Abstract:* | This contribution provides to modify the susbscription procedure for the request-unreachable receiver of the notification. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Rationale

This contribution provides to modify the susbscription procedure for the request-unreachable receiver of the notification.

- Proposed

=================================  Start of 1st Change  =================================

### 10.2.9 	<subscription> Resource Procedures

#### 10.2.9.1		Introduction

An Originator can create a <subscription> resource on a subscribed-to resource Hosting CSE to be notified when the resource is modified. After successful <subscription> resource creation, the Hosting CSE shall notify the Originator of a subscribed-to resource modification that meets conditions configured in the subscription resource.

Note: When the Receiver of the notification is a request-unreachable AE or CSE, the subscriber should not only subscribe to subscribed-to resource in the Hosting CSE, but also notifiy the Receiver of information related to the notification (e.g., notificationURI) in order that the Receiver gets the notification from the <pollingChannel> resource. However, the specific notification procedure from the subscriber to the Receiver of the notification is out-of-scope.A subscription shall be represented by a <subscription> resource (see clause 9.6.9). This allows manipulation of the subscription in a resource oriented manner, e.g. the conditions of a subscription may be modified by modifying a <subscription> resource, or a resource subscriber may unsubscribe by deleting the <subscription> resource.

The following clauses describe procedures for Creation, Retrieval, Update and Deletion of a <subscription> resource.

#### 10.2.9.2		Create <subscription>

This procedure shall be used to request a new subscription to be notified for the modifications of a subscribable resource.

Originator: The Originator can be an AE or a CSE. The Originator shall request to create a <subscription> resource. The Request shall address a subscribable resource.

The Request shall include notificationURI(s).

Hosting CSE: The Hosting CSE shall validate the followings:

- if the subscribed-to resource, addressed in the to parameter in the Request, is a subscribable resource

- if the Originator has RETRIEVE permission to the subscribed-to resource

- if the Originator has access rights to send notifications to the entity(ies) hosting notificationURI(s) when the Originator is not a hosting notificationURI

- if it has access rights to send notifications to the entity(ies) that hosting notificationURI(s).

Editor's Note: Access right to send notification to an entity can be represented as NOTIFY permission.

Editor’s Note: The validation process described in the last two bullet points above needs to be investigated further, This is FFS.

If all those checks are successfully done, the Hosting CSE shall send positive Response to the Originator.

Table 10.2.9.2-1: <subscription> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | The Originator configures proper permissions and access rights described above. |
| Information on Request message | op: C fr: ?? to: ?? cn: Mandatory and/or optional attributes defined in section 9.6.9. |
| Local processing on Hosting CSE | Check access rights regarding creation of the subscription resource and sending notification to the notificationURI. |
| Information on Response message | No change from the basic procedure in section 10.1.1 |
| Post-Conditions | None |
| Exceptions | One of validations on the Hosting CSE above fails. |

#### 10.2.9.3	Retrieve <subscription>

This procedure shall be used to retrieve information of a subscription such as notificationURI, filterCriteria, expirationTime etc.

Originator: The Originator can be an AE or a CSE. The Request shall address a <subscription> resource or one of its attributes.

Hosting CSE: If the Hosting SCE validates the Originator has RETRIEVE permission referring accessRightID , it shall return the complete representation of the <subscription> resource or the value of a specific attribute of the <subscription> resource..

Table 10.2.9.3-1: <subscription> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | The Originator has RETRIEVE permission to the subscription resource. |
| Information on Request message | fr: ?? to: ?? No change from the basic procedure. |
| Local processing on Hosting CSE | fr: ?? to: ?? No change from the basic procedure. |
| Information on Response message | No change from the generic procedure. |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure. |

#### 10.2.9.4	Update <subscription>

This procedure shall be used to update an existing subscription, e.g. extension of its lifetime or the modification of the notificationURI.

Originator: The Originator can be an AE or a CSE. The Originator may send new value(s) for read-write attribute(s) of a <subscription> resource.

Hosting CSE: After the Hosting CSE verifying the existence of the addressed resource, the validity of the attributes provided and the permissions to modify them referring accessRightID, shall update the attributes provided and shall send positive response to the Originator.

Table 10.2.9.4-1: <subscription> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | The Originator has UPDATE permission to the subscription resource. |
| Information on Request message | No change from the basic procedure. |
| Local processing on Hosting CSE | No change from the basic procedure. |
| Information on Response message | No change from the generic procedure. |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure. |

#### 10.2.9.5	Delete <subscription>

This procedure shall be used to unsubscribe an existing subscription.

Originator: The Originator can be an AE or a CSE. The request shall address a subscription resource.

Hosting CSE: If the Hosting CSE validates the Originator has the DELETE permission to delete a subscription resource, it shall delete the resource and shall send a positive response to the Originator.

Table 10.2.9.5-1: <subscription> DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | The Originator has DELETE permission to the subscription resource. |
| Information on Request message | No change from the basic procedure. |
| Local processing on Hosting CSE | No change from the basic procedure. |
| Information on Response message | No change from the generic procedure. |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure. |

=================================  End of 1st Change  =================================