| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#9 |
| Title:* | Definition of mgmtDefinition |
| Source:* | Huawei Technologies Co., Ltd. China United Network Communications Group Company Limited |
| Contact: | Jiaxin Yin, yinjiaxin@huawei.com Changwei Hu, hucw5@chinaunicom.cn |
| Date:* | 2013-12-28 |
| Abstract:* | < An abstract of the document that may be used to help reader decide whether to read the entire document, and provide information that may be used in subsequent electronic searches> |
| Agenda Item:* | TBD |
| Work item(s): | WI0001 |
| Document(s) Impacted* | TS0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS0001 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

*************Start of change 1********************

Table 9.6.10-2: Attributes of <mgmtObj> resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType(rT) | 1 | WO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Specifies the type of mgmtObj resource e.g. software, firmware, memory. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessRightID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described |
| objectID | 0..1 | WO | Contains a URN that uniquely identifies the external management technology data model used for this <mgmtObj> resource as well as the managed function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> resource and shall not be modifiable afterwards. This is mandatory for the <mgmtObj>, for which the data model is not specified by oneM2M but mapped from external management technology data model specified in other device management protocols (e.g. OMA-DM, BBF TR-069 and LWM2M). |
| objectPath | 0..1 | WO | Contains the local path of the external management object instance on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the external management object instance on the managed entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local external management object path in the form as specified by existing management protocols. (e.g. "./anyPath/Fw1" in OMA DM, "Device.USBHosts.Host.3." in BBF TR-069). |
| moAttribute | 0..n | RW | Each moAttribute is mapped from a leaf node of a hierarchical structured management object (including oneM2M data model and the existing management data models) based on the mapping rules below the table. |
| description | 0..1 | RW | Text format description of mgmtObj. |

********************end of change 1**************************

********************start of change 2**************************

Figure 9.6.10-1: Structure of <mgmtObj> resource 
(only resource specific attributes are shown)

***********************end of change 2****************************