| INPUT CONTRIBUTION |
| --- |
| Group Name:* | ARC |
| Title:* | Application Port ID |
| Source:* | ZTE, DOCOMO, INTEL |
| Contact: | Rajesh Bhalla, rabhalla@ztetx.com Syed Husain, Shusain2016@gmail.com Puneet Jain, puneet.jain@intel.com |
| Date:* | 2014-02-19 |
| Abstract:* | This contribution proposes "Application Port ID" attribute for CSE-capable Nodes. |
| Agenda Item:* | ARC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Functional Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution proposes additional attribute "Application Port ID" in <CSEBase> for CSE-capable Nodes. This attribute needs to be reflected in <remoteCSE> resource as well.

----------------------- 1st Change  Start ----------------------

### 9.6.X	 Resource Type CSEBase

A <CSEBase> resource shall represent a local CSE. This <CSEBase> resource shall be the root for all the resources that are residing on local CSE.

Figure 9.6.19-1: Structure of <CSEBase> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.X-1 (0 indicates the optionality of the child resource).

Table 9.6.X-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCse> | 0..n | See section 9.6.19. |
| [variable] | <node> | 1 | See section 9.6.17. |
| [variable] | <application> | 0..n | See section 9.6.18. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <mgmtObj> | 0..n | See section 9.6.10. |
| [Variable] | <mgmtCmd> | 0..n | See section 9.6.12. |
| [Variable] | <locationPolicy> | 0..n | See section 9.6.7. |

Editor’s note: this list should be updated. Which resource types are added is FFS.

Editor’s note: how to extend functionality is FFS.

The <CSEBase> resource shall contain the attributes described in Table 9.6.X-2.

Table 9.6.X-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessRightID_[i] (aRI_[i]) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType (sRT) | 1 | RO | List of the resource types which are supported in local CSE. this attribute contains subset of resource types listed in section 9.2 |
| pointOfAccess_[i] (poA_[i]) | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this local CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| Application Port ID | 0..1 | RW | Application Port ID assigned to the CSE Execution Environment at an ASN/MN. This attribute can be used for device triggering service in some Underlying Networks |

----------------------- 2nd Change  Start ----------------------

### 9.6.19	Resource Type remoteCSE

A <remoteCse> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <baseRoot>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCse> resource in the registering CSE's <baseRoot>.

For example, when CSE1 registers with CSE2, there will be two <remoteCse> resources created: one in CSE1 <baseRoot1>/<remoteCse2> and one in CSE2 <baseRoot2>/<remoteCse1>.

Note that the creation of the two resources does not imply mutual registration. The <baseRoot1>/<remoteCse2> is only local to CSE1 and is for its internal use.

Figure 9.6.19-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicitly in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <Application> | 0..n | See section 9.6.18. |
| [variable] | <container> | 0..n | See section 9.6.3. |
| [variable] | <group> | 0..n | See section 9.6.5. |
| [variable] | <accessRight> | 0..n | See section 9.6.2. |
| [variable] | <subscription> | 0..n | See section 9.6.9. |
| [variable] | <mgmtObj> | 0..n | See section 9.6.10. |

The <remoteCSE> resource shall contain the attributes described in Table 9.6.19-2.

Table 9.6.19-2: Attributes of <remoteCSE> resource

| Attribute Name of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID_[i] | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| pointOfAccess_[i] | 0..n | RW | For server capable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not server capable. |
| baseRoot | 1 | WO | The URI of the baseRoot. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| Application Port ID | 0..1 | RW | Application Port ID assigned to the CSE Execution Environment at an ASN/MN. This attribute can be used for device triggering service in some Underlying Networks. |

Editor’s Note on CSE-ID: an alignment between CSE-ID and baseURI is needed.

Editor’s Note on baseURI: the alignment with naming convention proposed for inter-M2M service provider is needed.

Editor’s Note on child resources: child resources of <remoteCse> resource can accommodate listed resources and their announced versions.

----------------------- 2nd Change  End ----------------------

# Comments

mgmtCmd, locationPolicy are added based upon TS.