| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#9.2 |
| Source:* | Barbara Pareglio,NEC, barbara.pareglio@neclab.eu |
| Format:* | ARC#9.2 |
| Date:* | 2014-03-12 |
| Contact:* | Barbara Pareglio,NEC, barbara.pareglio@neclab.eu |
| Reason for Change/s:* | Correction: added parentID attribute where missing |
| CR against: | TS-0001 v 0.4.2 |
| Clauses/Sub Clauses Affected* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To agree to remove the section |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Do not conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Proposal to add parentID attribute to all resource where it is missing.

### ----------------------------------Start of change 1-------------------------------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.3-1 (0 indicates the optionality of the child resource).

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See section 9.6.4 |
| [variable] | <node> | 1 | See section 9.6.19 |
| [variable] | <application> | 0..n | See section 9.6.5 |
| [variable] | <container> | 0..n | See section 9.6.6 |
| [variable] | <group> | 0..n | See section 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See section 9.6.2 |
| [variable] | <subscription> | 0..n | See section 9.6.8 |
| [variable] | <mgmtObj> | 0..n | See section 9.6.15 |
| [Variable] | <mgmtCmd> | 0..n | See section 9.6.17 |
| [Variable] | <locationPolicy> | 0..n | See section 9.6.10 |

Editor’s Note: this list should be updated. Which resource types are added is FFS.

Editor’s Note: how to extend functionality is FFS.

The <CSEBase> resource shall contain the attributes described in Table 9.6.3-2.

Table 9.6.3-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aRI) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType (sRT) | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in section 9.2 |
| pointOfAccess (poA) | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <application> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. |

### ---------------------------------End of change 1---------------------------------------------

### ----------------------------------Start of change 2-------------------------------------------

### 9.6.23	Resource Type cmdhPolicy

The <cmdhPolicy> resource type represents a set of rules defining which CMDH parameters will be used by default when a request issued by a local originator (eg. locally registered AE or another CSF inside the local CSE) contains the “ec” parameter but not all other CMDH parameters.

One or several resources of type <cmdhPolicy> may be linked as child resources of the local <CSEBase> resource, thus defining a set of CMDH policies applicable whenever this local hosting CSE receives requests.

In addition, one or several resources of type <cmdhPolicy> may be linked as child resources of other resources of type <application> or <remoteCSE>, thus overriding the default set of policies for the relevant locally registered Application Entities or remote CSEs.

Editor’s Note: The parent resource for this <cmdhPolicy> resource type is TBD. The <cmdhPolicy> resource type will be defined as a management Object.

Figure 9.6.23-.1: Structure of <cmdhPolicy> resource 
(only resource specific attributes are shown)

The resource <cmdhPolicy> shall contain child resources according to their multiplicity shown in Table 9.6.23-1. A value of  "0" for multiplicity indicates the child resource is optional.

Table 9.6.23-1: Child resources of <cmdhPolicy> resource

| Child Resource Name of <cmdhPolicy> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <cmdhDefaults> | 1. | See section 9.6.24 where the type of this child resource is described. |
| [variable] | <cmdhLimits> | 1..n | See section 9.6.27 where the type of this child resource is described. |
| [variable] | <cmdhNetworkAccessRules> | 1..n | See section 9.6.28 where the type of this child resource is described. |
| [variable] | <cmdhBuffer> | 1..n | See section 9.6.30 where the type of this child resource is described. |

The resource <cmdhPolicy> shall contain attributes according to their multiplicity shown in Table 9.6.23-2.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.23-2: Attributes of <cmdhPolicy> resource

| Attribute Name of <cmdhPolicy> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| name | 1 | RW | A name under which the CMDH policy will be referred. |
| status | 1 | RW | Either “active” or “inactive”, this attribute allows to provision policies without activating them immediately, thus sparing the need to completely erase policies and then reprovision them remotely when one only needs to deactivate them temporarily. Only one policy can be “active” at any given time. |

NOTE: In order to avoid race conditions, it may be better that the CSE refers to the currently active cmdhPolicy instead of using the “status” attribute.

Editor’s Note: When the <CSEBase> resource is accepted, an attribute or link in the <CSEBase> resource could be used to point to the active <cmdhPolicy> resource.

### 9.6.24	Resource Type cmdhDefaults

The <cmdhDefaults> resource type is used to define default values that shall be used for CMDH-related parameters when requests issued by Originators (registered AEs or functions inside the CSE itself) do not contain a value for the parameters ec (event category), rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence), and/or da (delivery aggregation).

Upon receiving a request, the CSE will first look if the ec (event category) parameter is set. If not, it will use the cmdhDefEcValue child resources (see below) to determine a value that should be used for ec.

Then, if any of the parameters rqet, rset, oet, rp or da is not set, the CSE will use the cmdhEcDefParamValues child resources (see below) to populate the missing parameters (and only the missing ones).

Figure 9.6.24-.1: Structure of <cmdhDefaults> resource 
(only resource specific attributes are shown)

The resource <cmdhDefaults> shall contain child resources according to their multiplicity shown in Table 9.6.24-1. A value of "0" for multiplicity indicates the child resource is optional.

Table 9.6.24-1: Child resources of <cmdhDefaults> resource

| Child Resource Name of <cmdhDefaults> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <cmdhDefEcValue> | 1..n | See section 9.6.25 where the type of this child resource is described. |
| [variable] | <cmdhEcDefParamValues> | 1..n | See section 9.6.26 where the type of this child resource is described. |

The resource <cmdhDefaults> shall contain attributes according to their multiplicity shown in Table 9.6.24-2.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.24-2: Attributes of <cmdhDefaults> resource

| Attribute Name of <cmdhDefaults> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 |
| creationTime (cT) | 1 | RO | See section 9.6.1 |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 |

### 9.6.25	Resource Type cmdhDefEcValue

The <cmdhDefEcValue> is used to define a value for the ec (event category) parameter of an incoming request when it is not defined.

Upon receiving a request, the CSE will go through all the <cmdhDefEcValue> resources (in the order of their "order" attribute), check the <requestOrigin> and any present<requestContext> and <requestCharacteristics> sub-resources to see if they match (see description of matching), and if they all do, assign the value stored in the defEcValue attribute to the ec parameter.

Figure 9.6.25-1: Structure of <cmdhDefEcValue> resource 
(only resource specific attributes are shown)

The resource <cmdhEcDefEcValue> shall contain attributes according to their multiplicity shown in Table 9.6.25-1.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.25-1: Attributes of <cmdhDefEcValue> resource

| Attribute Name of <cmdhDefEcValue> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 |
| creationTime (cT) | 1 | RO | See section 9.6.1 |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 |
| order(or) | 1 | RW | The index indicating in which order the cmdhDefEcValue resource will be treated by the CSE to determine a value for the ec parameter |
| defEcValue (dev) | 1 | RW | The actual value to use for the ec parameter if the conditions expressed in the requestOrigin, requestContext and requestCharacteristics all match. If none of these attributes are defined, then the defEcValue shall be applied. |
| requestOrigin (rorig) | 1 | RW | The requestOrigin attribute is a list of zero or more local App-Inst-IDs, App-IDs, or the strings ‘localAE’ or ‘thisCSE’. When an App-Inst-ID appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec if the request was issued by that specific Application Instance. When an App-ID appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec if the request was issued by any instance of the Application with that App-ID unless covered by another <cmdhDefEcValue> resource with a requestOrigin attribute containing its specific App-Inst-ID.. When the string ‘localAE’ appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec for requests issued by all local AEs unless covered by another <cmdhDefEcValue> resource with a requestOrigin attribute containing the specfifc App-Inst-ID or App-ID of the originator of the request. When the string ‘thjsCSE’ appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec for requests that are originating from within the local CSE . The hosting CSE shall contain at least one <cmdhDefEcValue> resource that contains ‘localAE’ in the ‘requestOrigin’ attribute and has no ‘requestContext’ and no ‘requestCharacteristics’ attribute. The hosting CSE shall contain at least one <cmdhDefEcValue> resource that contains ‘thisCSE’ in the ‘requestOrigin’ attribute and has no ‘contextCondtion’ and no ‘requestCharacteristics’ attribute. |
| requestContext (rctxt) | 0..1 | RW | The requestContext attribute represents the Dynamic Context condition under which the default ec value defined inside the defEcValue attribute is applicable for the ec. This may refer to conditions such as current battery status, or current network signal strength. |
| requestContextNotification | 0..1 | RW | True or false. If set to true, then this CSE will establish a subscription to the dynamic context information defined in the requestContext attribute as well as a subscription to this <cmdhDefEcValue> resource for all AEs corresponding to the App-Inst-ID or an App-ID appearing in the requestOrigin attribute. Both, changes in the context information and changes to the <cmdhDefEcValue> resource will be notified to the respective AEs. The subscription(s) is/are established when the <cmdhDefEcValue> is provisioned or updated. |
| requestCharacteristics | 0..1 | RW | The requestCharacteristics attribute represents conditions pertaining to the request itself, such as the requested response type (rt attribute) or other attributes of the request. |

### 9.6.26	Resource Type cmdhEcDefParamValues

The <cmdhEcDefParamValues> resource type is used to represent a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request.

Figure 9.6.26-.1: Structure of <cmdhEcDefParamValues> resource 
(only resource specific attributes are shown)

The resource <cmdhEcDefParamValues> shall contain attributes according to their multiplicity shown in Table 9.6.26-1.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.26-1: Attributes of <cmdhEcDefParamValues> resource

| Attribute Name of <cmdhEcDefParamValues> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 |
| creationTime (cT) | 1 | RO | See section 9.6.1 |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 |
| applicableEventCategory (aEC) | 1 | RW | This attribute defines the event categories for which this set of default parameters defined in this <cmdhEcDefParamValues> resource are applicable.This attribute is a list of zero or more Event Category values (‘ec’ parameter of a request), or the string ‘default’. When an Event Category value appears in the ‘applicableEventCategory’ attribute, the set of default parameters defined in this <cmdhEcDefParamValues> resource are applicable for requests associated with that specific Event Category (‘ec’) value. When the string ‘default’ appears in the ‘applicableEventCategory’ attribute, the set of default parameters defined in this <cmdhEcDefParamValues> resource are applicable for all requests whose associated Event Category value (‘ec’) is not listed in the ‘applicableEventCategory’ attribute of any other provisioned <cmdhEcDefParamValues> resource on the hosting CSE. A specific Event Category value (‘ec’) shall appear at most once in any of the ‘applicableEventCategory’ attributes of any of the provisioned <cmdhEcDefParamValues> resources on the hosting CSE. The string ‘default’ shall appear exactly once in any of the ‘applicableEventCategory’ attributes of any of the provisioned <cmdhEcDefParamValues> resources on the hosting CSE. . |
| defaultRequestExpTime (dRqET) | 1 | RW | Default value for the request expiration time parameter (‘rqet’) in a request when the ‘rqet’ attribute of the request is not set. |
| defaultResultExpTime (dRsET) | 1 | RW | Default value for the result expiration time parameter (‘rset’) in a request when the ‘rset’ attribute of the request is not set. |
| defaultOpExecTime | 1 | RW | Default value for the operational execution time parameter (‘oet’) in a request when the ‘oet’ attribute of the request is not set. |
| defaultRespPersistence | 1 | RW | Default value for the response persistence parameter (‘rp’) in a request when the ‘rp’ attribute of the request is not set. |
| defaultDelAggregation | 1 | RW | Default value for the delivery aggregation parameter (‘da’) in a request when the ‘da’ attribute of the request is not set. |

### 9.6.27	Resource Type cmdhLimits

The <cmdhLimits> resource type is used to define limits for CMDH related parameter values used in requests issued by Originators (registered AEs or functions inside the CSE itself). When an incoming request is processed that does not comply with the limits defined by the corresponding <cmdhLimits> resource, the request shall be rejected by the CSE.

Figure 9.6.27-.1: Structure of <cmdhLimits> resource 
(only resource specific attributes are shown)

The resource <cmdhLimits> shall contain attributes according to their multiplicity shown in Table 9.6.27-1.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.27-1: Attributes of <cmdhLimits> resource

| Attribute Name of <cmdhLimits> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| order(or) | 1 | RW | The index indicating in which order the cmdhLimits resource will be treated by the CSE to determine a value for the limit parameters. |
| requestOrigin(rorig) | 1 | RW | The requestOrigin attribute is a list of zero or more local App-Inst-IDs, App-IDs, or the strings ‘localAE’ or ‘thisCSE’. When an App-Inst-ID appears in the requestOrigin attribute, the CMDH parameter limits defined inside <cmdhLimits> child resources are applicable for requests issued by that specific Application Instance. When an App-ID appears in the requestOrigin attribute, the CMDH parameter limits defined inside <cmdhLimits> child resources are applicable for requests issued by any instance of the Application with that App-ID unless already covered by another <cmdhLimits> resource with a requestOrigin attribute containing its specific App-Inst-ID. When the string ‘localAE’ appears in the requestOrigin attribute, CMDH parameter limits defined inside <cmdhLimits> child resources are applicable for all local AEs unless covered by another <cmdhLimits> resource with a requestOrigin attribute containing the specific App-Inst-ID or App-ID of the originator of the request. When the string ‘thisCSE’ appears in the requestOrigin attribute, CMDH parameter limits defined inside <cmdhLimits> resources are applicable for all requests that are originating from within the hosting CSE. The hosting CSE shall contain at least one <cmdhLimits> resource that contains ‘localAE’ in the ‘requestOrigin’ attribute and has no ‘contextCondtion’ and no ‘requestCharacteristics’ attribute. The hosting CSE shall contain at least one <cmdhLimits> resource that contains ‘thisCSE’ in the ‘requestOrigin’ attribute and has no ‘requestContext’ and no ‘requestCharacteristics’ attribute. |
| requestContext (rctxt) | 0..1 | RW | The requestContext attribute represents the Dynamic Context condition under which CMDH parameter limits defined inside the <cmdhLimits> resource is applicable. This may refer to conditions such as current battery status, or current network signal strength. |
| requestContextNotification | 0..1 | RW | True or false. If set to true, then this CSE will establish a subscription to the dynamic context information defined in the requestContext attribute as well as a subscription to this <cmdhLimits> resource for all AEs corresponding to the App-Inst-ID or an App-ID appearing in the requestOrigin attribute. Both, changes in the context information and changes to the <cmdhLimits> resource will be notified to the respective AEs. The subscription(s) is/are established when the <cmdhLimits> is provisioned or updated |
| requestCharacteristics | 0..1 | RW | The requestCharacteristics attribute represents conditions pertaining to the request itself, such as the requested response type (rt attribute) or other attributes of the request. |
| limitsEventCategory (lEC) | 1 | RW | Allowed values for the event category parameter (‘ec’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsRequestExpTime (lRqET) | 1 | RW | Range of allowed values for the request expiration time parameter (‘rqet’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsResultExpTime (lRsET) | 1 | RW | Range of allowed values for the result expiration time parameter (‘rset’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsOpExecTime (lOET) | 1 | RW | Range of allowed values for the operational execution time parameter(‘oet’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsRespPersistence (IRP) | 1 | RW | Range of allowed values for the response persistence parameter (‘rp’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsDelAggregation(lDA) | 1 | RW | List of allowed values for the delivery aggregation parameter (‘da’) in a request of any of the originators indicated in the requestOrigin attribute. |

### 9.6.28	Resource Type cmdhNetworkAccessRules

The <cmdhNetworkAccessRules> resource type is used to define the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE. When an incoming request is processed by a CSE, it can only use underlying networks for forwarding any information to other CSEs in compliance with the rules defined by the corresponding <cmdhNetworkAccessRules> resource.

If a request cannot be successfully completed in compliance with the rules defined in the corresponding <cmdhNetworkAccessRules> resource, that request shall either be rejected in case it has not already been accepted by the CSE or it has to be purged. Error reporting on failed CMDH processing depends on error reporting parameters (TBD).

Figure 9.6.28-.1: Structure of <cmdhNetworkAccessRules> resource 
(only resource specific attributes are shown)

The resource <cmdhNetworkAccessRules> shall contain child resources according to their multiplicity shown in Table 9.6.28-1. A value of "0" for multiplicity indicates the child resource is optional.

Table 9.6.28-1: Child resources of <cmdhNetworkAccessRules> resource

| Child Resource Name of <cmdhNetworkAccessRules>> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <cmdhNwAccessRule> | 0..n | See section 9.6.29 where the type of this child resource is described. |

If a <cmdhNetworkAccessRules> resource has no <cmdhNwAccessRules> child resources (i.e. multiplicity of 0), requests that match with the ’applicableEventCategories’ attribute (see description of attributes in Table 9.6.28-2) will not be allowed to use any underlying network for forwarding information, i.e such requests need to be rejected.

The resource <cmdhNetworkAccessRules> shall contain attributes according to their multiplicity shown in Table 9.6.28-2.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.28-2: Attributes of <cmdhNetworkAccessRules> resource

| Attribute Name of <cmdhNetworkAccessRules> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| applicableEventCategories (aec) | 1 | RW | This attribute defines for which requests the rules contained in <cmdhNwAccessRule> child resources of this <cmdhNetworkAccessRules> resource shall be applied. This attribute is a list of zero or more Event Category values (‘ec’ parameter of a request), or the string ‘default’. When an Event Category value appears in the ’applicableEventCategories’ attribute, the network usage rules defined inside <cmdhNwAccessRule> child resources are applicable for requests associated with that specific Event Category (‘ec’) value. When the string ‘default’ appears in the ’applicableEventCategories’attribute, the network usage rules defined inside <cmdhNwAccessRule> child resources are applicable for all requests whose associated Event Category value (‘ec’) is not listed in the ’applicableEventCategories’attribute of any other provisioned <cmdhNetworkAccessRules> resource on the hosting CSE. A specific Event Category value (‘ec’) shall appear at most once in any of the ’applicableEventCategories’attributes of any of the provisioned <cmdhNetworkAccessRules> resources on the hosting CSE. The string ‘default’ shall appear exactly once in any of the ’applicableEventCategories’attributes of any of the provisioned <cmdhNetworkAccessRules> resources on the hosting CSE. |

### O9.6.29	Resource Type cmdhNwAccessRule

The <cmdhNwUsageRule> resource type is used define limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests.

Figure 9.6.29-.1: Structure of <cmdhNwAccessRule> resource 
(only resource specific attributes are shown)

The resource <cmdhNwAccessRule> shall contain child resources according to their multiplicity shown in Table 9.6.29-1. A value of "0" for multiplicity indicates the child resource is optional.

Table 9.6.29-1: Child resources of <cmdhNwAccessRule> resource

| Child Resource Name of <cmdhNwAccessRule> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| allowedSchedule | <schedule> | 1 | See section 9.6.9 where the type of this child resource is described. |

The allowedSchedule child resource defines the periods of time during which it is allowed to use the underlying networks that match with the ’targetNetwork’ attribute of this <cmdhNwAccessRule> resource (see description of attributes in Table 9.6.29-2) when forwarding information to other CSEs due to requests that match the ’applicableEventCategories’ attribute of the parent <cmdhNetworkAccessRules> resource of this <cmdhNwAccessRule> resource.

The resource <cmdhNwAccessRule> shall contain attributes according to their multiplicity shown in Table 9.6.29-2.  A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.29-2: Attributes of <cmdhNwAccessRule> resource

| Attribute Name of <cmdhNwAccessRule> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| targetNetwork (tNet) | 1 | RW | The targetNetwork attribute defines for which underlying networks the usage limits contained in this <cmdhNwAccessRule> resource shall be applied. The targetNetwork attribute is a list of one or more strings identifying names of underlying networks or the string ‘default’. Note: An agreed naming convention for Underlying Network names are TBD. When a name of an Underlying Network appears in the targetNetwork attribute, the usage limits contained in this <cmdhNwAccessRule> resource shall be applied for usage of that specific Underlying Network when processing requests matching with the parent <cmdhNetworkAccessRules> resource’s ’applicableEventCategories’attribute. When the string ‘default’ appears in the targetNetwork attribute, the usage limits contained in this <cmdhNwAccessRule> resource shall be applied for usage of all Underlying Networks that are not listed with their specific name in the targetNetwork attribute of any other <cmdhNwAccessRule> sibling under the same parent <cmdhNetworkAccessRules> resource when processing requests matching with the parent <cmdhNetworkAccessRules> resource’s targetNetwork. Each Underlying Network name or the string ‘default’ shall appear at most once in any of the targetNetwork attributes of any of the provisioned <cmdhNwAccessRule> sibling resources under the same parent <cmdhNetworkAccessRules> resource. |
| minReqVolume (mRV) | 1 | RW | Minimum amount of data that needs to be aggregated before any of the Underlying Networks matching with the targetNetwork attribute of this <cmdhNwAccessRule> resource can be used for forwarding information to other CSEs. |
| backOffParameters (bOP) | 1 | RW | Parameters that define how usage of any of the Underlying Networks matching with the targetNetwork attribute of this <cmdhNwAccessRule> resource shall be handled when attempts to use such networks have failed. The backOffParameters attribute consists of 3 values: A back-off time that defines how long a CSE needs to wait before attempting to use a specific Underlying Network again after a first failed attempt A back-off time increment that defines by how much the back-off time shall be increased after each additional consecutive failed attempt to use the same Underlying Network without success A maximum back-off time that defines the maximum wait time before attempting to use an Underlying Network again after previous failures. |
| otherConditions | 0..n | RW | Additional conditions that needs to be fulfilled before any of the Underlying Networks matching with the targetNetwork attribute of this <cmdhNwAccessRule> resource can be used for forwarding information to other CSEs. |

### 9.6.30	Resource Type cmdhBuffer

The <cmdhBuffer> resource type is used to define limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE. When an incoming request is processed by a CSE, it can only use buffers for temporary storage in compliance with the rules defined by the corresponding <cmdhBuffer> resource.

If a request cannot be processed in compliance with the rules defined in the corresponding <cmdhBuffer> resource, that request shall either be rejected in case it has not already been accepted by the CSE or it has to be purged. Error reporting on failed CMDH processing depends on error reporting parameters (TBD).

Figure 9.6.30-.1: Structure of <cmdhBuffer> resource 
(only resource specific attributes are shown)

The resource <cmdhBuffer> shall contain attributes according to their multiplicity shown in Table 9.6.30-1. A value of "0" for multiplicity indicates the attribute is optional.

Table 9.6.30-1: Attributes of <cmdhBuffer> resource

| Attribute Name of <cmdhBuffer> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| applicableEventCategory (aEC) | 1 | RW | The ‘applicableEventCategory’ attribute defines for which requests the limits contained in this <cmdhBuffer> resource shall be applied. The ‘applicableEventCategory’ attribute is a list of zero or more Event Category values (‘ec’ parameter of a request), or the string ‘default’. When an Event Category vlaue appears in the ‘applicableEventCategory’ attribute, the buffer usage limits defined inside this <cmdhBuffer> resource are applicable for requests associated with that specific Event Category (‘ec’) value. When the string ‘default’ appears in the ‘applicableEventCategory’ attribute, the buffer usage limits defined inside this <cmdhBuffer> resource are applicable for all requests whose associated Event Category value (‘ec’) is not listed in the ’applicableEventCategory’ attribute of any other provisioned <cmdhBuffer> resource on the hosting CSE. A specific Event Category value (‘ec’) shall appear at most once in any of the ‘applicableEventCategory’ attributes of any of the provisioned <cmdhBuffer> resources on the hosting CSE. The string ‘default’ shall appear exactly once in any of the ‘applicableEventCategory’ attributes of any of the provisioned <cmdhBuffer> resources on the hosting CSE. |
| maxBufferSize (mBS) | 1 | RW | Maximum amount of memory that can be used for buffering requests matching with the ‘applicableEventCategory’ attribute of this <cmdhBuffer> resource. |
| storagePriority (sP) | 1 | RW | Storage priority for data that is stored for buffering requests matching with the ‘applicableEventCategory’ attribute of this <cmdhBuffer> resource. The storage priority defines the how to handle purging of buffered data when buffer memory is exhausted and buffered requests need to be purged. Buffered requests associated with a lower storage priority shall be purged before buffered requests with a higher storage priority. The range of storage priority is from 1 … 10. |

### ---------------------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Does this change request avoid conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change  include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?