| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | Barbara Paareglio, NEC, barbara.pareglio@neclab.eu |
| Format:* | ARC#9.2 |
| Date:* | 2014-03-12 |
| Contact:* | Barbara Paareglio, NEC, barbara.pareglio@neclab.eu |
| Reason for Change/s:* | Resolution of issue item for parentID |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v 0.4.2 |
| Clauses/Sub Clauses* | 9.4.2, 9.6.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Resolution for the issue related to parentID

### -----------------------Start of change 1-------------------------------------------

### 9.4.2	Link Types

The following links are defined:

Table 9.4.2-1: Link Types

| Linked Resource Type (link destination) | Linking Resource Type (link origin) | Linking method | Description |
| --- | --- | --- | --- |
| accessControlPolicy | Several (node, application, remoteCSE, container…) | Attribute named “accessControlPolicyID” | See section 9.6.2 |
| node | CSEBase | Attribute named “nodeID” OR Child resource of type “node” | See section 9.6.19 |
| CSEBase or remoteCSE | node | Attribute named “hostedCSEID” OR parent resource of type CSEBase | See section 9.6.3 See section 9.6.4 |
| the parent resource of any resourceType | a child resource of any resourceType | Attribute named “parentID” | See section 9.6.1 |
| child resource of any resourceType | the parent resource of any resourceType | Child resource of a specific type | See section 9.6.5 |

Editor’s Note: There are more links to define in this Table to reflect the current state of the TS.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.1	Common Attributes

Many of the attributes of the resources described in the present document are common. Such attributes are described here once in order to avoid duplicating the description for every resource that contains it.

Attributes that are only used in one or two resource types are described only in the clause for that resource type.

In all tables representing resource attributes, each attribute name is followed by its "short name" in brackets that shall be used in resource representations to be transferred across reference points.

# Table 9.6.1-1: Common Attributes

| Common Attribute | Description |
| --- | --- |
| resourceType (rT) | Resource Type. This WO resourceType attribute stores <in a two capital letters token> the information useful for procedure processing, e.g. CO for <container>, CI for <instance>. |
| parentID (pID) | Establishes the parent-child relationship by identification of the parent of this child resource. Such identifier shall use the flat URI representation. For example, an application resource with the identifier ”myAE1” which has been created under the resource “…//example.com/oneM2M/myCSE”, the value of the parentID attribute will contain “…//parent” |
| accessControlPolicyID (aRI) | The URI of an <accessControlPolicy> resource. The permissions defined in the <accessControlPolicy> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g. Retrieve, Update, Delete, etc.). If a resource type does not have an accessControlPolicyID attribute definition, then the accessControlPolicy for resources of that type are governed in a different way, for example, the accessControlPolicy associated with the parent may apply to a child resource that does not have an accessControlPolicyID attribute definition, or the permissions for access are fixed. Refer to the corresponding procedures to see how permissions are handled in such cases. If a resource type does have an accessControlPolicyID attribute definition, but the (optional) accessControlPolicyID attribute is not set, or it is set to a value that does not correspond to a valid, existing <accessControlPolicy> resource, or it refers to an <accessControlPolicy> resource that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access permissions shall apply. The system default access permissions grant all permissions (i.e. the full set of permissionsFlags) to the following permission holders depending on the prefix of URI of the resource.: << Editor's Note: what is the list of permission holders>> |
| creationTime (cT) | Time/date of creation of the resource. |
| expirationTime (eT) | Time/date after which the resource will be deleted by the hosting CSE. This attribute can be provided by the Originator, and in such a case it will be regarded as a hint to the hosting CSE on the lifetime of the resource. The hosting CSE can however decide on the real expirationTime. If the hosting CSE decides to change the expirationTime attribute value, this is communicated back to the Originator. The lifetime of the resource can be extended by providing a new value for this attribute in an UPDATE verb. Or by deleting the attribute value, e.g. by not providing the attribute when doing a full UPDATE, in which case the hosting CSE can decide on a new value. |
| lastModifiedTime (lMT) | Last modification time/date of the resource. |
| versionTag (vT) | An incremental counter of modification on the resource. When a resource is created, this counter is set to 0, and it will be incremented on every modification of the resource. NOTE: In order to enable detection of overflow, the counter needs to be capable of expressing sufficiently long numbers. . |
| labels(lBs) | Tokens used as keys for discovering resources. |
| creator (cr) | The App-inst-ID or CSE-ID of the entity which created the resource |
| link (ln) | This attribute shall be present only for the announced resource. This attribute shall provide the URI to the original resource. |
| announceTo (aT) | This attributes shall be present for the announceable original resource only. This attribute maintains the list of URIs to the announced resources. Updates on this attribute will trigger new resource announcement or de-announcement. In case of new resource announcement, either the exact URI to the announced resource that is to be created can be provided, or the CSE-ID of the remote CSE can be provided. This means the original resource-hosting CSE will decide the exact location of the announced resource in the remote CSE identified by the CSE-ID. |
| announcedAttribute (aA) | This attributes shall be present for the announceable original resource only. This attribute maintains the list of the announced attributes in the original resource. Updates on this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |

Editor's Note:  The usage of creator (cr) attribute is FFS.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?