| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2014-03-27 |
| Contact:* | SeungMyeong Jeong (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* | Due to the decision on ARC-2013-514 (App-Inst vs. AE), “application instance” should be replaced with AE and some “application” depending on context will be replaced to AE too. This contribution also contains other terminology clarifications such as M2M Application Service Provider. R01: Also proposed to change the name for <application> to <AE> in change 32 R02: Due to the new baseline v0.4.2, several changes from v0.3.2 clause numbers and their texts has been updated. Also, new changes have been added for new texts in v.0.4.2. |
| Clause/Sub Clause Affected* |  |
| Agenda Item:* | n/a |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate changes to the next ARC TS baseline for TP#10 contributions. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Changes from R01 to R02 of this CR

Several updates from R01 due to v0.3.2 ( v.0.4.2 change

- 6.2.9 Registration text has been changed (change 7)

- 6.2.12 Service Session Management has been moved to Annex I (change 9)

- 6.4 Security Aspects added 2 editor’s notes. One is suggested to be removed (change 10)

- 7.1.7 M2M Request Identifier text has been changed (change 15)

- 7.2 M2M Identifiers lifecycle and characteristics text has been changed (change 16)

- 8.1.1 Description text/figure has been changed (change 18)

- 9.6.1 specified resource types has been changed (change 23)

Also, new changes are added in R02 since v0.4.2 has new clauses.

- 9.6 specified resource types has been added (change 23)

- 9.6.3 resource type CSEBase has been added (change 24)

- 9.6.4 resource type remoteCSE has been added (change 25)

- Etc.

Notion of application/CSE instance is deleted in change 7 and 11. Also in change 16, two “instantiation”s are removed.

************************ START OF CHANGE 1  ************************

6.2.1.2.2.2	CSE Monitoring

CSE Monitoring provides operating characteristics of the CSE capabilities. These operating characteristics include attributes for operational status, configuration and statistics as well as management of alerts.

CSE Monitoring is provided by the following CSF’s:

- ASM Software Management Function:

- Retrieval of  log files associated with the software module

- Retrieval of the lifecycle state and associated information related to the artefacts and software modules of the Software Package

- Notifications for faults associated with software lifecycle state transitions

- Others ... TBD

A CSE’s operational characteristics information exchange shall be provided to an AE by the CSE as a result of a retrieval request, alert generation or bulk transfer operations.

************************* END OF CHANGE 1  *************************

************************ START OF CHANGE 2  ************************

6.2.3	Data Management and Repository

6.2.3.1	General Concepts

One of the goals of CSEs is to enable AEs to exchange data with each other.

Data Management and Repository (DMR) CSF is responsible for providing data storage and mediation functions. It includes the capability of collecting and aggregating large amounts of data, converting this data into a specified format, and storing it for analytics and semantic processing. The "data" can be either raw data transparently retrieved from an M2M Device, or processed data which is calculated and/or aggregated by M2M entities. This collection of large amounts of data constitutes what is known as the Big Data Repository functionality.

6.2.3.2	Detailed Descriptions

DMR CSF shall provide the capability to store data such as Application data, subscriber information, location information, device information, semantic information, communication status, access permission, etc. The "data" stored by the DMR CSF enables management of the data and provides the foundation of Big Data. Further, the DMR CSF shall be able to support the physical replacement of M2M Devices and/or Gateways in terms of the stored data.

The DMR CSF shall support transfer of data to/from the AEs, other CSFs and remote CSEs. The DMR CSF shall support transfer of data regardless of the peer entity being on-line or not. The DMR CSF shall support operations such as Create, Read, Update and Delete. The DMR CSF may associate event categorization (e.g., normal, urgent) with the data for supporting differentiated services. External entities such as AFs, other CSFs or remote CSEs shall be able to be granted access to the data in the DMR CSF based on defined policies.

Editor's Note:  Needs to clarify what is meant by "peer entity" being on-line or not. Is the reference to peer-CSE or something more than that?

The organization of the data helps describe how they relate with each other and how they are addressed. DMR CSF shall allow removal, addition, search of the data. The DMR CSF shall support structured data. Some structures may be specified by oneM2M, others may not. Elements of data stored in the DMR CSF shall be uniquely addressable.

The DMR CSF shall support aggregating the data from the same device or from different devices.

The DMR CSF shall enable the sharing of the data amongst local CSFs, remote CSEs and AFs.

Contextual information such as data types, semantic information, time stamps, location etc. shall complement the data stored by the DMR CSF. This will allow the DMR CSF to access and search the data based on a rich set of parameters. The DMR CSF shall be able to trigger data processing based on access to its data.

The DMR CSF shall provide a means to perform analytics on large amount of data, so that service providers can provide value-added services to AEs. The DMR CSF shall be responsible for enabling AEs to discover, execute and use analytics based on large amount of data from different sources.

Semantic information needs to be available on the data that are transferred within the M2M System. The DMR CSF shall provide functions annotating such semantic information to M2M data and exposing M2M resources using the semantic information so that the M2M resources can be discovered by AEs that do not have prior knowledge of them. The DMR CSF shall be responsible for enabling AEs to discover, interpret and use M2M data from different sources.

************************* END OF CHANGE 2  *************************

************************ START OF CHANGE 3  ************************

6.2.5	Discovery

6.2.5.1	General Concepts

Discovery (DIS) CSF is responsible for searching information e.g., supported attributes and resources according to a Request from an Originator within a given scope and subject to permissions, including those allowed by M2M service subscription. An Originator could be an AE or another CSE. The scope of the search could be in one CSE, or in more than one CSE. The discovery results are returned back to the Originator.

************************* END OF CHANGE 3  *************************

************************ START OF CHANGE 4  ************************

6.2.6	Group Management

6.2.6.1	General Concepts

Group Management (GMG) CSF is responsible for handling Group related requests. The request is sent for the management of a Group and its membership as well as for the bulk operations supported by the Group. When adding or removing members to/from a Group, it is necessary to validate if the member complies with the purpose of the Group. Bulk operations includes read, write, subscribe, notify, device management, etc. Whenever a request or a subscription is made via the Group, the Group is responsible for aggregating its responses and notifications. The members of a Group can have the same role with regards to access rights control towards a resource. In this case, access control is facilitated by grouping. When the Underlying Network provides broadcasting and multicasting capability, the GMG CSF is able to utilize such capability.

6.2.6.2	Detailed Descriptions

GMG CSF shall be responsible for the management of a Group and its membership. The GMG CSF shall support bulk operations to multiple resources of interest and aggregate the results. The GMG CSF shall be able to facilitate access control based on grouping. When needed and available, the GMG CSF may leverage the existing capabilities of the Underlying Network including broadcasting/multicasting.

The GMG CSF handles requests from AEs and/or from other CSEs.

Grouping enables the oneM2M System to perform bulk operations to multiple devices, applications, or resources. The GMG CSF shall manage the resources and operations associated with grouping.

The GMG CSF shall handle the requests to create, query, update, and delete a Group. An AE or a CSE may request the creation/retrieve/update/deletion of a Group as well as the addition and deletion of members of the Group. The GMG CSF shall be able to create one or more Groups in CSEs in any of the Nodes in oneM2M System for a particular purpose (i.e. facilitation of access control, device management, fan-out common operations to a group of devices, etc.). The GMG CSF shall handle the requests to retrieve the information (e.g. URI, metadata, etc.) of a Group and its associated members.

The GMG CSF shall manage Group membership. The GMG CSF shall handle requests to add or remove members to and from a Group’s member list. A member may belong to one or more Groups. A Group may be a member of another Group. When new members are added to a Group, the GMG CSF should validate if the member complies with the purpose of the Group.

In order to fulfil the functionalities of the GMG CSF, functionalities from other CSFs may be needed. Examples include Network Service Exposure CSF for leveraging broadcasting/multicasting capability from the Underlying Network, Security CSF for authentication and authorization etc.

Editor’s Note: How the Underlying Network supports broadcasting/multicasting is FFS.

When facilitating access control using a Group, only members with the same access rights towards a resource shall be included in the same Group. Also, only AEs or CSEs which have a common role with regards to access rights shall be included in the same Group. This shall be used as a representation of the "role" when facilitating role based access control.

Editor's Note:  Suggest adding description on what is meant by Group member, what entities can be members of a Group?  Can a Group consist of heterogeneous members?

The GMG CSF shall forward requests to all members in the Group. In case the Group contains another Group as a member, the forwarding process shall be done recursively, i.e. the nested Group shall forward the request to its members. After forwarding the request to all members in the Group, the GMG CSF shall generate an aggregated response by aggregating the corresponding responses from the Group members.

Editor’s Note: The structure of the resource in oneM2M System is FFS.

The GMG CSF shall support subscriptions to individual Groups. Subscriptions to a Group shall be made only if the subscriber is interested in all members of the Group. If subscription to a Group is made, the GMG CSF shall aggregate the notifications from the Group members, and it shall notify the subscriber with the aggregated notification. Responses and event notifications relevant to a subscription may be selectively filtered by filtering criteria. The filtering criteria shall be managed by the GMG CSF. In order to subscribe to or query a Group, methods for group discovery shall be provided.

************************* END OF CHANGE 4  *************************

************************ START OF CHANGE 5  ************************

6.2.7	Location

6.2.7.1	General Concepts

The Location (LOC) CSF allows M2M AEs to obtain geographical location information of M2M Nodes (e.g., ASN, MN) for location-based services. Such location information requests may be from an M2M AE residing on either a local Node or a remote Node.

NOTE: Geographical location information can be more than simply the longitude and the latitude information.

6.2.7.2	Detailed Descriptions

LOC CSF shall obtain and manage geographical location information based on the requests from M2M AEs residing on either a local Node or a remote Node. The LOC CSF shall interact with any of the following: a location server in the Underlying Network, a GPS module in the M2M Node, or, information for inferring location stored in other M2M Nodes.

In order to Update the location information, an M2M AE shall be able to configure an attribute (e.g., update period). Based on the such defined attribute, the LOC CSF shall Update the location information using one of interactions defined above.

NOTE: The location technology (e.g., Cell-ID, Assistant-GPS, and Fingerprint) used by the Underlying Network depends on the capabilities of the Underlying Network.

The LOC CSF shall be able to request M2M Nodes to share and report their own or other M2M Node's geographical location information with the requesting AEs.

The LOC CSF shall be able to provide means for protecting the confidentiality of geographical location information.

************************* END OF CHANGE 5  *************************

************************ START OF CHANGE 6  ************************

6.2.8	Network Service Exposure, Service Execution and Triggering

6.2.8.1	General Concepts

Network Service Exposure, Service Execution and Triggering (NSSE) CSF manages communications with the Underlying Networks for accessing network service functions over the Mcn reference point. The NSSE CSF uses the available/supported methods for service "requests" on behalf of AEs. The NSSE CSF shields other CSFs and AFs from the specific technologies and mechanisms supported by the Underlying Networks.

NOTE: The NSSE CSF provides adaptation for different set of network service functions supported by various Underlying Networks.

The network service functions provided by the Underlying Network include service functions such as, but not limited to, device triggering, small data transmission, location notification, policy rules setting, location queries, IMS services, device management. Such services do not include the general transport services.

6.2.8.2	Detailed Descriptions

NSSE CSF shall manage communication with the Underlying Networks for obtaining network service functions on behalf of other CSFs, remote CSEs or AEs. The NSSE CSF shall use the Mcn reference point for communicating with the Underlying Networks.

NOTE: The network services provided by the Underlying Networks include services such as, but not limited to, device triggering, small data transmission, location notification, policy rules setting, location queries, IMS services, device management. Such services do not include general transport services.

The M2M System shall allow the Underlying Networks to control network service procedures and information exchange over the Underlying Networks while providing such network services. For example, for the 3GPP networks, the Underlying Network may chose to provide the network services based on control plane signalling mechanisms.

Other CSFs in a CSE that need to use the services offered by the Underlying Network shall use the NSSE CSF.

The NSSE CSF shall shield other CSFs and AFs from the specific technology and mechanisms supported by the Underlying Networks.

NOTE: The NSSE CSF provides adaptation for different set of network service functions supported by various Underlying Networks.

The NSSE CSF shall maintain over the Mcn reference point, the necessary connections and/or sessions between the CSE and the Underlying Network when local CSFs are in need of a network service.

The NSSE CSF shall provide to the CMDH CSF information related to the Underlying Network so the CMDH CSF can include them to determine proper communication handling.

************************* END OF CHANGE 6  *************************

************************ START OF CHANGE 7  ************************

### 6.2.9	Registration

#### 6.2.9.1	General Concepts

Registration (REG) CSF is responsible for processing a request from an AE or another CSE to register with a CSE in order to allow the registered entities to use the services offered by the registered-with CSE. The REG CSF processes registration of a Device also, to allow registration of Device's properties/attributes with the CSE.

#### 6.2.9.2	Detailed Descriptions

Registration is the process of delivering AE or CSE information to another CSE in order to use M2M Services.

An AE on an Application Service Node, a Middle Node, or an Infrastructure Node shall perform registration locally with the corresponding CSE in order to use M2M services offered by that CSE. An AE on an Application Dedicated Node shall perform registration with the CSE on a Middle Node or Infrastructure Node in order to use M2M services offered by that CSE. A node-less AE shall perform registration with the corresponding CSE on an Infrastructure node in order to use M2M services offered by that CSE. A registered Application shall be able to have interactions with its local CSE (when it is the target CSE) without the need to have the local CSE register with other CSEs.

The CSE on an Application Service Node shall perform registration with the CSE in the Middle Node in order to be able to use M2M services offered by the CSE in the Middle Node. As a result of successful ASN-CSE registration with the MN-CSE, the CSE on the ASN Node establish a peering relationship and shall be able to exchange information.

The CSE on a Middle Node shall perform registration with the CSE of another Middle Node in order to be able to use M2M services offered by the CSE in the other Middle Node. As a result of successful MN-CSE registration with the other MN-CSE, the CSE on the Middle Nodes establish a peering relationship and shall be able to exchange information.

The CSE on an Application Service Node or on a Middle Node shall perform registration with the CSE in the Infrastructure Node in order to be able to use M2M services offered by the CSE in the Infrastructure Node. As a result of successful ASN/MN registration with the IN-CSE, the CSEs on ASN/Middle Node and Infrastructure Node establish a peering relationship and shall be able to exchange information.

AEs shall be able to exchange information via CSEs following successful registration of:

- AEs with their associated CSE

- One of these CSEs with the other CSE, as per Table 6.2.9.2-1

Such registrations are applicable to a single M2M Service Provider Domain.

A (physical) Device shall be able to register with its local CSE for registering its properties/attributes. Such registration enables correlation of Devices Identities such as M2M-Node-ID with the CSE-ID.

Editor's Note: The need for Device Registration and the relationship with CSE Registration are FFS.

Editor's Note: The use of External ID in Registration is FFS.

The following Table shows which oneM2M entity types may register with which other entity types.

- Table 6.2.9.2-1: Entity Registration

| Originator (Registree) | Receiver (Registrar) | Registration Procedure |
| --- | --- | --- |
| ADN-AE | MN-CSE, IN-CSE | AE registration procedure see clause TBD |
| ASN-AE | ASN-CSE |  |
| MN-AE | MN-CSE |  |
| IN-AE | IN-CSE |  |
| Nodeless AE | IN-CSE |  |
| ASN-CSE | MN-CSE, IN-CSE | CSE registration procedure see clause TBD |
| MN-CSE | MN-CSE, IN-CSE |  |

The Originator (Registree) in Table 6.2.9.2-1 requests the registration and the Receiver (Registrar) is responsible for verifying the request, and checking the authentication and authorization of the Originator in order to establish a peer relationship.

Editor’s Note: Authorization above might only be needed for AEs, this is FFS in Security WG

An AE shall register to one CSE (ASN-CSE, MN-CSE or IN-CSE) at one time.

An ASN-CSE shall register with one other CSE (MN-CSE or IN-CSE) at one time.

An MN-CSE shall register with one other IN-CSE at one time.

An MN-CSE shall support only a single registration towards another MN-CSE or an IN-CSE. A concatenation (registration chain) of multiple uni-directional registrations shall not form a loop. E.g. Two MN-CSEs A and B, shall not register with each other. Three MN-CSEs A, B and C, where A registers to B, and B registers to C, then C shall not register to A.

Editor’s Note: The use of “instance” above might be removed if other definitions are changed. If kept, the description regarding “instances” should be expanded.

Registration information shall be able to include:

- Identifier.

- Reachability schedules; which are elements of a node's policy, and specify when messaging may occur between nodes. Reachability schedules may be used in conjunction with other policy elements. When reachability schedules are not present in a node then that node is expected to be always reachable.

Editor's note: Further Registration information is FFS.

************************* END OF CHANGE 7  *************************

************************ START OF CHANGE 8  ************************

### 6.2.10	Security

6.2.10.1	General Concepts

Security (SEC) CSF comprises the following functionalities:

- Sensitive Data Handling functionality;

- Security Administration functionality;

- Security Association Establishment functionality;

- Authorization and Access Control functionality;

- Identity Protection Functionality.

Sensitive Data Handling functionality in the SEC CSF protects the local credentials on which security relies during storage and manipulation. Sensitive Data Handling functionality performs other sensitive functions as well such as security algorithms. This functionality is able to support several cryptographically separated security environments.

Security Administration functionality enables services such as the following:

- Creation and administration of dedicated security environment supported by Sensitive Data Handling functionality;

- Post-provisioning of a root credential protected by the security environment;

- Provisioning and administration of subscriptions related to M2M Services and M2M Application Services.

Security Association Establishment functionality is responsible for establishing security association between corresponding M2M nodes, in order to provide services such as confidentiality, integrity, authentication, authorization, etc.

Authorization and Access Control functionality is responsible for authorizing services and data access to authenticated entities, according to provisioned security policies and assigned roles.

While unique identifier of an entity are used for authentication, the Identity Protection functionality provides pseudonyms which serve as temporary identifiers which cannot be linked to the true identity of either the associated entity or its user.

6.2.10.2	Detailed Descriptions

SEC CSF shall comprise the following functionalities:

- Sensitive Data Handling functionality;

- Security Administration functionality;

- Security Association Establishment functionality;

- Authorization and Access Control functionality;

- Identity Protection Functionality.

Sensitive Data Handling Functionality in the SEC CSF shall have the capability to protect the local credentials on which security relies during storage and manipulation. The SEC CSF shall be able to extend sensitive data handling functionality to other sensitive data used in the M2M Systems such as subscription related information, security policies and personal data pertaining to individuals. The Sensitive Data Handling functionality shall perform other sensitive functions as well, such as security algorithms. The Sensitive Data Handling functionality shall be able to support several cryptographically separated security environments.

Security Administration functionality in the SEC CSF shall enable the following services:

- Creation and administration of a dedicated security environment supported by Sensitive Data Handling functionality;

- Post-provisioning of a root credential protected by the security environment;

NOTE: The security environment can also be pre-provisioned with a root credential prior to deployment; therefore this capability is not always required. Post-provisioning is required when the security bootstrapping needs to be performed or re-initiated after deployment.

- Provisioning and administration of subscriptions related to M2M services and M2M application services. Besides the root secret, a subscription includes other information classified as sensitive data such as associated authorization and security policies.

Security Association Establishment functionality in the SEC CSF shall be able to establish security associations between corresponding M2M nodes, in order to provide specific security services (e.g. confidentiality, integrity, authentication, authorisation, or support for application level signature generation and verification) involving specified security algorithms and sensitive data. This involves key derivation based on provisioned root secrets. This functionality of the SEC CSF is mandatory when security is supported.

Editor's Node: The definition of Security Association will be provided by WG4. A definition may be: "Security associations (SAs) are logical relationships between 2 entities that may be associated with a communications link, but SAs are not communications links. Security associations may take a number of forms but in each case they identify the nature of the security service (confidentiality, integrity, authentication or authorisation), the required algorithm and key. Security associations may be established for single transactions (and thus their establishment may form part of the transaction itself) or for session based associations (in such instances the association is generally established independently of the individual transactions that are to be secured)".

The Authorization and Access Control functionality in the SEC CSF shall be able to authorize services and data access to authenticated entities, according to provisioned security policies and assigned roles. This functionality is mandatory when any services relying on authorization and access control are present. Among other usages, the services of this functionality may be applied to personal information as a means to preserve privacy.

Although a Subscriber is generally considered to be an AE or functional agent that represents a human, there are links between a device and its User that can be either directly derived or indirectly deduced. Consequently, identifiers used for communication in the M2M System shall not be directly related to the real identity of either the device or its User, except where this is a requirement for operation of a specific AE.

While the unique identifier of an entity shall be used for authentication, the identity protection functionality provides pseudonyms which serve as temporary identifiers which shall not be able to be linked to the true identity of either the associated entity or its user.

************************* END OF CHANGE 8  *************************

************************ START OF CHANGE 9  ************************

## I.1	Service Session Management Text for Removal

6.2.12	Service Session Management

6.2.12.1	General Concepts

An M2M service session is an end-to-end Service Layer connection managed by the Service Session Management (SSM) CSF.  The SSM CSF manages M2M service sessions between AEs, between an AE and a CSE, or between CSEs.

Editor's Note: Provide information as to when an M2M service session is needed.

The management of a M2M service session includes capabilities such as the management of session state, session authentication and establishment, management of Underlying Network connections and services related to the session, coordination of sessions spanning multiple hops of CSEs, exchange of information between session endpoints, and session termination.

The SSM CSF uses the CMDH CSF within its local CSE for sending/receiving messages to/from the next-hop CSE or to/from an AE for a given M2M service session. The SSM CSF also uses the SEC CSF for the management of session related security credentials and authentication of session participants. The SSM CSF generates session specific charging events also that it communicates to the SCA CSF within its local CSE.

6.2.12.2	Detailed Descriptions

An M2M service session is an end-to-end Service Layer connection managed by the SSM CSF. The SSM CSF shall support the management of the following M2M service session related information.

- Session Identifier: The Service Session Identifier is used by the SSM CSF and session endpoints to uniquely identify M2M service layer session.

- Session Credentials: Security credentials associated with M2M service session.  For example, E2E security certificates, public keys, etc. An M2M service session can support an independent set of credentials or it can optionally leverage security credentials from Underlying Network sessions or network connections.

- Session Descriptor: Information describing the M2M service session that can be used by the existing session endpoints or prospective session participants in order to discover an existing session.  For example, a description for each session participant (e.g. device identifiers, type of participant, services that participant supports, interface requirements of participant, type of compression used, etc.).

- Session Routing Information: Information describing how to route M2M service session messages. For example, list of CSEs in the routing path, or next-hop CSE in the routing path.

- Session Context/History: Information related to M2M service session activity such as session related events that have occurred or transactions that have been processed.  For example, keeping track of the type, number, rate, size, etc. of the resources targeted by the session endpoints. Or keeping track of different service sessions that a specific application establishes (e.g. rate, type, etc).

- Session Policies: Policies that define rules for how SSM CSF manages sessions. For example, session routing policies, session store-and-forward policies, session access control policies, session data management policies, etc.  The SSM CSF can use these policies by itself or provide such policies to other CSFs (e.g. CMDH CSF, DMR CSF, SEC CSF, etc).

Some M2M service sessions may require security. In order to secure an M2M service session, proper security credentials shall be used by session endpoints (e.g., AEs and/or CSEs).  If M2M service session credentials are not pre-provisioned, the SSM CSF shall support securely bootstrapping of the session credentials to the session endpoints. The SSM CSF shall use the SEC CSF for supporting such bootstrapping. The SSM CSF may also leverage security credentials and trust relationships from Underlying Networks.

The SSM CSF shall support requests to establish an M2M service session between AEs, between an AE and a CSE, or between CSEs.  Before a request to establish an M2M service session is granted, the SSM CSF shall first authenticate the requester using session credentials. The SSM CSF shall use the SEC CSF to support session authentication. Once authenticated, the SSM CSF shall establish the M2M service session between the requesting and targeted session endpoints. This shall involve the SSM CSF coordinating with the targeted session endpoint on an agreed upon session ID that can be used to identify the session messages. The SSM CSF shall return this session ID to the requester. The SSM CSF shall also maintain additional session information for the management of the session such as session policies, session routing information, session descriptor, etc.

The SSM CSF shall support layering of a M2M service session over the top of Underlying Network connections. The SSM CSF shall support persistency of the M2M service sessions with respect to the Underlying Network connections.  The SSM CSF shall maintain an active M2M service session independent of the state of the Underlying Network connections and shall be robust to network connections that are dynamically torn-down and re-established. The SSM CSF shall support initiating or providing input to other CSFs and/or the Underlying Network on whether the network connections should be torn-down/re-established based on M2M service session activity or state.

The SSM CSF shall support requests to terminate an M2M service session between AEs, between an AE and a CSE, or between CSEs. Before a request to terminate an M2M service session is granted, the SSM CSF shall first authenticate the requester using session credentials. The SSM CSF shall use the SEC CSF to support session authentication. Once authenticated, the SSM CSF shall terminate the M2M service session between the requesting and targeted session endpoints. This shall involve removal of session information on the session endpoints as well as the SSM CSF.

The SSM CSF shall support M2M service sessions that span multiple intermediate CSE hops. The SSM CSF shall leverage the SEC CSF on its local CSE as well the SSM CSF and the SEC CSF on intermediate CSEs to support multi-hop M2M service sessions. In doing so, SSM CSFs on different CSEs shall support coordinated M2M service session management. This includes bootstrapping of session credentials, session authentication and establishment, management of underlying network connections and services related to the session, management of session routing information, and session termination across multiple SSM CSFs.

Editor' Note: Security related descriptions for this CSF need to be updated.

Editor' Note: The session involves Mcn reference point or does it involve Mca and Mcc reference points as well. This is FFS.

Editor’s Note: This Annex shall be removed at the time of approval of TS-0001 Release-1.

************************* END OF CHANGE 9  *************************

************************ START OF CHANGE 10  ************************

6.4	Security Aspects

The oneM2M Security Analysis Technical Report [i.x] differentiates security domains related to the transport layer (Underlying Network), service layer (M2M common services) and Application Layer. It also considers possible trust scenarios involving these different security domains, and investigates countermeasures to threats that potentially affect the security of the M2M System.

Each of the security domains may provide their own set of security capabilities. The oneM2M security solution shall provide configurable security services through an API for upper security domains to leverage on, or enable the use of the exposed security features of other security domains when appropriate.

As a result, beyond providing security solutions that protect the integrity of the M2M Service Layer, the oneM2M architecture exposes, through its APIs, further security services that are made available to M2M Applications. This enables M2M Applications to benefit from security solutions deployed in the M2M Service Architecture, without adding redundant and/or proprietary security solutions on application nodes and devices.

Editor's Note: Clarify the difference between "application nodes and devices" in the para above.

NOTE: It remains the responsibility of M2M Application Service Providers to perform their own risk assessment process to identifying the specific threats affecting them and derive their actual security needs.

************************* END OF CHANGE 10  *************************

************************ START OF CHANGE 11  ************************

## 6.5	Other Aspects

### 6.5.1	Inter M2M SP communication for oneM2M compliant nodes

To enable M2M entities (eg. CSE, AE) in different M2M Service Provider domains to communicate, there is a need to configure within the M2M domain if such a communication is allowed. If allowed, the M2M System shall support routing the traffic across the M2M Service Provider (SP) domain and within the target domain.

Communication between different M2M SPs which occurs over the reference point Mcc', is subject to business agreements. The offered functionality is typically a subset of the functionality offered over the Mcc reference point.

The following Table shows which oneM2M entity types may register with which other entity types across the Mcc’ reference point.

- Table 6.5.1-1 - Inter M2M SP Entity Registration

| Originator (Registree) | Receiver in different M2M SP domain (Registrar) | Registration Procedure |
| --- | --- | --- |
| IN-CSE | IN-CSE | Inter M2M SP registration procedure see clause TBD |

An IN-CSE is allowed to register to a single IN-CSE of multiple different M2M SP domains at one time.

Any interM2M SP communication in support of a request originating from one M2M SP domain shall be processed and forwarded through the Infrastructure Node of the originating M2M domain towards the Infrastructure Node of the target M2M SP domain and finally forwarded to its target CSE, if different from the Infrastructure Node. Hence the Infrastructure Node in both M2M domains shall be the exit and entry points, respectively, for all inter M2M SP communication traffic.

In this configuration approach, public DNS shall be used to support traffic routing for inter M2M SP communication in accordance with [i.7]. This relies on public domain names being allocated to communicating CSE entities within the oneM2M architecture, and to whom access across domains is permitted through policies.  To that effect, an M2M SP supporting inter- M2M SP communication shall ensure that the public domain names for the CSEs whose functionality is available across domains are held in its public DNS and shall always point to the IP address associated with the Infrastructure Node for the domain (being the entry point) for accessibility purposes.

The M2M SP could optionally also have additional policies (example: black list or white list) that governs accessibility from other domains to CSE functionality located within its own domain. These policies are however out of scope.

The public domain names of CSEs to whom access from other domains is allowed by policies, shall be created in the DNS of the M2M SP by the Infrastructure Node at registration time of these CSEs, and shall be removed at de-registration. DNS entries for CSEs can also be created/removed for registered CSEs at any time by the M2M SP through administrative means to handle dynamic policies.

Editors Note: The CSE registration procedures will be updated to include normative text for the creation of the needed DNS entries

#### 6.5.1.1	Public Domain Names and CSEs

To enable the usage of public DNSs as described above, there is a need for a naming convention for public names for CSEs.  This naming convention facilitates the creation of the necessary entries of the public domain names of CSEs in the DNS by the infrastructure node.

CSEs public domain names shall be a sub-domain of the Infrastructure Node public domain name. This naming convention allows the Infrastructure Node to include the needed DNS entry corresponding to the CSE to whom access from other domains is allowed. This would typically occur when the CSE registers with the Infrastructure Node, subject to policies, or administratively. The Infrastructure Node shall also have a public domain name.

Accordingly, the structure of the public domain of the CSEs in IN/MN/ASN shall follow the following naming convention, which relies on the CSE identifier (CSE-ID) as part of the naming convention to facilitate the entry creation:

- IN-CSE public domain name: <Infrastructure Node CSE Identifier>.<M2M Service Provider domain name>.

- MN-CSE public domain name: <Middle Node CSE Identifier>.<Infrastructure Node public domain name>.

- ASN-CSE  public domain name: <Application Service Node CSE Identifier>.<Infrastructure Node public domain name>.

Both the MN-CSE and the ASN-CSE are sub-domains of the Infrastructure Node.

The A/AAAA records in the DNS, as per [i.5], [i.6], and [i.10] shall consist of the public domain name of the CSE and the IP address of the M2M Infrastructure Node, since the M2M Infrastructure Node is the entry point of the M2M Service Provider domain name where it belongs to.

Note that entries in the public domain names of the three nodes depicted above do not imply that the actual CSE-Identifier allocated for that node has to be used in the DNS entry. Rather any name, including indeed the CSE Identifier for the node, can be used there as long as the entry resolves to the intended service node.

Example:

These 3 host entries are valid entries in the DNS:

IntermediatenodeCSEID.infrastructurenodeCSEID.m2m.myoperator.org

node1.node2.m2m.myoperator.org

IntermediatenodeCSEID.node22.m2m.myoperator.org

#### 6.5.1.2	M2M Service Subscription

The M2M Service Subscription defines the technical part of the contract between an M2M Subscribers (typically an M2M Application Service Provider) and an M2M Service Provider. Each M2M Service Subscription shall have a unique identifier, the M2M-Sub-ID, as specified in 7.1.11. An M2M Service Subscription establishes a link between one or more AEs; one or more M2M Nodes, one or more M2M Service roles as well as subscriber defined groups used for Access Rights.

Editor’s Note: Change Access Right to Access Control Policy if such a recommendation is made by WG4

An M2M Service is the marketable service offered to M2M service subscriber (organizations or individuals). Examples of services include Device Management, Location, Data Exchange, etc.

In each M2M Service, one or multiple M2M Service role(s) shall be defined by the M2M Service Provider. M2M Service role is defined as a set of privileges pertaining to a resource types which are associated with M2M Service. The M2M Subscriber subscribes one or multiple roles within the M2M Services, which M2M Subscribers are interested in.

The set of M2M Services and M2M Service roles supported in this specification is depicted in Annex X (the list of roles is provided as informative).

It shall also be possible for an M2M Service Provider to define his own services and roles.

An M2M Service Subscription governs for an M2M subscription, the M2M nodes where AEs can reside and execute. It also governs the M2M Service roles as well as subscriber defined groups used for Access Right.  An example of the Subscriber defined group is all node applications within this service subscription with App-ID set to a specific value. Access Right resource configuration shall be in line with M2M Service Subscription. For Authorization of accessing the resource, Access Right is applied. Details of configuring Access Right are FFS.

How to authorize the request operation based on M2M Service Subscription resource will be defined in section FFS of TS-0003 [TS-0003].

An M2M Service Subscription shall be used for the following purposes:

- Serve as a basis for authorization for resource operations

- Serve as the basis for charging.

- Identify which nodes are part of this M2M Service Subscription

### 6.5.2	Inter M2M SP Generic Procedures

This section describes the behaviour of the M2M nodes in support of inter-M2M SP procedures.

#### 6.5.2.1	Actions in  the originating M2M node in Originating Domain

The issuer in the originating domain can be any M2M node such as ADN, an MN, or an ASN, etc.. , and shall issue a request to the local CSE to retrieve a resource located in another M2M Service Provider domain.

The issuer shall use any of the options defined in X.X.X to identify the target host and resource for that purpose.

#### 6.5.2.2 	Actions in  the Receiving CSE  in originating domain

The receiving CSE in the originating domain shall check if the addressed resource is locally available. If the addressed resource is not locally available, then the request shall be forwarded to the next hop.

If the receiving CSE is on an IN, it shall check if the addressed resource is locally available within its domain.  If the addressed resource is not located within its own domain, then the IN shall perform a DNS lookup by using the target hostname provided in the RETRIEVE request. A successful DNS lookup shall return to the origin IN in the originating domain the IP address of the M2M IN residing in the target M2M Service Provider Domain.

Subsequently, the IN in the originating domain shall forward the request to the IN of the target domain.

#### 6.5.2.3	Actions in  the IN of the target domain

The IN is the entry point of the target M2M Service Provider domain. The IN shall check if the addressed resource is a local resource. If it is not a local resource it shall forward the request to the appropriate CSE, after identifying the hosting CSE within its domain, using the pointOfAccess attribute.

Once the request reaches the target Hosting-CSE, the CSE shall apply the access rights applicable to the request.  Consequently, the Hosting-CSE shall forward the response for the incoming request following the same path of the incoming request.

************************* END OF CHANGE 11  *************************

************************ START OF CHANGE 12 ************************

7.1.2	Application Entity Identifier (AE-ID)

An Application Entity Identifier (AE-ID) uniquely identifies an AE resident on an M2M Node, or an AE that requests to interact with an M2M Node. An AE-ID shall identify an Application for the purpose of all interactions from/to the Application within the M2M System.

It is the responsibility of the M2M Service Provider to ensure that the AE-ID is globally unique. The AE-ID shall include the Application ID (see section 7.1.3.)

************************* END OF CHANGE 12  *************************

************************ START OF CHANGE 13  ************************

7.1.5	M2M Node Identifier (M2M-Node-ID)

An M2M Node, hosting a CSE and/or AE(s) shall be identified by a globally unique identifier, the M2M-Node-ID.

The M2M System shall allow the M2M Service Provider to set the CSE-ID and the M2M-Node-ID to the same value.

The M2M-Node-ID enables the M2M Service Provider to bind a CSE-ID to a specific M2M node.

Examples of allocating globally unique M2M-Node-ID include Object Identity (OID) and IMEI. For details on OID, see Annex H.

************************* END OF CHANGE 13  *************************

************************ START OF CHANGE 14  ************************

7.1.6	M2M Service Subscription Identifier (M2M-Sub-ID)

The M2M-Sub-ID enables the M2M Service Provider to bind AE(s), M2M Nodes, CSEs and services identified by service identifiers to a particular M2M service subscription.

Editor's Note: The specification needs to include a section on services, service identifiers.

The M2M Service Subscription Identifier has the following characteristics:

•	belongs to the M2M Service Provider,

•	identifies the subscription to an M2M Service Provider,

•	enables communication with the M2M Service Provider,

•	can differ from the M2M Underlying Network Subscription Identifier,

There can be multiple M2M Service Subscription Identifiers per M2M Underlying Network subscription.

************************* END OF CHANGE 14  *************************

************************ START OF CHANGE 15  ************************

7.1.7	M2M Request Identifier (M2M-Request-ID)

This is an identifier that tracks a Request initiated by an AE over the Mca reference point, and by a CSE over the Mcc and Mcn reference points, if applicable, end to end. It is also included in the Response to the Request over all the above reference points.

To enable AE to track Requests and corresponding Responses over the Mca reference point, AEs shall include a distinct M2M Request Identifier per request over the Mca Reference point to the CSE for any initiated request.

The CSE shall make such M2M Request Identifier received from the AE globally unique by appending its CSE-ID to it.

If the CSE creates a Request Identifier, then the CSE shall maintain a binding between the M2M Request Identifier received from the AE and the CSE Request Identifier it created in its interactions towards other peer CSEs. The CSE shall include the M2M Request Identifier received from the AE in its response to the AE. This binding shall be maintained by the CSE until the Request is deposed off. Note that the Request initiated by the CSE could be the result of an application request, or a request initiated autonomously by the CSE to fulfil a service.

A CSE receiving a Request from a peer CSE shall include the received Request Identifier in all additional requests unspanned (i.e.1:1) it has to generate (including propagation of the incoming Request) and that are associated with the incoming Request, where applicable.

The CSE shall include the same received Request Identifier in its interactions with the Underlying Network, over the Mcn reference point where applicable

Note that the M2M Request Identifier can be made globally unique by including the CSE-ID in combination with any random number.

Editor's Note:  Bring in a contribution to indicate where this information will carried.

Editor's Note:  In order to allow interworking, how the platform understands whether the Request Identifier is globally unique or not needs to be specified.

************************* END OF CHANGE 15  *************************

************************ START OF CHANGE 16  ************************

## 7.2 M2M Identifiers lifecycle and characteristics

Table 7.2-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | FFS |  |
| Application Entity Identifier | FFS | AE | AE start-up | Application Entity Registration | Global | - Application Entity Registration - Security Context Establishment - Other operations FFS | Security requirements apply for Security Context Establishment |
| CSE Identifier | M2M SP | CSE | Security Provisioning | Life of the CSE | Global | - Information flows (clause 10) - Security Context Establishment | Secuirty requirements apply for Secuirty Context Establishment |
| M2M Node Identifier | Out of Scope | M2M Node hosting CSE | Pre-provisioned | Life of the M2M Node | Global | Security provisioning (FFS) | Needs to be Read Only |
| M2M Subscription Identifier | M2M SP | Application Entities, and one or more CSEs belonging to the same M2M subscriber | At service signup | Life of the M2M Service Subscription with the M2M SP | Global | - Charging and Information Recorded - Other operations are FFS | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M-Request-ID | Mcc: CSE Mca: Application Entity | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global | Requests and corresponding responses |  |
| External Identifier | Manual mode: Jointly between the Underlying Network provider and M2M SP, where applicable. Plug-And- Play: FFS | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Manual Mode: Administrative Agreement. Plug-And- Play: FFS | Life of the CSE. | FFS | Requests initiated by a CSE over the Interface, where applicable. |  |
| Underlying Network Identifier | M2M SP | Underlying Networks | Pre-provisioned | Life of the Underlying Network | Local to M2M SP domain | UL Network selection |  |
| Trigger Recipient Identifier | Execution Environment | ASN/MN-CSE | ASN/MN-CSE start-up or wake-up | Life of the CSE | Execution Environment-wide | Device Trigerring procedures |  |

************************* END OF CHANGE 16  *************************

************************ START OF CHANGE 17  ************************

7.3.2.2		Locating Application Entities

Locating an AE is a two-step process as follows:

- Step 1: There is a need to locate the CSE where the AE is registered. Locating the CSE shall be accomplished as follows:

- For AEs associated with ASNs/MNs/INs, the CSE-PoA of the ASN-CSE/MN-CSE/IN-CSE registered object shall be used.

- For AEs associated with ADNs, the CSE-PoA of the MN-CSE/IN-CSE registered object shall be used.

- Step 2:  the CSE shall locate the appropriate AE using its Application Entity Identifier (AE-ID).

************************* END OF CHANGE 17 *************************

************************ START OF CHANGE 18  ************************

8.1.1	Description

Figure 8.1.1-1 shows the general flow that governs the information exchange within a procedure, which is based on the use of Request and Response scheme. The scheme applies to communications such as:

- between an AE and a CSE (Mca reference point), and

- among CSEs (Mcc reference point).

The communications can be initiated either by AEs or by CSEs depending upon the operation in the Request message.

Figure 8.1.1-1: General Flow

************************* END OF CHANGE 18  *************************

************************ START OF CHANGE 19  ************************

8.2.2	Accessing Resources in CSEs – Blocking Requests

For the procedures described herein, the addressed resource can be stored in different CSEs. Table 8.2.2-1 describes the possible scenarios, where the addressed resource may be on the local-CSE or on a CSE located elsewhere in the oneM2M System.

In this sub-clause – for simplicity – it is assumed that the Originator of a Request can always wait long enough to get a Response to the Request after the requested operation has finished. This implies potentially long or unknown blocking times (time for which a pending Request has not been responded to) for the Originator of a Request.

For scenarios that avoid such possibly long blocking times, section 8.2.3 specifies mechanisms to handle synchronous and asynchronous resource access procedures via returning appropriate references.

Editor’s Note: How the target of a Request (i.e, an Application or local/hosting CSE) is identified and addressed, is FFS.

Editor’s Note: A message (Request, Response) can be forwarded immediately or forwarded at a later time (e.g in the case of congestion).The procedures related to the forwarding of the Request at a later time are FFS.

Table 8.2.2-1 Accessing Resources in different CSEs

| Traversals across X/Y Reference Points | Description | Reference |
| --- | --- | --- |
| No Hops | The Originator of the Request accesses a resource. The Originator of the Request can be an AE or a CSE. Local CSE and Hosting CSE are the same entity. The CSE shall check the Access Rights for accessing the resource. Depending on the expected result content, the CSE shall respond to the Originator of the Request, either with a Success or Failure Response, or not at all. | Figure 8.2.2-1 |
| 1 Hop | The Originator of the Request accesses a resource. The Originator of the Request may only be an AE. Local CSE and Hosting CSEs different entities. Local CSE shall forward the Request to the Hosting CSE, after an optional checking of the Access Rights for accessing the resource and the syntax of the Request message. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-2 (Editor's Note-1) |
| Multi Hops | The Originator of the Request accesses a resource. The Originator of the Request may be an AE or a CSE. Local CSE, Intermediate CSE(s) and the Hosting CSE are different entities. Local CSE shall forward the Request to an Intermediate CSE (e.g. MN-CSE) that the Local CSE is registered with, if it cannot communicate with the Hosting CSE directly. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message may be performed prior to forwarding the Request. Intermediate CSE may forward the Request to another Intermediate CSE (e.g. another MN-CSE) that the Intermediate CSE is registered with, if it cannot communicate with the Hosting CSE directly. An optional checking of the Access Rights for accessing the resource and the syntax of the Request message can be performed prior to forwarding the Request. The Intermediate CSE shall forward the request to the Hosting CSE. An optional checking of the Access Rights and the syntax of the Request message can be performed prior to forwarding the Request. Hosting CSE shall check the Access Rights for accessing the resource and depending on the expected result content respond with a Success or Failure Response, or not at all. | Figure 8.2.2-3 (Editor's Note-2) |
| Editor's Note-1: One-Hop case could potentially include the CSE-to-CSE communication also. The need for such procedures is FFS. Editor's Note-2: The multi-hop procedures address the scenario when the target is on a specific remote CSE. How a flow will work when the target is distributed on multiple remote CSEs is FFS. |

Figure 8.2.2-1: Originator accesses a resource on the Local CSE (No Hops)

Figure 8.2.2-2: AE accesses a resource at the Hosting CSE (One Hop)

Figure 8.2.2-3: Originator accesses a resource at the Hosting CSE (Multi Hops)

************************* END OF CHANGE 19  *************************

************************ START OF CHANGE 20  ************************

8.2.3.3	Asynchronous Case

In the asynchronous case, it is assumed that the Originator of a Request is actually able to receive notification messages, i.e. the Local CSE could send an unsolicited message to the Originator at an arbitrary time to send the result to a notification target. The possible mechanisms how the notification then reaches the Originator are the same as in the case of a notification after a subscription.

In that case the information flow depicted in Figure 8.2.3.3-1 is applicable. In this case it is assumed that the Originator of the Request provided a reference – notificationReference – for notification when the result of the requested operation is available.

Equivalent information flows are valid also for cases where the target resource of the requested operation is hosted on the Local CSE. From an Originator’s perspective there is no difference as the later notification of the result of a requested operation would always be an exchange of request/response messages between the Originator and the Local CSE using reference to the original Request.

Figure 8.2.3.3-2 Non-blocking access to resource in notification mode 
(Hosting CSE not equal to Local CSE), Originator provided reference for notification.

************************* END OF CHANGE 20  *************************

************************ START OF CHANGE 21  ************************

# 9	Resource Management

All entities in the oneM2M System, such as AEs, CSEs, "data", etc., are represented as "resources". A "resource structure" is specified as a representation of the "resources". Such "resources" are uniquely addressable. Procedures for accessing such resources are also specified.

## 9.1	General Principles

The following are the general principles for the design of the resource model.

The "type" of each resource shall be specified. New resource types shall be supported as the need for them is identified.

The root of the resource structure in a CSE shall be assigned an absolute address. See section 9.3.1 for additional information.

The resource structure shall be keptsimple. In particular:

<AE> Resources belonging to the local CSE shall be located directly under the <CSEBase> resource.

<accessControlPolicy> Resources belonging to the local CSE shall be located either directly under the <CSEBase> resource, or under an <AE> resource.

<group> resources belonging to the local CSE shall be located either directly under the <CSEBase> resource, or under an <AE> resource.

<remoteCSE> resources representing a remote CSE shall be located directly under the base <CSEBase> resource.

<container> Resources belonging to the local CSE shall be located either under the <CSEBase> resource or, or under an <AE> resource, or under another <container> resource.

Editor's Note: These above stated resource types needs to be validated as for clause 9.6.

Editor’s note: This section may need fixing due to inconsistency.

Editor’s note: local CSE terminology needs discussing.

The attributes for all resource type shall be specified.

Each resource type can have multiple instances.

Editors note: All the highlighted text  (in magenta) shall be removed once some figures are available (as per ARC#2014-101R02)

All resource and associated attributes shall be uniquely addressable via their associated Universal Resource Identifiers (URI), consisting of:

a structured URI based on the chain of child-parent relations;

a flat URI made of a unique identifier addressable via the base root.

Editor's Note: Contribution #0505R1 already address the fact that URI is not used in a proper manner in the TS. However the term structured and flat URI still use the term URI. Detailed definition on how to do addressing in oneM2M still needs to be drafted. Alignment of the proper terminology in the TS is needed.

Editor's Note: how the flat URI can be distinguished from the structured URI is for FFS.

Editor's Note: if there is a need to provide both structured URI or flat URI of a resource if for FFS.

Examples:

Root example "myCSE" (well known, common to structured and flat).

EXAMPLE 1:	The following two examples address the same resource:

//myCSE/123(structured).

//myCSE/123 (flat).

EXAMPLE 2:	The following two examples address the same resource:

//myCSE/myApplication/987 (structured).

//myCSE/234 (flat).

EXAMPLE 3:	The following two examples address the same resource

//myCSE//myContainer (structured).

//myCSE/mC (flat).

The flat URI is always stored in the parent attribute, that is a mandatory attribute.

In case of structured URI, the relationship parent-child and vice-versa is determined in the structured URI. When created via the flat URI, the parent child-relation is determined by the parentID attribute.

This, however, does not imply any specific storage structure for the <container> resource. The structure of a <container> resource is subject to implementations.

Parts (or all) of the URIs may be replaced with pseudonym (or shorten) URIs.

Both structured and flat URIs shall be supported simultaneously over Mcc, and Mca for IN-CSE and MN-CSE

Both structured and flat URIs should be supported simultaneously over Mcc, and Mca for ASN-CSE. For example, the structured URI can be supported for CREATE while both URI types can be supported for other operations (i.e. RETRIEVE, UPDATE and DELETE).

************************* END OF CHANGE 21  *************************

************************ START OF CHANGE 22  ************************

## 9.5	Resource Specification Guidelines

The following guidelines shall be used for the specification of resources.

Resources shall be specified by a tabular notation and the associated graphical representation as follows:

- The resources shall be specified in association with a CSE. The resources are the representation in the CSE of the components and elements within the M2M System. Other CSEs, AEs, application data representing sensors, commands, etc. are known to the CSE by means of their resource representation.

Resource: is a uniquely addressable entity in the RESTful architecture. A resource shall be transferred and manipulated using the verbs, such as those specified in section 8.1.

************************* END OF CHANGE 22  *************************

************************ START OF CHANGE 23  ************************

## 9.6	Specified Resource Types

Table 9.6-1 introduces the defined resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

- Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Permissions for entities’ access modes | subscription | AE, remoteCSE | 9.6.2 |
| AE | Represents information about an AE | subscription, container, group, accessControlPolicy, software, commCapabilities | remoteCSE | 9.6.5 |
| cmdhBuffer |  |  |  | 9.6.30 |
| cmdhDefaults |  |  |  | 9.6.24 |
| cmdhEcDefParamValues |  |  |  | 9.6.26 |
| cmdhDefEcValue |  |  |  | 9.6.25 |
| cmdhLimits |  |  |  | 9.6.27 |
| cmdhNetworkAccessRules |  |  |  | 9.6.28 |
| cmdhNwAccessRule |  |  |  | 9.6.29 |
| cmdhPolicy |  |  |  | 9.6.23 |
| container | Shares data instances among entities | container, instance, subscription, | AE, container, remoteCSE | 9.6.6 |
| CSEBase |  |  |  | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | None documented | None documented | 9.6.11 |
| eventConfig |  |  |  | 9.6.32 |
| execInstance | Represents a successful instance of mgmtCmd | None documented | ?? | 9.6.18 |
| group | Represents a group of resources | members | AE, remoteCSE | 9.6.13 |
| instance | Data instance in a container | None documented | container | 9.6.7 |
| locationPolicy | Obtains/manages geographical location | None documented | None documented | 9.6.10 |
| members | Virtual resource target for group requests | None documented | group | 9.6.14 |
| mgmtCmd | Method to execute management procedures / model commands and RPCs for existing protocols | execInstance | None documented | 9.6.17 |
| mgmtObj | Represents individual management functions | parameters | remoteCSE | 9.6.15 |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | None documented | None documented | 9.6.20 |
| node | Represents specific Node information | schedule, others | AE(in ADN) | 9.6.19 |
| nodeInfo |  |  |  | 9.6.21 |
| parameters | Parameters/attributes for management purposes | parameters | mgmtObj, parameters | 9.6.16 |
| pollingChannel |  |  |  | 9.6.22 |
| remoteCSE | Represents a remote CSE registered to the local CSE | AE, container, group, accessControlPolicy, subscription, mgmtObj | None documented | 9.6.4 |
| request | Expresses/access context of an issued Request | None documented | None documented | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | None documented | node, subscription | 9.6.39 |
| statsCollect |  |  |  | 9.6.33 |
| statsConfig |  |  |  | 9.6.31 |
| subscription | Information of subscribed-to resources | schedule | accessControlPolicy, AE, container, group, remoteCSE | 9.6.8 |

Editor’s Note: This Table was based upon revision 0.3.2 and may be missing information from subsequent agreed contributions. It is expected to be updated as we further define resources. Cells marked “None Documented” indicate the status of 0.3.2, if no addition is needed to these cells then they should be marked “None” when this Table is finalised.

### 9.6.1	Common Attributes

Many of the attributes of the resources described in the present document are common. Such attributes are described here once in order to avoid duplicating the description for every resource that contains it.

Attributes that are only used in one or two resource types are described only in the clause for that resource type.

In all tables representing resource attributes, each attribute name is followed by its "short name" in brackets that shall be used in resource representations to be transferred across reference points.

# Table 9.6.1-1: Common Attributes

| Common Attribute | Description |
| --- | --- |
| resourceType (rT) | Resource Type. This WO resourceType attribute stores <in a two capital letters token> the information useful for procedure processing, e.g. CO for <container>, CI for <instance>. |
| parentID (pID) | The identifier identifies the parent resource. Editor's Note: The adoption of a URI format is still to be confirmed. |
| accessControlPolicyID (aRI) | The URI of an <accessControlPolicy> resource. The permissions defined in the <accessControlPolicy> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g. Retrieve, Update, Delete, etc.). If a resource type does not have an accessControlPolicyID attribute definition, then the accessControlPolicy for resources of that type are governed in a different way, for example, the accessControlPolicy associated with the parent may apply to a child resource that does not have an accessControlPolicyID attribute definition, or the permissions for access are fixed. Refer to the corresponding procedures to see how permissions are handled in such cases. If a resource type does have an accessControlPolicyID attribute definition, but the (optional) accessControlPolicyID attribute is not set, or it is set to a value that does not correspond to a valid, existing <accessControlPolicy> resource, or it refers to an <accessControlPolicy> resource that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access permissions shall apply. The system default access permissions grant all permissions (i.e. the full set of permissionsFlags) to the following permission holders depending on the prefix of URI of the resource.: << Editor's Note: what is the list of permission holders>> |
| creationTime (cT) | Time/date of creation of the resource. |
| expirationTime (eT) | Time/date after which the resource will be deleted by the hosting CSE. This attribute can be provided by the Originator, and in such a case it will be regarded as a hint to the hosting CSE on the lifetime of the resource. The hosting CSE can however decide on the real expirationTime. If the hosting CSE decides to change the expirationTime attribute value, this is communicated back to the Originator. The lifetime of the resource can be extended by providing a new value for this attribute in an UPDATE verb. Or by deleting the attribute value, e.g. by not providing the attribute when doing a full UPDATE, in which case the hosting CSE can decide on a new value. |
| lastModifiedTime (lMT) | Last modification time/date of the resource. |
| versionTag (vT) | An incremental counter of modification on the resource. When a resource is created, this counter is set to 0, and it will be incremented on every modification of the resource. NOTE: In order to enable detection of overflow, the counter needs to be capable of expressing sufficiently long numbers. . |
| labels(lBs) | Tokens used as keys for discovering resources. |
| creator (cr) | The AE-ID or CSE-ID of the entity which created the resource |
| link (ln) | This attribute shall be present only for the announced resource. This attribute shall provide the URI to the original resource. |
| announceTo (aT) | This attributes shall be present for the announceable original resource only. This attribute maintains the list of URIs to the announced resources. Updates on this attribute will trigger new resource announcement or de-announcement. In case of new resource announcement, either the exact URI to the announced resource that is to be created can be provided, or the CSE-ID of the remote CSE can be provided. This means the original resource-hosting CSE will decide the exact location of the announced resource in the remote CSE identified by the CSE-ID. |
| announcedAttribute (aA) | This attributes shall be present for the announceable original resource only. This attribute maintains the list of the announced attributes in the original resource. Updates on this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |

Editor's Note:  The usage of creator (cr) attribute is FFS.

Editor's Note: The following attributes are FFS depending on resource structure discussions:

child: resources with child relation with the considered resource

parent: resources with parent relation with the considered resource

************************* END OF CHANGE 23  *************************

************************ START OF CHANGE 24  ************************

#### 9.6.2.1	originatorPrivileges

The following originator privilege types shall be considered for access control policy check.

- Table 9.6.2.1-1: originatorPrivileges types

| Name | Description |
| --- | --- |
| Domain | FQDN domain |
| originator identifier | CSE-ID or idea-ID which represent a originator identity |
| Token | Access token usually provided as query parameter |
| All | All originators |
| Role | A role name associated with the URL the a Service Subscription resource where such role is defined |

************************* END OF CHANGE 24  *************************

************************ START OF CHANGE 25  ************************

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.3-1 (0 indicates the optionality of the child resource).

- Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See section 9.6.4 |
| [variable] | <node> | 1 | See section 9.6.19 |
| [variable] | <AE> | 0..n | See section 9.6.5 |
| [variable] | <container> | 0..n | See section 9.6.6 |
| [variable] | <group> | 0..n | See section 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See section 9.6.2 |
| [variable] | <subscription> | 0..n | See section 9.6.8 |
| [variable] | <mgmtObj> | 0..n | See section 9.6.15 |
| [Variable] | <mgmtCmd> | 0..n | See section 9.6.17 |
| [Variable] | <locationPolicy> | 0..n | See section 9.6.10 |

Editor’s Note: this list should be updated. Which resource types are added is FFS.

Editor’s Note: how to extend functionality is FFS.

The <CSEBase> resource shall contain the attributes described in Table 9.6.3-2.

- Table 9.6.3-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aRI) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType (sRT) | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in section 9.2 |
| pointOfAccess (poA) | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <AE> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. |

************************* END OF CHANGE 25  *************************

************************ START OF CHANGE 26  ************************

### 9.6.4	Resource Type remoteCSE

A <remoteCSE> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCSE> resource in the registering CSE's <CSEBase>.

For example, when CSE1 registers with CSE2, there will be two <remoteCSE> resources created: one in CSE1 <CSEBase1>/<remoteCSE2> and one in CSE2 <CSEBase2>/<remoteCSE1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCSE2> is only local to CSE1 and is for its internal use.

Figure 9.6.4-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.4-1 (0 indicates the optionality of the child resource).

# Table 9.6.4-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <AE> | 0..n | See clause 9.6.5 | <AEAnnc> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <mgmtObj> | 0..n | See clause 9.6.15 | <mgmtObjAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. If requestReachability is FALSE, the CSE that created this <remoteCSE> should create a <pollingChannel> resource and perform long polling. | ?? |
| [variable] | <node> | 0..1 | See section 9.6.19. This child resource contains the node specific information only when the information represented by this resource is from a node of type ASN or MN. | ?? |

The <remoteCSE> resource shall contain the attributes described in Table 9.6.4-2.

# Table 9.6.4-2: Attributes of <remoteCSE> resource

| Attribute Name of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <remoteCSEAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. | OP |
| pointOfAccess (poA) | 0..n | RW | For request-reachable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not request-reachable. | OP |
| CSEBase (bRt) | 1 | WO | The URI of the CSEBase of the original CSE represented by remote CSE. | OP |
| CSE-ID | 1 | WO | The globally unique CSE identifier. | OP |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. | ?? |
| requestReachability | 1 | RW | If the CSE that created this <remoteCSE> can receive a request from other AE/CSE(s), this attribute is set to “TRUE” otherwise “FALSE”. NOTE: Even if this attribute is set to “FALSE”, it does not mean it AE/CSE is always unreachable by all entities. E.g., the requesting AE/CSE is behind the same NAT, so it can communicate within the same NAT. | ?? |

<remoteCSE> and announced <remoteCSE> shall have different resourceType coding.

Editor's Note on CSE-ID: an alignment between CSE-ID and CSEBase is needed.

Editor's Note on CSEBase: the alignment with naming convention proposed for inter-M2M service provider is needed.

Editor's Note on child resources: child resources of <remoteCse> resource can accommodate listed resources and their announced versions.

************************* END OF CHANGE 26  *************************

************************ START OF CHANGE 27  ************************

### 9.6.5	Resource Type AE

The <AE> resource represents information about an Application Entity known to a given Common Services Entity.

Figure 9.6.5-1: Structure of <AE> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.5-1 (0 indicates the optionality of the child resource)

# Table 9.6.5-1: Child resources of <AE> resource

| Child Resource Name of <AE> | Child Resource Type | Multiplicity | Description | <AEAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| software | <mgmtObj> | 1..n | See clause 9.6.15 for <mgmtObj>. This resource represents the software component (or components, if the multiplicity is greater than 1) that compose the AE. This mgmtObj shall have at least the following <parameters> child resources of its "parameters" subresource: name (multiplicity 1) version (multiplicity 1) state (multiplicity 1) | <mgmtObjAnnc> |
| [variable] | <commCapabilities> | 1..n | Resource <commCapabilities> needs to be defined. This resource describes the communication capabilities (essentially the protocols) supported and used by the corresponding Application Entity over the Mca reference point to this CSE. | <commCapabilitiesAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. When the local CSE of this AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. | ?? |

The <AE> resource shall contain the attributes described in Table 9.6.5-2.

# Table 9.6.5-2: Attributes of <AE> resource

| Attribute Name of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <AEAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (e.g. "HeatingMonitoring") | OP |
| App-ID | 1 | RO | Application Identifier | OP |
| AE-ID | 1 | RO | Application Entity Identifier which created this resource. | OP |
| pointOfAccess | 0..n | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g., IP address, FQDN, URI). This attribute shall be accessible only by the AE and the hosting CSE. | ?? |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the AE; to be passed to the AE | OP |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <AE> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. | ?? |

Editor's Note: Cardinality of pointOfAccess attribute (0..n) needs to be investigated for all its occurrences.

************************* END OF CHANGE 27  *************************

************************ START OF CHANGE 28  ************************

### 9.6.12	Resource Type request

The use of this resource type is optional depending on the configuration.

When a CSE is requested to initiate an operation for which the result should be available to the Originator by reference ('rt' information of the request set to 'Acknowledgement'), the local CSE which received the Request directly from the Originator may need to provide a reference back to the Originator so that the Originator can access attributes of the Request at a later time - for instance in order to retrieve the result of an operation that was taking a longer time. The Originator (or any other authorized entity depending on access rights) can access the request status and the requested operation result through it.

The <request> resource may get deleted by the CSE that is hosting it:

when the result of the requested operation (if any result was requested at all) has been sent back to the Originator (either by notification to the Originator or by retrieval initiated by the Originator);

when the expiration time of the <request> resource is reached;

at any other time -  depending on local settings in the CSE that hosts the <request> resource.

Editor's Note: The exact way how to define that setting (e.g. via DM) is FFS.

For the purpose of providing a standardized structure for expressing and accessing the context of a previously issued Request, the resource type request is defined.

Figure 9.6.12-1: Structure of <request> resource
(only resource specific attributes are shown)

The resource <request> shall contain the attributes according to their multiplicity shown in Table 9.6.12-1.

# Table 9.6.12-1: Attributes of <request> resource

| Attribute Name of <request> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime (et) | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| versionTag (vT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| operation | 1 | RO | The operation requested by the Originator, e.g. modifying the content of a container, registering an AE. |
| target | 1 | RO | The address or the target resource for the requested operation. |
| originator | 1 | RO | The originating entity for the request. |
| metaInformation | 1 | RO | Meta information about the request. The content of this attribute is equivalent to the "mi" information in clause 8.1. |
| content | 1 | RO | Contains the content that is supposed to be sent to the target resource. |
| requestStatus | 1 | RO | Contains information on the current status of the Request, e.g. "accepted and pending". |
| operationResult | 1 | RO | Contains information on the result of the requested action, e.g. "Resource created with URI: XXX". |

Creation of a <request> resource can only be done on a local CSE implicitly by an AE issuing a generic CRUD request for any other resource type to the Local CSE. A Local CSE cannot accept requests to create a <request> resource directly.

Retrieving of <request> resources or attributes of a <request> resource is allowed for authorized entities.

Update of a <request> resource can only be done by the CSE that hosts the <request> resource or by CSEs that provide operation results pertaining to the request (for instance when the result of an operation requested for a remote CSE becomes available).

Deletion of a <request> resource is possible by authorized entities. If the execution of the request was still pending at the time of deletion, the hosting CSE should to stop any further attempts to execute the request.

************************* END OF CHANGE 28  *************************

************************ START OF CHANGE 29  ************************

### 9.6.13	Resource Type group

The <group> resource represents a group of resources of the same or mixed types. The <group> resource can be used to do bulk manipulations on the resources represented by the members. The <group> resource contains an attribute that represents the members of the group and a virtual resource (the members) that allows verbs to be applied to the resources represented by those members.

When used as one of the permission holders in an <accessControlPolicy> resource, the group can be used to grant a collection of AEs (represented by <AE> resources) or CSEs (represented by <remoteCSE> resources) permissions for accessing (Creating children, Retrieving, etc.) a resource.

************************* END OF CHANGE 29  *************************

************************ START OF CHANGE 30  ************************

### 9.6.19	Resource Type node

The <node> resource represents specific information of a M2M Node that can be utilized by other oneM2M operations. For example, the CMDH CSF can determine when the CSE sends a request message to the target CSE based on the target CSE's reachability schedule. This resource type mainly contains the properties of an M2M Node such as reachability schedule, context information (e.g. memory and storage) and network topology.

This node specific information stored in this resource type such as memory and storage can be obtained either by the existing device management technologies (OMA DM, BBF TR-069 [i.12]) or any other way (e.g. through JNI (Java Native Interface)). Since <mgmtObj> resource type represents the management functions including both ways, the types of sub-resources are <mgmtObj> resource type.

The location of <node> resource can be differentiated according to the type of node.

ASN: under <CSEBase> of the ASN-CSE.

ADN: under <CSEBase> resource of the local CSE. The <AE> resource regarding the ADN shall have the proper link (URI) to the <node> resource that contain node specific information of the ADN.

MN: under <CSEBase> of the MN CSE.

************************* END OF CHANGE 30  *************************

************************ START OF CHANGE 31  ************************

### 9.6.20	Resource Type m2mServiceSubscription

This resource represents an M2M Service Subscription. It is used to represent all data pertaining to the M2M Service Subscription (the technical part of the contract between an M2M Application Service Provider and an M2M Service Provider).

************************* END OF CHANGE 31  *************************

************************ START OF CHANGE 32  ************************

### 9.6.23	Resource Type cmdhPolicy

The <cmdhPolicy> resource type represents a set of rules defining which CMDH parameters will be used by default when a request issued by a local originator (eg. locally registered AE or another CSF inside the local CSE) contains the “ec” parameter but not all other CMDH parameters.

One or several resources of type <cmdhPolicy> may be linked as child resources of the local <CSEBase> resource, thus defining a set of CMDH policies applicable whenever this local hosting CSE receives requests.

In addition, one or several resources of type <cmdhPolicy> may be linked as child resources of other resources of type <AE> or <remoteCSE>, thus overriding the default set of policies for the relevant locally registered Application Entities or remote CSEs.

************************* END OF CHANGE 32 *************************

************************ START OF CHANGE 33  ************************

### 9.6.25	Resource Type cmdhDefEcValue

The <cmdhDefEcValue> is used to define a value for the ec (event category) parameter of an incoming request when it is not defined.

Upon receiving a request, the CSE will go through all the <cmdhDefEcValue> resources (in the order of their "order" attribute), check the <requestOrigin> and any present<requestContext> and <requestCharacteristics> sub-resources to see if they match (see description of matching), and if they all do, assign the value stored in the defEcValue attribute to the ec parameter.

Figure 9.6.25-1: Structure of <cmdhDefEcValue> resource 
(only resource specific attributes are shown)

The resource <cmdhEcDefEcValue> shall contain attributes according to their multiplicity shown in Table 9.6.25-1.  A value of "0" for multiplicity indicates the attribute is optional.

- Table 9.6.25-1: Attributes of <cmdhDefEcValue> resource

| Attribute Name of <cmdhDefEcValue> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 |
| expirationTime (eT) | 1 | RW | See section 9.6.1 |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 |
| creationTime (cT) | 1 | RO | See section 9.6.1 |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 |
| order(or) | 1 | RW | The index indicating in which order the cmdhDefEcValue resource will be treated by the CSE to determine a value for the ec parameter |
| defEcValue (dev) | 1 | RW | The actual value to use for the ec parameter if the conditions expressed in the requestOrigin, requestContext and requestCharacteristics all match. If none of these attributes are defined, then the defEcValue shall be applied. |
| requestOrigin (rorig) | 1 | RW | The requestOrigin attribute is a list of zero or more local AE-IDs, App-IDs, or the strings ‘localAE’ or ‘thisCSE’. When an AE-ID appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec if the request was issued by that specific Application Entity. When an App-ID appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec if the request was issued by any AE with that App-ID unless covered by another <cmdhDefEcValue> resource with a requestOrigin attribute containing its specific AE-ID.. When the string ‘localAE’ appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec for requests issued by all local AEs unless covered by another <cmdhDefEcValue> resource with a requestOrigin attribute containing the specfifc AE-ID or App-ID of the originator of the request. When the string ‘thjsCSE’ appears in the requestOrigin attribute, the default ec value defined inside the defEcValue attribute is applicable for the ec for requests that are originating from within the local CSE . The hosting CSE shall contain at least one <cmdhDefEcValue> resource that contains ‘localAE’ in the ‘requestOrigin’ attribute and has no ‘requestContext’ and no ‘requestCharacteristics’ attribute. The hosting CSE shall contain at least one <cmdhDefEcValue> resource that contains ‘thisCSE’ in the ‘requestOrigin’ attribute and has no ‘contextCondtion’ and no ‘requestCharacteristics’ attribute. |
| requestContext (rctxt) | 0..1 | RW | The requestContext attribute represents the Dynamic Context condition under which the default ec value defined inside the defEcValue attribute is applicable for the ec. This may refer to conditions such as current battery status, or current network signal strength. |
| requestContextNotification | 0..1 | RW | True or false. If set to true, then this CSE will establish a subscription to the dynamic context information defined in the requestContext attribute as well as a subscription to this <cmdhDefEcValue> resource for all AEs corresponding to the AE-ID or an App-ID appearing in the requestOrigin attribute. Both, changes in the context information and changes to the <cmdhDefEcValue> resource will be notified to the respective AEs. The subscription(s) is/are established when the <cmdhDefEcValue> is provisioned or updated. |
| requestCharacteristics | 0..1 | RW | The requestCharacteristics attribute represents conditions pertaining to the request itself, such as the requested response type (rt attribute) or other attributes of the request. |

************************* END OF CHANGE 33  *************************

************************ START OF CHANGE 34  ************************

### 9.6.27	Resource Type cmdhLimits

The <cmdhLimits> resource type is used to define limits for CMDH related parameter values used in requests issued by Originators (registered AEs or functions inside the CSE itself). When an incoming request is processed that does not comply with the limits defined by the corresponding <cmdhLimits> resource, the request shall be rejected by the CSE.

Figure 9.6.27-.1: Structure of <cmdhLimits> resource 
(only resource specific attributes are shown)

The resource <cmdhLimits> shall contain attributes according to their multiplicity shown in Table 9.6.27-1.  A value of "0" for multiplicity indicates the attribute is optional.

- Table 9.6.27-1: Attributes of <cmdhLimits> resource

| Attribute Name of <cmdhLimits> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aR) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| order(or) | 1 | RW | The index indicating in which order the cmdhLimits resource will be treated by the CSE to determine a value for the limit parameters. |
| requestOrigin(rorig) | 1 | RW | The requestOrigin attribute is a list of zero or more local AE-IDs, App-IDs, or the strings ‘localAE’ or ‘thisCSE’. When an AE-ID appears in the requestOrigin attribute, the CMDH parameter limits defined inside <cmdhLimits> child resources are applicable for requests issued by that specific Application Instance. When an AE appears in the requestOrigin attribute, the CMDH parameter limits defined inside <cmdhLimits> child resources are applicable for requests issued by any instance of the Application with that App-ID unless already covered by another <cmdhLimits> resource with a requestOrigin attribute containing its specific AE-ID. When the string ‘localAE’ appears in the requestOrigin attribute, CMDH parameter limits defined inside <cmdhLimits> child resources are applicable for all local AEs unless covered by another <cmdhLimits> resource with a requestOrigin attribute containing the specific App-Inst-ID or App-ID of the originator of the request. When the string ‘thisCSE’ appears in the requestOrigin attribute, CMDH parameter limits defined inside <cmdhLimits> resources are applicable for all requests that are originating from within the hosting CSE. The hosting CSE shall contain at least one <cmdhLimits> resource that contains ‘localAE’ in the ‘requestOrigin’ attribute and has no ‘contextCondtion’ and no ‘requestCharacteristics’ attribute. The hosting CSE shall contain at least one <cmdhLimits> resource that contains ‘thisCSE’ in the ‘requestOrigin’ attribute and has no ‘requestContext’ and no ‘requestCharacteristics’ attribute. |
| requestContext (rctxt) | 0..1 | RW | The requestContext attribute represents the Dynamic Context condition under which CMDH parameter limits defined inside the <cmdhLimits> resource is applicable. This may refer to conditions such as current battery status, or current network signal strength. |
| requestContextNotification | 0..1 | RW | True or false. If set to true, then this CSE will establish a subscription to the dynamic context information defined in the requestContext attribute as well as a subscription to this <cmdhLimits> resource for all AEs corresponding to the AE-ID or an App-ID appearing in the requestOrigin attribute. Both, changes in the context information and changes to the <cmdhLimits> resource will be notified to the respective AEs. The subscription(s) is/are established when the <cmdhLimits> is provisioned or updated |
| requestCharacteristics | 0..1 | RW | The requestCharacteristics attribute represents conditions pertaining to the request itself, such as the requested response type (rt attribute) or other attributes of the request. |
| limitsEventCategory (lEC) | 1 | RW | Allowed values for the event category parameter (‘ec’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsRequestExpTime (lRqET) | 1 | RW | Range of allowed values for the request expiration time parameter (‘rqet’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsResultExpTime (lRsET) | 1 | RW | Range of allowed values for the result expiration time parameter (‘rset’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsOpExecTime (lOET) | 1 | RW | Range of allowed values for the operational execution time parameter(‘oet’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsRespPersistence (IRP) | 1 | RW | Range of allowed values for the response persistence parameter (‘rp’) in a request of any of the originators indicated in the requestOrigin attribute. |
| limitsDelAggregation(lDA) | 1 | RW | List of allowed values for the delivery aggregation parameter (‘da’) in a request of any of the originators indicated in the requestOrigin attribute. |

************************* END OF CHANGE 34  *************************

************************ START OF CHANGE 35  ************************

### 10.1.1	CREATE (C)

The CREATE procedure shall be used by an Originator CSE or AE to create a resource on a Receiver CSE (also called the hosting CSE). The procedure will be divided in two, since there is a need to distinguish between registration related creation and non-registration related procedures.

The registration related procedure is only applicable for the following resource types:

<AE>, and

<remoteCSE>

While non-registration related procedure is applicable for all other resource types described in section 9.6.

************************* END OF CHANGE 35  *************************

************************ START OF CHANGE 36  ************************

#### 10.1.1.2	 Registration related CREATE procedure

This section described the CREATE procedure for <remoteCSE> and <AE> resource type.

##### 10.1.1.2.1	 CSE Registration procedure

The procedure for CSE registration follows the procedure described in section 10.1.1.1, but with some exceptions. Below is the detailed description on how to perform the CSE registration and which part of the procedure deviates from the one described in section 10.1.1.1.

The registration procedure requires the creation of two resources (a <remoteCSE> on the Receiver CSE and a <remoteCSE> on the Originator CSE) rather than one resource. The registration procedure is always initiated by a CSE in the field domain and follows the restrictions described in section 6.2.9.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall allow the creation of the <remoteCSE> resource since at registration time there are no appropriate privileges associated with the AE yet.

************************* END OF CHANGE 36  *************************

************************ START OF CHANGE 37  ************************

##### 10.1.1.2.2	 Application Entity Registration procedure

The procedure for AE registration follows the procedure described in section 10.1.1.1 with the following exception:

Receiver, once the Originator has been successfully authorized (as described in section XXX), the Receiver shall allow the creation of the <AE> resource according to the Access Right. The receiver shall use, if present, the suggested name from the information parameter nm in the request. If the suggested name of the resource cannot be use (i.e a resource with that name already exists) the Receiver shall reject the CREATE request. If the request does not provide the optional nm, then the Receiver shall create the resource and assign a name to it.

Editor’s Note: which accessControlPolicy needs to be used is FFS.

Step 001: The Originator shall send the following information in the CREATE Request message:

fr: credentials of the Originator, as defined in section XXX

Editor’s Note: more investigation is needed in WG4 for clarify what will be the value of fr and in which section it will be described.

Step 002: for the <AE> resource the Receiver cannot perform the action described in the first bullet of 10.1.1.1:

All the other parameters of the request and the following steps do not deviate from section 10.1.1.1.

************************* END OF CHANGE 37  *************************

************************ START OF CHANGE 38 ************************

## 10.2	Resource Type-Specific Procedures

### 10.2.1	<AE> Resource

#### 10.2.1.1	Create <AE>, aka Application Registration

This flow is used for creating an <AE> resource. This operation is part of the registration procedure for AEs on the Local CSE (which is also the Hosting SCE), as described in section 10.1.1.2.2

Originator: The Originator shall be an Application Entity. The Originator may suggest in the request the AE-ID.

Receiver: Once the Originator has been successfully authorized (as described in section XXX), the Receiver (which is also the Hosting CSE) shall grant the Request after successful validation of the Request.

Editor’s Note: Currently there is no section with specific text on the authentication/access control from SEC.

Editor’s note: It is not clear if the case of non-authenticated AE can register to a local CSE, but with a very limited access. This case is FFS.

Editor’s note: the relation with the accessControlPolicy is for FFS.

Table 10.2.1.1-1 <AE> CREATE flow

| CREATE: Description |
| --- |
| Pre-Conditions | The Originating AE has to be successfully authenticated and the access to the Receiver has been granted |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: fr: Credentials of the Originator, as defined in section XXX Editor’s Note: More investigation is needed in WG4 to clarify what will be the value of fr and in which section it will be described. nm: The name of the <AE> resource is optional. cn: The resource content shall provide the information as defined in section 9.6.18. The following attributes from section 9.6.18 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the AE resource as defined in 9.6.1 “name” “App-ID” The following attributes from section 9.6.18 are optional for the request: “expirationTime” “Labels” “AE-ID” “ontologyRef” Editor’s Note: fix Table 7 for optional App-Inst-ID |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1) |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: URI of the created <AE> resource, according to section 10.1.1 |
| Post-Conditions | None |
| Exceptions | All exception described in the basic procedure (section 10.1.1) are applicable. |

#### 10.2.1.2	Retrieve <AE>

This flow is used for retrieving the representation of the <AE> resource with its attributes.

Originator: The Originator can be an Application Entity or a CSE.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall retrieve the <AE> resource.

- Table 10.2.1.2-1 <AE> RETRIEVE flow

| RETRIEVE: Description |
| --- |
| Pre-Conditions | The targeted <AE> has been created (as part of the registration) |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: void |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.2) |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: attributes of the <AE> resource as defined in section 9.6.18. |
| Post-Conditions | No changes on the resource as consequence of the RETRIEVE operation |
| Exceptions | All exception described in the basic procedure (section 10.1.2) are applicable. |

#### 10.2.1.3	Update <AE>

This flow is used for updating the attributes and the actual data of an <AE> resource.

Originator: The Originator shall be an Application Entity.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), , the Receiver shall update the <AE> resource.

- Table 10.2.1.3-1 <AE> UPDATE flow

| UPDATE: Description |
| --- |
| Pre-Conditions | The targeted <AE> has been created (as part of the registration) |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: attributes of the <AE> resource as defined in 9.6.18 which need be updated, with the exception of the following that cannot be modified: “lastModifiedTime” ”name”, “App-ID" “AE-ID”. |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.3) |
| Information on Response message | No change from the basic procedure (section 10.1.3) |
| Post-Conditions | The <AE> resource should contain the new information |
| Exceptions | All exception described in the basic procedure (section 10.1.3) are applicable. |

#### 10.2.1.4	Delete <AE>, aka De-Register

This flow is used for de-registering and deleting the <AE> resource with all related information.

Originator: The Originator can be an Application Entity or a CSE.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall delete the <application>.

- Table 10.2.1.4-1 <AE> DELETE flow

| DELETE: Description |
| --- |
| Pre-Conditions | The targeted <AE> has been created (as part of the registration) |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table. |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.4).. |
| Information on Response message | No change from the basic procedure (section 10.1.4) |
| Post-Conditions | The targeted resource and all the children resources shall not exist anymore. Also all the related credential are deleted. Editor’s note: if and how credentials are cleaned is FFS, in scope of WG4. |
| Exceptions | All exception described in the basic procedure (section 10.1.4) are applicable. |

************************* END OF CHANGE 38  *************************

************************ START OF CHANGE 39  ************************

#### 10.2.4.3	Retrieve <delivery>

This procedure shall be used for requesting a CSE to provide information on a previously created <delivery> resource which represents delivery of data to a target CSE.

Originator: Originator can be a CSE or an AE.

Receiver: The Receiver shall provide the content of the addressed <delivery> resource or the addressed attributes thereof.

************************* END OF CHANGE 39  *************************

************************ START OF CHANGE 40  ************************

#### 10.2.4.4	Update <delivery>

This procedure shall be used for requesting a CSE to update information on a previously created <delivery> resource which represents a pending delivery of data to a target CSE. The update may have impact on further processing of the delivery.

Originator: Originator can be a CSE or an AE. Originator needs to be authorized to modify the addressed <delivery> resource, i.e. it needs to be authorized to change the represented delivery process.

************************* END OF CHANGE 40  *************************

************************ START OF CHANGE 41  ************************

#### 10.2.4.5	Delete <delivery>

This procedure shall be used for requesting a CSE to cancel a pending delivery of data to a target CSE or to delete the <delivery> resource of an already executed delivery.

Originator: Originator can be a CSE or an AE. Originator needs to be authorized to modify the addressed <delivery> resource, i.e. it needs to be authorized to change the represented delivery process.

Receiver: The Receiver shall remove the addressed <delivery> resource and stop the corresponding delivery process if it is still pending

************************* END OF CHANGE 41  *************************

************************ START OF CHANGE 42  ************************

#### 10.2.6.5	Delete <group>

This procedure shall be used for deleting an existing <group> resource.

Originator: The Originator shall request to delete an existing <group> type resource by using the DELETE verb. The request shall address the specific <group> resource of a Hosting CSE. The Originator may be an AE or a CSE.

Receiver: The Receiver shall check if the Originator has DELETE permission on the <group> resource. Upon successful validation, the CSE shall remove the resource from its repository and shall respond to the Originator with the appropriate responses.

************************* END OF CHANGE 42  *************************

************************ START OF CHANGE 43  ************************

#### 10.2.8.2	Create <mgmtCmd>

A CREATE request is used by an Originator to create a specific <mgmtCmd> resource in a hosting CSE.

The created <mgmtCmd> resource will be mapping a RESTful method to management commands and/or procedures which may be translated from existing management protocols (e.g. BBF TR-069 [refs]). At run-time the hosting CSE can expose the translated commands, over the Mcc reference point, to the remote entities (i.e. ASN/MN-CSE).

Originator: The Originator shall request to create a new <mgmtCmd > resource to be named as "mgmtCmd" by using a CREATE verb. The request shall address <CSEBase> resource of the hosting CSE. The request may also provide the attributes of the <mgmtCmd> resource to be created as described in clause 9.6.15 such as "cmdType".

The Originator may be:

- An AE registered to the IN-CSE.

- The local CSE on the managed entity: In this case, the local CSE transforms supported management command into the <mgmtCmd> resource representation, then requests the hosting CSE to create the corresponding <mgmtCmd> resource.

NOTE 1:	The hosting IN-CSE in the network domain may also create the <mgmtCmd> resource locally by itself. The details are out of scope. Then an AE can discover the created <mgmtCmd> and manipulate it.

NOTE 2:	The <mgmtCmd> resource may also be created in the hosting CSE by other offline provisioning means which are out of scope.

Receiver: The Receiver shall check if the Originator has the CREATE permission on the addressed <CSEBase> resource (or the parent <mgmtCmd> resource in the case of child resource creation). The hosting CSE shall also check the validity of provided attributes. Upon successful validation, a new resource with name "mgmtCmd" shall be created in the hosting CSE with the provided attributes. The hosting CSE shall maintain the mapping between the created <mgmtCmd> resource and the corresponding nonRESTful commands represented by the "cmdType" attribute of <mgmtCmd> resource. The hosting CSE shall respond to the Originator with the appropriate generic response code. It shall also provide in the Response the URL of the created new resource.

The hosting CSE shall be:

- An  IN-CSE.

# Table 10.2.8.2-1: <mgmtCmd> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | The CSE on the originating node shall first collect local management command. |
| Information on Request message | op: C fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | No change from the basic procedures |
| Information on Response message | fr: Receiver CSE-ID to: Originator AE-ID or CSE-ID cn: URI of created <mgmtCmd> resource |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the creation is not allowed, the <mgmtCmd> resource shall not be created, and a proper error code shall be returned to the originator in the Response message |

#### 10.2.8.3	Retrieve <mgmtCmd>

A RETRIEVE Request is used by an Originator to retrieve all or part information from an existing <mgmtCmd> resource on a hosting CSE. Alternatively, the Originator can request to retrieve only a specific attribute or part of an attribute.

Originator: The Originator shall request to retrieve all or part of the information from an existing <mgmtCmd> resource by using a RETRIEVE verb. The request shall address a specific "<mgmtCmd>" resource to retrieve all attributes and the references to the sub-resources of the <mgmtCmd> resource.  Alternatively, the request shall address the individual attributes of the specific "<mgmtCmd>" resource to retrieve the corresponding attribute value.

Editor's Note: We need to agree on a terminology on how to refer to a specific instance of a resource type.

The Originator may be:

- An AE.

- A CSE.

Receiver: The Receiver shall check if the Originator has the READ permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall retrieve the corresponding attributes the <mgmtCmd> resource and the references to the sub-resources from its repository and shall respond to the Originator with the appropriate generic responses.

The hosting CSE shall be:

- An IN-CSE.

# Table 10.2.8.3-1: <mgmtCmd> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to create a resource |
| Information on Request message | op: R fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | No change from the basic procedures |
| Information on Response message | No change from the basic procedures |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the retrieval is not allowed, or the specific <mgmtCmd> resource does not exist in the IN-CSE, a proper error code shall be returned to the originator |

#### 10.2.8.4	Update <mgmtCmd>

An UPDATE request is used by an Originator to update all or part information of an existing <mgmtCmd> resource on a hosting CSE with new attributes. Alternatively, the Originator can request to update only a specific attribute or part of an attribute.

Originator: The Originator shall request to update all or part information of an existing <mgmtCmd> resource by using a UPDATE verb. The request shall address a specific "<mgmtCmd>" resource of a CSE to update all attributes of the <mgmtCmd> resource with the provided new value.  Alternatively, the request shall address the individual attribute of the specific "<mgmtCmd>" resource to update the corresponding attribute with the provided new value.

The Originator may be:

- An AE.

- A CSE.

Receiver: The Receiver shall check if the Originator has the WRITE permission on the addressed <mgmtCmd> resource. The hosting CSE shall also check the validity of provided attributes if any. Upon successful validation, the hosting CSE shall overwrite the corresponding attributes of the <mgmtCmd> resource with the provided new data. The CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An IN-CSE.

# Table 10.2.8.4-1: <mgmtCmd> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to retrieve a resource |
| Information on Request message | op: U fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | No change from the basic procedures |
| Information on Response message | No change from the basic procedures |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the update is not allowed or the specific <mgmtCmd> resource (or its sub-resource) does not exist in the IN-CSE, a proper error code shall be returned to the Originator |

#### 10.2.8.5	Delete <mgmtCmd>

A DELETE request is used by the Originator to delete an existing <mgmtCmd> resource on a hosting CSE. An AE may also use this procedure to cancel all initiated <execInstance> of an <mgmtCmd> if applicable.

Originator: The Originator shall request to delete an existing <mgmtCmd> resource by using a DELETE verb. The request shall address the specific "<mgmtCmd>" resource on the hosting CSE.

The Originator may be:

- The CSE on the manageable entity: In this case, the local -CSE issues the request to the hosting CSE to hide the corresponding management command from being exposed by the <mgmtCmd> resource.

- An AE: In this case, the AE requests the hosting CSE to delete the <mgmtCmd> resource from the hosting CSE and cancel all initiated <execInstance> of an <mgmtCmd> if applicable.

NOTE 1:	The hosting CSE in the network domain may also delete an <mgmtCmd> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <mgmtCmd> resource may also be deleted in the hosting CSE by other offline provisioning means which are out of scope.

Receiver: The Receiver shall check if the Originator has the DELETE permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall remove the resource from its repository. If the Originator is an AE and there is any initiated <execInstance> under the <mgmtCmd> that can be cancelled by a corresponding management command. The hosting CSE shall also issue the management command to the remote entity to cancel those initiated <execInstance> based on existing management protocol (i.e. BBF[refs] TR-0069 [i.12]). Then the CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An IN-CSE.

# Table 10.2.8.5-1: <mgmtCmd> DELETE by ASN-CSE or MN-CSE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Before issuing a DELETE request to the IN-CSE, the originating CSE may perform cancelling of the corresponding management command locally. |
| Information on Request message | op: D fr: Originator CSE-ID. to: Receiver CSE-ID. cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | The <mgmtCmd> resource shall be deleted from the repository of the IN-CSE |
| Information on Response message | No change from the basic procedures |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the deletion is not allowed or the specific <mgmtCmd> resource does not exist in the IN-CSE, the deletion shall be failed and a proper error code shall be returned to the Originator |

# Table 10.2.8.5-2: <mgmtCmd> DELETE by an AE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Originator needs to delete the resource. |
| Information on Request message | op: D fr: Originator AE-ID to: Receiver CSE-ID cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | If there is any initiated <execInstance> under <mgmtCmd> and it is cancellable, IN-CSE shall cancel those initiated <execInstance> from the remote entity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF[refs] TR-0069 [i.12]) The <mgmtCmd> resource shall be deleted from the repository of the IN-CSE |
| Information on Response message | No change from the basic procedures |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the deletion is not allowed or the specific <mgmtCmd> resource does not exist, there is no local processing in the IN-CSE and a proper error code shall be returned to AE If the corresponding initiated commands cannot be deleted from remote entity due to some reason (e.g. not found) a response with the proper indication shall be returned to AE |

#### 10.2.8.6	Execute <mgmtCmd>

The Execute procedure is used by an originator for execution of a specific management command on a remote entity, through an existing <mgmtCmd> resource on the hosting CSE.

Originator: The Originator shall request to execute a specific management command which is represented by an existing <mgmtCmd> resource by using an UPDATE verb. The UPDATE request shall address the execEnable attribute of the <mgmtCmd> resource without any payload. Alternatively, the UPDATE request shall address the URI provided as the value of the execEnable attribute of the <mgmtCmd> resource.

After issuing the execution request, the Originator may request to retrieve the execution result or status from an <execInstance> sub-resource of the <mgmtCmd>by using a RETRIEVE method as described in clause 10.2.6.2.

The Originator shall be:

- An AE.

Receiver: The Receiver shall check if the Originator has the WRITE permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall perform command conversion and mapping, and send the converted management command over mId reference point to execute the corresponding management command with the provided arguments on the remote entity based on existing device management protocol (i.e. BBF[refs] TR-0069 [i.12]). Then the hosting CSE shall create a corresponding <execInstance> resource under <mgmtCmd> for this command execution. And the hosting CSE shall respond to the originator with the appropriate generic responses. It shall also provide in the response the URL of the created <execInstance> resource.

Upon receiving from the remote entity a management notification (i.e. BBF TR-0069 [i.12] "Inform" message) regarding the execution result or status, the hosting CSE may update the corresponding <execInstance> sub-resource locally.

The hosting CSE shall be:

- An IN-CSE.

Editor's note: The definition of Execute is to be for FFS in clause 10.1.

# Table 10.2.8.6-1: <mgmtCmd> EXECUTE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to retrieve a retrieve a resource. |
| Information on Request message | op: U. fr: Originator AE-ID or CSE-ID. to: Receiver CSE-ID. cn: <mgmtCmd>/execEnbale The UPDATE request shall address to <mgmtCmd>/execEnable without any payload. The mandatory and/or optional attributes defined in clause 9.6.15, as needed. |
| Local processing on Hosting CSE | (a) If the execution is allowed, Hosting CSE will do command conversion and mapping. (b) The Hosting CSE shall trigger existing device management procedures (i.e. BBF TR-0069 [i.12]) to execute the corresponding management command on the remote entity. (c) The Hosting CSE shall perform local processing: if Step b is successful, the IN-CSE shall create an <execInstance> resource under the triggered <mgmtCmd> to maintain status and results for this execution. |
| Information on Response message | No change from the basic procedures. |
| Post-Conditions | The following processing on the Hosting CSE is dependent on the type of the command and execution status and may occur after the Response message has been sent. (a) After the command execution is finished, the remote entity sends response including execution results to the Hosting CSE, who will store the execution results in corresponding <execInstance> resource. This step may occur any time after the Response message has been sent and might occur after step b below. (b) The AE may use normal RETRIEVE procedure to retrieve the execution results or status of an <execInstance>. (c) After receiving the RETRIEVE request from the AE, the Hosting CSE can retrieve the execution status or results on the remote entity using existing management protocol. If step d. occurs before step e, step f. may not be needed. (d) A response shall be returned to the AE. |
| Exceptions | If the execution is not allowed or the specified <mgmtCmd> resource or its attribute/sub-resource does not exist in the IN-CSE, no further processing is required in the Hosting CSE and a proper error code shall be returned to AE in the Message response. If the corresponding management command cannot be executed in remote entity due to some reason, step 004 <??> shall be skipped and a proper error code shall be returned to AE in step 005 <??>. |

#### 10.2.8.7	Cancel <execInstance>

The Cancel procedure is used by an originating AE to disable/stop/cancel an initiated management command execution on the remote entity, through an existing <execInstance> resource on the hosting CSE.

Originator: The Originator shall request to disable/stop/cancel an initiated management command execution which is represented by an existing <execInstance> resource, by using an UPDATE verb. The UPDATE request shall address the execDisable attribute without any payload.

The Originator shall be:

- An AE.

Receiver: The Receiver shall check if the Originator has the WRITE permission on the addressed <mgmtCmd> resource. Upon successful validation, the hosting CSE shall perform command conversion and mapping, then use existing management protocol (i.e. BBF TR-0069 [i.12]) to cancel the corresponding management command execution initiated on the remote entity, and the hosting CSE shall respond to the originator with the appropriate responses.

The hosting CSE shall be:

- An IN-CSE.

# Table 10.2.8.7-1: <execInstance> CANCEL

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to disable/stop/cancel an initiated management command execution on the remote entity |
| Information on Request message | op: U fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID cn: <mgmtCmd>/execInstance. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | If the cancellation is allowed, IN-CSE will do command conversion and mapping The IN-CSE shall cancel the <execInstance> from the remote entity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF TR-069) The IN-CSE shall delete the corresponding <execInstance> resource |
| Information on Response message | No change from the basic procedures |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the execution is not allowed or the specified <execInstance> resource does not exist in the IN-CSE or the <execInstance> is finished, the local processing on Hosting CSE shall be skipped and a proper error code shall be returned to AE in the Response message If the corresponding management command cannot be executed in remote entity due to some reason, the IN-CSE shall still delete the corresponding <execInstance> resource and return a Response message |

Editor's Note: The Cancel flow shall be updated based on the definition of EXEC procedure.

#### 10.2.8.8	Retrieve <execInstance>

A RETRIEVE request is used by an Originator to retrieve an existing <execInstance> resource, including individual attributes, from a hosting CSE. Alternatively, the Originator can request to retrieve only a specific attribute or part of an attribute.

Originator: The Originator shall request to retrieve all or part of information from an existing <execInstance> resource by using a RETRIEVE verb. The Request shall address a specific "<execInstance>" resource of a hosting CSE to retrieve all attributes of the <execInstance> resource. Or the request shall address the individual attribute of the specific "<execInstance>" resource to retrieve the corresponding attribute value.

The Originator shall be:

- An AE.

Receiver: The Receiver shall check if the Originator has the READ permission on the addressed <mgmtCmd> resource. Upon successful validation, the CSE shall retrieve the corresponding attributes of the <execInstance> resource and the references to the sub-resources from its repository and shall respond to the originator with the appropriate generic responses.

The hosting CSE may be:

- An IN-CSE.

# Table 10.2.8.8-1: <execInstance> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to create a resource. |
| Information on Request message | op: R fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID cn: <mgmtCmd> resoruce. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | If the retrieval is allowed, the IN-CSE can retrieve the execution status or results on the remote entity using existing management protocol (i.e. BBF TR-0069 [i.12]) If the retrieval is allowed, the addressed attributes of the <execInstance> resource shall be retrieved from the repository of the IN-CSE |
| Information on Response message | No change from the basic procedures |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the retrieval is not allowed or the specific <execInstance> resource does not exist in the IN-CSE, there is no local processing on the hosting CSE and a proper error code shall be returned to AE in the Response Message |

#### 10.2.8.9	Delete <execInstance>

The DELETE request is used by an originating AE to delete an existing <execInstance> resource on a hosting CSE.

Originator: The Originator shall request to delete an existing <execInstance> resource by using a DELETE verb. The request shall address the specific "<execInstance>" resource of an <mgmtCmd> on the hosting CSE.

The originator shall be:

- An AE.

NOTE 1:	The hosting CSE in the network domain may also delete an <execInstance> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <execInstance> resource may also be deleted in the hosting CSE by other offline provisioning means which are out of scope.

Receiver: The Receiver shall check if the Originator has the DELETE permission on the addressed <execInstance> resource. Upon successful validation, the hosting CSE shall remove the resource from its repository. If the <execInstance> is not finished on the remote entity and it is cancellable, the hosting CSE shall also use existing management protocols (i.e. BBF TR-0069 [i.12] CancelTransfer RPC) to cancel the corresponding management currently initiated at the remote entity. Then the CSE shall respond to the originator with the appropriate generic responses.

The hosting CSE shall be:

- An IN-CSE.

# Table 10.2.8.9-1: <execInstance> DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Originator needs to delete the resource |
| Information on Request message | op: D fr: Originator AE-ID or CSE-ID to: Receiver CSE-ID cn: Name of <mgmtCmd> resource. The mandatory and/or optional attributes defined in clause 9.6.15, as needed |
| Local processing on Hosting CSE | If the <execInstance> is not finished yet and it is cancellable, the IN-CSE shall cancel the <execInstance> from the remote entity using corresponding management procedures in existing management protocol (i.e. CancelTransfer RPC in BBF TR-0069 [i.12]) The <execInstance> resource shall be deleted from the repository of the IN-CSE. If the corresponding initiated commands cannot be deleted from remote entity due to some reason (e.g. not found), the <execInstance> resource shall be still deleted be performed |
| Information on Response message | No change from the basic procedures |
| Post-Conditions | No change from the basic procedures |
| Exceptions | If the deletion is not allowed or the specific <execInstance> resource does not exist in the IN-CSE, there is no processing on the Hosting CSE and a proper error code shall be returned to AE in the Response message If the <execInstance> is already complete or it is not cancellable, there is no processing on the Hosting CSE |

************************* END OF CHANGE 43  *************************

************************ START OF CHANGE 44  ************************

#### 10.2.13.2	Create <pollingChannel>

This procedure is used to create a <pollingChannel> resource and an AE/CSE can be an Originator. After the creation of the <pollingChannel> resource, the AE/CSE can perform Long Polling on it.

Originator: Can be an AE/CSE. If an AE is the Originator, it addresses the <AE> resource that it already created. Otherwise, if a CSE is the Originator, it addresses the <remoteCSE> resource that it already created. With to parameter addressing the <AE> or <remoteCSE> resource, the Originator sends the request to the Receiver.

Receiver: shall perform the following.

- Check if the Originator has a CREATE privilege to create <pollingChannel> resource under <AE> resource or <remoteCSE> resource. If the Originator is the AE who created the <AE> resource that the request is targeting, the request shall be granted. If the Originator is the CSE who created the <remoteCSE> resource that the request is targeting, the Request shall be granted. Otherwise, the Request will be rejected.

- Send the successful/unsuccessful Response to the Originator depending on the check above.

Table 10.2.13.2-1: <pollingChannel> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | The Originator is request-unreachable. |
| Information on Request message | op: C fr: ID of the Originator to: URI of <AE> or <remoteCSE> resource cn: Mandatory and/or optional attributes defined in section 9.6.9. |
| Local processing on Hosting CSE | Check access rights regarding creation of the <pollingChannel> resource. |
| Information on Response message | No change from the basic procedure in section 10.1.1 |
| Post-Conditions | None |
| Exceptions | No change from the basic procedure in section 10.1.1 |

************************* END OF CHANGE 44  *************************

************************ START OF CHANGE 45  ************************

#### 10.2.16.1	Create <m2mServiceSubscription>

This flow is used for creating a <m2mServiceSubscription> resource.

Originator: The Originator can be an Application Entity (e.g., administrator AE of M2M Service Provider) or a Hosting CSE.

Receiver: The Receiver or Hosting CSE shall validate whether the Originator has CREATE privilege for a <m2mServiceSubscription> resource. The Receiver or Hosting CSE shall be IN-CSE.

- Table 10.2.16.1-1: <m2mServiceSubscription> CREATE

| CREATE: Description |
| --- |
| Pre-Conditions | The access to the this Resource at Receiver has been granted |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: fr: Originator ID nm: the name of the <m2mServiceSubscription> resource is optional cn: the resource content shall provide the information as defined in section 9.6.20. The following attributes from section 9.6.20 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the m2mServiceSubscription resource as defined in 9.6.1 “subsSer&RoleList” The following attributes from section 9.6.21 are optional for the request: “expirationTime” “appID” “subsGroup” |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1) |
| Information on Response message | No change from the basic procedure (section 10.1.1) |
| Post-Conditions | A new <m2mServiceSubscription> resource is created. |
| Exceptions | All exception described in the basic procedure (section 10.1.1) are applicable. |

************************* END OF CHANGE 45  *************************

************************ START OF CHANGE 46  ************************

#### 10.2.17.1	Create <nodeInfo>

This flow is used for creating a <nodeInfo> resource which is sub-resource of <m2mServiceSubscription> resource.

Originator: The Originator can be an Application Entity or a CSE.

Receiver or Hosting CSE: The Receiver or Hosting CSE shall validate whether the Originator has CREATE privilege for a <nodeInfo> resource. The Receiver or Hosting CSE is IN-CSE.

- Table 10.2.17.1-1: <nodeInfo> CREATE

| CREATE: Description |
| --- |
| Pre-Conditions | The access to the this Resource at Receiver has been granted |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: fr: Originator AE-ID or CSE-ID nm: the name of the <nodeInfo> resource is optional cn: the resource content shall provide the information as defined in section 9.6.16. The following attributes from section 9.6.16 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the nodeInfo resource as defined in 9.6.1 “nodeID” The following attributes from section 9.6.16 are optional for the request: “appID” “CSEID” |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.1) |
| Information on Response message | No change from the basic procedure (section 10.1.1) |
| Post-Conditions | A new <nodeInfo> resource is created. |
| Exceptions | All exception described in the basic procedure (section 10.1.4) are applicable |

************************* END OF CHANGE 46  *************************

************************ START OF CHANGE 47  ************************

### 12.1.1	Information Recording Triggers

Triggers have to be configured in the IN node by the M2M service provider to initiate information recording.

The M2M infrastructure nodes shall be able to initiate recording based on any of the following triggers:-

- A request received by the M2M IN over the Mcc reference point.

- A request received by the M2M IN over the Mca reference point

- A request initiated by the M2M IN over any reference point

- Timer- based triggers for non- request based information recording. This trigger is used only when the memory size of a container over a period of time is required.

More than one trigger can be simultaneously configured.

The recording triggers may also be configurable, for example, as follows:

- On a per CSE basis, or a group of CSEs for requests originating/arriving from/at the M2M IN.

- On a per AE basis or a group of AEs

- The default behaviour is that no  CSEs/AEs are configured.

************************* END OF CHANGE 47  *************************

************************ START OF CHANGE 48  ************************

#### 12.1.2.2	Information Elements within an M2M Event Record

The information elements within an M2M event record are defined in Table 12.1.2.2-1.

Every M2M event record shall be tagged to depict its content according to the following classification:

Data related procedures: represent procedures associated with data storage or retrieval from the M2M IN (eg. Container related procedures)

Control related procedures: represent all procedures that are not associated with data storage/retrieval from the M2M IN with the exclusion of group and device management related procedures (e.g. subscription procedures, registration)

Group related procedures: represent procedures that handle groups.  The group name may be derived from the target resource in these cases.

Device Management Procedures

Occupancy based trigger for recording the occupancy as described in Section 12.1.1

- Table 12.1.2.2-1: Information Elements within an M2M Event Record

| Information Element | For request based triggers Mandatory / optional | For timer based triggers Mandatory / optional | Description |
| --- | --- | --- | --- |
| M2M Subscription Identifier | M | M | The M2M subscription ID associated with the request. This is inserted by the IN (see 12.1.3) |
| Application Entity ID | CM (when applicable) | NA | The M2M Application Entity ID if applicable |
| External ID | CM (when Applicable) | NA | The external ID to communicate over Mcn where applicable |
| Receiver | M | NA | Receiver of an M2M request (can be any M2M Node) |
| Issuer | M | NA | Issuer of the M2M request (can be any M2M node) |
| Hosting CSE-ID | O | NA | The hosting CSE-ID for the request in case the receiver is not the host, where applicable |
| Target ID | M | NA | The target URL for the M2M request if available. Alternatively can be the target resource identifier |
| Protocol Type | O | NA | Eg. HTTP, CoAP |
| Request Operation | O | NA | Request Operation as defined in section 8.1.2 |
| Request Headers size | O | NA | Number of bytes for the headers in the Request, or number bytes of control information |
| Request Body size | O | NA | Number of bytes of the body transported in the Request if applicable |
| Response Headers size | O | NA | Number of bytes for the headers in the Response or number bytes of control information |
| Response Body size | O | NA | Number of bytes of the body transported in the Response if applicable |
| Response Code | O | NA |  |
| Time Stamp | M | M | The time for the recording the M2M event record |
| M2M-Event-Record-Tag | M | M | A Tag for the M2M event record for classification purposes. This tag is inserted by the IN and is M2M SP specific |
| Control Memory Size | O | NA | Storage Memory (in bytes), where applicable, to store control related information associated with the M2M event record(excludes data storage associated with container related operations) |
| Data Memory Size | O | NA | Storage Memory in Kbytes, where applicable, to store data associated with container related operations |
| Access Network Identifier | O | O | Identifier of the access network associated with the M2M event record. |
| Additional Information | O |  | Vendor specific information |
| Occupancy | NA | M | Overall size (in Bytes) of the containers generated by a set of AEs identified by the M2M Subscription Identifier |
| Group Name | CM | NA | Shall be included by the IN in the following cases: - Fanning operation initiated by the M2M IN - A request received by the M2M IN as a result of a fanning operation initiated elsewhere. The group tag shall also be set in this case |
| maxNrOfMembers | O | NA | Maximum number of members of the group for Create and Update operation. |
| currentNrOfMembers | O | NA | Current number of members in a group. The request shall be logged and information elements shall be recorded from the request before processing it or sending it out. After obtaining corresponding response, currentNrOfMembers shall be updated with the values from the response. |
| Subgroup Name | CM | NA | Includes the subgroup member name of a group. It shall be included by the M2M IN in the case when - Fanning operation initiated by the M2M IN and one of the members of the group is a subgroup - A request received by the M2M IN as a result of a fanning operation initiated elsewhere. The group tag shall also be set in this case |

The choice for the mandatory elements is motivated by the need to include all M2M identifiers within an M2M event record so that it is possible to support multiple charging scenarios.

For all non-mandatory elements, the M2M IN shall be configurable by the M2M service provider to select any additional desired information to be recorded in addition to the mandatory elements.

### 12.1.3	Identities Associations in support of Recorded Information

To enable the M2M IN to record the necessary information, as described above, the following associations shall be maintained by the M2M service provider:-

The CSE-ID  (for all M2M nodes in the M2M framework)  and the allocated M2M subscription ID

The AE-ID   and the allocated M2M subscription ID

For established associations, as described above, the M2M IN shall derive the appropriate M2M subscription ID for insertion in the M2M record event.

************************* END OF CHANGE 48  *************************

************************ START OF CHANGE 49  ************************

### 12.2.2	Filtering of Recorded Information for Offline Charging

Recorded information is the basis for offline charging. To fulfil the needs of different billing systems not all recorded information is required in all cases. Hence, the M2M Charging Function shall be configurable to only select the desired information from the recorded information for transfer to the Charging Server. This configuration shall support selecting the desired information based on the following capabilities:

- On a per CSE basis, or a group of CSEs, for requests originating/arriving from/at the IN. This applies to all M2M nodes within the M2M framework

- On a per AE basis or a group of AEs.

- The default behaviour is that no CSEs/AEs are configured.

The charging function shall ensure that information selected for transfer to the charging server has also been selected for recording before a configuration is deemed acceptable for execution.

************************* END OF CHANGE 49 *************************

************************ START OF CHANGE 50  ************************

# Annex A			(Informative): Mapping of Requirements with CSFs

The following table illustrates the mapping of the Requirements specified in TS-0002 [ref] with the CSFs specified in this document.

# Table A-1: Mapping of Requirements to CSFs

| CSF Name | Supported Sub-Functions | Associated Requirements | Notes |
| --- | --- | --- | --- |
| Addressing and Identification (AID) | Management of identifiers | OSR-026 OSR-023 OSR-024 OSR-025 | Overlap w/: DSC for OSR-023, OSR-024, and OSR-025 |
| Communication Management/Delivery Handling (CMDH) | Providing communications with other CSE's, AE's, and NSE's Communications management: best effort Communications policy management Underlying Network connectivity management Communications management: data store and forward Ability to trigger off-line device | OSR-001 OSR-002 OSR-005 OSR-006 OSR-008 OSR-009 OSR-012 OSR-013 OSR-014 OSR-015 OSR-018 OSR-019 OSR-021 OSR-027 OSR-032 OSR-035 OSR-038 OSR-039 OSR-040 OSR-048 OSR-049 OSR-050 OSR-053 OSR-062 OSR-063 OSR-064 OSR-065 OSR-066 OSR-067 OSR-068 CRPR-001 CRPR-002 CRPR-003 MGR-016 | Overlap w/: DMR for OSR-001, OSR-009, OSR-021, OSR-032 SSM for OSR-009 LOC for OSR-006 GMG for OSR-006 NSSE for OSR-006, OSR-027 SSM for OSR-009 |
| Data Management and Repository (DMR) | Data storage and management Semantic support Data aggregation Data analytics Device data backup and recovery | OSR-001 OSR-007 OSR-009 OSR-016 OSR-020 OSR-021 OSR-032 OSR-034 OSR-036 OSR-058 SMR-006 SER-015 | Overlap w/: CMDH for OSR-001, OSR-009, OSR-021, OSR-032 SUB for OSR-016 GMG for OSR-020 . |
| Device Management (DMG) | Configuration Management Diagnostics and Monitoring Firmware management Software management Device Area Network topology management | OSR-017 OSR-069 OSR-070 OSR-071 OPR-001 OPR-002 OPR-003 MGR-001 MGR-003 MGR-004 MGR-006 MGR-007 MGR-008 MGR-009 MGR-011 MGR-012 MGR-013 MGR-014 MGR-015 MGR-019 MGR-020 MGR-021 SER-013 SER-014 | Overlaps w/: GMG for OSR-017 SEC for SER-013 |
| Discovery (DIS) | Discover resource Local discovery (within CSE) Directed remote discovery | OSR-023 OSR-024 OSR-025 OSR-059 OSR-060 OSR-061 MGR-002 SMR-004 | Overlaps w/: AID for OSR-023, OSR-024, OSR-025 |
| Group Management (GMG) | Management of a group and its membership CRUD Use Underlying Network group capabilities Bulk operations Access control | OSR-006 OSR-017 OSR-020 OSR-029 OSR-030 OSR-031 OSR-037 OSR-047 MGR-005 | Overlaps w/: CMDH for OSR-006 LOC for OSR-006 GMG for OSR-006 NSSE for OSR-006, OSR-037 DMR for OSR-020 DMG for OSR-017 |
| Location (LOC) | Location management Network-provided GPS-provided Confidentiality enforcement as it relates to location | OSR-006 OSR-051 OSR-052 SER-026 |  |
| Network Service Exposure /Service execution and triggering (NSSE) | Access Underlying Network service Location Device triggering Small data Policy and charging Support multiple Underlying Network functions | OSR-006 OSR-011 OSR-027 OSR-037 OSR-054 OSR-055 OSR-056 MGR-017 MGR-018 OPR-004 OPR-005 OPR-006 | Overlaps w/: CMDH for OSR-027 GMG for OSR-006, OSR-037 LOC for OSR-006 |
| Registration (REG) | CSE registration AE registration Device registration ID correlation | MGR-010 | Overlaps w/: SEC |
| Security (SEC) | Sensitive Data Handling Secure storage Secure execution Independent environments Security administration Pre-provisioning Dynamic bootstrap Network bootstrap Security association Link level Object level Authorization and access Identity protection | SER-001 SER-002 SER-003 SER-004 SER-005 SER-006 SER-007 SER-008 SER-009 SER-010 SER-011 SER-012 SER-013 SER-016 SER-017 SER-018 SER-019 SER-020 SER-021 SER-022 SER-023 SER-024 SER-025 MGR-010 | Overlap w/: DMG for SER-013 REG for MGR-010 SSM for SER-007 |
| Service Charging and Accounting (SCA) | Charging enablers Sending charging information to charging server Subscription-based charging Event-based charging Session-based charging Service-based charging Correlation with Underlying Network Charging management Offline charging Online charging | CHG-001, CHG-002a, CHG-002b, CHG-003, CHG-004, CHG-005 |  |
| Service Session Management (SSM) | Service Session Management (CSE to CSE, AE to CSE, and AE to AE) Session persistence over link outage Session context handling Assignment of session ID Session routing Multi-hop session management Session policy management | OSR-003 OSR-004 OSR-009 OSR-045 SER-007 | Overlap w/: CMDH and DMR for OSR-009 SEC for SER-007 |
| Subscription/Notification Support (SUB) | Subscribe (CSE, AE) Local Remote Subscription to a group Notification Synchronous Asynchronous | OSR-010 OSR-016 OSR-033 | Overlaps w/: DMR for OSR-016 |

************************* END OF CHANGE 50  *************************

************************ START OF CHANGE 51  ************************

# Annex E			(Informative) CSE Minimum Provisioning

The present section defines the minimum set of resources instantiated in a CSE node with the scope to make it ready to provide services to entities that will register to.

For the purpose of the initial configuration two roles are identified:

superuser: this role allows the full CSE control according to infrastructure provider policies. Only one superuser role is allowed per CSE;

user: is the role associated to an AE that will register itself to local CSE. More than one user roles are allowed per CSE. More than one applications can access to CSE with the same role.

Superuser role may be created with the following associated resources:

- Definition or assignment of CSE-ID name that may be unique in the node hosting the CSE to be instantiated.

- Creation of <CSEBase> resource with name equal to CSE-ID.

- Creation of following child resources belonging to a tree with <CSEBase> as root:

<accessControlPolicy> child resource enabling full access control for superuser’s invoked operations to the tree resources. Subsequent created resources may have accessControlPolicyID attribute addressing this <accessControlPolicy> resource.

<AE> child resource to be used as registered AE dedicated to superuser related activities.

Each user role may be created with the following associated resources:

- Definition or assignment of an AE name that may be unique in the CSE.

- Creation of <AE> child resource of <CSEBase> resource named as described in step 1, to be used as registered AE dedicated to user related activities.

- Creation of following child resources belonging to a tree with <AE> as root:

- <accessControlPolicy> resource enabling partial access control (e.g. these resources cannot be deleted be the user, superuser’s resources can only be read by user) for user’s invoked operations to the tree resources. <AE> resource can be updated with accessControlPolicyID attribute addressing <accessControlPolicy> resource.

The above described operations may be executed in the node in order provide the elements and the access rights required to provide the initial access to resource operations.

Same user can create more than one <AE> resources and other child resource types.

Once user role resource trees have been created the registered AE associated to <AE> resource (defined for a user role in step 2) is able to create its own <container> resource to store business logic application data that can be shared to other registered AEs in a controlled way acting on its own <accessControlPolicy> resource.

************************* END OF CHANGE 51  *************************