| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | NEC |
| Format:* | TP9 |
| Date:* | 2013-01-07 |
| Contact:* | Barbara Pareglio (barbara.pareglio@neclab.eu); |
| Reason for Change/s:* | Cleaning up the definition section. |
| Clause/Sub Clause Affected* | 3 |
| Agenda Item:* | Contribution |
| Work item(s): |  |
| Document(s) Impacted* | oneM2M-TS 0001 Technical Architecture v 0 4 3 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Discussion

Introduction

Since the document is still work in progress some of the definitions require an update.

Proposal

This contribution proposes to modify some of the definition in section 3, it tries to:

- add the Application Entity and Network Services Entity to the list

- general editorial changes

======================== START 1ST CHANGE ===========================

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply:

Application Layer: The Application Layer comprises oneM2M Applications and related business and operational logic.

Common Services Layer: The Common Services Layer consists of oneM2M service functions that enable oneM2M Applications ( e.g. management, discovery and policy enforcement).

Common Services Function: A Common Services Function (CSF) is a service function that is common to the M2M environment and specified by oneM2M. A set of CSFs is contained in the CSE.

Device	(6.2.9.2)

# Device Entity (6.2.9.2)

# Device Management Resource

# Enabler Function (6.3)

Error (10.x)	either define Error, or use lower case in Clause 10

Execution Environment: An Execution Environment is a logical entity that represents an environment capable of running some software modules.

Hosting CSE: A Hosting CSE is the CSE where the addressed master/original resource resides.

Local CSE: A Local CSE  is the CSE where an Application or a CSE has registered. It is the first CSE that receives Request from an Originator. For example:

If an Application on an Infrastructure Node is the Originator, the Local CSE is the CSE on the Infrastructure Node.

If an Application on a Middle Node is the Originator, the Local CSE is the CSE on the Middle Node.

If an Application on an End Node is the Originator, the Local CSE is the CSE on the End Node.

{3.1.c} Editor's Note: Need to provide definition of an End Node. This is FFS.

{3.1.d} Editor's Note: The concept of a CSE registering at a Local CSE needs to be understood. This is FFS.

{3.1.e} Editor's Note: Review/clarify "or a CSE" in the definition of Local CSE.  Should "or a CSE" be replaced with "or a Node"?  This is FFS.

{3.1.f} Editor's Note: Need definition for "Application Entity". Need to define relationship between an Application Entity and an Application.

M2M Service Provider Domain: A M2M Service Provider Domain is the part of the M2M System that is associated with a given M2M Service Provider.

Managed Entity: A Managed Entity  is an M2M Device, M2M Gateway, devices in the M2M Area Network as well as M2M Application Layer and M2M Service Layer software components.

# Management Adapter

# Management ClientManagement Resource

# Management Server

Network Services Layer: The Network Services Layer provides transport, connectivity and service functions.

Node: A functional entity containing one of the following:

one or more M2M Applications;

one CSE and zero or more M2M Applications.

Originator: The Originator is the actor that initiates a Request. An Originator can either be an AE or a CSE.

Receiver: The Receiver is the actor that receives the Request. A Receiver can be a CSE or an AE.

# Request (7.1.7)

# Response (7.1.7

Resource: A Resource is a uniquely addressable entity in oneM2M System (e.g. by the use of a Universal Resource Identifier (URI)). A resource can be accessed and manipulated by using the specified procedures.

{3.1.g} Editor's Note: The above stated definition of Resource needs to be revisited. This is FFS.

{3.1.h} Editor's Note: It is expected that more definitions are needed. This is FFS.

# Role

Service Charging and Accounting: A set of functionalities within the M2M service layer  that enable configuration of information collection and charging policies, collection of Charging Records based on the policies, and correlate Charging Records to users of M2M common services.

Service Charging Record: Formatted collection of information about a chargeable operation.

Service Layer Offline Charging: Charging mechanism where charging information does not affect, in real-time, the service rendered.

Service Layer  Online Charging: Charging mechanism where charging information can affect, in real-time, the service rendered, including real time credit control

Software Package: A Software Package is an entity that can be deployed on the Execution Environment.  It can consist of entities such as software modules, configuration files, or other entities.

Software Module: A Software Module is  ....

Structured Data: Structured Data  is data that either have a structure according to a specified Information Model or are otherwise organized in a defined manner.

======================== END 1ST CHANGE =============================