| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#10 |
| Source:* | LG Electronics, NTT DOCOMO, AT&T |
| Format:* | Plenary |
| Date:* | 2014-03-21 |
| Contact:* | Hongbeom Ahn, LG Electronics, Hongbeom.ahn@lge.com Syed Husain, NTT DOCOMO, shusain2016@live.com Jianrong Wang, AT&T, jw8065@att.com |
| Reason for Change/s:* | This CR provides a detail procedure for Location Request as a Service Request which is conveyed over Mcn reference point and relevant informative references are proposed. R01: Remove the normative verb from NOTEs. R02: Add AT&T as a consigner |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001-oneM2M-Functional-Architecture-V0.4.2 |
| Clauses/Sub Clauses* | 8.3.2 Service Requests 8.5 Location Request 2.2 Informative references |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR provides a detail procedure for Location Request as a Service Request which is conveyed over Mcn reference point and relevant informative references are proposed.

### -----------------------Start of change 1-------------------------------------------

### 8.3.2 	Service Requests

#### 8.3.2.1 	Connection Request

Editor’s Note:  Connection request is for FFS

#### 8.3.2.2 	Location Request

See section 8.5 for detailed description on the Location Request.

#### 8.3.2.3 	Device Management

See section 6.2.4 for a detailed description on the interaction with a Device Management

Editor's Note:  The detailed content from section 6.2.4 might fit better in this section than in the high level CSF description.

#### 8.3.2.3 	Device Triggering

See section 8.4 for detailed description on the Device triggering

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2--------------------------------------------

## 8.5	Location Request

### 8.5.1	Definition and Scope

Location Request is a means by which a Node requests the geographical or physical location information of a target Node to the location server located in the Underlying Network over Mcn reference point.

### 8.5.2	General Procedure for Location Request

This procedure describes a scenario that a Node sends a request to obtain the location information of a target Node to the location server and the location server responses to the Node.

The figure 8.5.2.1-1 shows the general procedure for Location Request.

Figure 8.5.2 1-1: General Procedure for Location Request

NOTE: the detail description from the step-1 to the step-3 is described in the section 10.2.10.

Step-1: Create <locationPolicy>

The Originator requests to CREATE <locationPolicy> resource into the local CSE. The locationSource attribute of the <locationPolicy> resource shall be set by ‘Network-Based’ and the proper value for locationTargetID and LocationServer attributes shall be properly set for the Location Request.

Step-2: Local Processing for creating <locationPolicy> resource

After verifying privilege and given attributes, the local CSE shall create the <locationPolicy> resource. The linked <container> can be created after successful creation of <locationPolicy> resource.

Step-3: Response for creating <locationPolicy>

The local CSE shall respond with a response message.

Step-4: Location Request

The local CSE issues the Location Request to the selected Underlying Network. For doing this, the local CSE shall transform the location configuration information received from the Originator into Location Request that is acceptable for the Underlying Network. For example, the Location Request can be one of existing location acquisition protocols such as OMA Mobile Location Protocol[i-a] or OMA RESTful NetAPI for Terminal Location[i-b]. Additionally, the local CSE shall provide default values for other parameters (e.g., required quality of position) in the Location Request according to local policies.

NOTE: This Location Request can be triggered by the given conditions: 1) when the locationUpdatePeriod attribute has expired, or if the locationUpdatePeriod attribute is not given from the step-1, 2) the <locationPolicy> has created or 3) the linked <container> has been retrieved.

Step-5: Underlying Specific Location Procedure

The Underlying Network shall perform positioning procedure.

Step-6: Location Response

The NSE shall respond to the local CSE. Some positioning related values such as altitude, longitude shall be able to be returned.

Step-7: Local Processing after Location Response

The received response shall be contained in the <container> resource that is related the <locationPolicy> resource.

NOTE: Please see the section 10.2.10.2 for detail information.

NOTE: For notification regarding the location response toward the Originator, the subscription mechanism is needed.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules.

NOTE:	Available at http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc.

[i.2]	OMA-ER-DMClientAPIfw-V1_0: "DM Client Side API Framework (DMClientAPIfw)".

[i.3]	oneM2M TR-0008: "Security Analysis: ...".

[i.4]	IETF RFC 3986: "Uniform Resource Identifier (URI): General Syntax".

[i.5]	IETF RFC 1035: "Domain names - Implementation and specification".

[i.6]	IETF RFC 3596: "DNS Extensions to Support IP Version 6".

[i.7]	GSMA-IR.67: "DNS/ENU Guidelines for Service Providers & GRX/IPX Providers".

[i.8]	IETF RFC 2929: "DNS IANA Considerations".

[i.9]	IETF RFC 6874: "Representing IPV6 Zone Identifiers in Address Literals and Uniform Resources Identifiers".

[i.10]	IETF RFC 6895: "DNS IANA Considerations".

[i.11]	3GPP TS 23.682: "Architecture Enhancements to facilitate communications with packet data networks and applications".

[i.12]	TR-0069: " ...".

[i-13]	3GPP2 X.P0068, "Network Enhancements for Machine to Machine (M2M)"

[i-a]	OMA-TS-MLP-V3_4-20130226-C: “Mobile Location Protocol”, Version 3.4

[i-b]	OMA-TS-REST-NetAPI_TerminalLocation-V1_0-20130924-A: “RESTful Network API for Terminal Location”, Version 1.0

[Y] 	3GPP 32.240  “3rd Generation Partnership Project;Technical pecification Group Services and System Aspects; Telecommunication management;Charging management;Charging Architecture and Principles.

[Z] 	3GPP 32.299  “3rd Generation Partnership Project;Technical pecification Group Services and System Aspects; Telecommunication management;Charging management;Diameter charging application.

[i.x]	IETF RFC 3588: "Diameter Base Protocol".

[i.y]	IETF RFC 4006: "Diameter Credit-Control Application".

Note: The above stated references are for section -12

### -----------------------End of Changes to References  -------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?