| CHANGE REQUEST |
| --- |
| Group Name:* | TP#10 |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Plenary |
| Date:* | 2014-3-27 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* | State machine added to the annex D for the management of software and firmware. |
| CR against: Release* | <Release One> |
| CR against: TS/TR* | TS0001 v0.4.2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution is to add state machine for the management of software and firmware in oneM2M. The issue is left over from the last TP. To solve the editor’s note “Editor’s Note: The state machine diagram is to be added according to section 6.2.1.2.3. The names of the attributes also need to be aligned with the wording in the same section.”

### -----------------------Start of change 1-------------------------------------------

## D.3	Resource software

Figure D.3-1: Structure of <software> resource 
(only resource specific attributes are shown)

The <software> resource shall contain the attributes described in Table D.3-1.

Table D.3-1: Attributes of <software> resource

| Attribute Name of <software> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See section 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See section 9.6.1 where this common attribute is described |
| accessControlPolicyID | 1 | RW | See section 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See section 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | Has fixed value “Software” to indicate the resource is for software management. |
| objectID | 0..1 | WO | See section 9.6.13 |
| objectPath | 0..1 | WO | See section 9.6.13 |
| description | 0..1 | RW | See section 9.6.13 |
| version | 1 | RW | The version of the software. |
| name | 1 | RW | The name of the software to be used on the device. |
| URL | 1 | RW | The URL from which the software package can be downloaded. |
| install | 1 | RW | The action that downloads and installs new software in a single operation. |
| installStatus | 1 | RO | Indicates the status of the install. |
| activate | 0..1 | RW | The action that activates software previously installed. |
| deactivate | 0..1 | RW | The action that deactivates software. |
| activeStatus | 0..1 | RW | The status of active or deactivate action. |

The state machine for managing the software in oneM2M is shown in the following figure.

Figure D.3-1: State machine for software management

### -----------------------End of change 1---------------------------------------------

# Text boxes

<software>

mgmtDefinition

objectID

objectPath

description

version

name

URL

install

installStatus

1

0..1

0..1

0..1

1

1

1

1

1

activate

deactivate

activateStatus

1

1

1

Created

Installed and Activated

Delete: ./[software]

Deactivated

Removed

Execute: ./[software]/Activate

Execute: ./[software]/Deactivate

Execute: ./[software]/Install

Delete: ./[software]