| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | Rajesh Bhalla, ZTE, rabhalla@ztetx.com Barbara Pareglio, NEC, barbara.pareglio@neclab.eu Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Format:* | ARC TP#10 |
| Date:* | 2014-04-07 |
| Contact:* | Rajesh Bhalla, ZTE Barbara Pareglio, NEC Seungkyu Park, LG Electronics |
| Reason for Change/s:* | Attribute announcement procedure is broken. This is Part -1 of the clean up proposals |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Attribute announcement procedure is broken.

This is Part -1 of the clean up proposals

- R02 version addresses comments regarding announcement of child resources

### -----------------------Start of change 1-------------------------------------------

### 9.1.1	Announced Resource

An announced resource is a resource at a remote CSE that is linked to the original resource that has been announced, and it maintains some of the characteristics of the original resource.

Resource announcement can facilitate resource discovery. The announced resource at a remote CSE can also be used for creating child resources at the remote CSE that are not present as children of the original resource or are not announced children of the original resource.

The following are the resource specification guidelines for the resource announcement:

In order to support announcement of resources, an additional column in the resource template (clause 9.5.1), shall to specify the attributes to be announced for inclusion in the associated announced resource type.

For each announced <resourceType>, the addition of suffix "Annc" to the original <resourceType> shall be used to indicate its associated announced resource type. For example, resource <containerAnnc> shall indicate the announced resource type for resource type <container>; <groupAnnc> shall indicate announced resource type for resource type <group>, etc.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.5.1	Resource Template

#### 9.5.1.1	Resource Type resourceType

<Fill a short description of the resourceType>

Figure 9.5.1.1-1: Structure of resource <resourceType>
(only child resources and resource specific attributes are shown)

The resource <resourceType> shall contain child resources according to their multiplicity shown in Table 9.5.1.1-1. A value of "0" for multiplicity indicates the child resource is optional.
The child resource table for an announce-able <resourceType> resource shall include an additional column titled '<resourceTypeAnnc> Child Resource', indicating the type of announced child resources.See the section 9.6.34 for further details.

An announced resource may have child resources, such child resources can be of type normal or announced. When a resource is announced, the associated child resources shall be announced independently of the original resource, as needed by the resource announcing CSE. The child resources at the announced resource shall be of the child resource Announced type.

When child resources at the announced resource are created locally by the remote CSE, the child resources shall be of normal child resource type.

# Table 9.5.1.1-1: Child Resources of <resourceType>

| Child Resource Name of <resourceType> | Child Resource Type | Multiplicity | Description | <resourceTypeAnnc> Child Resource |
| --- | --- | --- | --- | --- |
| <Fill in the name of Child Resource1 if a fixed name is required or [variable] if no fixed name is required> | <Fill in the type of Child Resource1> | <Fill in Multiplicity> | See clause <XRef <clause> where the type of this child resource is described. | <Fill the child resource type for the announced resource. It can be none or <crTypeAnnc> or <crType>; where the <crType> is the child resource type of the original Child Resource1. |
| <Fill in the name of Child ResourceN if a fixed name is required or [variable] if no fixed name is required> | <Fill in the type of Child ResourceN> | <Fill in Multiplicity> | See clause <XRef <clause> where the type of this child resource is described. | <Fill the child resource type for the announced resource. It can be none or <crTypeAnnc> or <crType>; where the <crType> is the child resource type of the original Child ResourceN. |

<Fill Additional information about child resources (as needed)>.

The resource <resourceType> shall contain attributes according to their multiplicity shown in Table 9.5.1.1-2.  A value of "0" for multiplicity indicates the attribute is optional.

The attributes table for announce-able <resourceType> resource shall include an additional column titled 'Attribute for <resourceTypeAnnc>', indicating the attributes that are to be announced for that <resourceType>. See the section 9.6.34 for further details.

# Table 9.5.1.1-2: Attributes of <resourceType>

| Attribute Name of <resourceType> | Multiplicity | RW/ RO/ WO | Description | <resourceTypeAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| <Fill in name of Common Attribute1> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute…to be moved later to a common attribute section. | <Fill in MA or OA or NA> |
| <Fill in name of Common AttributeN> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute…to be moved later to a common attribute section. | <Fill in MA or OA or NA> |
| <Fill in name of Resource Specific Attribute1> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute .. to be moved later to a central attribute table that also defines the type of the attribute, allowed ranges etc. | <Fill in MA or OA or NA> |
| <Fill in name of Resource-Specific AttributeN> | <Fill in Multiplicity> | <Fill in RW or RO or WO> | Provide description of this attribute .. .. to be moved later to a central attribute table that also defines the type of the attribute, allowed ranges etc. | <Fill in MA or OA or NA> |

<Fill additional information about attributes (as needed)>.

The attributes for <resourceTypeAnnc> in the attribute table can be of the following type:

MA (Mandatory Announced): Such attributes in the original resource shall be announced to the announced resources. The content of such announced attributes shall be the same as the content of the original attributes.

OA (Optional Announced): Such attributes in the original resource may be announced to the announced resources depending on the contents of the announcedAttribute attribute at the original resource. The content of such announced attributes shall be the same as the content of the original attributes.

NA (Not Announced): Such attributes shall not be announced to the announced resources.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 9.6	Specified Resource Types

Table 9.6-1 introduces the defined resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6-1 lists the supported <resourceTypes>. An addition of suffix "Annc" to such <resourceTypes> shall indicate the associated announced resource type.  The Tag Values for the supported <resourceTypes> and the associated <resourceTypeAnnc> shall be as specified in <Stage 3 specification>.

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 9.6.1	Common Attributes

Many of the attributes of the resources described in the present document are common. Such attributes are described here once in order to avoid duplicating the description for every resource that contains it.

Attributes that are only used in one or two resource types are described only in the clause for that resource type.

In all tables representing resource attributes, each attribute name is followed by its "short name" in brackets that shall be used in resource representations to be transferred across reference points.

# Table 9.6.1-1: Common Attributes

| Common Attribute | Description |
| --- | --- |
| resourceType (rT) | Resource Type. This WO resourceType attribute stores <in a two capital letters token> the information useful for procedure processing, e.g. CO for <container>, CI for <instance>. |
| parentID (pID) | The identifier identifies the parent resource. Editor's Note: The adoption of a URI format is still to be confirmed. |
| accessControlPolicyID (aRI) | The URI of an <accessControlPolicy> resource. The permissions defined in the <accessControlPolicy> resource that are referenced determine who is allowed to access the resource containing this attribute for a specific purpose (e.g. Retrieve, Update, Delete, etc.). If a resource type does not have an accessControlPolicyID attribute definition, then the accessControlPolicy for resources of that type are governed in a different way, for example, the accessControlPolicy associated with the parent may apply to a child resource that does not have an accessControlPolicyID attribute definition, or the permissions for access are fixed. Refer to the corresponding procedures to see how permissions are handled in such cases. If a resource type does have an accessControlPolicyID attribute definition, but the (optional) accessControlPolicyID attribute is not set, or it is set to a value that does not correspond to a valid, existing <accessControlPolicy> resource, or it refers to an <accessControlPolicy> resource that is not reachable (e.g. because it is located on a remote CSE that is offline or not reachable), then the system default access permissions shall apply. The system default access permissions grant all permissions (i.e. the full set of permissionsFlags) to the following permission holders depending on the prefix of URI of the resource.: << Editor's Note: what is the list of permission holders>> |
| creationTime (cT) | Time/date of creation of the resource. |
| expirationTime (eT) | Time/date after which the resource will be deleted by the hosting CSE. This attribute can be provided by the Originator, and in such a case it will be regarded as a hint to the hosting CSE on the lifetime of the resource. The hosting CSE can however decide on the real expirationTime. If the hosting CSE decides to change the expirationTime attribute value, this is communicated back to the Originator. The lifetime of the resource can be extended by providing a new value for this attribute in an UPDATE verb. Or by deleting the attribute value, e.g. by not providing the attribute when doing a full UPDATE, in which case the hosting CSE can decide on a new value. |
| lastModifiedTime (lMT) | Last modification time/date of the resource. |
| versionTag (vT) | An incremental counter of modification on the resource. When a resource is created, this counter is set to 0, and it will be incremented on every modification of the resource. NOTE: In order to enable detection of overflow, the counter needs to be capable of expressing sufficiently long numbers. . |
| labels(lBs) | Tokens used as keys for discovering resources. |
| creator (cr) | The App-inst-ID or CSE-ID of the entity which created the resource |
| link (ln) | This attribute shall be present only on the announced resource. This attribute shall provide the link (URI) to the original resource. |
| announceTo (aT) | This attributes shall only be present on the original resource if it has been announced to other CSEs. This attribute maintains the list of URIs to the announced resources. Updates on this attribute will trigger new resource announcement or de-announcement. In case of new resource announcement, either the exact URI to the announced resource that is to be created can be provided, or the CSE-ID of the remote CSE can be provided. In the later case the original resource-hosting CSE will decide the exact location of the announced resource in the remote CSE identified by the CSE-ID. |
| announcedAttribute (aA) | This attributes shall only be present on the original resource if some OA type attribute has been announced to other CSEs. This attribute maintains the list of the announced optional attributes (OA type attributes) in the original resource. Updates to this attribute will trigger new attribute announcement if a new attribute is added or de-announcement if the existing attribute is removed. |

Editor's Note:  The usage of creator (cr) attribute is FFS.

Editor's Note: The following attributes are FFS depending on resource structure discussions:

child: resources with child relation with the considered resource

parent: resources with parent relation with the considered resource

### -----------------------End of change 4 ---------------------------------------------

# Comments

I moved it up in the first sentence.