| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | Rajesh Bhalla, ZTE, rabhalla@ztetx.com Barbara Pareglio, NEC barara.pareglio@neclab.eu |
| Format:* | ARC TP#10 |
| Date:* | 2014-04-07 |
| Contact:* | Rajesh Bhalla, ZTE Barbara Pareglio, NEC |
| Reason for Change/s:* | Attribute announcement procedure is broken. This is Part -4 of the proposal to fix the deficiencies. |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Attribute announcement procedure is broken.

This is Part -4 of the proposal to fix the deficiencies.

### -----------------------Start of change 1-------------------------------------------

### 10.2.18	Resource Announcement Procedure

#### 10.2.18.0 	Introduction

#### The procedure for announcing a resource involves a set of operation over one or two reference points depending on who is performing the request. The following are the allowed cases:

#### Originator: AE

#### Request over Mca reference point, where the receiver is the original resource hosting CSE

#### Request over Mcc reference point, where the receiver is the target CSE hosting the announced resource.

#### Originator: CSE

#### Request can be either over Mcc or internal (for the case of the original resource CSE), where the receiver is the original resource hosting CSE

#### Request over Mcc reference point, where the receiver is the target CSE hosting the announced resource.

#### The following clauses describe all the procedures over both reference points and for both type of originators.

#### 10.2.18.1 Procedure for AE and CSE to initiate the Creation of an Announced Resource

This section describes the procedure for an AE or a CSE  to initiate the creation of an announced resource.

Originator: The Originator of a Request for initiating resource announcement can be either an AE or a CSE. The Originator can initiate the creation of an announced resource during the creation of the original resource by providing the announceTo attribute in the cn parameter of the CREATE Request. The Originator can request to initiate the creation of an announced resource by using  UPDATE Request to the announceTo attribute in the original resource as wll.

The Originator shall perform the following for  the creation of an announced resource:

The Originator can provide either the exact URI(s) for the announced resource or the list ofCSE-IDs of the remote CSEs where the original resource needs to be announced by including such information within the attributeTo of the cn parameter of the UPDATE or CREATE Request. In case of the CSE-IDs, the Receiver (original resource hosting CSE) shall decide the exact location for the announced resource at the remote CSE identified by the CSE-ID.

Receiver: Once the Originator has been successfully authorized, the Receiver (which shall be the original resource hosting CSE) shall grant the Request after successful validation of the Request.

For UPDATE Request, the Originator shall add the received exact URI or the CSE-ID to the announceTo attribute at the original resource, if such exact URI or CSE-ID is not already stored in the announceTo attribute.

For CREATE Request, the Originator shall include the received exact URI or the CSE-ID in the announceTo attribute created at the original resource.

If the Request provides an exact URI(s) that are not already stored in the announceTo attribute or for newly created announceTo attribute , the Receiver shall announce the resource to the location identified by the URI(s) as per procedures in clause10.2.18.4.

If the Request provides a list of CSE-IDs of the remote CSE that are not already stored in the announceTo attribute of for newly created announceTo attribute , the Receiver shall decide the location at the remote CSE(s) identified by CSE-ID(s) for announcing the resource and shall perform the procedures in in clause 10.2.18.4.

Receiver after completion of the resource announcement procedure in clause 10.2.18.xx:

On successful completion of resource announcement as in clause 10.2.18.4, the Receiver receives the exact location (at remote CSE) where the announced resource has been created.

The Receiver shall provide the exact URI(s) of the announced resource to the Originator by updating the content of the announceTo attribute in the original resource and by providing itin the UPDATE/CREATE Response message.

Table 10.2.18.1-1: Resource Announcement: UPDATE and CREATE

| UPDATE or CREATE Description |
| --- |
| Pre-Conditions | The Originator suggests the URI(s) or the CSE-ID(s) to which the resource will be announced. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table, in addition in case of CREATE the procedure for the specific resource is described in clause 10.2. The specific information relevant for announcing is: cn: contains address where the resource needs to be announced (within announcedTo attribute) |
| Local processing on Hosting CSE | Steps described for the Receiver of the Request as described above |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for cn asdescribed above for the Receiver of the Response |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedures (section 10.1.1) are applicable. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 8.1.2	Request

Request from an Originator to a Receiver includes the following information:

op: operation to be executed: Create (C), Retrieve (R), Update (U), Delete (D).

to: URI of the target resource or the parent of the target resoruce, e.g. /m2m.provider1.com/netBase/temp1.

Editor's Note: This is made under the assumption that the CSE-ID is incorporated in the  URI of the target resource or the parent of the target resoruce.

fr: ID of the Originator.

NOTE 1:	fr is used for access control of the target resource.

mi: meta-information about the Request.

Editor's Note: Defaults for meta-information are FFS.

cn: resource content to be transferred.

NOTE 2:	The to target resource needs to be known by the Originator. It can be known either by pre-provisioning or by discovery.

Editor's Note: How pre-provisioning and discovery are performed is FFS.

The op information shall indicate the operation to be executed at the Receiver:

Create (C): a new resource addressable with to parameter is created.

Retrieve (R): an existing to addressable resource is read and provided back to the Originator.

Update (U): the content of an existing to addressable resource is replaced with cn new content.

Delete (D): an existing to addressable resource and all its sub-resources are deleted from the Resource Storage.

Notify (N):  information to the Receiver, processing on the Receiver is not indicated by the Originator.

Editor's Note: This is an initial list of the verbs. The need for more verbs is anticipated to cover all use cases, configuration and functions.

The to information shall address the target resource in the Receiver. The to information shall conform to section 9.3.1.The fr information shall be used by the Receiver to check the Originator identity for access permission verification.

The ty information shall be present in Request for the following operations:

Create: ty is the type of the resource to be created.

The cn information shall be present in Request for the following operations:

Create: cn is the content of the new resource with the resource type tag as in Table 9.2-1.

Update: cn is the content to be replaced in an existing resource.

Retrieve: cn is the filter to be applied for discovery purposes.

Notify: cn is the notification information.

Note that the cn information can also be empty.

The mi information shall be as follows:

ot: optional originating timestamp of when the message was built.

Example usage of the originating timestamp includes: to measure and enable operation (e.g. message logging, correlation, message prioritisation/scheduling, accept performance requests, charging, etc.) and to measure performance (distribution and processing latency, closed loop latency, SLAs, analytics, etc.)

rqet: optional request expiration timestamp.

Example usage of the request expiration timestamp includes to indicate when request messages (including delay-tolerant) should expire due to their staleness being no longer of value, and to inform message scheduling/prioritisation. When a request has set request expiration timestamp to a specific time and the Request demands an operation on a Hosting CSE that is not the CSE currently processing the request, then the current CSE shall keep on trying to deliver the Request to the Hosting CSE until the request expiration timestamp time, in line with provisioned policies.

rset: optional result expiration timestamp.

Example usage of the result expiration timestamp includes to indicate when result messages (including delay-tolerant) should expire due to expected staleness of the result, being no longer of value, and to inform message scheduling/prioritisation. It can be used to set the maximum allowed total request/result message sequence round trip deadline.

rt: optional response type: indicates  what the response to the issued request shall contain and when the response is sent to the Originator:

Acknowledgement: In case the request is accepted by the Local CSE, the Local CSE responds after acceptance with an Acknowledgement confirming that the Local CSE will further process the request.

Result: In case the request is accepted by the Local CSE, the Local CSE responds with the result of the requested operation  after completion of the requested operation.

Example usage of the response type set to Acknowledgment: An Originator that is optimized to minimize communication time and energy consumption wants to express a Request to the local CSE and get an acknowledgement on whether the Request got accepted. After that the Originator may switch into a less power consuming mode and retrieve a Result of the requested Operation at a later time.

rd: optional result destination:

Local CSE: The Local CSE includes in the response to an accepted request a reference that can be used to access the status of the request and the result of the requested operation at a later time.

Originator: The result of the requested operation needs to be sent as a notification to the Originator.

Example usage of the result destination set to Local CSE includes when the result content is extremely large, or when the result consists of multiple content parts from a target group which are to be aggregated asynchronously over time.

rc: optional result content: Indicates what are the expected components of the result of the requested operation. The Originator of a request may not need to get back a result of an operation at all. This shall be indicated in the rc information. Which exact settings of rc are possible depends on the requested operation specified in op. Possible values of rc are:

"resource": Only a representation of the requested resources will be returned as content, without any mention of the links of the requested resources to other resources. This is the default value.

"resource;links-of-types:A,B,C": A representation of the requested resources, along with links of types A, B and C to other resources (possibly limited by a maximum number of retrieved links), will be returned as content.

Editor's Note: Link types A, B, C are examples and are FFS. Or should it be converted to a NOTE.

"resource;links": A representation of the requested resources, along with all links to other resources (possibly limited by a maximum number of retrieved links), will be returned as content.

"links": Only the links of the requested resources to other resources (possibly limited by a maximum number of retrieved links), without any representation of the actual resources requested, will be returned as content.

"nothing": Nothing will be returned as content of the Response.

"result-notification": A notification will be returned when the operation is completed.

"announced-resource": information from the announced resource at local CSE shall be returned. If such information is not available at local CSE, information at original resource shall be returned. This option shall not be used if the optional meta information fc (filter criteria) is included.

Editor's Note: Details on what settings for rc are possible can be added at a later when the specific operations that can be requested are defined (e.g. register an AE, modify content of a container, etc.)

rp: optional response persistence: indicates the duration for which the address containing the responses is to persist.

Example usage of response persistence includes requesting sufficient persistence for analytics to process the response content aggregated asynchronously over time. If a result expiration timestamp is specified then the response persistence should last beyond the  result expiration time.

ri: Request Identifier mandatory over the Mca, Mcc, and Mcn reference points.

Example usage of request identifier includes enabling the correlation between a Request and one of the many received Responses.

oet: optional operational execution time: indicates the time when the specified operation op is to be executed by the target CSE. A target CSE shall execute the specified operation of a Request having its operational execution time indicator set, starting at the operational execution time. If the execution time has already passed or if the indicator is not set, then the specified operation shall be immediately executed, unless the request expiration time, if set, has been reached.

Example usage of operational execution time includes asynchronous distribution of flows, which are to be executed synchronously at the operational execution time.

NOTE 3:	Time-based flows may not be able to be supported depending upon time services available at CSEs.

ec: optional event category: Indicates the event category that should be used to handle this request. Event categories are impacting how Requests to access remotely hosted resources are processed in the CMDH CSF. Selection and scheduling of connections via CMDH are driven by policies that can differentiate event categories.

Editor's Note: Details on how to limit use of ec by AEs and relationship to provisioned policies are FFS.

Example usage of "event category" set to specific value X: When the request is demanding an operation to be executed on a Hosting CSE that is different from the Local CSE, the request may be stored in the CSE that is currently processing the request on the way to the Hosting CSE until it is allowed by provisioned policies for that event category X to use a communication link to reach the next CSE on a path to the Hosting CSE or until the request expiration timestamp is expired.

da: optional delivery aggregation on/off: Use CRUD operations of <delivery> resources to express forwarding of one or more original requests to the same target CSE(s).

NOTE 4:	Since da is optional, there could be a default value to be used when not present in the Request. This parameter 	may not be exposed to AEs via Mca.

Example usage of delivery aggregation set on: The CSE processing a request shall use aggregation of requests to the same target CSE by requesting CREATE of a <delivery> resource on the next CSE on the path to the target CSE.

gid: optional group request identifier: Identifier added to the group request that is to be fanned out to each member of the group.

fc:  optional filter criteria: conditions for filtered retrieve operation are described in Table 8.1.2-1.

Table 8.1.2-1: Filter criteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| labels | 0..n | The labels attributes of the resource matches the specified value. |
| resourceType | 0..n | The resourceType attribute of the resource is the same as the specified value. It also allows discriminating between normal and announced resources. |
| sizeAbove | 0..1 | The contentSize attribute of the <instance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <instance> resource is smaller than the specified value. |
| contentType | 0..n | The typeOfContent attribute of the <instance> resource matches the specified value |
| limit | 0..1 | Limitation the number of matching resources to the specified value. |
| attribute | 0..n | Attribute token name to be provided to reduce the scope of filtering to resource attributes. |

Example usage of filter criteria conditions in a HTTP query: an HTTP GET operation can be requested applying also a filter in the query part of the request itself:

GET /root?label=one&label=two&createdBefore=2014-01-01T00:00:00&limit=128

The example discovers a maximum of 128 resources matching the following logical condition: createdBefore < 2014-01-01T00:00:00 AND (label = one OR label = two).

Once the Request is delivered, the Receiver shall analyze the Request to determine the target resource.

If the target resource is addressing another M2M node, the Receiver shall route the request appropriately.

If the target resource is addressing the Receiver, it shall:

Check the existence of to addressed resource.

Identify the resource type with the tag value as in Table 9.2-1.

Check the permission for fr Originator to perform the requested operation.

Perform the requested operation (using cn content when provided).

Perform the requested operation (using cn content when provided) according to the operational execution time.

Depending on the request result content, respond to the Originator with indication of successful or unsuccessful operation results. In some specific cases (e.g. limitation in the binding protocol or based on application indications), the Response could be avoided.

The message flow procedure started with an Originator Request shall be considered closed when either:

A Request is received with an expired rqet (request expiration timestamp).

A Response is delivered to the Originator.

- The requested operation at the Receiver is successfully completed and no Response is needed.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 10.2.18.2 	Procedure at AE or CSE to Retrieve information from an Announced Resource

This section describes the procedures for an AE or a CSE to retrieve information about an announced resource or its attributes.

Originator: The Originator of a Request for initiating retrieval of information about a resource can be either an AE or a CSE. The Originator initiates this procedure by using RETRIEVE Request. Clause 8.1.2 specified the information to be included in the Request message. Specifically, the to parameter is set to the address (e.g., URI) of the resource to be retrieved. If a specific attribute is to be retrieved, the address of such attribute is included in the to parameter. The Originator can request retrieval of information from an announced resource at the hosting CSE by using the request message parameter rc. If rc is  set to "announced-resource" it means that the actual announced resource representation is requested. If rc is set to ”links”, only the content of the link attribute is requested. If rc is not present, by default the originator request the content of the original resource that is linked by the announced resource.

The Originator shall perform as follows for retrieving information from an announced resource.

The Originator shall set the to parameter in the RETRIEVE Request to the address (e.g., URI) of the resource or attribute to be retrieved.

The Originator can request retrieval of information from an announced resource at the hosting CSE. Optionally the Originator can specify one of the values for the optional rc parameter.

Receiver: Once the Originator has been successfully authorized, the Receiver (hosting CSE) shall grant the Request after successful validation of the Request.

If rc request message parameter set to "announced-resource" is included in the Request message, the Receiver shall provide in the RETRIEVE Response the announced resource representation, as described in clause 9.6.34.

If rc request message parameter is set to "links" is included in the Request message, the Receiver shall provide in the RETRIEVE Response the content of the attribute link.

If no rc request message parameter is provided in the Request message, the Receiver shall provide in the RETRIEVE Response the resource representation for the original resource that is linked by the link attribute.

For a successful match, information from the identified announced resource (at hosting CSE) shall be returned to Originator via RETRIEVE Response.

Table 10.2.18.2-1: Resource Retrieval at local CSE: RETRIEVE

| RETRIEVE Description |
| --- |
| Pre-Conditions | For RETRIEVE operation, the Originator knows the exact URI of the resource or the attribute that needs to be retrieved. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for: rc: either: not present set to "announced-resource" set to “links” cn: void |
| Local processing on Hosting CSE | Steps as described by the basic procedure (clause 10.1.2) still apply, in addition the steps described above for the Receiver of the Request apply. |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for: cn: according to what described above for the Receiver of the Response |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section 10.1.2) are applicable. |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

#### 10.2.18.3 	Procedure for AE and CSE to initiate Deletion of an Announced Resource

This section describes the procedure for an AE or a CSE (not the original resource hosting CSE) to initiate the deletion of an announced resource.

Originator: The Originator of a Request for initiating resource de-announcement can be either an AE or a CSE The Originator can request to initiate the deletion of an announced resource by using UPDATE Request to the announceTo attribute at the original resource hosting CSE. Resource de-announcement (deletion) shall also be performed when the Originator deletes the resource at the original resource hosting CSE by using DELETE Request.

The Originator shall perform as follows for the deletion of an announced resource.

the Originator shall update the announceTo attribute at the original resource hosting CSE by providing new content of the announceTo which does not include the URI of the announced resource that needs to be de-announced (deleted) in the UPDATE operation.

the Originator shall update the original resource in the hosting CSE by providing new representation of the resource that does not contain the announceTo attribute for de-announced (deleted) all the previously announced resources by using an UPDATE operation

.Receiver: Once the Originator has been successfully authorized, the Receiver (which shall be the original resource hosting CSE) shall grant the Request after successful validation of the Request.

The Receiver shall be the resource hosting CSE. On receiving an UPDATEoperation, the Receiver shall perform as follows:

For UPDATE Request, the Receiver shall de-announce such resource as per procedures in clause 10.2.18.5 and update the announceTo attribute as per information received by the de-announcing procedure. The UPDATE operation results in the removal of some URI(s) that is currently stored in the announceTo attribute or the removal of the attribute itself

For DELETE Request, the Receiver shall de-announce all announced resources in the announcedTo attribute as per procedures in clause 10.2.18.5.

Receiver after completion of the resource de-announcement procedure in clause 10.2.18.5:

On successful completion of resource de-announcement procedure in clause 10.2.18.5, the Receiver knows that the desired resource has been de-announced.

The Receiver shall provide confirmation of resource de-announcement to the Originator using the UPDATE/DELETE Response message.

Table 10.2.18.3-1: Resource De-Announcement: UPDATE and DELETE

| UPDATE and DELETE Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for. cn: contains Either the modified announceTo attribute Or a complete representation of the original resource without the announceTo attribute In case of op: D, the generic procedure is described in clause 10.1.4 cn: void |
| Local processing on Hosting CSE | The basic procedure (clause 10.1.3 for UPDATE and 10.1.14 for DELETE) still applies in addition the steps described above for the Receiver of the Request also apply |
| Information on Response message | The basic procedure (clause 10.1.3 for UPDATE and 10.1.4 for DELETE) still applies in addition the steps described above for the Receiver of the Request also apply |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section10.1.2) are applicable for UPDATE operation.All exceptions described in the basic procedure (section10.1.4) are applicable for DELETE operation |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

#### 10.2.18.4	Procedure for original resource hosting CSE to Create Announced Resource

This section explains  resource announcement procedure This procedure shall be used by the original resource hosting CSE to announce the original resource to a remote CSE.

Originator: The Originator of this Request shall be the original resource hosting CSE. The Originator shall request to create the announced resource by using  CREATE Request. The Request shall provide the information as follows:

Attributes marked with MA and attributes marked with OA that are included in the announcedAttribute attribute at the original resource shall be provided in the CREATE Request. Such attributes shall have the same value as for the original resource.

Attributes marked with NA for the original resource shall not be provided in the CREATE Request.

accessControlPolicyID attribute shall always be provided in the CREATE Request even if it is not present in the original resource. In this case the original resource shall include accessControlPolicyID from its parent resource or from the local policy at the original resource, as needed.

Note: accessControlPolicyID and labels attributes, if present at the original resource, shall be marked MA and shall be provided by the original resource hosting CSE in the CREATE Request. Such attributes shall have the same value at the original resource and at the announced resource(s).

Receiver: Once the Originator has been successfully authorized, the Receiver shall grant the Request after successful validation of the Request. The Receiver shall:

Create the announced resource that includes the common attributes specified in clause 9.6.34.1

Set the accessControlPolicyID attribute to the value received in the Request message.

Set the labels attribute (if present) to the value received in the Request message.

Set the link attribute to the URI of the original resource.

Create the attributes marked as OA that are received in the Request and set them to values provided.

Respond to the Originator with the CREATE Response. In this Response, the location (URI) of the announced resource shall be provided.

The Originator after receiving the Response from the Receiver shall perform the following steps:

If the announced resource has been successfully created, the announceTo attribute of the original resource shall be updated  to include the URI(s) for the successfully announced resource at the Receiver. The announcedAttribute attribute shall be updated as well to represent the successfully announced attributes as received  in the Response

For the attributes marked as MA and for the attributes marked as OA that are included in the announcedAttribute attribute, the Originator shall further take the responsibility to keep their values synchronized at the announced resource by using UPDATE operation (clause 10.1.3).

Table 10.2.18.4-1: Resource Hosting CSE to Announce Resource: CREATE

| CREATE Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for the following attributes from section 9.6.34 are mandatory for the request: cn: contains MA attributes and OA attributes that are included in announcedAttribute attribute The following attributes from section 9.6.34 are mandatory for the Request: “resourceType” which shall be set to the appropriate tag that identify the <Annc> resource; “accessControlPolicy” which it contains the value provided by the Originator, as described above. “expirationTime” provided by the originator equal to the one of the original resource “labels” provided by the originator equal to the one of the original resource, if present All attributes from the original resource that are present in the announcedAttribute shall be created in the announced resource and the value of these attribute shall be equal to the one from the original resource. |
| Local processing on Hosting CSE | The basic procedure (section 10.1.1) and the steps described above for the Receiver of the CREATE Request apply |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: URI of the created <Anc> resource, according to section 10.1.1 |
| Post-Conditions | Steps described for the 'Originator on receiving the Response from the Receiver' as described above |
| Exceptions | All exception described in the basic procedure (section 10.1.1) are applicable. |

### -----------------------End of change 5-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

#### 10.2.18.5	Procedure for original resource hosting CSE to Delete an Announced Resource

This section explains the procedure for deleting an announced resource (i.e., the resource de-announcement). This procedure shall be used by the original resource hosting CSE for deleting the announced resource that resides at the remote CSE.

Originator: The Originator of this Request shall be the original resource hosting CSE. The Originator shall request to delete an announced resource by using the DELETE Request in which the to parameter provides a URI that identifies the announced resource to be deleted.

Receiver: Once the Originator has been successfully authorized, the Receiver shall grant the Request after successful validation of the Request.

Delete the announced resource identified by the to parameter in the Request.

Respond to the Originator with the appropriate Response.

Originator after receiving the Response from the Receiver: .

If the announced resource is successfully deleted, the announceTo attribute in the original resource shall be updated to delete the URI for the de-announced resource.

Table 10.2.18.5-1: Resource Hosting CSE to Announce Resource: DELETE

| DELETE Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table. op: D fr: Identifier of the CSE that initiates the Request to: the URI where announced resource needs to be deleted |
| Local processing on Hosting CSE | No change from the basic procedure (section 10.1.4).Steps for the Receiver as described above |
| Information on Response message | No change from the basic procedure (section 10.1.4) |
| Post-Conditions | Steps for the 'Originator on receiving the Response from the Receiver' as described above |
| Exceptions | All exception described in the basic procedure (section 10.1.4) are applicable. |

### -----------------------End of change 6-------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### Clause 10.2.18.6 and 10.2.18.7 need to be updated. These clauses describe procedures for announcing and de-announcing "attributes" within the announced resources. Such procedure results in the creation and deletion of attributes at resources. So far, we do not have procedures for attribute creation and deletion AFTER a resource has been created.

### There are two options to consider:

### 1.  Define procedure for attribute announcement and de-announcement. With this option, such support for attribute creation/deletion will be supported only within the context of resource announcement/de-announcement.

### 2. Define procedures for attribute creation/deletion in general context. (partial addressing). With such procedures, attribute creation/deletion is supported not only for announced resources but for ALL resource.

### The recommendation is for Option 2 above.

### As regards Option 1:  Procedure for attribute announcement/de-announcement (creation/deletion) is described in proposal ARC-2014-1214R01_Attribute Announcement Procedure Option 2.

It is suggested to approve ARC-2014-1214R0. Based on such accepted procedures, the contributors will bring Change-Request to define general attribute creation/deletion procedure (Option 2 above) that will be applicable for all resources.

### -----------------------End of change 7-------------------------------------------

-----------------------Start of change 8-------------------------------------------

#### 10.2.18.6	Procedure for AE and CSE to initiate the creation or deletion of the Announced Attribute

In this section, the procedure for the AE and CSE (not the original resource hosting CSE) to initiate the creation or deletion of the announced attribute is explained using the relevant common attributes in the section 9.6.1.

Originator: The Originator of a Request for initiating the attribute announcement can be either AE or CSE (not the original resource hosting CSE). The Originator shall request to initiate the creation or deletion of the announced attribute by using the UPDATE Request to the announcedAttribute attribute in the original resource. The Originator shall perform as follows depending on whether it is a creation or a deletion of the announced attribute:

To create an announced attribute: The Originator shall add the attribute name of the original resource into the announcedAttribute attribute in the original resource using the UPDATE Request. Note that only the attribute marked with OP can be announced to the remote announced resource.

To delete an announced attribute: The Originator shall remove the attribute name from the announcedAttribute of the original resource by using the UPDATE Request.

Receiver: The Receiver shall be only the original resource hosting CSE. On receiving the Request, the Receiver shall perform as follows:

Check whether the Originator is authorized to the Request, and further check whether the Request is valid. The Request, that adds or deletes an attribute name that are not marked with OP, is invalid

If the Request provides a new attribute name that is not stored in the announcedAttribute attribute and is marked with OP as well, then the Receiver will announce the attribute to all announced resources listed in the announceTo attribute. The Receiver can use the CREATE Request to create the attribute in the announced resource. The initial value for the announced attribute shall use the same value with the original resource

If the Request removes the attribute name from the announcedAttribute attribute, then the Receiver will delete the attribute from all announced resources listed in the announceTo attribute. The Receiver can use the DELETE Request to delete the attribute in the announced resource

Table 10.2.18.6-1: Creating or Deletion of Announced Attribute

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | None |
| Information on Request message | Steps described for the Originator of the Request as described above |
| Local processing on Hosting CSE | Steps described for the Receiver of the Request as described above |
| Information on Response message | Steps described for the Receiver of the Request as described above |
| Post-Conditions | None |
| Exceptions | Local processing on the Receiver: The Request is invalid as described above |

#### 10.2.18.7	Procedure for original resource hosting CSE to Announce Attribute

In this section, the attribute announcement procedure is explained using the relevant common attributes in the section 9.6.1. This procedure shall be used for the original resource hosting CSE to create the announced attribute to the announced resource in the remote CSE (i.e., the attribute announcement).

Originator: The Originator of this Request shall only be the original resource hosting CSE. Only attributes marked with OP can be announced to the announced resource in the remote CSE. Originator shall request to create the announced attribute by using the CREATE Request as the same value with the original resource.

Receiver: On receiving the Request, the Receiver shall perform as follows:

Check whether the Originator is authorized for the Request, and further check whether the Request is valid. If the Request is valid, then the Receiver shall create the announced attribute according to the Request.

Respond to the Originator with the appropriate generic Response.

Originator after receiving the Response from the Receiver: On receiving the Response, the Originator shall perform as follows:

If the announced attribute is successfully created, then the announcedAttribute attribute shall be updated accordingly to include the attribute name for the successfully announced attribute in the Receiver.

For the newly announced attributes in the announcedAttribute attribute, the Originator shall further take the responsibility to synchronize attributes between the original resource and the announced resource

Table 10.2.18.7-1: Original Resource Hosting CSE to Announce Attribute: CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | Only the attribute marked with OP can be announced. |
| Information on Request message | Information described for the Originator of the CREATE Request as described above |
| Local processing on Hosting CSE | Steps described for the Receiver of the CREATE Request as described above |
| Information on Response message | Steps described for the Receiver of the CREATE Request as described above |
| Post-Conditions | Steps described for the 'Originator on receiving the Response from the Receiver' as described above |
| Exceptions | Local processing on the Receiver: The Request is invalid as described above |

#### 10.2.18.6	Procedure for original resource hosting CSE to delete the Announced Attribute

In this section, the procedure for deleting the announced attribute (i.e., the attribute de-announcement) is explained. This procedure shall be used for the original resource hosting CSE to delete the announced attribute that resides in the announced resource in the remote CSE.

Originator: The Originator of this Request shall only be the original resource hosting CSE. The Originator shall request to delete the announced attribute by using the DELETE Request in which the to parameter provides a URI that identifies the announced attribute to be deleted

Receiver: On receiving the Request, the Receiver shall perform as follows:

Check whether the Originator is authorized for the Request, and further check whether the Request is valid

If the Originator is authorized for the Request and the Request is valid, then delete the announced attribute identified by the to parameter in the Request

Respond to the Originator with the appropriate generic Response

Originator after receiving the Response from the Receiver: On receiving the Response, the Originator shall perform as follows:

If the announced attrubute is successfully deleted, then the announcedAttribute attribute in the original resource shall be updated accordingly to delete the attribute name that was de-announced.

Table 10.2.18.6-1: Original Resource Hosting CSE to Announce Attribute: DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | None |
| Information on Request message | No change from the generic procedure |
| Local processing on Hosting CSE | Steps described for the Receiver as described above |
| Information on Response message | No change to the generic procedure |
| Post-Conditions | Steps described for the 'Originator on receiving the Response from the Receiver' as described above |
| Exceptions | Local processing on the Receiver: The Request is invalid as described above |

-----------------------End of change 8-------------------------------------------

### -----------------------End of change 1 ---------------------------------------------

# Comments

This is Originator part and not Receiver

There are no specific error described above

Please note that the retrieval of the announced resource can only happening at the hosting CSE, the intermediate CSE don’t check anything, just forward the request.