| CHANGE REQUEST |
| --- |
| Group Name:* | TP#10 |
| Source:* | LG Electronics |
| Format:* | Plenary |
| Date:* | 2014-03-31 |
| Contact:* | Hongbeom Ahn, LG Electronics, Hongbeom.ahn@lge.com |
| Reason for Change/s:* | To answer the question, WHO creates the <node> resource. All AEs or IN-AE? |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_4_2 |
| Clauses/Sub Clauses* | 10.2.14 <node> Resource Procedure |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

It was asked that WHO creates the <node> resource. All AEs or IN-AE?

To answer this question,

- We can start discussing the principle of our current architecture. Based on our architecture, any AE with the proper authorization is able to do something (CRUD) to a target resource.

- As discussed in MAS #9.2 call, <node> resource is a placeholder for a set of <mgmtObj> resources. Further, any authorized AE can create this <node> resource under the Resource-Hosting CSE resource tree and easily gets the physical object information of a Node, this information is obtained by DM technologies or local service layer call instead of the AE.

- Any authorized CSE can create this <node> resource as well. For example, if an CSE creates CMDH Policy  resources under its <CSEBase> tree, some CMDH policies is linked with some specific(physical) context information of a Node to be applied, here for example battery status. In this case, the CSE can create <node> information to obtain batter status information.

Thus, the creator of <node> resource does not need to be limited to any specific AE. Rather any AE or CSE can create the <node> resource subject to proper authorization.

Further, as a result of MAS call, the <schedule> sub-resource will be taken out from <node> resource, the relevant Note will be removed and announcement-related sentence is removed from the CREATE description.

### -----------------------Start of change 1-------------------------------------------

### 10.2.14	<node> Resource Procedure

#### 10.2.14.1	Create <node>

This procedure shall be used for creating a <node> resource.

Originator: The Originator shall request to create a new <node> resource. The request shall address different resources depending on the type of node that is issuing the request, as described in 9.6.20. Following that, the Originator can create the child resources (defined in the 9.6.20) to acquire node specific information as occasion demands of the originator. The Originator shall be either an AE or CSE.

NOTE: The creation and usage of the  <node> resource is limited by M2M Service Provider policy for the management of the node.

Receiver: The Receiver or Hosting CSE shall:

- Check whether the Originator is authorized to request the procedure.

- Check whether the provided attributes of the <node> resource represent a valid Request.

- Upon successful validation of the above procedures, create a new <node> resource with given name in the Hosting CSE with the provided attributes.

Table 10.2.14.1-1: <node> CREATE

| Description |
| --- |
| Pre-Conditions | Originator has already registered. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: The representation of the <node> resource described in section 9.6.20. The following attributes from section 9.6.20 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the <node> resource as defined in 9.6.1 The following attributes from section 9.6.20 are optional for the request: “accessControlPolicyID” “expirationTime” “Labels” |
| Local processing on Hosting CSE | No change from the basic procedure described in section 10.1.1 |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: URI of the created <node> resource , according to section 10.1.1 |
| Post-Conditions | None |
| Exceptions | All exception described in the basic procedure (section 10.1.1) are applicable. |

#### 10.2.14.2	Retrieve <node>

This flow is used for retrieving the attributes of a <node> resource.

Originator: The Originator shall request to obtain <node> resource information by using RETRIEVE operation. The Originator can be either an Application Entity or a CSE.

Receiver: The Receiver shall:

- Check if the Originator has RETRIEVE privileges on the <node> resource and the request is valid.

- Upon successful validation, the Hosting CSE shall respond to the Originator with the appropriate responses.

Table 10.2.14.2-1: <node> RETRIEVE

| Description |
| --- |
| Pre-Conditions | The targeted <node> has been already created |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: void |
| Local processing on Hosting CSE | No change from the basic procedure described in section 10.1.2 |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: attributes of the <node> resource as defined in section 9.6.20. |
| Post-Conditions | None |
| Exceptions | All exception described in the basic procedure (section 10.1.2) are applicable. |

#### 10.2.14.3	Update <node>

This flow is used for updating the attributes and the actual data of a <node> resource and its child resources.

Originator: The Originator shall request to update attributes of an existing <node> resource by using an UPDATE operation. The request shall address the specific <node> resource reside in a CSE. The Originator may be either an AE or a CSE.

Receiver: The Receiver of an UPDATE request shall check whether the Originator is authorized to request operation. The Receiver shall check whether the provided attributes of the <node> resource represent a valid request for updating <node> resource.

Table 10.2.14.3-1: <node> UPDATE

| Description |
| --- |
| Pre-Conditions | The targeted <node> has been already created |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: attributes of the <node> resource as defined in 9.6.20 which need be updated, with the exception of the Read Only (RO) attributes cannot be modified |
| Local processing on Hosting CSE | No change from the generic procedure from section 10.1.3. |
| Information on Response message | No change from the generic procedure from section 10.1.3. |
| Post-Conditions | None |
| Exceptions | All exception described in the basic procedure (section 10.1.3) are applicable. |

#### 10.2.14.4	Delete <node>

This procedure shall be used for deleting an existing <node> resource.

Originator: The Originator shall request to delete an existing <node> resource by using DELETE operation. The Originator can be either an AE or a CSE.

Receiver or Hosting CSE: The Receiver shall check if the Originator has DELETE permission on the <node> resource and the request is valid. Upon successful validation, the CSE shall remove the resource from its repository and shall respond to the Originator with appropriate responses.

Table 10.2.14.4-1: <node> DELETE

| Description |
| --- |
| Pre-Conditions | The targeted <node> has been already created |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table. |
| Local processing on Hosting CSE | No change from the generic procedure from section 10.1.4. |
| Information on Response message | No change from the generic procedure from section 10.1.4. |
| Post-Conditions | The targeted resource and all the children resources shall not exist anymore. Also all the related credential shall be deleted. Editor’s Note: if and how credentials are cleaned is FFS, in scope of WG4. |
| Exceptions | All exception described in the basic procedure (section 10.1.4) are applicable. |