| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#10.0 |
| Source:* | InterDigital |
| Format:* | Plenary |
| Date:* | 2014-03-28 |
| Contact:* | Guang Lu, InterDigital, guang.lu@interdigital.com |
| Reason for Change/s:* | Need to add <statsConfig> and <statsCollect> child resource to <CSEBase> |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0001 v0.4.2 |
| Clauses/Sub Clauses* | 9.6.3 Resource Type CSEBase |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Agreed contribution ARC-2014-1177R02 states that the <statsConfig> and <statsCollect> resources “shall be located directly under <CSEBase> of IN-CSE”, but a corresponding update to <CSEBase> was overlooked at that time.

### -----------------------Start of change 1-------------------------------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.3-1 (0 indicates the optionality of the child resource).

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See section 9.6.4 |
| [variable] | <node> | 1 | See section 9.6.19 |
| [variable] | <application> | 0..n | See section 9.6.5 |
| [variable] | <container> | 0..n | See section 9.6.6 |
| [variable] | <group> | 0..n | See section 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See section 9.6.2 |
| [variable] | <subscription> | 0..n | See section 9.6.8 |
| [variable] | <mgmtObj> | 0..n | See section 9.6.15 |
| [Variable] | <mgmtCmd> | 0..n | See section 9.6.17 |
| [Variable] | <locationPolicy> | 0..n | See section 9.6.10 |
| [Variable] | <statsConfig> | 0..n | See section 9.6.31 |
| [Variable] | <statsCollect> | 0..n | See section 9.6.33 |

Editor’s Note: this list should be updated. Which resource types are added is FFS.

Editor’s Note: how to extend functionality is FFS.

The <CSEBase> resource shall contain the attributes described in Table 9.6.3-2.

Table 9.6.3-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aRI) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType (sRT) | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in section 9.2 |
| pointOfAccess (poA) | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <application> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. |

### -----------------------End of change 1---------------------------------------------