| CHANGE REQUEST |
| --- |
| Group Name:* | TP10 |
| Source:* | Guang Lu, InterDigital, Guang.Lu@InterDigital.com |
| Format:* | ARC 10 |
| Date:* | <2014-03-28> |
| Contact:* | Guang Lu, InterDigital, Guang.Lu@InterDigital.com |
| Reason for Change/s:* | Define the <mgmtObj> instance for the SCA resource <statsConfig> |
| CR against: Release* | 1 |
| CR against: TS/TR* | oneM2M-TS-0001 , V-0.4.2 |
| Clauses/Sub Clauses* | Annext D |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In clause 9.6.31 Resource Type statsConfig, it meantioned that this resource “may be provisioned using device management” as one way to establish the resource. To support this statement, the resource needs to be defined as an instance of the mgmtObj resource type.

This contribution provided the texts for Annex D to define statsConfig as an instance of mgmtObj.

Note that this contribution needs to align with any latest updates of the mgmtObj, if the update is agreed.

Revision 1: updated (shown in different revision marks) to align with the agreed approach of mapping to mgmtObj by WG5, based on Option 3 proposed in contribution MAS-2014-0358.

Revision 2: updated the name of the link to mgmtLink to be consistent with what’s defined for the <mgmtObj> resource type by ARC-2014-1266.

### -----------------------Start of change 1-------------------------------------------

## D.X	Resource statsConfig

This management resource corresponds to the <statsConfig> resource type defined in clause 9.6.31, and it shall be used when <statsConfig> is provisioned by management. The resource is mapped to an instance of the <mgmtObj> resource type.

Figure D.X-1: Structure of <statsConfig> resource

This resource shall contain the attributes according to their multiplicity in Table D.X-1 (0 indicates the optionality of the attribute).

Table D.X-1: Attributes of <statsConfig> resource

| Attribute Name of <statsConfig> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyID | 1..n | RW | See clause 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described |
| mgmtDefinition | 1 | WO | See clause 9.6.15. This attribute shall have the fixed value “statsConfig”. |
| objectID | 0..1 | WO | See clause 9.6.15 |
| objectPath | 0..1 | WO | See clause n 9.6.15 |
| description | 0..1 | RW | See clause 9.6.15 |
| mgmtLink | 0..n | RW | Link to the <eventConfig> resource |

## D.Y	Resource Type eventConfig

This resource is the instance for representing each type of event that the statistics can be collected, as defined in clause 9.6.32. The resource type of eventConfig is <mgmtObj>.

Figure D.Y-1: Structure of <eventConfig> resource

This resource shall contain the attributes according to their multiplicity in Table D.Y-1 (0 indicates the optionality of the attribute).

Table D.Y-1: Attributes of <eventConfig> resource

| Attribute Name of <eventConfig> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyID | 1..n | RW | See clause 9.6.1 where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described |
| objectID | 0..1 | WO | See clause 9.6.15 where this attribute is described |
| objectPath | 0..1 | WO | See clause 9.6.15 where this attribute is described |
| description | 0..1 | RW | See clause 9.6.15 where this attribute is described |
| eventID | 1 | RO | See clause 9.6.32 where this attribute is described |
| eventType | 1 | RW | See clause 9.6.32 where this attribute is described |
| eventStart | 0..1 | RW | See clause 9.6.32 where this attribute is described |
| eventEnd | 0..1 | RW | See clause 9.6.32 where this attribute is described |
| transactionType | 0..1 | RW | See clause 9.6.32 where this attribute is described |
| dataSize | 0..1 | RW | See clause 9.6.32 where this attribute is described |

### -----------------------End of change 1---------------------------------------------