| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC10 at |
| Title:* | Additional guidelines for how the system creates application instance IDs |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2014-03-30 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes adding some guidelines for how the system creates application instance ID

* * * Start of 1st Change * * *

### 7.1.2	Application Instance Identifier (App-Inst-ID)

An Application Instance Identifier (App-Inst-ID) uniquely identifies an M2M Application instance resident on an M2M node, or an M2M Application instance that requests to interact with an M2M node. An App-Inst-ID shall identify an Application for the purpose of all interactions from/to the Application within the M2M System.

It is the responsibility of the M2M Service Provider to ensure that the App-Inst-ID is globally unique. To that effect, there are 2 cases:

Case 1: The application itself creates its own AE-ID and shall provide it at registration

Case 2: The application does not provide an AE-ID at registration. In this case the local CSE shall create the AE-ID upon successful application registration, and shall return it to the AE.

For case 1, the local CSE shall assume that the AE-ID is made up of two parts. Part one shall include the Application ID (see 7.1.3). For the second part, the local CSE shall append its own CSE-ID to the application provided AE-ID to guarantee global uniqueness.

For case 2, the local CSE shall assume that the AE-ID is made up of two parts. Part one  shall include the Application ID (see clause 7.1.3). Part two shall include the CSE-ID of the local CSE concatenated with the either the username and phoneNumber attributes, if present, or any string at the discretion of the local CSE if these attributes are not available.

It is the responsibility of the local CSE to ensure global uniqueness of the AE-ID for either cases 1 or case 2, otherwise an appropriate response is returned in the response to the registration request

* * * End of 1st Change * * *

* * * Start of 2ndChange * * *

# Table 9.6.5-2: Attributes of <application> resource

| Attribute Name of <application> | Multiplicity | RW/ RO/ WO | Description | <applicationAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <applicationAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (e.g. "HeatingMonitoring") | OP |
| App-ID | 1 | RO | Application Identifier | OP |
| App-Inst-ID | 1 | RO | When the application resource refers to an actual application instance in the executing environment. | OP |
| pointOfAccess | 0..n | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g., IP address, FQDN, URI). This attribute shall be accessible only by the Application and the hosting CSE. | ?? |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the application; to be passed to the application | OP |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <application> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. | ?? |
| username | 0..1 | RW | The username of the user in a multi-user application | OP |
| phoneNumber | 0..1 | RW | The phoneNumber of the user in a multi-user application. This attribute shall be provided if the username attribute is prersent | OP |

Editor's Note: Cardinality of pointOfAccess attribute (0..n) needs to be investigated for all its occurrences.

* * * End of 2nd Change * * *

* * * Start of 3rd Change * * *

Figure 9.6.5-1: Structure of <application> resource 
(only resource specific attributes are shown)

Editor's Note: To update the picture to include "username", "phoneNumber”

* * * End of 3rd Change * * *