| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC10 at |
| Title:* | Additional guidelines for Resource Addressing during Discovery |
| Source:* | Ericsson |
| Contact: | George Foti |
| Date:* | 2014-03-30 |
| Abstract:* | Proposal to include the following in the TS |
| Agenda Item:* | To be defined |
| Work item(s): | M2M Architecture |
| Document(s) Impacted* | Architecture TS (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to discuss the definitions for inclusion in the TS architecture |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution proposes adding some guidelines for the selection of the a resource addressing scheme to be returned during a discovery procedure

* * * Start of 1st Change * * *

#### 10.2.3.1	Introduction

The resource discovery procedures allow discovering of resources residing on a CSE. The use of filter criteria allows limiting the scope of the results. Filtering shall be performed on a subset of the offered resource attributes using a query string. A match, that may include ranges, may be performed on the query string, and a successful response may be returned with a list for the resources addressable in any of the forms expressed in section 9.3.1 that contains the matching attributes or a URI of a temporary resource holding the list.

Editor's Note: It is FFS how this temporary resource is operated such as the access right of this temporary resource, expiration time, the condition for creation.

Resource discovery shall be done using the RETRIEVE method by an Originator which shall also include the root of where the discovery begins: <startURI>. Filter criteria may be provided as a parameter to the Retrieve method. The filter criteria describe the rules for resource discovery, e.g. searching scope, topic, semantic relationships, and matching string. The filter criteria can also contain the parameters for specifying the maximum size of the answer (upper limit), and/or sorting criteria for specifying in which order the searching result should be organized.

The resource discovery procedures shall identify all matching resources from the entire hierarchy under <startURI>. The filter criteria provided by an Originator or the discovery results may be modified by the Hosting CSE to restrict the scope of discoverable resources according to the Originator's access right or service subscription.

The Hosting CSE may also implement a configured upper limit on the size of the answer. In such a case when both the Originator and the Hosting CSE have the upper limits, the smaller of the upper limit in the Hosting CSE and the upper limit of the Originator shall apply.

#### 10.2.3.2	Discovery procedure via Retrieve Operation

This procedure shall be used for the discovery of resources under <startURI> that match the provided filter criteria. The discovery result shall be returned to the Originator using a successful message.

Originator: The Originator can be an AE or a CSE. The Originator shall provide the <startURI> URI in the Request message. Filter criteria may be provided as a parameter by the Originator.

Receiver or Hosting CSE: The Hosting CSE shall read the values of all attributes belonging to the addressed resource structure and the references of all sub-resources and it shall build a representation of these. The Hosting CSE shall use the appropriate addressing (see section 9.3.1) for each element included in the list in accordance with the incoming request. If filter criteria is provided in the request, the Hosting CSE uses it identifying the resources whose attributes match the filter criteria. The Hosting CSE shall respond to the Originator with the appropriate list of discovered resources in the Hosting CSE. If sorting criteria has been provided by the Originator, the list of discovered resources shall be sorted in that order.

The Hosting CSE may modify the filter criteria including upper limit provided by the Originator or the discovery results based on the local policies.

If the size of the result list is bigger than the upper limit, or the scope of discoverable resources, according to the Originator's access right or service subscription has been reduced by the Hosting CSE, the full list is not returned. Instead, an incomplete list is returned and an indication is added in the response for warning the device.

The Hosting CSE may propagate the discovery request to other CSEs according to resource discovery policies.

Editor's Note: It is FFS about discovery propagation mechanism, i.e. multi-hop discovery propagation and its policies.

# Table 10.2.3.2-1: Discovery procedure via Retrieve Operation

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to discover resources in the Hosting CSE |
| Information on Request message | URI of the discovery resource: <startURI> Filter criteria for searching and expected returned result |
| Local processing on Hosting CSE | Checks the validity of the Request (e.g. format of filter criteria) Checks if the request is in accordance with the M2M service subscription May change the filter criteria according to local policies Searches matched resources from the addressed resource hierarchy Propagates the discovery request to other CSEs if it is permitted by discovery policies Limits the discovery result according to access rights of the discovered resources Limits the discovery result according to the upper limit on the size of the answer Sorts the results according to the sorting criteria |
| Information on Response message | Contains the URI list of discovered resources expressed in any of the methods depicted in section 9.3.1. Contains an incomplete list warning if the full list is not returned |
| Post-Conditions | None |
| Exceptions | Local processing on Hosting CSE: The requesting M2M AE or CSE is not registered The request contains invalid parameters |

* * * End of 1st Change * * *

* * * Start of 2nd Change * * *

### Introduce the following additional mi parameter in section 8.1.2 Request

- Disresptype: conditionally mandatory parameter applicable only to resource discovery related requests to indicate the preference of the originator for the returned information in the response. This parameter shall take on one of the following values reflecting the options in section 9.3.1:

  - Hierarchal URI option

  - Non-hierarchal URI option

  - CSE, and resource identifier option

  - Don’t care

* * * End of 2nd Change * * *