| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* | Plenary |
| Date:* | 2014-04-01 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Reason for Change/s:* | Make multiplicity of accessControlPolicyID consistent throughout TS |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0001 V0.4.3 |
| Clauses/Sub Clauses* | Some clauses |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Since multiplicity of accessControlPolicy is different for several resource types, this contribution proposes to make it consistent.

Since <AccessControlPolicy> resource is able to contain multiple privileges, there is no reason to keep more than 1.

Hosting CSE makes use of accessControlPolicyID of parent resource when the resource doesn’t have accessControlPolicyID attribute or the accessControlPolicyID attribute contains wrong link. ( make multiplicity of accessControlPolicyID 0..1 for entire resource types except CSEBase resource type (multiplicity 1).

### -----------------------Start of change 1-------------------------------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.3-1 (0 indicates the optionality of the child resource).

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See section 9.6.4 |
| [variable] | <node> | 1 | See section 9.6.19 |
| [variable] | <application> | 0..n | See section 9.6.5 |
| [variable] | <container> | 0..n | See section 9.6.6 |
| [variable] | <group> | 0..n | See section 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See section 9.6.2 |
| [variable] | <subscription> | 0..n | See section 9.6.8 |
| [variable] | <mgmtObj> | 0..n | See section 9.6.15 |
| [Variable] | <mgmtCmd> | 0..n | See section 9.6.17 |
| [Variable] | <locationPolicy> | 0..n | See section 9.6.10 |

{9.6.3.a} Editor’s Note: this list should be updated. Which resource types are added is FFS.

{9.6.3.b} Editor’s Note: how to extend functionality is FFS.

The <CSEBase> resource shall contain the attributes described in Table 9.6.3-2.

Table 9.6.3-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aRI) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType (sRT) | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in section 9.2 |
| pointOfAccess (poA) | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <application> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.4	Resource Type remoteCSE

A <remoteCSE> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCSE> resource in the registering CSE's <CSEBase>.

For example, when CSE1 registers with CSE2, there will be two <remoteCSE> resources created: one in CSE1 <CSEBase1>/<remoteCSE2> and one in CSE2 <CSEBase2>/<remoteCSE1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCSE2> is only local to CSE1 and is for its internal use.

Figure 9.6.4-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

{9.6.4.a} Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.4-1 (0 indicates the optionality of the child resource).

# Table 9.6.4-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <application> | 0..n | See clause 9.6.5 | <applicatoinAnnc> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <mgmtObj> | 0..n | See clause 9.6.15 | <mgmtObjAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. If requestReachability is FALSE, the CSE that created this <remoteCSE> should create a <pollingChannel> resource and perform long polling. | ?? |
| [variable] | <node> | 0..1 | See section 9.6.19. This child resource contains the node specific information only when the information represented by this resource is from a node of type ASN or MN. | ?? |

The <remoteCSE> resource shall contain the attributes described in Table 9.6.4-2.

# Table 9.6.4-2: Attributes of <remoteCSE> resource

| Attribute Name of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <remoteCSEAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| cseType (csT) | 1 | WO | Indicates the type of CSE node represented by the created resource. | OP |
| pointOfAccess (poA) | 0..n | RW | For request-reachable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not request-reachable. | OP |
| CSEBase (bRt) | 1 | WO | The URI of the CSEBase of the original CSE represented by remote CSE. | OP |
| CSE-ID | 1 | WO | The globally unique CSE identifier. | OP |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. | ?? |
| requestReachability | 1 | RW | If the CSE that created this <remoteCSE> can receive a request from other AE/CSE(s), this attribute is set to “TRUE” otherwise “FALSE”. NOTE: Even if this attribute is set to “FALSE”, it does not mean it AE/CSE is always unreachable by all entities. E.g., the requesting AE/CSE is behind the same NAT, so it can communicate within the same NAT. | ?? |

<remoteCSE> and announced <remoteCSE> shall have different resourceType coding.

{9.6.4.b} Editor's Note on CSE-ID: an alignment between CSE-ID and CSEBase is needed.

{9.6.4.c} Editor's Note on CSEBase: the alignment with naming convention proposed for inter-M2M service provider is needed.

{9.6.4.d} Editor's Note on child resources: child resources of <remoteCse> resource can accommodate listed resources and their announced versions.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

Kindly request rapporteur to change multiplicity of accessControlPolicyID to 0..1 for the below resource types listed.

9.6.5 <application>

9.6.10 <locationPolicy>

9.6.16 <parameters>

9.6.17 <mgmtCmd>

9.6.18 <execInstance>

9.6.19 <node>

9.6.22 <pollingChannel>

9.6.23 <cmdhPolicy>

9.6.24 <cmdhDefaults>

9.6.25 <cmdhDefEcValue>

9.6.26 <cmdhEcDefParamValues>

9.6.27 <cmdhLimits>

9.6.28 <cmdhNetworkAccessRules>

9.6.29 <cmdhNwAccessRule>

9.6.30 < cmdhBuffer>

9.6.31 <statsConfig>

9.6.32 <eventConfig>

9.6.33 <statsCollect>

D.2 <firmware>

D.3 <software>

D.4 <memory>

D.5 <areaNwkInfo>

D.6 <areaNwkDeviceInfo>

D.7 <battery>

D.8 <deviceInfo>

D.9 <deviceCapability>

D.10 <capabilityInstance>

D.11 <reboot>

D.12 <eventLog>

### -----------------------End of change 3---------------------------------------------