| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Barbara Pareglio, NEC barara.pareglio@neclab.eu |
| Format:* | ARC#10 |
| Date:* | 2014-03-30 |
| Contact:* | Barbara Pareglio, NEC |
| Reason for Change/s:* | Cleaned up clause 9.6.12 |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Propose to clean up the clause 9.6.12 for the <request> resource type.

Please note that there is already a contribution that add the AccessControlPolicy attribute but it covers the whole TS, so it is added here for simplicity.

### -----------------------Start of change 1-------------------------------------------

### 9.6.12	Resource Type request

The use of this resource type is optional depending on the configuration.

Creation of a <request> resource can only be done on a local CSE implicitly when an AE issues a request for any other resource type to the Local CSE. Creation of such resourceType is only permitted by the Local CSE as a result of any request from the Originator which contains the rt parameter in the request message.

When a CSE is requested to initiate an operation for which the result should be available to the Originator by reference ('rt' information of the request set to 'Acknowledgement'), the local CSE which received the Request directly from the Originator may need to provide a reference back to the Originator so that the Originator can access attributes of the Request at a later time - for instance in order to retrieve the result of an operation that was taking a longer time. The Originator (or any other authorized entity depending on access rights) can access the request status and the requested operation result through it.

The <request> resource may get deleted by the CSE that is hosting it:

- when the result of the requested operation (if any result was requested at all) has been sent back to the Originator (either by notification to the Originator or by retrieval initiated by the Originator) or successfully Retrieved by the originator;

- when the expiration time of the <request> resource is reached;

- at any other time -  depending on local settings in the CSE that hosts the <request> resource or depending on the entity that is authorized to delete the resource.

{9.6.12.a} Editor's Note: The exact way how to define that setting (e.g. via DM) is FFS.

For the purpose of providing a standardized structure for expressing and accessing the context of a previously issued Request, the resource type request is defined.

Figure 9.6.12-1: Structure of <request> resource
(only resource specific attributes are shown)

The resource <request> shall contain the attributes according to their multiplicity shown in Table 9.6.12-1.

# Table 9.6.12-1: Attributes of <request> resource

| Attribute Name of <request> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| expirationTime (et) | 1 | RW | See clause 9.6.1 where this common attribute is described. The value of the expirationTime is chosen by the CSE dependent on the rqet and rset parameter if present or the expirationTime of the original request. |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyID | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| versionTag (vT) | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| operation | 1 | RO | It contains the value of the parameter op in the request message. |
| target | 1 | RO | It contains the value of the parameter to from the request message. |
| originator | 1 | RO | It contains the value of the fr parameter from the request message. |
| metaInformation | 1 | RO | Meta information about the request. The content of this attribute is equivalent to informational the optional parameters described in clause 8.1. |
| content | 1 | RO | Contains the content that is carried in the cn parameter in request message.. |
| requestStatus | 1 | RO | Contains information on the current status of the Request, e.g. "accepted and pending". |
| operationResult | 1 | WO | Contains the URI of the resource that represent the result of the request. |

.

All other operations on <request> resource are controlled by the Access Control Policy.

### -----------------------End of change 1-------------------------------------------

# Comments

Which configuration? Do we mean policy or configuration? Is there any relation with CMDH?

Is this resource given back in the ack or not? It is never stated how the originator gets this resource.

Which status are possible? We should say it in this TS.

Is it a text information or is it the URI of the result resource?

Make it clear from the beginning that this is not possible to CREATE//DELETE from any reference point Mca, Mcc but it can only be RETRIEVE and UPDATED

For which the AccessControlPolicy is missing, so how that is managed?

Any operation in general shall be authorized according to the accessControl Policy, however if we want to really block CREATE and DELETE and let only the hosting CSE do that then ita has t obe clearly specified that there is a restriction.