| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 Architecture |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | ARC10.0 |
| Date:* | 2014-04-01 |
| Contact:* | Josef Blanz, jblanz@qti.qualcomm.com |
| Reason for Change/s:* | The procedures to access remotely hosted resources via CMDH and <delivery> resources are not defined correctly. References to outdated parameters that are not anymore supported in TS-0001 are used. Also the usage of blocking requests has been missing. This CR is correcting these errors. Without such corrections, the access to remotely hosted resources via CMDH using <delivery> resources is not implementable. |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* | 10.2.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR suggests to correct the following errors in the description of procedures to access use remotely hosted resources via CMDH and usage of <delivery> resource types in clause 10.2.4:

- Remove or correct references to unsupported paramterts for requests (defined in clause 8.1)

  - Some of the descriptions still refers to parameters that do not exist anymore in clause 8.1 or have been replaced by others

  - Some of the descriptions assume that certain parameters would be part of the cn information, which is not the case anymore.

- Define that blocking requests shall be used (as defined in clause 8.2) for requests between CSEs to create <delivery> resources on hops following the original request(s)

  - It is important to define precisely in the specification how a CSE has to forward requests to another CSE via the creation of a <delivery> resource on the next CSE on the path to the target CSE. I.e. it needs to be defined wheather that would need to be done  with a blocking versus a non-blocking request.

  - When requesting the creation of a <delivery> resources – which can only happen between neighboring CSEs – it does not make sense to use non-blocking requests since the CSE that is making the request for creating a new <delivery> resource on a neighboring CSE wants to know whether the other CSE is willing to assume the responsibility for delivering the data. In order to know how to proceed with buffered data (can it be removed? Is another delivery attempts needed?), the CSE which issues a request to create a <delivery> resource on another CSE needs to know about the acceptance of this request in a failry short time. Therefore it seems unreasonable to issue a non-blocking request for creating a <delivery> resource.

- Corrections to avoid any implications on stage 3 details in stage 2 specifications.

- Use of normative language

### -----------------------Start of change 1-------------------------------------------

### 10.2.4	Access to Remotely Hosted Resources via CMDH CSF

#### 10.2.4.1	Introduction to useage of <delivery> resource type

In this introduction an example for delivering information from a source CSE to a target CSE via the use of the <delivery> resource is explained.

The information flow depicted in figure 10.2.4.1-1 defines the exchange of Requests/Responses for processing an original request targeting a resource that is not hosted on the Local CSE of the request Originator. The following assumptions hold:

Originator is AE1;

AE1 is registered with CSE1, i.e. CSE1 is the local CSE for AE1;

The original Request is an UPDATE to a remote resource hosted on CSE3, i.e. CSE3 is the Hosing CSE for the target resource;

UPDATE options in the original Request are selected such that no feedback after completion of the update operation was requested, i.e. AE1 decided that it does not need to hear back from CSE3; this is expressed by setting the rc information to "nothing", see section 8.1.2.

Delivery related parameters included in the original UPDATE request (may be set via CMDH policies): rqet , ec, da and rp;

rqet indicates how long the forwarding of the request can last at most

ec  indicates the event category that should be used by CMDH to handle this request

rp indicates how long after the request has expired, the local request context should still be available for retrieving status or result information.

da would be set to ON indicating that <delivery> resource shall be used for forwarding the request

CSE1 is the CSE of an Application Service Node.

CSE1 is registered with CSE2 and interacts with CSE2 via the reference point Mcc(1).

CSE2 is the CSE of a Middle Node

CSE2 is registered with CSE3 and interacts with CSE3 via the reference point Mcc(2)

CSE3 is the CSE of an Infrastructure Node.

The Originator AE1 shall get a confirmation from CSE1 when the original Request is accepted. The response informs AE1 that CSE1 has accepted the Request and has accepted responsibility to execute on the requested operation. Furthermore, AE1 has expressed by setting rc to "nothing" that no result of the requested operation is expected to come back from CSE3. With the provided reference (Req-Ref in figure 10.2.2.1-1), AE1 can retrieve the status of the issued request at a later time, for instance to find out if the request was already forwarded to CSE2 or if it is still waiting for being forwarded on CSE1. Before accepting the request from AE1, CSE1 has also verified if the delivery related parameters expressed by AE1 (settings of "rqet" and "ec") are in line with provisioned CMDH policies. AE1 may not be authorized to use certain values for "rqet" or "ec".

In line with the delivery related parameters, CSE1 is generating a local <delivery> resource on CSE1 and attempts to forward the content of it in line with provisioned CMDH policies at a suitable time and via a suitable connection to CSE2 by requesting the creation of a <delivery> resource on CSE2. In this example case, the lifespan attribute of this delivery resource is set to the same value as the rqet parameter expressed by AE1. In general – i.e. also in cases where more than one original request is aggregated into a single create request for a <delivery> resource – the lifespan and eventCat attributes of the to be created <delivery> resource shall be set consistent with the rqet and ec parameters in the set of original requests, see the attribute definitions in clause 9.6.11

CSE1 shall use a blocking request for requesting creation of a <delivery> resource on CSE2.

When CSE2 has accepted the incoming request from CSE1, CSE1 may delete the data attribute of the local <delivery> resource. Furthermore - if the expiration time of the local <delivery> resource is not exhausted - the local CSE shall update the status of the local <delivery> resource to indicate that it has been forwarded to CSE2. CSE1 shall also update the status of the original request to indicate that it has been forwarded and it may delete the data attribute of the original request.

When CSE2 has accepted the request to create a local <delivery> resource, it shall attempt to forward it to CSE3. In line with the delivery related parameters, CSE2 shall create a local <delivery> resource on CSE2 and and shall attempt to forward it in line with provisioned CMDH policies at a suitable time and via a suitable connection to CSE3 by requesting the creation of a <delivery> resource on CSE3.

CSE2 shall use a blocking request for requesting creation of a <delivery> resource on CSE3.

When CSE3 has accepted the incoming request from CSE2, CSE2 may delete the data attribute of the local <delivery> resource. Furthermore - if the expiration time of the local <delivery> resource is not exhausted - the local CSE shall update the status of the local <delivery> resource to indicate that it has been forwarded to CSE3.

When CSE3 has accepted the request to create a local <delivery> resource, it shall determine that the target of the delivery was CSE3 itself. Therefore it shall forward internally the original request contained in the data attribute of the <delivery> resource.

Within CSE3, CSFs that are responsible for checking and executing local access to resources in DMR CSF will execute the originally requested UPDATE operation. If successful, the targeted resource will be updated with the content provided by the Originator.

Since in the depicted case no result needed to be sent back to the Originator, the processing for the requested operation is then completed.

Figure 10.2.4.1-1: CMDH information flow for 2 hops - 
no result needs to be returned after operation completes

The following procedures shall be triggered by requesting the corresponding operations on a <delivery> resource:

Initiate the delivery of one or more original request(s) stored for later forwarding from one CSE to another CSE:

Request a CREATE operation for a <delivery> resource from an issuing CSE to a receiving CSE.

The original request(s) need to be contained in the "data" attribute of the <delivery> resource.

If successful, the receiving CSE takes the responsibility to further execute on the delivery process for the original Request.

If not successful, the issuing CSE cannot assume that the receiving CSE will carry out the delivery of the original request.

Get information about the status of a pending delivery process for an original request:

Request a RETRIEVE operation of the content of a <delivery> resource representing a pending delivery or part of it.

The status of the pending forwarding process is reflected the "deliveryMetaData" attribute defined in the <delivery> resource.

Change parameters of pending delivery process:

Request an UPDATE operation on applicable attributes of the <delivery> resource representing the pending delivery.

For instance the time allowed for completion of a delivery process could be modified by updating the "lifespan" attribute of an existing <delivery> resource.

Cancel a pending delivery request:

Request a DELETE operation of a <delivery> resource that represents a pending delivery process.

-----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 10.2.4.2	Create <delivery>

This procedure shall be used for requesting a CSE to take responsibility to deliver the provided data to a target CSE in line with CMDH parameters and provisioned CMDH policies in case <delivery> resource based CMDH processing is used. If indicated by the Originator, the Receiver shall confirm the acceptance of delivery responsibility by a successful Response.

Originator: The Originator of a Create request for a <delivery> resource can only be a CSE. The Originator needs to provide the content of a <delivery> resource type together with the Create request or can Update it after a successful creation of the <delivery> resource with empty data attribute. Otherwise the Receiver cannot accept the Create Request. The Originator shall use a blocking request for issuing the Create request to the Receiver.

Receiver: The receiver of a Create request for a <delivery> resource shall check whether the Originator is authorized to request a delivery procedure. The Receiver of the Create Request shall further check whether the provided attributes of the <delivery> resource that is requested to be created represents a valid request for forwarding data to a target CSE. If the Originator of the Create request is authorized and the Request is valid, the Receiver shall check whether it can actually satisfy the requested delivery in line with provisioned CMDH policies and requested eventCat and lifespan attributes of the <delivery> resource. If all these checks are positive, the Receiver shall create the requested <delivery> resource and assumes responsibility for delivering the requested data to the target CSE as soon as the content of the data attribute is available. In case an operation result is expected by the Originator, the Receiver shall confirm acceptance of the responsibility by indicating a successful creation of the <delivery> resource. If the Receiver CSE is the target CSE of the requested delivery, it shall forward the content of the delivered data - which represents one or more forwarded original request(s) -  to the internal CSFs that handle incoming requests and continue processing of the forwarded request(s).

# Table 10.2.4.2-1: <delivery> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | Originator is a CSE and is responsible for delivery of data to a target CSE. Originator needs to forward the data and delivery responsibility to the Receiver. |
| Information on Request message | rt: Shall be set to ‘Result’ which means a blocking request is issued cn: Content of a <delivery> resource in line with the definition in clause 9.6.11 representing a valid request for delivery of data to a target CSE All other information in the Request message are the same as in the generic procedure. |
| Local processing on Hosting CSE | Check whether the originator is authorized to request a delivery procedure on the receiver CSE Check whether the provided attributes of the <delivery> resource that is requested to be created represents a valid request for delivering data to a target CSE. Check whether Receiver CSE can actually satisfy the requested delivery in line with provisioned policies and requested delivery parameters If all checks are positive, the receiver shall create the requested <delivery> resource and assumes responsibility for delivering the provided data to the target CSE. If the Receiver CSE is the target CSE of the requested delivery, it shall forward the content of the delivered data attribute to the internal CSFs that will interpret the delivered data as a forwarded request from a remote Originator. |
| Information on Response message | In case the Originator CSE has not asked for a Result of the requested Operation(rc set to ‘nothing’), the Response only contains an Acknowledgement indicator. This only indicates that the Receiver CSE received the Request. It does NOT indicate whether the Receiver CSE was able to take on responsibility for delivery of the data. In case the Originator CSE asked for the status of the requested Operation to be contained in the Result of the requested Operation(rc not set to ‘nothing’), the Receiver CSE shall respond with a Success or Failure indicator. In case the Originator CSE asked for the status of the requested Operation and the URI of the created Resource to be contained in the Result of the Request, the Receiver CSE shall respond with a Success indicator including the URI of the created <delivery> resource in case it has taken on responsibility to deliver the data to the target CSE or with Failure indicator including an error indication otherwise. |
| Post-Conditions | The Originator CSE shall update the local <delivery> resource to reflect the new status of the delivery process (e.g. '{Receiver-CSE-ID} accepted delivery responsibility'). In case the Originator CSE got a Success indicator as a Response, it shall stop any further delivery attempts. In that case or if there was no indication of a need to provide a result of the operation, the Originator CSE may delete the content of the 'data' attribute of the local <delivery> resource. In case the Originator CSE got a Failure indicator as a response, it may initiate further delivery attempts in line with CMDH policies and delivery parameters and depending on the reason for Failure. In case the Receiver CSE is the target CSE of the delivery, the Receiver CSE needs to execute on the forwarded request contained in the delivered data. |
| Exceptions | The Originator CSE is not authorized to request a delivery procedure on the Receiver CSE The provided content of the <delivery> resource is not in line with the specified structure. The provided content of the <delivery> resource represents a request for delivery that is not consistent (e.g. lifespan attribute already expired) The provided content of the <delivery> resource represents a request for delivery that cannot be met by the Receiver CSE within the limits of the provided delivery parameters and the provisioned CMDH policies on the Receiver CSE. |

#### 10.2.4.3	Retrieve <delivery>

This procedure shall be used for requesting a CSE to provide information on a previously created <delivery> resource which represents delivery of data to a target CSE.

Originator: Originator can be a CSE or an Application.

Receiver: The Receiver shall provide the content of the addressed <delivery> resource or the addressed attributes thereof.

# Table 10.2.4.3-1: <delivery> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | Originator needs to retrieve information about a previously issued delivery |
| Information on Request message | All information in the Request message are the same as in the generic procedure |
| Local processing on Hosting CSE | No change to generic procedure |
| Information on Response message | No change to generic procedure |
| Post-Conditions | None |
| Exceptions | The Originator CSE is not authorized to retrieve the <delivery> resource or the addressed parts of it The addressed <delivery> resource does not exist |

#### 10.2.4.4	Update <delivery>

This procedure shall be used for requesting a CSE to update information on a previously created <delivery> resource which represents a pending delivery of data to a target CSE. The update may have impact on further processing of the delivery.

Originator: Originator can be a CSE or an application. Originator needs to be authorized to modify the addressed <delivery> resource, i.e. it needs to be authorized to change the represented delivery process.

Receiver: The Receiver shall change the content of the addressed <delivery> resource or the addressed attributes thereof and also modify the corresponding parameters of the delivery process

# Table 10.2.4.4-1: <delivery> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Originator needs to modify information about a previously issued delivery that is still pending, i.e. it has not yet been forwarded to another CSE |
| Information on Request message | cn: URI of the <deliver> resource Content of a <delivery> resource in line with the definition in clause 9.6.11 representing a valid request for delivery of data to a target CSE All other information in the Request message are the same as in the generic procedure |
| Local processing on Hosting CSE | Receiver CSE checks if the requested changes to the delivery process can actually be accomplished. If possible, the Receiver CSE modifies the previously established delivery process and changes the respective content of the <delivery> resource |
| Information on Response message | Same as in the generic procedure. Successful Response messages indicate that the delivery process was modified as requested |
| Post-Conditions | None |
| Exceptions | The Originator CSE is not authorized to modify the <delivery> resource or the addressed parts of it The addressed <delivery> resource does not exist The responsibility for the further processing of the delivery process represented by the addressed <delivery> process was already forwarded to another CSE |

#### 10.2.4.5	Delete <delivery>

This procedure shall be used for requesting a CSE to cancel a pending delivery of data to a target CSE or to delete the <delivery> resource of an already executed delivery.

Originator: Originator can be a CSE or an Application. Originator needs to be authorized to modify the addressed <delivery> resource, i.e. it needs to be authorized to change the represented delivery process.

Receiver: The Receiver shall remove the addressed <delivery> resource and stop the corresponding delivery process if it is still pending

# Table 10.2.4.5-1: <delivery> DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Originator needs to cancel a previously issued delivery that is still pending, i.e. it has not yet been forwarded to another CSE or Originator needs to remove the <delivery> resource representing an already executed delivery |
| Information on Request message | No change to generic procedure |
| Local processing on Hosting CSE | Receiver CSE checks if the corresponding delivery process is still pending. If so, it stops that delivery process Receiver CSE removes the addressed <delivery> resource |
| Information on Response message | Same as in the generic procedure. Successful Response messages indicate that the delivery process was stopped as requested |
| Post-Conditions | None |
| Exceptions | The Originator CSE is not authorized to delete the <delivery> The addressed <delivery> resource does not exist |

### -----------------------End of change 2---------------------------------------------