| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Huawei, NTT DOCOMO |
| Format:* | ARC_10.1 or ARC #10.0 bis |
| Date:* | <2014-04-23> |
| Contact:* | Mitch Tseng, Huawei Technologies, mitch@T-infoserv.com Syed Husain, NTT DOCOMO, shusain2016@gmail.com |
| Reason for Change/s:* | This contribution proposes modifications related to Registration CSF to clarify the support for Application Discovery. |
| CR against: Release* | Release 1.0.0 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_5_0 |
| Clauses/Sub Clauses* | Clause 6.2.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# The Registration CSF is defined in clause 6.2.9. Although an AE is allowed to register with another AE or a CSE, the current text does not reflect the information covering the handling of  AEs.  This CR proposes to have add Registration information to explicitly include the application/service information so that an AE registrated on a CSE can be discovered via Discovery CSF with the same procedure as discovering a resource on a CSE. This contribution is also revised to remove normative text, based on agreement reached on ARC-2014-1218 at the TP#10 meeting.

### ------------------------------Start of changes -------------------------------------------

### 6.2.9	Registration

#### 6.2.9.1	General Concepts

The Registration (REG) CSF is responsible for processing a request from an AE or another CSE to register with a local CSE in order to allow the registered entities to use the services offered by the registered-with local CSE. The REG CSF also processes registration of a device (i.e., ASN or ADN), to allow registration of device's properties/attributes with the CSE.

#### 6.2.9.2	Detailed Descriptions

Registration is the process of delivering AE or CSE information to another CSE in order to use M2M Services.

An AE on an ASN, a MN, or an IN performs registration locally with the corresponding CSE in order to use M2M services offered by that CSE. An AE on an ADN performs registration with the CSE on a MN or IN in order to use M2M services offered by that CSE. A node-less AE performs registration with the corresponding CSE on an IN in order to use M2M services offered by that CSE. A registered AE interacts with its local CSE (when it is the target CSE) without the need to have the local CSE register with other CSEs.

The CSE on an ASN performs registration with the CSE in the MN in order to be able to use M2M services offered by the CSE in the MN. As a result of successful ASN-CSE registration with the MN-CSE, the CSE on the ASN establishs a peering relationship allowing it to exchange information.

The CSE on a MN performs registration with the CSE of another MN in order to be able to use M2M services offered by the CSE in the other Middle Node. As a result of successful MN-CSE registration with the other MN-CSE, the CSE on the MNs establishes a peering relationship allowing it to exchange information.

The CSE on an ASN or on a MN performs registration with the CSE in the IN in order to be able to use M2M services offered by the CSE in the IN. As a result of successful ASN/MN registration with the IN-CSE, the CSEs on ASN/MN and IN establishes a peering relationship allowing it to exchange information.

For an AE/CSE registering with another CSE, it is possible that  the other CSE can expose (assuming permission is granted) the resources and applications/services registeded locally through DIS CSF.

The service functions supported by the REG CSF are as follows:

- Ability for AEs to exchange information via CSEs following successful registration of:

- AEs with their associated CSE.

- One of these CSEs with the other CSE, as per Table 6.2.9.2-1.

Note: Such registrations are applicable to a single M2M Service Provider Domain.

- A (physical) device registers with its local CSE for registering its properties/attributes. Such registration enables correlation of device identities such as M2M-Node-ID with the CSE-ID.

- The Originator (Registree) in Table 6.2.9.2-1 requests the registration and the Receiver (Registrar) is responsible for verifying the request, and checking the authentication and authorization of the Originator in order to establish a peer relationship.

- An instance of the same AE registers to one CSE (ASN-CSE, MN-CSE or IN-CSE) at one time.

- An instance of the same ASN-CSE registers with one other CSE (MN-CSE or IN-CSE) at one time.

- An instance of the same MN-CSE registers with one other IN-CSE at one time.

- An MN-CSE supports only a single registration towards another MN-CSE or an IN-CSE. A concatenation (registration chain) of multiple uni-directional registrations forming a loop must be avoided. E.g., Two MN-CSEs A and B registering with each other must be avoided. Three MN-CSEs A, B and C, where A registers to B, and B registers to C, is allowed but then C registering to A is not allowed.

- Registration information includes:

- Identifier.

- Reachability schedules; which are elements of a node's policy, and specify when messaging may occur between nodes. Reachability schedules may be used in conjunction with other policy elements. When reachability schedules are not present in a node then that node is expected to be always reachable.

- Description of resources or applications/services of the registeree AE/CSE.

The following Table shows which oneM2M entity types may register with which other entity types.

Table 6.2.9.2-1: Entity Registration

| Originator (Registree) | Receiver (Registrar) | Registration Procedure |
| --- | --- | --- |
| ADN-AE | MN-CSE, IN-CSE | AE registration procedure see clause TBD |
| ASN-AE | ASN-CSE |  |
| MN-AE | MN-CSE |  |
| IN-AE | IN-CSE |  |
| Nodeless AE | IN-CSE |  |
| ASN-CSE | MN-CSE, IN-CSE | CSE registration procedure see clause TBD |
| MN-CSE | MN-CSE, IN-CSE |  |

{6.2.9.2.d} Editor’s Note: The use of “instance” above might be removed if other definitions are changed. If kept, the description regarding “instances” should be expanded.

{6.2.9.2.e} Editor's note: Further Registration information is FFS.

### -------------------------------End of changes ---------------------------------------------