| CHANGE REQUEST |
| --- |
| Group Name:* | ARC bis Ad-Hoc |
| Source:* | LG Electronics |
| Format:* | ad hoc |
| Date:* | 2014-04-24 |
| Contact:* | Hongbeom Ahn, LG Electronics, Hongbeom.ahn@lge.com |
| Reason for Change/s:* | This CR is to remove the editor’s notes related to <instance> resource type. |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS0001 |
| Clauses/Sub Clauses* | 9.6.7 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is to remove the editor’s notes related to <instance> resource type.

{9.6.10.a} Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

- [To be Removed] those attributes are common attributes.

[9.6.7.b]  Editor's Note: Clarify forward reference to Stage 3.

- [The reference needs to be included] the informative references are included.

### -----------------------Start of change 1-------------------------------------------

### 9.6.7	Resource Type instance

The <instance> resource represents a data instance in the container. The content of the instance is opaque to the M2M platform and it might even be encrypted. However, there is meta-data associated with an instance which shall be accessible.

Contrary to other resources, the <instance> resource cannot be modified once created, regardless of the accessControlPolicyID associated with the parent resource. An instance may be deleted explicitly or it may be deleted by the platform based on policies. If the platform has policies for the instance retention these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge on the <container> resource. If multiple policies are in effect, the strictest policy shall apply.

The <instance> resource inherits the same access rights of the parent <container> resource, and does not have its own <accessControlPolicy> attribute.

Figure 9.6.7-1: Structure of <instance>resource
(only child resources and resource specific attributes are shown)

This resource shall contain the child resource according to their multiplicitly in Table 9.6.7-1.

# Table 9.6.7-1: Child resources of <instance> resource

| Child Resource Name of <instance> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

This resource shall contain the attributes according to their multiplicity in Table 9.6.7-2 (0 indicates the optionality of the attribute).

# Table 9.6.7-2: Attributes of <instance> resource

| Attribute Name of <instance> | Multiplicity | RW/ RO/ WO | Description | <instanceAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| stateTag | 1 | RO | See clause 9.6.1 where this common attribute is described. The stageTag attribute of the parent resource should be incremented first and copied into this stateTag attribute when a new instance is added to the parent resource. | ?? |
| Link | 1 | WO | See clause 9.6.1 where this common attribute is described. This is only for <instanceAnnc>. | MP |
| announceTo | 1 | RW | See clause 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See clause 9.6.1 where this common attribute is described. | NP |
| typeOfContent | 0..1 | WO | Type of the content included in the content attribute. This is media-type as defined in [i.2].. | OP |
| contentSize | 1 | WO | Size in bytes of the content attribute. | OP |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is stored in the instances of the container. If this attribute is not present, the instance inherits the ontologyRef from the parent <container> resource if present (see note) NOTE: Access to this URI is out of scope of oneM2M. | OP |
| content | 1 | WO | Actual opaque content of an instance. This may for example be an image taken by a security camera, or a temperature measurement taken by a temperature sensor. | OP |