| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | NTT DOCOMO, Oberthur Technologies, Gemalto |
| Format:* | ARC# 10.0 bis Ad Hoc |
| Date:* | 2014-04-28 |
| Contact:* | Syed Husain, NTT DOCOMO – shusain2016@live.com Dragan Vujcic, Oberthur – v.dragan@oberthur.com |
| Reason for Change/s:* | Cleanup of SEC CSF description |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.5.0 |
| Clauses/Sub Clauses* | 6.2.10 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to clean-up the SEC CSF description based on the reasoning provided in ARC-2014-1218R01. The current description contains several “shall” requirements which are unverifiable. These are removed. The text is organized for better readability.

### ---------------------------------Start of changes -----------------------------------------

### 6.2.10	Security

#### 6.2.10.1	General Concepts

The Security (SEC) CSF comprises the following functionalities:

Sensitive data handling;

Security administration;

Security association establishment;

ccess Control including identification, authentication and authorization;

Identity management.

Sensitive data handling functionality in the SEC CSF protects the local credentials on which security relies during storage and manipulation. Sensitive data handling functionality performs other sensitive functions such as security algorithms. This functionality is able to support several cryptographically separated security environments.

Security administration functionality enables services such as the following:

Creation and administration of dedicated secure environment supported by sensitive data handling functionality;

Post-provisioning of a master credentials protected by the secure environment;

Provisioning and administration of subscriptions related to M2M common services and M2M application services.

Security association establishment functionality is responsible for establishing security association between corresponding M2M nodes, in order to provide services such as confidentiality and integrity.

Access Control functionality is responsible for authorizing services and specific operations (e.g. Read/Update) on resources to identified and authenticated entities, according to provisioned access control policies and assigned roles.

While unique identifier of an entity are used for authentication, the identity management functionality provides pseudonyms which serve as temporary identifiers which cannot be linked to the true identity of either the associated entity or its user.

#### 6.2.10.2	Detailed Descriptions

The functionalities supported by the SEC CSF are as follows:

- Sensitive data handling:

  - Provides the capability to protect the local credentials on which security relies during storage and manipulation.

  - Extends sensitive data handling functionality to other sensitive data used in the M2M Systems such as subscription related information, access control policies and personal data pertaining to individuals.

  - Performs other sensitive functions as well, such as security algorithms running in cryptographically separated secure environments.

- Security administration :

- Creation and administration of a dedicated secure environment supported by sensitive data handling functionality

- Post-provisioning of master credentials protected by the secure environment.

- NOTE:	The secure environment can also be pre-provisioned with a master credentials prior to deployment; therefore this capability is not always required. Post-provisioning is required when the security remote provisioning needs to be performed or re-initiated after deployment.

- Provisioning and administration of subscriptions related to M2M services and M2M application services. Besides the associated master credentials, a subscription includes other information classified as sensitive data such as authorization roles and identifiers for access control management.

- Security association establishment:

  - Responsible to establish security associations between corresponding M2M nodes, in order to provide specific security services (e.g., confidentiality, integrity, , or support for application level signature generation and verification) involving specified security algorithms and sensitive data. This involves key derivation based on provisioned master credentials. This functionality of the SEC CSF is mandatory when security is supported.

- Access control:

  - Responsible to authorize services and specific operations (e.g. Read/Update) on resources to identified and authenticated entities, according to provisioned access control policies and assigned roles. This functionality is mandatory when any services relying on authorization and access control are present. Among other usages, the services of this functionality may be applied to personal information as a means to preserve privacy.

- Identity protection:

  - Provides pseudonyms to be used instead of the unique identifiers of an entity to serve as temporary identifiers not linkable to the true identity of either the associated entity or its user.

Detailed functionalities are described in the Security Solutions Technical Specification [TS-0003].

### -----------------------------------End of change ------------------------------------