| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ad hoc |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Plenary |
| Date:* | <2014-4-25> |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* |  |
| CR against: Release* | <Release One> |
| CR against: TS/TR* | TS0001 v0.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution deals with the editor’s note and the editorial mistakes in group management procedures. As well as the name of the <members> resource to eliminate confusion.

### -----------------------Start of change 1-------------------------------------------

### 9.6.13	Resource Type group

The <group> resource represents a group of resources of the same or mixed types. The <group> resource can be used to do bulk manipulations on the resources represented by the membersList attribute. The <group> resource contains an attribute that represents the members of the group and a virtual resource (the <fanOutPoint>) that allows verbs to be applied to the resources represented by those members.

When used as one of the permission holders in an <accessControlPolicy> resource, the group can be used to grant a collection of AEs (represented by <AE> resources) or CSEs (represented by <remoteCSE> resources) permissions for accessing (Creating children, Retrieving, etc.) a resource.

Figure 9.6.13-1: Structure of <group> resource
(only child resources and resource specific attributes are shown)

[9.6.13.a]  Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.This resource shall contain the child resources according to their multiplicity in Table 9.6.13-1.

Table 9.6.13-1: Child resources of <group> resource

| Child Resource Name of <group> | Child Resource Type | Multiplicity | Description | <groupAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | none |
| fanOutPoint | <fanOutPoint> | 1 | See clause 9.6.14 | none |

# The <group> resource shall contain the attributes with the indicated multiplicity in Table 9.6.13-2

Table 9.6.13-2: Attributes of <group> resource

| Attribute Name of <group> | Multiplicity | RW/ RO/ WO | Description | <groupAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicies | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creator | 0..1 | RW | The AE-ID or CSE-ID of the entity which created the resource. | MP |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| Link | 1 | WO | See clause 9.6.1 where this common attribute is described. This is only for <groupAnnc>. | MP |
| announceTo | 1 | RW | See clause 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See clause 9.6.1 where this common attribute is described. | NP |
| memberType | 1 | WO | It is the resource type of the member resources of the group if all member resources (including the member resources in any sub-groups) are of the same type. Otherwise, it's a type of 'mixed'. | OP |
| currentNrOfMembers | 1 | RO | Current number of members in a group. It is limited by the maxNrOfMembers. | OP |
| maxNrOfMembers | 1 | RW | Maximum number of members in the group. | OP |
| membersList | 1 | RW | List of zero or more member URIs referred to in the remaining of this specification as memberID. Each URI (memberID) should refer to a member resource or a (sub-) group resource of the group. | OP |
| membersAccessControlPolicies | 0..1 | RW | URIs of the accessControlPolicy resources defining who is allowed to access the <fanOutPoint> resource. | OP |
| memberTypeValidated | 1 | RO | Denotes if memberType of all member resources of the group has been validated. | OP |
| consistencyStrategy | 0..1 | WO | This attribute determines how to deal with the <group> resource if the memberType validation fails. Which means delete the inconsistent member if the attribute is ABANDON_MEMBER; delete the group if the attribute is ABANDON_GROUP; set the memberType to "mixed" if the attribute is SET_MIXED. | OP |
| groupName | 0..1 | RW | Human readable name of the group. | OP |

### 9.6.14	Resource Type fanOutPoint

The <fanOutPoint> resource is a virtual resource because it does not have a representation. It is the child resource of a <group> resource. Whenever the request is sent to the <fanOutPoint> resource, the request is fanned out to each of the members of the <group> resource indicated by the membersList attribute of the <group> resource. The responses (to the request) from each member are then aggregated and returned to the Originator.

The <fanOutPoint> resource does not have a resource representation by itself and consequently it does not have an accessControlPolicies attribute. The <accessControlPolicy> resource used for access control validation is indicated by the membersAccessControlPolicies attribute in the parent <group> resource.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 10.2.6	Group Management Procedures

#### 10.2.6.1	Introduction

This clause describes different procedures for managing membership verification, creation, retrieval, update and deletion of the information associated with a <group> resource as well as the bulk management of all group member resources by invoking the corresponding verbs upon the virtual resource <fanOutPoint> of a <group> resource.

#### 10.2.6.2	Create <group>

This procedure shall be used for creating a group resource.

Originator: The Originator shall request to Create a new group type resource to be named as <group> by using the CREATE verb. The request shall address <CSEBase> resource of a Hosting CSE. The Request shall also provide list of member URI and may provide expirationTime attributes. The list of member URI means a list of URIs of the member resources corresponding to the memberType attribute provided in the Request. The originator may be an AE or a CSE.

Receiver: For the CREATE procedure, the Receiver shall:

Check if the Originator has CREATE permissions on the <CSEBase> resource.

Check the validity of the provided attributes.

Validate that the resource type of every member conforms to the memberType attribute of the <group> resource, if the memberType attribute of the <group> resource is not 'mixed'. Set the memberTypeValidated attribute to TRUE upon successful validation.

Upon successful validation of the provided attributes, create a new group resource including the <fanOutPoint> child resource in the Hosting CSE.

Conditionally, in the case that the group resource contains temporarily unreachable sub-group resources as member resource, set the memberTypeValidated attribute of the <group> resource to FALSE.

Respond to the Originator with the appropriate generic Response with the representation of the <group> resource if the memberTypeValidated attribute is FALSE, and the URI of the created <group> resource if the CREATE was successful.

As soon as any unreachable resource becomes reachable, the memberType validation procedure shall be performed. If the memberType validation fails, the Hosting CSE shall deal with the <group> resource according to the policy defined by the consistencyStrategy attribute of the <group> resource provided in the request. or by default if the attribute is not provided.

# Table 10.2.6.2-1: <group> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | None |
| Information on Request message | op: C fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <CSEBase> where the <group> resource is intended to be Created. cn: The representation of the <group> resource for which the attributes are described in clause 9.6.13 |
| Local processing on Hosting CSE | Steps described for the Receiver of the CREATE Request as described above |
| Information on Response message | The representation of the <group> resource if the memberTypeValidated attribute is FALSE |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.6.3	Retrieve <group>

This procedure shall be used for retrieving <group> resource.

Originator: The Originator shall request to obtaining <group> resource information by using the RETRIEVE verb. The request shall address the specific <group> resource of a hosting CSE. The Originator may be an AE or a CSE.

Receiver: The Receiver shall check if the Originator has READ permission on the group resource. Upon successful validation, the hosting CSE shall respond to the Originator with the appropriate responses and the resource representation.

# Table 10.2.6.3-1: <group> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | None |
| Information on Request message | op: R fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <group> resource |
| Local processing on Hosting CSE | Same as the generic procedure |
| Information on Response message | Same as the generic procedure |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.6.4	Update <group>

This procedure shall be used for updating an existing <group> resource.

Originator: The Originator shall request to Update attributes of an existing <group> resource by using an UPDATE verb. The Request shall address the specific <group> resource of a CSE. The Originator may be an AE or a CSE.

Receiver: The UPDATE procedure shall be:

Check if the Originator has WRITE permissions on the <group> resource.

Check the validity of provided attributes.

Validate that the resource type of every member conforms to the memberType attribute of the <group> resource, if the memberType attribute of the <group> resource is not 'mixed'. Set the memberTypeValidated attribute to TRUE upon successful validation.

Upon successful validation of the provided attributes, update the group resource in the Hosting CSE.

Conditionally, in the case that the group resource contains temporarily unreachable sub-group resources as member resource set the memberTypeValidated attribute of the <group> resource to FALSE.

Respond to the Originator with the appropriate generic response with the representation of the <group> resource if the memberTypeValidated attribute is FALSE, and the URI of the created <group> resource if the UPDATE is successful.

As soon as any unreachable resource becomes reachable, the memberType validation procedure shall be performed. If the memberType validation fails, the Hosting CSE shall deal with the <group> resource according to the policy defined by the consistencyStrategy attribute of the <group> resource provided in the request, or by default if the attribute is not provided.

# Table 10.2.6.4-1: <group> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | None |
| Information on Request message | op: U fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <group> resource |
| Local processing on Hosting CSE | Steps described for the Receiver of the UPDATE Request as described above |
| Information on Response message | The representation of the <group> resource if the memberTypeValidated attribute is FALSE |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.6.5	Delete <group>

This procedure shall be used for deleting an existing <group> resource.

Originator: The Originator shall request to delete an existing <group> type resource by using the DELETE verb. The request shall address the specific <group> resource of a Hosting CSE. The Originator may be an AE or a CSE.

Receiver: The Receiver shall check if the Originator has DELETE permission on the <group> resource. Upon successful validation, the CSE shall remove the resource from its repository and shall respond to the Originator with the appropriate responses.

# Table 10.2.6.5-1: <group> DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | None |
| Information on Request message | op: D fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <group> resource |
| Local processing on Hosting CSE | Same as the generic procedure |
| Information on Response message | Same as the generic procedure |
| Post-Conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.6.6	Create <fanOutPoint>

This procedure shall be used for creating the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to create the content in all member resources belonging to an existing <group> resource by using a CREATE verb. The Request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group hosting CSE to create the same content under all member resources. The request may also address the URI that results from appending a relative URI to the <fanOutPoint> URI in order to create the same content (e.g. attribute or child resource) under the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The Originator may be an AE or CSE.

Group Hosting CSE: For the CREATE procedure, the Group Hosting CSE shall:

Check if the Originator has WRITE permission in the accessControlPolicy resource referenced by the membersAccessControlPolicyID in the <group> resource. In the case membersAccessControlPolicyID is not provided the access control policy defined for the <group> resource shall be used.

Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource.

Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.2.6-1. fr parameter in the request is set to ID of the Originator from the request from the original Originator.

In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier.

If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

After receiving the responses from the member hosting CSEs, respond to the Originator with the aggregated results and the associated memberIDs.

Member Hosting CSEs: For the CREATE procedure, the Member Hosting CSE shall:

Perform the corresponding CREATE procedure for the resource type in the request (clause 10.2 resource specific procedures).

Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifiers stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier.

Check if the original Originator has the CREATE permission on the addressed resource. Upon successful validation, perform the create procedures for the corresponding type of addressed resource as described in other subclauses of clause 10.2.

Send the corresponding response to the Group Hosting CSE.

# Figure 10.2.6.6-1: Group content management procedures

The procedures illustrated in figure 10.2.6.6-1 apply to clauses 10.2.6.6 to 10.2.6.9.

# Table 10.2.6.6-1: <fanOutPoint> CREATE

| CRETAE: Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | op: C fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <fanOutPoint> virtual resource cn: The representation of the resource the Originator intends to create gid: The group request identifier |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE, addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups |
| Information on Response message | Converged responses from member hosting CSEs |
| Post-Conditions | None |
| Exceptions | Same request with identical group request identifier received Originator does not have the access control privilegesright to access the <fanOutPoint> resource |

#### 10.2.6.7	Retrieve <fanOutPoint>

This procedure shall be used for retrieving the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to obtain the content or specific information (e.g. attributes) of all member resources belonging an existing <group> resource by using a RETRIEVE verb. The request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group hosting CSE for retrieving the content of all member resources. The request may also address the URI that results from appending a relative URI to the <fanOutPoint> URI in order to retrieve the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The originator may be an AE or CSE.

Group Hosting CSE: For the RETRIEVE procedure, the Group Hosting CSE shall:

Check if the Originator has READ permission in the accessControlPolicy resource referenced by the membersAccessControlPolicies in the addressed <group> resource. In the case membersAccessControlPolicies is not provided, the access control policy defined for the group resource shall be used.

Upon successful validation, obtain the URIs of all member resources from the membersList attribute of the addressed <group> resource.

Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.2.6-1. fr parameter in the request is set to ID of the Originator from the request from the original Originator.

In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier.

If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated memberIds.

Member Hosting CSEs: For the RETRIEVE procedure, the Member Hosting CSE shall:

Perform the corresponding RETRIEVE procedure for the resource type in the request (clause 10.2 resource specific procedures).

Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the request identifier.

Check if the original originator has the READ permission on the addressed resource. Upon successful validation, perform the retrieve procedures for the corresponding type of addressed resource as described in other subclauses of clause 10.2.

Send the corresponding response to the group hosting CSE.

# Table 10.2.6.7-1: <fanOutPoint> RETRIEVE

| RETRIEVE: Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | op: R fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <fanOutPoint> resource gid: The group request identifier |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE, addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups |
| Information on Response message | Converged responses from member hosting CSEs |
| Post-Conditions | None |
| Exceptions | Same request with identical request identifier received Originator does not have the access control privilegesright to access the <fanOutPoint> resource |

#### 10.2.6.8	Update <fanOutPoint>

This procedure shall be used for updating the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to update the content of all member resources belonging to an existing <group> resource with the same new data by using a UPDATE verb. The request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group hosting CSE to update all member resources. The request may also address the URI that results from appending a relative URI to the <fanOutPoint> in order to update only the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The originator may be an AE or CSE.

Group Hosting CSE: For the UPDATE procedure, the Group Hosting CSE shall:

Check if the originator has WRITE permission in the accessControlPolicy resource referenced by the membersAccessControlPolicies in the group resource. In the case membersAccessControlPolicies is not provided the access right defined for the group resource shall be used.

Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource.

Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.2.6-1. fr parameter in the request is set to ID of the Originator from the request from the original Originator.

In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include it in all the requests to be fanned out and locally store the group request identifier.

If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated memberIDs.

Member Hosting CSEs: For the UPDATE procedure, the Member Hosting CSE shall:

Perform the corresponding UPDATE procedure for the resource type in the request (clause 10.2 resource specific procedures).

Check if the request has a group request identifier. Check if the request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the request identifier.

Check if the original originator has the UPDATE permission on the addressed resource. Upon successful validation, perform the update procedures for the corresponding type of addressed resource as described in other subclauses of clause 10.2

Send the corresponding response to the group hosting CSE.

# Table 10.2.6.8-1: <fanOutPoint> UPDATE

| UPDATE: Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | op: U fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <group> resource cn: The representation of the resource the Originator intend to Update gid: The group request identifier |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups |
| Information on Response message | Converged responses from member hosting CSEs |
| Post-Conditions | None |
| Exceptions | Same request with identical request identifier received Originator does not have the access control privileges to access the <fanOutPoint> resource |

#### 10.2.6.9	Delete <fanOutPoint>

This procedure shall be used for deleting the content of all member resources belonging to an existing <group> resource.

Originator: The Originator shall request to delete the content of all member resources belonging to an existing <group> resource by using a DELETE verb. The request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group hosting CSE to delete all member resources. The request may also address the URI that results from appending a relative URI to the <fanOutPoint> in order to delete only the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The originator may be an AE or a CSE.

Group Hosting CSE: For the DELETE procedure, the Group Hosting CSE shall:

Check if the Originator has WRITE permission in the accessControlPolicy resource referenced by the membersAccessControlPoliciesRightID in the <group> resource. In the case membersAccessControlPoliciesRightID is not provided the access control policy defined for the group resource shall be used.

Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource.

Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in Figure 10.2.2.6-1. fr parameter in the request is set to ID of the Originator from the request from the original Originator.

In the case that the member resources contain a sub-group resource, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier.

If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated memberIDs.

Member Hosting CSEs: For the DELETE procedure, the Member Hosting CSE shall:

Perform the corresponding DELETE procedure for the resource type in the request (clause 10.2 resource specific procedures).

Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier.

Check if the original originator has the DELETE permission on the addressed resource. Upon successful validation, perform the delete procedures for the corresponding type of addressed resource as described in other subclauses of clause 10.2

Send the corresponding response to the Group Hosting CSE.

# Table 10.2.6.9-1: <fanOutPoint> DELETE

| DELETE: Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | op: D fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <group> resource gid: The group request identifier |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute membersList of the group resource appended with relative URI if any Generate group request identifier and include the identifier in the fanned out requests in the case of sub groups |
| Information on Response message | Converged responses from member hosting CSEs. |
| Post-Conditions | None |
| Exceptions | Same request with identical request identifier received Originator does not have the access control privileges to access the <fanOutPoint> resource |

#### 10.2.6.10	Subscribe and un-subscribe <members> of a group

This procedure shall be used for receiving information about modifications of all member resources belonging to an existing <group> resource.

Originator: shall request to create a subscription resource under all member resources belonging to an existing <group> resource by using a CREATE verb. The request shall address the child resource <fanOutPoint> of the specific <group> resource of a group hosting CSE appended with the ID of the <subscription> resource to be created to subscribe to the modifications of all member resources. The request shall include an empty aggregationURI attribute if the originator wants the group hosting CSE to aggregate the notifications. The request shall include the required information and may include the optional information as described in subscription management clause 10.2.11. The originator may be an AE or a CSE.

Group Hosting CSE: For the subscribe/un-subscribe procedure, the Group Hosting CSE shall:

Check if the originator has WRITE permission in the <accessControlPolicy> resource referenced by the membersAccessControlPolicies in the group resource. In the case membersAccessControlPolicies is not provided the access control policy defined for the group resource shall be used.

If the subscription resource in the request contains an aggregationURI attribute, assign an URI to the aggregationURI of the subscription resource. In case the aggregationURI attribute has a value, maintain the mapping of the generated aggregationURI and the former aggregationURI.

Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource and fan out requests to the member hosting CSEs addressing the obtained URIs appended with the ID of the <subscription> resource to be created.

If the group hosting CSE determines that multiple member resources belong to one CSE according to the URIs of the member resources, it may converge the requests accordingly before sending out. This may be accomplished by the group hosting CSE creating a <group> resource on the member hosting CSE to collect all the members on that member hosting CSE.

After receiving the responses from the member hosting CSEs, respond to the originator with the aggregated results and the associated memberIDs.

Member Hosting CSEs: For the subscribe/un-subscribe procedure, the Member Hosting CSE shall treat the request received from the group hosting CSE as a normal SUBSCRIBE request on the addressed member resource as if it comes from the original originator. Therefore the member hosting CSE shall:

Check if the original originator has the READ permission on the member resource.

Upon successful validation, perform the subscribe procedures for the corresponding type of member resource as described in clause 10.2.11.

Send the corresponding response to the group hosting CSE.

Table 10.2.6.10-1: <fanOutPoint> Subscribe/Un-subscribe

| Description |
| --- |
| Call flow type | CREATE |
| Pre-conditions | none |
| Information on Request message | op: C fr: Identifier of the AE or CSE that initiates the request. to: The URI of the <fanOutPoint> resource appended with the ID of the <subscription> resource to be created. gid: The group request identifier |
| Local processing on Hosting CSE | Fan out requests to each member hosting CSE addressing the obtained URI from the attribute membersList of the group resource appended with the ID of the <subscription> resource to be created. Generate request identifier and include the identifier in the fanned out requests in the case of sub groups. |
| Information on Response message | Converged responses from member hosting CSEs. |
| Post-condition | None |
| Exceptions | Same request with identical request identifier received. Originator does not have the access control priviledges to access the <fanOutPoint> resource. |

#### 10.2.6.11	Aggregate the notifications by group

This procedure is used for the group hosting CSE to aggregate the notifications from member hosting CSEs and forward the aggregated notification to the subscriber.

Member Hosting CSEs: Whenever the resource that is subscribed-to is modified in a way that matches the policies as is specified in clause 9.6.8, notification needs to be sent to the subscribe, the Member Hosting CSE shall:

If the subscription resource contains aggregationURI, notify the subscriber at the aggregationURI and include the notificationURI in the notification. Otherwise, notify at the URI represented by the attribute notificationURI.

Group Hosting CSE: For the notification procedure, the Group Hosting CSE shall:

On receiving the notifications from the member hosting CSEs at the aggregationURI, validate if the notification is sent from its member resource and contain a notificationURI attribute.

Upon successful validation, aggregate the notifications which have the same notificationURI address of a single subscriber. Send the aggregated notification to the subscriber according to the notificationURI in the notification. In the case the addressed group is the member of another group through which the subscription is created the notification shall be sent according to the mapping of the aggregationURI of the two group hosting CSEs.

Wait for the response. After receiving the response, split the response and respond the member hosting CSE separately.

The group hosting CSE may stop aggregating the notifications when the expirationTime of the corresponding subscription expires.

Subscriber: shall treat every notification extracted from the aggregated notification as a separate notification received from the subscribed resource and generate corresponding responses. The subscriber shall aggregate the responses to these notifications and send the aggregated response to the group hosting CSE.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the hosting CSE., It controls "who" is allowed to do "what" and can be used for privacy protection. | subscription | Application, remoteCSE, CSEBase | 9.6.2 |
| application | Stores information about the AE. It is created as a result of successful registration of an AE with the registrar CSE. | subscription, container, group, accessControlPolicy, mgmtObj, commCapabilities, pollingChannel | remoteCSE, CSEBase | 9.6.5 |
| cmdhBuffer | Defines CMDH buffer usage limits | subscription None documented | cmdhPolicy | D.12.7 |
| cmdhDefaults | Defines CMDH default values | cmdhDefEcValue, cmdhEcDefParamValues subscription | cmdhPolicy | D.12.1 |
| cmdhEcDefParamValues | Represent a specific set of default values for the CMDH related parameters | subscription None documented | cmdhDefaults | D.12.3 |
| cmdhDefEcValue | Defines a value for the ec (event category) parameter of an incoming request when it is not defined. | subscription None documented | cmdhDefaults | D.12.2 |
| cmdhLimits | Defines limits for CMDH related parameter values | subscription None documented | cmdhPolicy | D.12.4 |
| cmdhNetworkAccessRules | Defines rules for the usage of underlying networks | cmdhNwAccessRule subscription | cmdhPolicy | D.12.5 |
| cmdhNwAccessRule | Defines a rule for the usage of underlying networks | schedule subscription | cmdhNetworkAccessRules | D.12.6 |
| cmdhPolicy | A set of rules defining which CMDH parameters will be used by default | cmdhDefaults, cmdhLimits, cmdhNetworkAccessRules, cmdhBuffer subscription | None documented | D.12 |
| container | Shares data instances among entities. Used as a mediator that takes care of buffering the data to exchange "data" between AEs and/or CSEs. The exchange of data between AEs (e.g. an AE on an node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule. | container, instance, subscription, | application, container, remoteCSE, CSEBase | 9.6.6 |
| CSEBase | The structural root for all the resources that are residing on a CSE. It shall store information about the CSE itself. | remoteCSE, node, application, container, group, accessControlPolicy, subscription, mgmtObj, mgmtCmd, locationPolicy, statsConfig | None | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription None documented | None documented | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription None documented | statsConfig | 9.6.23 |
| execInstance | The Execution Instance resource contains all execution instances of the same management command mgmtCmd. | subscription None documented | mgmtCmd | 9.6.17 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group. | fanOutPoint subscription | Application, remoteCSE, CSEBase | 9.6.13 |
| instance | Represents a data instance in the container resource. | subscription None documented | container | 9.6.7 |
| locationPolicy | Includes information to obtains and managemanages geographical location It is only referred from container, in case that the instances of the container provide location information. | subscription None documented | CSEBase | 9.6.10 |
| fanOutPoint | Virtual resource containing target for group requests It is used for addressing bulk operations to all the resources that belong to a group. | None documented | group | 9.6.14 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols. | execInstance subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node | parameters subscription | remoteCSE, CSEBase | 9.6.15 Annex D |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | nodeInfo subscription | None documented | 9.6.19 |
| node | Represents specific Node information | schedule, mgmtObj subscription | CSEBase, remoteCSE | 9.6.18 |
| nodeInfo | Node information | subscription None documented | m2mServiceSubscription | 9.6.20 |
| parameters | Provides a mechanism to describe the management object in a generic way to easily import information from existing management protocols. | parameters subscription | mgmtObj, parameters | 9.6.16 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | subscription None documented | remoteCSE, application | 9.6.21 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource. | application, container, group, accessControlPolicy, subscription, mgmtObj, pollingChannel, node | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | subscription None documented | None documented | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | subscription None documented | node, subscription, cmdhNwAccessRule | 9.6.39 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | subscription None documented | CSEBase (in IN-CSE) | 9.6.24 |
| statsConfig | Stores configuration of statistics for applications | eventConfig subscription | CSEBase (in IN-CSE) | 9.6.22 |
| subscription | Subscription resource represents the subscription information related to a resource. Such a resource shall be a child resource for the subscribe-to resource. | schedule | accessControlPolicy, application, cmdhBuffer, cmdhDefaults, cmdhEcDefParamValues, cmdhDefEcValue, cmdhLimits, cmdhNetworkAccessRules, cmdhNwAccessRule, cmdhPolicy, container, CSEBase, delivery, eventConfig, execInstance, group, instance, locationPolicy, mgmtCmd, mgmtObj, m2mServiceSubscription, node, nodeInfo, parameters, remoteCSE, request, schedule, statsCollect, statsConfig | 9.6.8 |