| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ad hoc |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Plenary |
| Date:* | <2014-4-25> |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* |  |
| CR against: Release* | <Release One> |
| CR against: TS/TR* | TS0001 v0.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The procedure for mgmtObj management still exists some inconsistencies. The CR proposes to change them.

### -----------------------Start of change 1-------------------------------------------

### 10.2.7	mgmtObj Management Procedures

#### 10.2.7.1	Introduction

This clause describes the management procedures over Mca and Mcc reference points. If external management technologies are used for management, different operations addressing a <mgmtObj> resource (or its attributes or child resources) shall be translated into existing management commands and procedures performed on the mapped external management object on the managed entity. The Receiver in the following procedures is IN-CSE.

#### 10.2.7.2	Create <mgmtObj>

This procedure shall be used to create a specific <mgmtObj> resource in the hosting CSE to expose the corresponding management function of a managed entity (i.e. M2M Device/Gateway) over the Mca reference point. Depending on the data model being used, the created <mgmtObj> resource may be a partial or complete mapping from the external management object onto the managed entity. If such an external management object is missing from the managed entity, it shall be added to the managed entity. Further operations performed on the created <mgmtObj> resource shall be converted by the hosting CSE into a corresponding device management action performed on the mapped external management object on the managed entity using external management technology (e.g. OMA-DM [i.5] or BBF TR-069 [i.4]).

Originator: The Originator shall be an IN-AE, or a CSE on a managed entity:

- The Originator is a CSE: In this case, the CSE first collects the original external management object (the management tree structure or also the value of the tree nodes if needed) of the local device and transforms the data into the <mgmtObj> resource representation, then requests the Hosting CSE to create the corresponding <mgmtObj> resource.

- The Originator is an AE: In this case, the AE requests the Hosting- CSE to add the corresponding external management object to the managed entity by creating an <mgmtObj> resource in the Hosting CSE.

NOTE 1:	The IN-CSE can create the <mgmtObj> resource locally by itself. The details are out of scope. In this case, the Hosting CSE first collects the original external management object on the managed entity via external management technology (e.g. OMA DM [i.5], BBF TR-069 [i.4] or LWM2M [i.6]), then transforms the object into the <mgmtObj> resource representation and create the <mgmtObj> resource locally in the IN-CSE.

NOTE 2:	The <mgmtObj> resource can  be created in the Hosting CSE by other offline provisioning means which are out of scope.

Receiver: For the CREATE operation, the Receiver shall:

- Check if the Originator has the CREATE privilege on the addressed <node> resource. Then check the validity of the provided attributes.

- Upon successful validation, create a new <mgmtObj> resource in the Hosting CSE with the provided attributes.

- If the Originator is an AE: Check if there is existing management session between the management server and the managed entity. If not, request the management server to establish a management session towards the managed entity. Send the management request to the managed entity or to the management server to add the corresponding external management object to the managed entity based on external management technology.

- Maintain the mapping relationship between the created <mgmtObj> resource and the external management object on the managed entity.

- Respond to the Originator with the appropriate responses based on the response from the external  management technologies. It shall also provide in the response the URI of the created new resource.

# Table 10.2.7.2-1: <mgmtObj> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | None |
| Information on Request message | op: C fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <node> where the <mgmtObj> resource is intended to be Created cn: The representation of the <mgmtObj> resource for which the attributes are described in clause 9.6.15 |
| Local processing on Hosting CSE | New external management object created on the managed entity using external management technologies in case the Originator is IN-AE |
| Information on Response message | Error code if the new external management object is not created |
| Post-Conditions | None |
| Exceptions | The creation of the external management object is not allowed The created external management object already exists Corresponding external management object cannot be added to the managed entity for some reason (e.g. not reachable, memory shortage) |

#### 10.2.7.3	Retrieve <mgmtObj>

This procedure shall be used to retrieve information from an existing <mgmtObj> resource.

- Originator: The Originator shall be an AE, or a CSE on the managed entity.

Receiver: For the RETRIEVE operation, the Receiver shall:

- Check if the Originator has the READ privilege on the addressed <mgmtObj> resource.

- Upon successful validation, retrieve the corresponding <mgmtObj> resource.

- Respond to the Originator with the appropriate response.

- If the Originator is an AE and if the requested information of the <mgmtObj> resource is not available, identify the corresponding external management object on the managed entity according to the mapping relationship that the IN-CSE maintains. Check if there is an existing management session between the management server and the managed entity. If not, request the management server to establish a management session towards the managed entity. Send the management request to get the corresponding external management object from the managed entity based on the external management technology, then return the result to the Originator based on the response from the external management technology.

# Table 10.2.7.3-1: <mgmtObj> RETRIEVE

| Description |
| --- |
| Call Flow Type | RETRIEVE |
| Pre-Conditions | None |
| Information on Request message | op: R fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <mgmtObj> resource |
| Local processing on Hosting CSE | Get corresponding external management object from managed entity by existing management procedures in case the addressed <mgmtObj> is not available |
| Information on Response message | Error code if the external management object can not be retrieved |
| Post-Conditions | None |
| Exceptions | Corresponding external management object data cannot be retrieved from the managed entity (e.g. external management object not found). |

#### 10.2.7.4	Update <mgmtObj>

This procedure shall be used to update information of an existing <mgmtObj> resource.

Originator: The Originator shall be an IN-AE, or a CSE on a managed entity.

Receiver: For the UPDATE operation, the Receiver shall:

- Check if the Originator has the WRITE privilege on the address <mgmtObj> resource. Check the validity of provided attributes if any.

- Upon successful validation, update the corresponding attribute(s) of the <mgmtObj> resource accordingly.

- If the Originator is an IN-AE, identify the corresponding external management object on the managed entity according to the mapping relationship it maintains. Check if there is an existing management session between the management server and the managed entity. If not, request the management server to establish a management session towards the managed entity. Send the management request to update the corresponding external management object in the managed entity accordingly based on external management technology.

- Respond to the Originator with the appropriate response based on the response from the external management technology.

# Table 10.2.7.4-1: <mgmtObj> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | None |
| Information on Request message | op: U fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <mgmtObj> resource cn: The representation of the <mgmtObj> resource for which the attributes are described in clause 9.6.15 |
| Local processing on Hosting CSE | Override corresponding external management object in managed entity by existing management procedures |
| Information on Response message | Error code if the external management object can not be updated |
| Post-Conditions | None |
| Exceptions | Corresponding external management object cannot be updated to managed entity (e.g. not reachable, external management object not found) |

#### 10.2.7.5	Delete <mgmtObj>

This procedure shall be used to delete an existing <mgmtObj> resource so as to hide the management function of a managed entity from being exposed via Mca reference point. An IN-AE uses this procedure to remove the corresponding external management object (e.g. an obsolete software package) from the managed entity.

Originator: The Originator shall be an IN-AE, or CSE on a managed entity.

- The Originator is a CSE on the managed entity: In this case, the CSE issues the request to the Hosting CSE to hide the corresponding management function from being exposed by the <mgmtObj> resource.

- The Originator is an IN-AE: In this case, the IN-AE requests the Hosting CSE to delete the <mgmtObj> resource from the Hosting CSE and to remove the corresponding external management object from the managed entity.

NOTE 1:	The Hosting CSE in the network domain may also delete the <mgmtObj> resource locally by itself. This internal procedure is out of scope.

NOTE 2:	The <mgmtObj> resource may also be deleted in the Hosting CSE by other offline provisioning means which are out of scope.

Receiver: For the DELETE procedure, the Receiver shall:

- Check if the Originator has the DELETE privilege on the addressed <mgmtObj> resource.

- Upon successful validation, remove the addressed resource from its repository.

- If the Originator is an IN-AE, identify the corresponding external management object on the managed entity according to the mapping relationship it maintains. Check if there is an existing management session between the management server and the managed entity. If not, request the management server to establish a management session towards the managed entity. Send the management request to remove the corresponding external management object from the managed entity based on external management technology.

- Respond to the Originator with the appropriate generic responses based on the response from the external management technology.

# Table 10.2.7.5-1: <mgmtObj> DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | None |
| Information on Request message | op: D fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <mgmtObj> resource. |
| Local processing on Hosting CSE | Trigger existing (OMA-DM [i.5], BBF TR-069 [i.4] or LWM2M [i.6]) management procedures to delete the corresponding external management object from the managed entity. |
| Information on Response message | Proper error code if the external management object can not be deleted. |
| Post-Conditions | None |
| Exceptions | Corresponding external management object cannot be deleted from managed entity due to some reason (e.g. not reachable, external management object not found). |

#### 10.2.7.6	Execute <mgmtObj>

This procedure shall be used for executing a specific management command on a managed entity through an existing <mgmtObj> resource on the Hosting CSE.

Originator: The Originator shall request to execute a specific management command which is represented by an existing <mgmtObj> resource or its attribute by using an UPDATE verb. The request shall address the specific executable <mgmtObj> resource or its attribute and shall contain an empty body. In the case that the management command is represented by an attribute of a <mgmtObj> resource, such attribute shall contain a URI that the request may also address to trigger the command execution alternatively.

After the execution request, the Originator may request to retrieve the execution result or status from the executable <mgmtObj> resource or its attribute/child resource by using a RETRIEVE method as described in clause 10.2.7.3.

- The Originator shall be IN-AE.

Receiver: For the execute procedure, the Receiver shall:

- Check if the Originator has the WRITE permission on the addressed <mgmtObj> resource or its attribute.

- Upon successful validation, check if there is an existing management session between the management server and the managed entity. If not, request the management server to establish management session towards the managed entity. Send the management request to execute the corresponding management command (e.g. "Exec" in OMA DM [i.5]) on the managed entity based on external management technology.

- Respond to the Originator with the appropriate response based on the response from the external management technology. The Response may also contain execution results.

- Upon receiving a RETRIEVE request to retrieve the execution result or status from the executable <mgmtObj> resource or its attribute, perform the procedures as described in clause 10.2.7.3.

- Upon receiving from managed entity a management notification (e.g. OMA-DM [i.5] "Generic Alert" message or BBF TR-069 [i.4] "Inform" message) regarding the execution result or status, the receiver may actively send the management request to retrieve the execution result or status external management object information from the managed entity and update the corresponding <mgmtObj> resource or its attribute locally.

# Table 10.2.7.6-1: <mgmtObj> EXECUTE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | None |
| Information on Request message | op: U fr: Identifier of the AE that initiates the Request to: The URI of the <mgmtObj> resource cn: None |
| Local processing on Hosting CSE | Trigger existing (OMA DM [i.5], BBF TR-069 [i.4], LWM2M [i.6]) device management procedures to execute the corresponding management command on the managed entity |
| Information on Response message | Error code if the external management object can not be executed |
| Post-Conditions | None |
| Exceptions | Corresponding external management object operation cannot be executed in managed entity (e.g. not reachable, external management object not found) |

### -----------------------End of change 1---------------------------------------------

# Comments

No need to define execute, as it’s actually update.