| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* | Plenary |
| Date:* | 2014-04-29 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Reason for Change/s:* | This contribution proposes a restriction to update accessControlPolicyID due to security reason. |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0001 V0.4.3 |
| Clauses/Sub Clauses* | Some clauses |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

- Due to the change of m2mServiceSubscription resource type, “role” term specified in 9.6.2 needs to be replaced with “subscriber group”.

- Privilege type could be misleading (e.g., there are lots of privileges and privilege type categorizes them). ( remove privilege type

- Remove Domain from access control originator attributes

- Remove CSEID from NodeInfo resource type

### -----------------------Start of change 1-------------------------------------------

### 9.6.2	Resource Type accessControlPolicy

Access control policy  is defined as "white lists" or privileges, i.e., each privilege defines "allowed" entities (defined as accessControlOriginatorAttributes) for certain access modes (defined as accessControlOperationFlags). Sets of privileges are handled such that the resulting privileges for a group of  privileges are the sum of the individual privileges; i.e., an action is permitted if it is permitted by some/any privileges in the set. The selfPrivilege attribute lists those that have the rights to Read/Update/Delete for the resource <accessControlPolicy> itself.

Each privilege may also refer to a subscriber goup described as a subsGroup attribute in a <m2mServiceSubscription>.

All privileges defined in an access control policy are also contextualized to: location, time windows and IP address.

By setting an accessControlPolicyID attribute on a resource, the privileges for accessing that resource are then defined by the privileges defined in the <accessControlPolicy> resource.

[9.6.2.a]  Editor's Note: There is a need for a global replacement of accessRight with accessControlPolicy, accessRightsID with accessControlPolicyID, permission with privilege.

Figure 9.6.2-1: Structure of <accessControlPolicy> resource 
(only resource specific attributes are shown)

[9.6.2.b]  Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

# Table 9.6.2-1: Child resources of <accessControlPolicy> resource

| Child Resource Name of <accessControlPolicy> | Child Resource Type | Multiplicity | Description | <accessControlPolicyAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscriptionAnnc> |

[9.6.2.c]  Editor's Note: Contribution ARC-2014-0089R03 does not provide the table for the <subscription> child-resource. The contributor to verify the accuracy of the proposal.

This resource shall contain the attributes according to their multiplicity in Table 9.6.2-2 (0 indicates the optionality of the attribute).

# Table 9.6.2-2: Attributes of <accessControlPolicy> resource

| Attribute Name of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attribute |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| Link | 1 | WO | See clause 9.6.1 where this common attribute is described. This is only for <accessControlPolicyAnnc>. | MP |
| announceTo | 1 | RW | See clause 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See clause 9.6.1 where this common attribute is described. | NP |
| privileges | 1 | RW | The set of privileges defined by this <accessControlPolicy> resource. These privileges are applied to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | OP |
| selfPrivileges | 1 | RW | Defines the list of privileges for the <accessControlPolicy> resource itself. | OP |

[9.6.2.d]  Editor's Note:  Mechanisms for announcing are FFS.

The privileges could then be generalised to actions (which might be granting access, but might also be more specific, like granting access to a subset, i.e., filtering part of the data). The privileges could be generalised to conditions, which may include things like the identity of the requestor, everybody except specified identities, but it might also include time based conditions, etc.

The access granting mechanism based on access control policy operates by matching the request originator with access control originator attributes stored in an <accessControlPolicy> resource. When a positive match is found then the requested operation (e.g., RETRIEVE) is checked with a set of allowed operations associated to the matching privilege holder; if this check fail, then the request will be denied. These sets are called access control operation flags.

Self privileges and privileges are both lists of access control originator attribute associated with access control operation flags applied respecively to <accessControlPolicy> resource itself (self privileges) and to all other resource types addressing the <accessControlPolicy> resource with the accessControlPolicyID common attribute (privileges).

All privileges defined in an access control policy are also contextualized to: location, time windows and IP address before granting the access

Each privilege in the self privileges and privileges lists can be also constituted by one subscriber group. Such subscriber group is identified by a subscriber group and a URL addressing a <m2mServiceSubscription> resource where such subscriber group is defined. In case the originator is presenting itself with a specific subscriber group, the access control policy operates by matching the request originator with the list belonging to such specific subscriber group as described in the Service Subscription resource (achieved by partial addressing).

Each privilege in the privileges and selfprivileges lists is constituted by the following elements

Table 9.6.2-3: Elements of Privileges

| Name | Description |
| --- | --- |
| accessControlOriginatorAttributes | See clause 9.6.2.1 |
| accessControlcontexts | See clause 9.6.2.2 |
| accessControloperationFlags | See clause 9.6.2.3 |

#### 9.6.2.1	accessControlOriginatorAttributess

The following originators element shall be considered for access control policy check.

Table 9.6.2.1-1: Access Control Originator Attributes

| Name | Description |
| --- | --- |
| originator identifier | CSE-ID or AE-ID which represent a originator identity |
| Token | Access token usually provided as query parameter |
| All | All originators |
| Subscriber group | A subscriber group name associated with the URL the a Service Subscription resource where such subscriber group is defined |

#### 9.6.2.2	accessControlContexts

The following originator contexts element shall be considered for access control policy check.

Table 9.6.2.2-1: Access Control Contexts

| Name | Description |
| --- | --- |
| Contexts | Defines the context in which every privileges of the present access control policy resource applies, e.g., time windows, location, IP address. Editor’s note: the detailed definition for the context is FFS. |

#### 9.6.2.3	accessControlOperationFlags

The following operation flags shall be considered for access control policy check in association to an originator privilege.

Table 9.6.2.3-1: Access Control Operation Flags

| Name | Description |
| --- | --- |
| RETRIEVE | Privilege to retrieve the content of an addressed resource |
| CREATE | Privilege to create a child resource |
| UPDATE | Privilege to update the content of an addressed resource |
| DELETE | Privilege to delete an addressed resource |
| DISCOVER | Privilege to discover the resource |
| NOTIFY | Privilege to receive a notification |

[9.6.2.3.a]  Editor’s Note:  A non-verbose  privilege flag description could be the following: <pf>RcUeDN</pf> that means: RETRIEVE allowed, CREATE not allowed, UPDATE allowed, DELETE not allowed, DISCOVER allowed, NOTIFY allowed.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2--------------------------------------------

### 9.6.19	Resource Type m2mServiceSubscription

This resource represents an M2M Service Subscription described in clause 6.6. It is used to represent all data pertaining to the M2M Service Subscription (the technical part of the contract between an M2M Application Service Provider and an M2M Service Provider).

[9.6.20.a] Editor's Note: The link between the M2M Service Subscription resource and RBAC will be added once RBAC is included in the specification.

Figure 9.6.19-1: Structure of <m2mServiceSubscription> resource 
(only child resources and resource specific attributes are shown)

[9.6.20.b]  Editor's Note: the M2M-Sub-ID storage is FFS

This resource shall contain the child resources according to their multiplicity in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.19-1: Child resources of <m2mServiceSubscription> resource

| Child Resource Name of <m2mServiceSubscription> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| nodeInfo | <nodeInfo> | 0..n | See clause 9.6.20 |

The <m2mServiceSubscription> resource shall contain the attributes described in Table 9.6.19-2.

# Table 9.6.19-2: Attributes of <m2mServiceSubscription> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicies | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| subsSer&RoleList | 0..n | WO | This attribute indicates the list of subscribed services and roles. |
| appID | 0..n | RW | The value of this attribute shall be set to an application identifier as defined in clause 7.1.3 pertaining to applications in infrastructure domain (IN-AE) of this M2M service subscription. |
| subsGroup | 0..n | RW | This attribute contains a group and its associated members created by the subscriber for the purpose of helping easy setting of Access Control Privileges. An example of the subscriber defined group is all node applications within this service subscription with app-ID set to a specific value. |

### 9.6.20	Resource Type nodeInfo

This resource represents M2M node information that is needed as part of the M2M Service Subscription resource. It shall contain information about the node as well as application identifiers running on that node.

Figure 9.6.20-1: Structure of <nodeInfo> resource 
(only child resources and resource specific attributes are shown)

This resource shall contain the child resource according to their multiplicity in Table 9.6.20-1.

Table 9.6.20-1: Child resources of <nodeInfo> resource

| Child Resource Name of <nodeInfo> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

The <nodeInfo> resource shall contain the attributes described in Table 9.6.20-2.

Table 9.6.20-2: Attributes of <nodeInfo> resource

| Attribute Name of <nodeInfo> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicies | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| nodeID | 1 | RW | Node identifier indicating where the M2M Service Subscription applies. Wildcard may be used to allow all the Nodes within a M2M Service Provider. |
| appID | 0..n | RW | See clause 7.1.3. application ID pertaining to an application running on this node |

### -----------------------End of change 2----------------------------------------------

# Comments

Just comment.

Normally we use white list, which means if we don’t specify a certain operation, that operation isn’t allowed. Need clarification for specifying not-allowed-operation.