| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Huawei, NTT DOCOMO |
| Format:* | ARC #10.0 bis ad hoc |
| Date:* | <2014-04-23> |
| Contact:* | Mitch Tseng, Huawei Technologies, mitch@T-infoserv.com Syed Husain, NTT DOCOMO, shusain2016@gmail.com |
| Reason for Change/s:* | This contribution proposes modifications related to Registration CSF to clarify the support for Application Discovery. R09 replaces text and figure that should nt have been removed until a new normative clause containing them was agreed |
| CR against: Release* | Release 1.0.0 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_5_0 |
| Clauses/Sub Clauses* | Clause 6.2.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# The Registration CSF is defined in clause 6.2.9. Although an AE is allowed to register with another AE or a CSE, the current text does not reflect the information covering the handling of  AEs.  This CR proposes to have add Registration information to explicitly include the application/service information so that an AE registrated on a CSE can be discovered via Discovery CSF with the same procedure as discovering a resource on a CSE. This contribution is also revised to remove normative text, based on agreement reached on ARC-2014-1218 at the TP#10 meeting.

### ------------------------------Start of changes -------------------------------------------

### 6.2.9	Registration

#### 6.2.9.1	General Concepts

The Registration (REG) CSF processes a request from an AE or another CSE to register with a Registrar CSE in order to allow the registered entities to use the services offered by the  Registrar CSE.

#### 6.2.9.2	Detailed Descriptions

Registration is the process of delivering AE or CSE information to another CSE in order to use M2M Services.

An AE on an ASN, an MN or an IN performs registration with the corresponding CSE in order to use M2M services offered by that CSE. An AE on an ADN performs registration with the CSE on an MN or an IN in order to use M2M services offered by that CSE. An IN-AE performs registration with the corresponding CSE on an IN in order to use M2M services offered by IN-CSE. An  AE interacts with its Registrar CSE without the need to have the Registrar CSE register with other CSEs.

The CSE on an ASN performs registration with the CSE in the MN in order to be able to use M2M Services offered by the CSE in the MN. As a result of successful ASN-CSE registration with the MN-CSE, the CSEs on the ASN and the MN establish a relationship allowing them to exchange information.

The CSE on an MN performs registration with the CSE of another MN in order to be able to use M2M Services offered by the CSE in the other MN. As a result of successful MN-CSE registration with the other MN-CSE, the CSEs on the MNs establish a relationship allowing them to exchange information.

The CSE on an ASN or on an MN performs registration with the CSE in the IN in order to be able to use M2M Services offered by the CSE in the IN. As a result of successful ASN/MN registration with the IN-CSE, the CSEs on ASN/MN and IN establish a relationship allowing them to exchange information.

Registration is a pre-requisite for accessing services from the Registrar CSE.

Following a successful registration of an AE to a CSE, the AE is able to access, assuming access privilege is granted, the resources in all the CSEs that are potential targets of request from the Registrar CSE.

The capabilities supported by the REG CSF are as follows:

- Ability for AEs to register to their associated CSE, as per Table 6.2.9.2-1.

Ability for CSE to register to the other CSE, as per Table 6.2.9.2-1.

Ability for an ASN-CSE/MN-CSE to register association of its M2M-Ext-ID (if available) with its CSE-ID, (see clause 7.1.8)

Ability for an ASN-CSE/MN-CSE to register association of its Trigger-Recipient-ID (if available) with its CSE-ID, (see clause 7.1.8). When Trigger-Recipient-ID is not present, it is assumed that the CSE is not able to receive triggers.

Note: Such registrations are applicable to a single M2M Service Provider Domain.

Rapporteur’s Note: The following table and text are suggested to be moved to a new normative clause regarding Inter-CSE Registration

The following Table shows which oneM2M entity types can register with which other entity types.

Table 6.2.9.2-1: Entity Registration

| Originator (Registree) | Receiver (Registrar) | Registration Procedure |
| --- | --- | --- |
| ADN-AE | MN-CSE, IN-CSE | AE registration procedure see clause TBD |
| ASN-AE | ASN-CSE |  |
| MN-AE | MN-CSE |  |
| IN-AE | IN-CSE |  |
| ASN-CSE | MN-CSE, IN-CSE | CSE registration procedure see clause TBD |
| MN-CSE | MN-CSE, IN-CSE |  |

The Originator (Registree) in Table 6.2.9.2-1 requests the registration and the Receiver (Registrar) is responsible for verifying the request, and checking the authentication and authorization of the Originator in order to establish a peer relationship.

[6.2.9.2.c] Editor’s Note: Authorization above might only be needed for AEs, this is FFS in Security WG

An AE can not be registered to more than one CSE (ASN-CSE, MN-CSE or IN-CSE).

An ASN-CSE can be registered to at most one other CSE (MN-CSE or IN-CSE).

An MN-CSE can be registered to at most one other IN-CSE.

An MN-CSE can support only a single registration towards another MN-CSE or an IN-CSE. A concatenation (registration chain) of multiple uni-directional registrations shall not form a loop. E.g., Two MN-CSEs A and B, can not register with each other. Three MN-CSEs A, B and C, where A registers to B, and B registers to C, then C can not register to A.

Registration information shall be able to include:

Identifier.

Reachability schedules; which are elements of a node's policy, and specify when messaging can occur between nodes. Reachability schedules can be used in conjunction with other policy elements. When reachability schedules are not present in a node then that node is expected to be always reachable.

[6.2.9.2.e] Editor's note: Further Registration information is FFS.

### -------------------------------End of changes ---------------------------------------------

# Comments

This is needed before deleting Editor’s note 6.2.9.2.b and {8.4.2.1.a} :Editor’s Note: M2M-Ext-ID is set on registration, how the IN-CSE gets it is FFS. and [7.1.8.a} Editor's Note:  The method for dynamic plug-and-play association of M2M-Ext-ID and the 3GPP Underlying Network Identifier is FFS.