| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Barbara Pareglio, NEC barara.pareglio@neclab.eu Martin Bauer, NEC, Martin.Bauer@neclab.eu Joerg Swetina, NEC, Joerg.Swetina@neclab.eu Seongyoon Kim, LGE, seongyoon.kim@lge.com |
| Format:* | ARC#11 |
| Date:* | 2014-04-15 |
| Contact:* | Barbara Pareglio, Martin Bauer, Joerg Swetina, NEC |
| Reason for Change/s:* | Cleaned up clause 9.6.3, 9.6.4 and 10.2.2 |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Current description of CSE resources: CSEBase and remoteCSE includes 2 attributes that do not have a well-defined description and they need some refinements:

- cseType

- supportedResourcesType

Regarding the cseType it is not clear what the intention of the attribute and how it should be used. The specification never talks about different type of CSEs. It seems to be that these attributes should contain information depending on the topology, thus IN-CSE, MN-CSE and ASN-CSE.

This is probably the initial intention (even if it is not really said), but the TS never indicates how and when such an attribute should be used and by whom. Therefore, this contribution proposes to change the multiplicity from mandatory to optional and to make such an attribute read-only.

Regarding the supportedResourcesType attribute the idea is to extend the description and to indicate that the attribute will contain an exact list of the supported ResourceType and for each ResourceType also the supported attributes.

R02: Removing 10.2.9 since supportedResourceType contains supported attributes also.

### -----------------------Start of change 1-------------------------------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource 
(only resource specific attributes are shown)

This resource shall contain the child resources according to their multiplicity in Table 9.6.3-1 (0 indicates the optionality of the child resource).

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See section 9.6.4 |
| [variable] | <node> | 1 | See section 9.6.19 |
| [variable] | <application> | 0..n | See section 9.6.5 |
| [variable] | <container> | 0..n | See section 9.6.6 |
| [variable] | <group> | 0..n | See section 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See section 9.6.2 |
| [variable] | <subscription> | 0..n | See section 9.6.8 |
| [variable] | <mgmtObj> | 0..n | See section 9.6.15 |
| [Variable] | <mgmtCmd> | 0..n | See section 9.6.17 |
| [Variable] | <locationPolicy> | 0..n | See section 9.6.10 |

{9.6.3.a} Editor’s Note: this list should be updated. Which resource types are added is FFS.

{9.6.3.b} Editor’s Note: how to extend functionality is FFS.

The <CSEBase> resource shall contain the attributes described in Table 9.6.3-2.

Table 9.6.3-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| creationTime (cT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| accessControlPolicyID (aRI) | 0..n | RW | See section 9.6.1 where this common attribute is described. |
| labels (lBs) | 0..1 | RW | See section 9.6.1 where this common attribute is described. |
| cseType (csT) | 0..1 | RO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType (sRT) | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in section 9.2. For each supported resourceType this attribute also indicates the supported optional attributes. |
| pointOfAccess (poA) | 0..n | RW | represents the list of physical addresses to be used for remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information only if this <application> resource is about ADN-AE and the <node> resource is existed in the parent resource, <CSEBase>. |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. |

### 9.6.4	Resource Type remoteCSE

A <remoteCSE> resource shall represent a remote CSE that is registered to the local CSE. CSE resources shall be located directly under the <CSEBase>.

Conversely each registered CSE shall also be represented as a sub-set of <remoteCSE> resource in the registering CSE's <CSEBase>.

For example, when CSE1 registers with CSE2, there will be two <remoteCSE> resources created: one in CSE1 <CSEBase1>/<remoteCSE2> and one in CSE2 <CSEBase2>/<remoteCSE1>.

Note that the creation of the two resources does not imply mutual registration. The <CSEBase1>/<remoteCSE2> is only local to CSE1 and is for its internal use.

Figure 9.6.4-1: Structure of <remoteCSE> resource 
(only resource specific attributes are shown)

{9.6.4.a} Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

This resource shall contain the child resources according to their multiplicity in Table 9.6.4-1 (0 indicates the optionality of the child resource).

# Table 9.6.4-1: Child resources of <remoteCSE> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description | <remoteCSEAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <application> | 0..n | See clause 9.6.5 | <applicatoinAnnc> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicyAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <mgmtObj> | 0..n | See clause 9.6.15 | <mgmtObjAnnc> |
| [variable] | <pollingChannel> | 0..n | See section 9.6.22. If requestReachability is FALSE, the CSE that created this <remoteCSE> should create a <pollingChannel> resource and perform long polling. | ?? |
| [variable] | <node> | 0..1 | See section 9.6.19. This child resource contains the node specific information only when the information represented by this resource is from a node of type ASN or MN. | ?? |

The <remoteCSE> resource shall contain the attributes described in Table 9.6.4-2.

# Table 9.6.4-2: Attributes of <remoteCSE> resource

| Attribute Name of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| accessControlPolicyID (aRI) | 0..n | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| Link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <remoteCSEAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| cseType (csT) | 0..1 | RO | Indicates the type of CSE node represented by the created resource. | OP |
| pointOfAccess (poA) | 0..n | RW | For request-reachable remote CSE it represents the list of physical addresses to be used to connect to it (e.g. IP address, FQDN). The attribute is absent if the remote CSE is not request-reachable. | OP |
| CSEBase (bRt) | 1 | WO | The URI of the CSEBase of the original CSE represented by remote CSE. | OP |
| CSE-ID | 1 | WO | The globally unique CSE identifier. | OP |
| Trigger-Recipient-ID | 0..1 | RW | See section 7.1.10 where this attribute is described. | ?? |
| requestReachability | 1 | RW | If the CSE that created this <remoteCSE> can receive a request from other AE/CSE(s), this attribute is set to “TRUE” otherwise “FALSE”. NOTE: Even if this attribute is set to “FALSE”, it does not mean it AE/CSE is always unreachable by all entities. E.g., the requesting AE/CSE is behind the same NAT, so it can communicate within the same NAT. | ?? |

<remoteCSE> and announced <remoteCSE> shall have different resourceType coding.

{9.6.4.b} Editor's Note on CSE-ID: an alignment between CSE-ID and CSEBase is needed.

{9.6.4.c} Editor's Note on CSEBase: the alignment with naming convention proposed for inter-M2M service provider is needed.

{9.6.4.d} Editor's Note on child resources: child resources of <remoteCse> resource can accommodate listed resources and their announced versions.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 10.2.2	<RemoteCSE> Resource

#### 10.2.2.1	Create <RemoteCSE>, aka CSE Registration

This flow is used for creating a <RemoteCSE> resource. It is part of the registration procedure for remote CSEs on the local CSE (which is also the hosting CSE), as described in section 10.1.1.2.1

Originator:  A CSE.

Receiver : Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section XXX), the Receiver shall grant the request after successful verification of the request

Table 10.2.2.1-1 <remoteCSE> CREATE flow

| CREATE: Description |
| --- |
| Pre-Conditions | The Originating CSE is successfully authorized. The Originating CSE has an assigned CSE-ID.. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable plus specifically: fr: CSE-ID. nm: the name of the <remoteCSE> resource is optional cn: the resource content shall provide the information as defined in section 9.6.19. The following attributes from section 9.6.19 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the <remoteCSE> resource as defined in 9.6.1 “CSE-ID”: which contains the CSE-ID The following attributes from section 9.6.19 are optional for the request: “expirationTime” “accessControlPolicyID” “labels” “pointOfAccess” "cseType" |
| Local processing on Hosting CSE | No change from the basic CREATE procedure (section 10.1.1) |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: URI of the created <remoteCSE> resource, according to section 10.1.1 |
| Post-Conditions | Two new <remoteCSE> resources are created, one on the targeted CSE (Receiver) and one under the <CSEBase> of the Originator that correspond to the CSE of the Receiver. |
| Exceptions | All exception described in the basic CREATE procedure (section 10.1.1) are applicable. |

### -----------------------End of change 2-------------------------------------------

### ----------------------- Start of change 3-------------------------------------------

### -----------------------End of change 3-------------------------------------------