ARC-2014-1319R01

| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | Rajesh Bhalla, ZTE, rabhalla@ztetx.com Hao Wu, ZTE, wu.hao18@zte.com.cn Seungkyu Park, LGE, seungk.park@lge.com |
| Format:* | ARC #10.1 |
| Date:* | 2014-04-24 |
| Contact:* | Rajesh Bhalla, Hao Wu, ZTESeungkyu Park, LGE |
| Reason for Change/s:* | Specify attribute Announcement, De-announcement procedures. Such procedures use (partial addressing) methods specified in clause 10.1.3 and clause 10.1.4. |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes methods for supporting attribute announcement and de-announcement.

Attribute announcement/de-announcement is supported by the use of UPDATE and DELETE operations.

### -----------------------Start of change 1-------------------------------------------

#### 10.2.18.6	Procedure for AE and CSE to initiate the Creation of an  Announced Attribute

This clause describes the procedure for an AE and CSE  to initiate the creation of an announced attribute (attribute announcement).

Originator: The Originator of a Request, for initiating attribute announcement, can be either AE or CSE. The Originator shall request attribute announcement by updating the announcedAttribute attribute at the original resource:

The Originator shall update the announcedAttribute attribute at the original resource by adding to it the attributes that need to be announced by using the UPDATE Request. Only the attributes marked with OA can be announced to remote announced resources.

Receiver: Once the Originator has been successfully authorized, the Receiver, which shall be the original resource hosting CSE, shall grant the Request after successful validation of the Request.

The attributes received in the Request, which are not marked as OA, are invalid.

The attributes received in the Request, which are not present in the original resource structure, are invalid.

If some attributes received in the Request do not already exist in the announcedAttribute attribute, the Receiver shall announce such attributes to all announced resources listed in the announceTo attribute as per procedures in clause 10.2.18.8.

On successful announcement of attributes as per procedures in clause 10.2.18.8, the Receiver shall perform the following:

The Receiver shall respond to the requesting AE/CSE with UPDATE Response as specified in clause 10.1.3. The content of the announced attributes can be provided in such Response.

Table 10.2.18.6-1: Creating Announced Attributes

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | A resource has already been announced. |
| Information on Request message | Parameters defined in Table 8.1.2.1-1 that are applicable for UPDATE. cn parameter includes the names of the attributes to be announced. |
| Local processing on Hosting CSE | Steps described for the Receiver of the Request as described above |
| Information on Response message | Parameters defined in Table 8.1.2.1-1 that are applicable. |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedures in clause 10.1.3 are applicable. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 10.2.18.7	Procedure for AE and CSE to initiate the Deletion of an  Announced Attribute

This clause describes the procedure for an AE and CSE to initiate the deletion of an announced attribute (attribute de-announcement).

Originator: The Originator of a Request, for initiating attribute de-announcement, can be either AE or CSE. The Originator shall request attribute de-announcement by updating the announcedAttribute attribute at the original resource as follows:

The Originator shall update the announcedAttribute attribute at the original resource by deleting from it the attributes that need to be de-announced by using the UPDATE Request. Only the attributes marked with OA can be de-announced to remote announced resources.

Receiver: Once the Originator has been successfully authorized, the Receiver, which shall be the original resource hosting CSE, shall grant the Request after successful validation of the Request.

The attributes received in the Request, which are not marked as OA, are invalid.

If some attributes that exist in the announcedAttribute attribute are not received in the Request (i.e., those attributes will be deleted by the UPDATE Request), the Receiver shall de-announce such attributes to all announced resources listed in the announceTo attributes as per procedure in clause 10.2.18.9.

On successful de-announcement of all attributes as per procedures in clause 10.2.18.9, the Receiver shall perform the following:

The Receiver shall respond to the requesting AE/CSE with UPDATE Response as specified in clause 10.1.3. The names of the de-announced attributes can be provided in such Response.

Table 10.2.18.7-1: Deleting Announced Attributes

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | A resource has already been announced. |
| Information on Request message | Parameters defined in Table 8.1.2.1-1 that are applicable for UPDATE.. cn parameter does not include the names of the attributes to be de-announced. |
| Local processing on Hosting CSE | Steps described for the Receiver of the Request as described above |
| Information on Response message | Parameters defined in Table 8.1.2.1-1 that are applicable. |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedures in clause 10.1.3 are applicable. |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 10.2.18.8	Procedure for original resource hosting CSE for Announcing Attributes

This clause describes procedure that shall be used by the original resource hosting CSE to create announced attributes at the remote announced resources (i.e., the attribute announcement).

Originator: The Originator of this Request shall be the original resource hosting CSE. The Originator shall request to create announced attributes at the announced resources by using the UPDATE Request as specified in clause 10.1.3.

Receiver: Once the Originator has been successfully authorized, the Receiver (CSE hosting announced resource) shall grant the Request after successful validation of the Request. The Receiver shall perform as follows:

Create announced attributes at the announced resource as per procedures for partial addressing in clause 10.1.3. The initial value for the announced attribute shall use the same value with the original resource.

Respond to the Originator with UPDATE Response as in clause 10.1.3.

Originator after receiving the Response from the Receiver shall perform the following steps: If the announced attributes have been successfully created, the announcedAttribute attribute shall be updated to include the attribute names for the successfully announced attributes.

For the newly announced attributes in the announcedAttribute attribute, the Originator shall take the responsibility to keep their values synchronized at the announced resources by using UPDATE operation as in clause 10.1.3.

Table 10.2.18.8-1: Original Resource Hosting CSE to Announce Attribute: UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | Only the attribute marked with OA can be announced. |
| Information on Request message | Information described for the Originator of the UPDATE Request as in clause 10.1.3. |
| Local processing on Hosting CSE | Steps described for the Receiver of the UPDATE Request as described in clause 10.1.3. |
| Information on Response message | Steps described for the Receiver of the UPDATE Request as described in clause 10.1.3. |
| Post-Conditions | Steps described for the 'Originator on receiving the Response from the Receiver' as described in clause 10.1.3 |
| Exceptions | All exceptions described for the basic procedure in clause 10.1.3. |

### -----------------------End of change 3-------------------------------------------

-----------------------Start of change 4-------------------------------------------

#### 10.2.18.9	Procedure for original resource hosting CSE for De-Announcing Attributes

This clause describes procedure that shall be used by the original resource hosting CSE to remove announced attributes at remote announced resources (i.e., the attribute de-announcement).

Originator: The Originator of this Request shall be the original resource hosting CSE. The Originator shall request to delete an announced attribute by using the DELETE Request as specified in clause 10.1.4. The to parameter in the DELETE Request provides a URI that identifies the announced attribute to be deleted

Receiver: Once the Originator has been successfully authorized, the Receiver (CSE hosting announced resource) shall grant the Request after successful validation of the Request. The Receiver shall perform as follows:

Delete the de-announced attribute identified by the to parameter in the DELETE Request as per procedures for partial addressing in clause 10.1.4.

Respond to the Originator with the appropriate DELETE Response as in clause 10.1.4.

Originator after receiving the Response from the Receiver shall perform the following steps: If the de-announced attribute has been successfully removed, the announcedAttribute attribute shall be updated so as to remove the attribute name for the successfully de-announced attribute.

Table 10.2.18.9-1: Original Resource Hosting CSE to De-Announce Attribute: DELETE

| Description |
| --- |
| Call Flow Type | DELETE |
| Pre-Conditions | Only the attribute marked with OA can be de-announced |
| Information on Request message | Information described for the Originator of the DELETE Request as in clause 10.1.4. |
| Local processing on Hosting CSE | Steps described for the Receiver of the DELETE Request as described in clause 10.1.4. |
| Information on Response message | Steps described for the Receiver of the DELETE Request as described in clause 10.1.4. |
| Post-Conditions | Steps described for the 'Originator on receiving the Response from the Receiver' as described in clause 10.1.4. |
| Exceptions | All exceptions described for the basic procedure in clause 10.1.3. |

### -----------------------End of change 4-------------------------------------------