| CHANGE REQUEST |
| --- |
| Group Name:* | <WG2> |
| Source:* | Rajesh Bhalla, ZTE, rabhalla@ztetx.com Hao Wu, ZTE, wu.hao18@zte.com.cn Seungkyu Park, LGE, seungk.park@lge.com |
| Format:* | ARC#10.5 |
| Date:* | 2014-05-29 |
| Contact:* | Rajesh Bhalla, Hao Wu, ZTE Seungkyu Park, LGE |
| Reason for Change/s:* | Attribute announcement procedure is broken. |
| CR against: Release* |  |
| CR against: TS/TR* | TS-0001 v0.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

For current complete procedure of resource announcement, the announceTo attribute will be updated twice according clause 10.2.18.

For resource announcement:

In Clause 10.2.18.1 	Procedure for AE and CSE to initiate Creation of an Announced Resource

Receiver: Once the Originator has been successfully authorized, the Receiver (which shall be the original resource hosting CSE) shall grant the Request after successful validation of the Request.

For UPDATE Request, the Originator shall add the received exact URI or the CSE-ID to the announceTo attribute at the original resource, if such exact URI or CSE-ID is not already stored in the announceTo attribute.

For CREATE Request, the Originator shall include the received exact URI or the CSE-ID in the announceTo attribute created at the original resource.

In Clause 10.2.18.4	Procedure for original resource Hosting CSE to Create an Announced Resource

The Originator after receiving the Response from the Receiver shall perform the following steps:

If the announced resource has been successfully created, the announceTo attribute of the original resource shall be updated to include the URI(s) for the successfully announced resource at the Receiver. The announcedAttribute attribute shall be updated as well to represent the successfully announced attributes as received in the Response

This could cause the announceTo attribute to include the URIs for the successfully announced resource twice or the URIs for the unsuccessfully announced resource.

Same consideration is also for the procedure of resource de-announcement. To correct this problem, the following changes are proposed:

1. To delete the receiver behaviour for updating ‘announceTo’ attribute in 10.2.18.1 as in Change 1.

2. To delete the receiver behaviour for updating ‘announceTo’ attribute in 10.2.18.3 as in Change 2.

### -----------------------Start of change 1-------------------------------------------

### 10.2.18	Resource Announcement Procedure

#### 10.2.18.1 	Procedure for AE and CSE to initiate the Creation of an Announced Resource

This clause describes the procedure for an AE or a CSE to initiate the creation of an announced resource.

Originator: The Originator of a Request for initiating resource announcement can be either an AE or a CSE. The Originator can initiate the creation of an announced resource during the creation of the original resource by providing the announceTo attribute in the CREATE Request. The Originator can initiate the creation of an announced resource by using the UPDATE Request to the announceTo attribute in the original resource as follows:

The Originator shall perform the following for  the creation of an announced resource:

The Originator can provide either the exact URI(s) for the announced resource or the list of CSE-IDs of the remote CSEs where the original resource needs to be announced by including such information within the attributeTo of the UPDATE or CREATE Request. In case of the CSE-IDs, the Receiver (original resource hosting CSE) shall decide the exact location for the announced resource at the remote CSE identified by the CSE-ID.

Receiver: Once the Originator has been successfully authorized, the Receiver (which shall be the original resource hosting CSE) shall grant the Request after successful validation of the Request.

If the Request provides an exact URI(s) that are not already stored in the announceTo attribute or for newly created announceTo attribute, the Receiver shall announce the resource to the location identified by the URI(s) as per procedures in clause10.2.18.4.

If the Request provides a list of CSE-IDs of the remote CSE that are not already stored in the announceTo attribute of for newly created announceTo attribute, the Receiver shall decide the location at the remote CSE(s) identified by CSE-ID(s) for announcing the resource and shall perform the procedures in in clause 10.2.18.4.

On successful completion of resource announcement as in clause 10.2.18.4, the Receiver shall performs the following:.

The Receiver shall provide the exact URI(s) of the announced resource to the Originator by updating the content of the announceTo attribute in the original resource and by providing it in the UPDATE or CREATE Response message depending on the Request.

Table 10.2.18.1-1: Resource Announcement: UPDATE or CREATE

| UPDATE or CREATE Description |
| --- |
| Pre-Conditions | The Originator suggests the URI(s) or the CSE-ID(s) to which the resource will be announced. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table. In addition in case of CREATE the procedure for the specific resource is described in clause 10.2. The specific information relevant for announcing is: cn: contains address where the resource needs to be announced (within announcedTo attribute) |
| Local processing on Hosting CSE | Steps described for the Receiver of the Request as described above |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for cn asdescribed above for the Receiver of the Response |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedures (section 10.1.1) are applicable. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 10.2.18.3 	Procedure for AE and CSE to initiate Deletion of an Announced Resource

This section describes the procedure for an AE or a CSE (not the original resource hosting CSE) to initiate the deletion of an announced resource.

Originator: The Originator of a Request for initiating resource de-announcement can be either an AE or a CSE The Originator can request to initiate the deletion of an announced resource by using UPDATE Request to the announceTo attribute at the original resource hosting CSE. Resource de-announcement (deletion) shall also be performed when the Originator deletes the original resource at the original resource hosting CSE by using DELETE Request.

The Originator shall perform as follows for the deletion of an announced resource.

The Originator shall update the announceTo attribute at the original resource hosting CSE by providing new content of the announceTo which does not include the URI of the announced resource that needs to be de-announced (deleted) in the UPDATE operation.

The Originator shall update the original resource in the hosting CSE by providing new representation of the resource that does not contain the announceTo attribute for all the previously announced resources by using an UPDATE operation

For DELETE Request, the Originator shall include the URI ofr the original resource hosting CSE that needs to be deleted, in the DELETE Request.

Receiver: Once the Originator has been successfully authorized, the Receiver (which shall be the original resource hosting CSE) shall grant the Request after successful validation of the Request. The Receiver shall be the resource hosting CSE. On receiving the UPDATE or DELETE Request, the Receiver shall perform as follows:

For UPDATE Request, the Receiver shall request to delete the announced resource whose URI is deleted in the announceTo attribute as per procedures in clause 10.2.18.5

For DELETE Request, the Receiver shall request to delete all announced resources in the announcedTo attribute as per procedures in clause 10.2.18.5.

Receiver after completion of the resource de-announcement procedure in clause 10.2.18.5:

On successful completion of resource de-announcement procedure in clause 10.2.18.5, the Receiver knows that the announced resource has been deleted.

The Receiver shall provide confirmation of resource de-announcement to the Originator, and the content of the updated announceTo attribute shall be provided to the Originator to indicate the successfully deleted announced resource if the announceTo attribute is not deleted by the Originator.

Table 10.2.18.3-1: Resource De-Announcement: UPDATE and DELETE

| UPDATE and DELETE Description |
| --- |
| Pre-Conditions | None |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the specific details for. cn: contains Either the modified announceTo attribute Or a complete representation of the original resource without the announceTo attribute In case of DELETE, the generic procedure is described in clause 10.1.4 cn: void |
| Local processing on Hosting CSE | The basic procedure (clause 10.1.3 for UPDATE and 10.1.14 for DELETE) still applies in addition the steps described above for the Receiver of the Request also apply |
| Information on Response message | The basic procedure (clause 10.1.3 for UPDATE and 10.1.4 for DELETE) still applies in addition the steps described above for the Receiver of the Request also apply |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section10.1.2) are applicable for UPDATE operation. All exceptions described in the basic procedure (section10.1.4) are applicable for DELETE operation |

### -----------------------End of change 2-------------------------------------------