| CHANGE REQUEST |
| --- |
| Group Name:* | ARC 11.0 |
| Source:* | Philip Jacobs, Cisco Systems, phjacobs@cisco.com |
| Format:* | Teleconference |
| Date:* | 2014-05-20 |
| Contact:* |  |
| Reason for Change/s:* | Missing procedures for <schedule> resource. Outdated resource summary table. Missing relationship description between <schedule> and other resources Missing usage information of <schedule> for <subscription> R01 is due to meeting re-assignment |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | oneM2M-TS-0001 - V-0.6.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The is no clause covering procedures regarding the <schedule> type resource. This contribution proposes the addition of such a new clause.

The child and parent resource types regarding <subscription> Table 9.6-1 have become outdated. This contribution proposes an update.

The description of the resource type <schedule> has very little detail, and doesn’t say how it is used in oneM2M. This contribution proposes an update.

The <subscription> resource type does not describe how it uses <schedule> in Table 9.6.8.1. This contribution proposes an update.

### -----------------------Start of change 1-------------------------------------------

### 10.2.xx	<schedule> Resource Procedure

An Originator shall have the same access control privileges to the <schedule> resource as it has to its parent resource.

#### 10.2.xx.1	Create <schedule>

This procedure shall be used for creating a <schedule> resource.

Originator: The AE or CSE Originator shall request to create a new <schedule> resource following the procedures of clause 10.1.1.1

Receiver: The Hosting CSE shall follow the procedures of clause 10.1.1.1

Table 10.2.xx.1-1: <schedule> CREATE

| Description |
| --- |
| Information in Request message | Parameters for CREATE in Table 8.1.2.1-1 are applicable, with the specific details for: cn: which shall contain the representation of the <schedule> resource described in clause 9.6.9. |
| Local processing on Hosting CSE | No change from the non-registration CREATE procedure described in clause 10.1.1.1 |
| Information in Response message | Parameters for CREATE in Table 8.1.4.-1 are applicable, with the specific details for: cn: URI and/or content of the created <schedule> resource , according to clause 10.1.1.1 |
| Exceptions | All exceptions described in the clause 10.1.1.1 are applicable. |

#### 10.2.xx.2	Retrieve <schedule>

This procedure shall be used for retrieving the attributes of a <schedule> resource.

Originator: The AE or CSE shall request to retrieve <schedule> resource information following the procedures of clause 10.1.2.

Receiver: The Hosting CSE shall follow the procedures of clause 10.1.2.

Table 10.2.xx.2-1: <schedule> RETRIEVE

| Description |
| --- |
| Information in Request message | Parameters for RETRIEVE in Table 8.1.2.1-1 are applicable, with the specific details for: cn: is the filter to be applied for discovery purposes. |
| Local processing on Hosting CSE | No change from the basic procedure described in clause 10.1.2 |
| Information in Response message | Parameters for RETRIEVE in Table 8.1.4.-1 are applicable, with the specific details for: cn: attributes of the <schedule> resource |
| Exceptions | All exceptions described in clause 10.1.2 are applicable. |

#### 10.2.xx.3	Update <schedule>

This procedure shall be used for updating the attributes of a <schedule> resource. The set of scheduleElement attributes together represent the defined schedule. All scheduleElement attributes shall be updated as a set.

Originator: The AE or CSE shall request to update <schedule> resource information following the procedures of clause 10.1.3.

Receiver: The Hosting CSE shall follow the procedures of clause 10.1.3.

Table 10.2.xx.3-1: <schedule> UPDATE

| Description |
| --- |
| Information in Request message | Parameters for UPDATE in Table 8.1.2.1-1 are applicable, with the specific details for: cn: attributes of the <schedule> resource |
| Local processing on Hosting CSE | No change from the generic procedure from clause 10.1.3. |
| Information in Response message | No change from the generic procedure from clause 10.1.3. |
| Exceptions | All exceptions described in the clause 10.1.3 are applicable. |

#### 10.2.xx.4	Delete <schedule>

This procedure shall be used for deleting an existing <schedule> resource.

Originator: The AE or CSE shall request to delete an existing <schedule> resource following the procedures of clause 10.1.4.

Receiver: The Hosting CSE shall shall follow the procedures of clause 10.1.4.

Table 10.2.xx.4-1: <schedule> DELETE

| Description |
| --- |
| Information on Request message | Parameters for DELETE in Table 8.1.2.1-1 are applicable. |
| Local processing on Hosting CSE | No change from the generic procedure from clause 10.1.4. |
| Information on Response message | No change from the generic procedure from clause 10.1.4. |
| Exceptions | All exceptions described in clause 10.1.4 are applicable. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the hosting CSE. It controls "who" is allowed to do "what" and the context in which it can be used for accessing the resources. . | subscription | AE, remoteCSE, CSEBase | 9.6.2 |
| contentInstance | Represents a data instance in the container resource. | subscription | container | 9.6.7 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the registrar CSE. | subscription, container, group, accessControlPolicy, mgmtObj, commCapabilities, pollingChannel | remoteCSE, CSEBase | 9.6.5 |
| cmdhBuffer | Defines CMDH buffer usage limits | subscription | cmdhPolicy | D.12.7 |
| cmdhDefaults | Defines CMDH default values | cmdhDefEcValue, cmdhEcDefParamValues subscription | cmdhPolicy | D.12.1 |
| cmdhEcDefParamValues | Represent a specific set of default values for the CMDH related parameters | subscription | cmdhDefaults | D.12.3 |
| cmdhDefEcValue | Defines a value for the ec (event category) parameter of an incoming request when it is not defined. | subscription | cmdhDefaults | D.12.2 |
| cmdhLimits | Defines limits for CMDH related parameter values | subscription | cmdhPolicy | D.12.4 |
| cmdhNetworkAccessRules | Defines rules for the usage of underlying networks | cmdhNwAccessRule subscription | cmdhPolicy | D.12.5 |
| cmdhNwAccessRule | Defines a rule for the usage of underlying networks | subscription | cmdhNetworkAccessRules | D.12.6 |
| cmdhPolicy | A set of rules defining which CMDH parameters will be used by default | cmdhDefaults, cmdhLimits, cmdhNetworkAccessRules, cmdhBuffer subscription | None | D.12 |
| container | Shares data instances among entities. Used as a mediator that takes care of buffering the data to exchange "data" between AEs and/or CSEs. The exchange of data between AEs (e.g., an AE on a Node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule. | container, contentInstance, subscription, | application, container, remoteCSE, CSEBase | 9.6.6 |
| CSEBase | The structural root for all the resources that are residing on a CSE. It shall store information about the CSE itself. | remoteCSE, node, application, container, group, accessControlPolicy, subscription, mgmtObj, mgmtCmd, locationPolicy, statsConfig | None | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | None documented | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.23 |
| execInstance | The Execution Instance resource contains all execution instances of the same management command mgmtCmd. | subscription | mgmtCmd | 9.6.17 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group. | fanOutPoint subscription | Application, remoteCSE, CSEBase | 9.6.13 |
| locationPolicy | Includes information to obtain and manage geographical location. It is only referred from container, the contentInstances of the container provides location information. | subscription | CSEBase | 9.6.10 |
| fanOutPoint | Virtual resource containing target for group requests It is used for addressing bulk operations to all the resources that belong to a group. | None | group | 9.6.14 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols. | execInstance subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node | parameters subscription | remoteCSE, CSEBase | 9.6.15 Annex D |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | nodeInfo subscription | None documented | 9.6.19 |
| node | Represents specific Node information | mgmtObj subscription | CSEBase, remoteCSE | 9.6.18 |
| nodeInfo | Node information | subscription | m2mServiceSubscription | 9.6.20 |
| parameters | Provides a mechanism to describe the management object in a generic way to easily import information from existing management protocols. | parameters subscription | mgmtObj, parameters | 9.6.16 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | None | remoteCSE, application | 9.6.21 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource. | application, container, group, accessControlPolicy, subscription, mgmtObj, pollingChannel, node | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | subscription | None documented | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | subscription | remoteCSE, subscription | 9.6.9 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | subscription | CSEBase (in IN-CSE) | 9.6.24 |
| statsConfig | Stores configuration of statistics for applications | eventConfig subscription | CSEBase (in IN-CSE) | 9.6.22 |
| subscription | Subscription resource represents the subscription information related to a resource. Such a resource shall be a child resource for the subscribe-to resource. | schedule | accessControlPolicy, application, cmdhBuffer, cmdhDefaults, cmdhEcDefParamValues, cmdhDefEcValue, cmdhLimits, cmdhNetworkAccessRules, cmdhNwAccessRule, cmdhPolicy, container, CSEBase, delivery, eventConfig, execInstance, group, contentInstance, locationPolicy, mgmtCmd, mgmtObj, m2mServiceSubscription, node, nodeInfo, parameters, remoteCSE, request, schedule, statsCollect, statsConfig | 9.6.8 |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 9.6.9	Resource Type schedule

The <schedule> resource contains scheduling information. It represents a calendar of arbitrary duration during which specific time periods are either True or False. The meaning of these time periods is contextual based upon the parent resource’s usage.

The <schedule> resource may be located as a child of:

<remoteCSE> type resource, usage is to indicate the time periods when the entities of a node are reachable.

<subscription> type resource (named notificationSchedule), usage is to indicate the time periods during which the subscribers may be notified.

It may be linked to, from <cmdhNwAccessRule> type resources. Usage is to indicate time periods when use of specific underlying networks is allowed.

An Originator shall have the same access control privileges to the <schedule> resource as it has to its parent resource.

### Figure 9.6.9-1: Structure of <schedule> resource

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

The <subscription> resource shall contain the child resources in Table 9.6.8-1.

# Table 9.6.8-1: Child resources of <subscription> resource

| Child Resource Name of <subscription> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| notificationSchedule | <schedule> | 0..1 | Indicates the time periods during which the subscribers may be notified. See clause 9.6.9 |

### -----------------------End of change 4---------------------------------------------